## Slide 1: Gantry layouts for brainstorming
Elena Benedetto, SEEIIST Association
Ugo Amaldi, TERA Foundation

## Slide 2: SCANNING SYSTEM
“A Carbon Ion SuperconductingGantry and a Synchrotron based on Canted Cosine Theta magnets” (https://arxiv.org/abs/2105.04205)
E. Benedetto1,3, N.AlHarbi1, L.Brouwer2,D.Tommasini3, S.Prestemon2, P.Riboni1 and U.Amaldi1
1TERA Foundation, Novara, Italy; 2LBNL, Berkeley, USA; 3CERN, Geneva, Switzerland

## Slide 3: ADVANCED FIRST LAYOUT
4T AG-CCT magnets
External radius 5 m
Small aperture D= 40 mm
“A Carbon Ion SuperconductingGantry and a Synchrotron based on Canted Cosine Theta magnets” (https://arxiv.org/abs/2105.04205)
E. Benedetto1,3, N.AlHarbi1, L.Brouwer2,D.Tommasini3, S.Prestemon2, P.Riboni1 and U.Amaldi1
1TERA Foundation, Novara, Italy; 2LBNL, Berkeley, USA; 3CERN, Geneva, Switzerland

## Slide 4: SIGRUM - CONSERVATIVE DESIGN
“SIGRUM –A superconducting ion gantry with Riboni’s Unconventional Mechanics“
U,Amaldi, N. Alharbi, E Benedetto1, P.L. Riboni and M. Vaziri, TERA Foundation
D. Aguglia, V. Ferrentino. G. Le Godec, M. Karppinen, D. Perini, E. Ravaioli and D. Tommasini, CERN
CERN-NIMMS-Note-002: https://cds.cern.ch/record/2766876?ln=en
3T combined function magnets
Two bends, locally achromat  acceptance Dp/p=+/-1%
    3x 450 magnets (same gradient) w. 2 quads
    2x 22.50 magnets (same gradient) w. quad
External radius is large, aperture D=70mm

## Slide 5: COMPACT PROPOSAL FOR SIGRUM
  Reduce external radius
  Ease magnet manufacture

## Slide 6: FOUR IDENTICAL MAGNETS + special SC QUAD
“SIGRUM-45: A Ion Gantry a la Riboni
Based on Four 45° Superconducting Magnets”, June 2021
U. Amaldi, TERA Foundation,
E. Benedetto, TERA, CERN, SEEIIST
4T, pure dipole field (CF gradient is zero as baseline)
Special SC quad. superimposed to the dipoles coils (straight cosin-theta or CCT), ~2.6 T/m gradient, Lmag= 40cm
External radius 5.45 m
Small beta functions
tracking backward through last 2 magnets

## Slide 7: FOUR MAGNETS w. DIFFERENT GRADIENTS
“SIGRUM-45: A Ion Gantry a la Riboni
Based on Four 45° Superconducting Magnets”, June 2021
U. Amaldi, TERA Foundation,
E. Benedetto, TERA, CERN, SEEIIST
either combined functions (but all different!)
or with an independent quadrupole trim
both beta-functions and dispersion small!
tracking backward through last 2 magnets
@3.5 T

## Slide 8: CAN WE MAKE IT <5M RADIUS?
(1)
B=4T  4.5 T
rho=1.65m  1.32m
(2)
Reduce:
iron on the outer side (transverse)
space for end-coils (longitudinal)
interspace between dipoles
space for the cryostat
(3)
Reduce SAD by 15 cm:
still 26 cm x 30 cm

## Slide 9: CONCLUSIONS
Intermediate (size & complexity) solution between initial 4T 900 AG-CCT magnets and conservative 3T 450 – 22.50 combined function cosine-theta magnets designs allows to:
  Reduce dimensions: external radius & total length
  Ease manufacture
  Control beam dimensions & dispersion
Four 450 magnets at 4T. Two options :
  Identical (zero gradient) dipoles + special superimposed straight SC Quad coils
  Combined-function magnets with different gradients (ideally trimmable)