## Slide 1: Quattor and Virtualization
C. Loomis (CNRS/LAL)
Quattor Workshop (RAL)
13 October 2010

## Slide 2: Existing Virtualization Use & Support
Use of virtualization
  Survey showed that 80% of sites use some virtualization
  Easy integration as PXE booting supported by all hypervisors
Specific support
  S. Childs (TCD) provided configuration component for Xen
  Support in schema and component for associating hosts and guests

## Slide 3: StratusLab Contributions
New configuration components
  ncm-libvertd: configure and control libvirt
  ncm-oned: configure and control OpenNebula, a virtual machine mgr.
Quattor configuration of “cloud”
  Configures OpenNebula, incl. NFS mounts, etc.
  Configures private and public network bridges
  HTTPS proxy for OpenNebula XMLRPC server
  Ganglia for rudimentary monitoring of cloud infrastructure
Manual configuration:
  Definition/addition of hosts in the cloud ( register via cron/service)
  NFS mounts verification at installation ( autoconf)

## Slide 4: Contextualization
Need flexible, general solution to give virtual machine information about its execution environment.
StratusLab technique:
  Networking configuration done through DHCP
  Files and parameters passed through disk mounted on /dev/hdc
  Initialization script on disk run through rc.local
Handling of credentials
  SSH host keys, login keys, … can all be passed as part of context
  Grid host certificates can be handled in the same manner

## Slide 5: Cleaner Impl. of “Dummy” WNs
Dummy WNs
  Identify one reference WNs and fully compile profile
  Others copy this WN and change name, network config., …
  One profile per node
  Compilation time scales with number of nodes
Using virtualization
  Allow one reference WN compilation, without node specific information
  Node specific information passed in through contextualization
  One profile per group of machines
  Compilation time scales with number of nodes
Requires: Mechanism for specifying state of fabric!

## Slide 6: Quattor as Appliance Generator
Bookkeeping!
  Creating and sharing VMs means that knowing what is contained in the VM, how it behaves, etc. becomes a difficult task
  Quattor is an excellent tool for storing the state of machines and being able to (re)generate those images
Requirements
  Already able to boot machines through PXE in standard way
  Would like to interface to virt-install to allow automated generation of images and their deployment
Implementation
  Need service listening for profile changes
  Extract information from profiles and trigger virt-install
  More difficult: deployment/management of images on fabric