## Slide 1: WG on Field Quality for Curved Magnets – HITRIplus WP7-WP8
Elena Benedetto, SEEIIST (WP7) & DANIEL BARNA, Wigner U. (WP8)
Joint SEEIIST-NIMMS meeting, 2/7/2021

## Slide 2: HITRIplus MAGNETS
3-5 Tesla
Bending angle 90o (up to)
Bending radius < 2m
Aperture 100mm (up to)
Combined function or AG layers
L. Rossi

## Slide 3: MANDATE - WG ON FIELD QUALITY FOR CURVED MAGNETS
The working group will study the problem of the best way to define the field quality for strongly curved magnets used for ion therapy, both for gantry and synchrotron, where the field level of 3-5 T implies curvature radius of 1-3 m and large aperture.
The working group, beside proposing useful operative parameters to characterize and compare the FQ content of various design, will also examine the various methods to measure and model the FQ content and make practical recommendations.
BEAM DYNAMICS
Synchrotron & Gantry
MAGNET DESIGN
MAGNET MEASUREMENT
FQ

## Slide 4: STRONGLY CURVED, LARGE APERTURE MAGNET FIELD QUALITY
At least 2 or 3 communities, let’s try to
Understand how we do things…
And establish a common language (or at least a manual)
BEAM PHYSICIST
MAGNET EXPERT
...there was an interesting workshop in 2013, btw:
Beam Dynamics meets Magnets https://indico.gsi.de/event/2352/

## Slide 5: BEAM DYNAMICS VS. MAGNETS (DESIGN & MEASUREMENTS)
Vs.
Multipole expansion, FFT on a reference radius
Rotating coil method
Only in straight geometry the coefficients are the same…
https://cds.cern.ch/record/283218/files/SLAC-75.pdf
In a curved magnet, a field
rn cos(n ϑ) (aka “multipole”)
is non-Maxwellian!!
One can sample Br in a circle and Fourier-analyze it ( “naïve” multipoles), but the meaning of the obtained coefficients is not intuitive, and not clear
Beam optics code (PTC) uses field derivatives:
All other Taylor expansion coefficients can be recursively calculated, if these are given
This should be the common interface between optics, design and measurement

## Slide 6: TOROIDAL COORDINATES - MULTIPOLES
A. Wolski, A.T. Herrod “Explicit symplectic integrator for particle tracking in s-dependent static electric and magnetic fields with curved reference trajectory”, https://doi.org/10.1103/PhysRevAccelBeams.21.084001
P. Schnitzer, GSI, “Toroidal elliptical multipoles” for FAIR
L. Brouwer, S.Caspi et al., Toroidal multipoles for CCT magnets
(at which stage do we really need them?)
Pros:
For analytical calculations
Cons:
Not intuitive
Evaluation of toroidal harmonics is said to be difficult

## Slide 7: A practical parameterization with intuitive meaning of parameters
Amplitude of swing at main radius
Pitch at main radius
# of turns
Analogous parameter of axial position: ϕ ↔ z
So modulate ϕ in the same way as for the straight magnet

## Slide 8: FRINGE FIELDS
Large aperture, small bending radius
Fringe field are important:
  model
  measure
  optimize coil ends
E. Todesco, Masterclass 2020
not any longer
B. Muratori, http://dx.doi.org/10.1103/PhysRevSTAB.18.064001

## Slide 9: OTHER TOPICS
  Gantry (single-pass) vs. synchrotron
    Is particle tracking through field maps enough?
    For synchrotrons it is out of question, too slow! Use codes like MADX/PTC
  Integrated field or 3D map?
    Fringe fields are important  require modeling (integrated quantities still…)
    also transitions in AG-CCTs
  Magnet design: current pattern optimization to get required field coefficients
  Effect of laminated joke on the field quality
  Field quality, modeling, measurement…up to which detail?
    Characterizing quickly to compare and take decisions VS do the tracking !!!!
    Whatever the modeling (Fourier expansion or field derivatives) if the coefficients are small enough, the field quality is good enough! ;) S. Russenchuck provocative
    Completely measure full 3D map Vs. qualify the magnet to validate the model? (for 900 magnet no access)
  Trim coil to fine-tune independently quadrupole &dipole

## Slide 10: 1 or 2 SHORT TALKS (to learn what we do) + DISCUSSION SESSION
  Magnetic field measurements in curved geometry (C. Petroni CERN, G .Montenero PSI, E.DeMatteis INFN)
  Field characterization, common framework (D. Barna)
  Gantry (E. Felcini)
  Synchrotron (E. Benedetto)
  Identifications of tasks (D. Barna)
Topics for future meetings
  Tracking and optimization inside the PSI CCT gantry (A.Gerbershagen CERN, will be invited)
  RAT code to generate CCT coils geometry (J.Van Nugteren will be invited)
  ISOLDE synchrotron based on CCTs (Liverpool group, Glyn Kirby)
  Analytical reconstruction of field from flux measurements (S. Russenchuck and collaborators…)
  Results from tasks…

## Slide 11: SUMMARY - WG on Field Quality for Curved Magnets
1 meeting per month (approx)
15 people present at the last meting
  CERN (Magnets group & NIMMS), PSI, INFN (MI, GE), CNAO, Wigner University, SEEIIST
3 communities represented, need to find a common ground:
  beam dynamics, magnet design, magnet measurements
Program of work starts taking shape…

## Slide 12: Progress
Set up a regular scheme for meetings
Proposed a convention for coordinate systems and coordinate symbols, variables
Proposed common framework: field derivatives
Naïve “multipoles” discussed
Discussed measurement possibilities
Converged on winding parametrization