## Slide 1: RFQ3 beam dynamics design
Questions
Alessandra Lombardi
6/5/2021
Skip to slide 7 for update 15/7/2021

## Slide 2: Some improvements that will try
Smoother rms :
  to ease the matching from the LEBT
  to aloow for more space between the last solenoid and the rfq
Output rms :
  to simmetrise the beam before exiting the RFQ
  Entails readjustment of the MEBT

## Slide 3: Source
Forget about the 80mA, lets fix 50mA peak current?
Extraction energy : lower / higher : what is the acceptable range

## Slide 4: Transverse acceptance
Higher acceptance? Is this a good idea? We need to consider the next bottleneck in the linac/PSB transfer
95% transmission ?

## Slide 5: Maximum electric field on the vanetip
This is an input to the beam dynamics design currently 33MV/m
What shall we take?
Constant along the vanes or concentrated in one point?
Shall we avoid max efield in loss area? Is there a correlation?

## Slide 6: Meeting 1 -6/5/2021
Summary:
  Ok for 50 mA as limit
  No particular feedback on input energy
  No more than 35MV/m

## Slide 7: RFQ3 beam dynamics design
Update and first draft
Alessandra Lombardi
15/7/2021

## Slide 8
Fixed parameters :
  35MV/m max field on vanetip
  Current 60mA and emit=0.4 rms norm mm mrad
  Energy from 35 to 55 kV
  Rho/ro = 0.75 no room to furthere reduce Emax-what I quote in the next slides is already minimised
Divide capture and acceleration-design capture choose together and then optimize acceleration that goes with it
LINAC4 present RFQ:
  Designed for 80mA , 0.25 mm mrad T=93%
  Capture 45keV to 400KeV length =118cm + 182 cm acceleration
  V=78KV, emax 35 MV/m
  At the time of design we were not considering emittances bigger than 0.25 mm mrad, we had the acceptance =1.5 emittance that is 0.375 mm mrad

## Slide 9: Version 1- 35keV
First design the capture (to about 0.4 MeV) then worry about acceleration to the final energy
Start at 35keV to 400kV
V kV Emax MV/m | Min a // B | L | T (%) 60mA 0.4mmmrad | T (%) 60 mA 0.3 mm mard | filename | 
75 | 1.9// 6.11 | 76cm | 84% | 87% | RFQ1.in | 
75 //33MV/m | 2.1 // 5.99 | 80cm | 81% | 85% | RFQ2.in | Parametric res see losses and phase ramps
70/29MV/m |  |  |  |  |  | 
Losses correspond to too fast phase ramp - smooth the phase from 30 to 40

## Slide 10: Version 2
Increase the energy
Start at 58keV
Bunch and capture to 350keV
V Emax | Min a // B | L | T 60mA 0.4mmmrad | T 60 mA 0.3 mm mard | filename | 
70//29 MV/m | 2.3//5.7 | 98cm | 93% | 96% | RFQ3.in | Higher long emittance but we have margin in the DTL
75 |  |  |  |  | RFQ4.in | 
Higher long emittance but we have margin in the DTL

## Slide 11: Version 3
Stay at 45 kev
Bunching to 350 keV
V Emax | Min a // B | L | T 60mA 0.4mmmrad | T 60 mA 0.3 mm mard | filename | 
70//29 | 2.3 //5.7 | 171 cm | 96% | 97% | RFQ5.in | 
75//29 | // 5.1 | 120 | 88% | 91.% | RFQ6.in | 
This is similar to the existing linac4 RFQ with a tradeoff between transverse acceptance and longitudinal emittance delivered to the DTL and a lower voltage

## Slide 12: Next steps
Accelerate to 3 MeV (forego exact length of 3 m for the moment)
Track into and through the DTL
Emittance measurement at the new source at 35 and 45 keV
Track particles from measurements
Check point with this group mid september