## Slide 1
Stefan Ulmer
RIKEN
2021 / 02 / 11
Superconductivity in BASE and BASE haloscope
Geneva – "PBC technology" workshop

## Slide 2
Precise CPT test with baryons
S. Ulmer, et al., Nature 524, 196 (2015)
To be improved by another factor of 10 to 100
Rexp,c = 1.001 089 218 755 (64) (26)
Observation of spin flips with
a single trapped proton
Application of the double
Penning-trap technique
S. Ulmer, et al., PRL 106, 253001 (2011)
A. Mooser, et al., PLB 723, 78 (2013)
Reservoir trap for antiprotons
C. Smorra, et al., Int. Journ. Mass Spec. 389, 10 (2015).
S. Sellner et al., NJPhys. 19, 083023 (2017)
Most precise antiproton/proton
g-factor measurments
A. Mooser, et al., PRL 110, (2013)
C. Smorra et al., Nature 550, 371 (2017)
g/2 = 2.792 847 344 1 (42)
3000-fold improvement compared to previous measurement
G. Schneider et al., Science 358, 1081 (2017).
g/2 = 2.792 847 344 62 (82)
BASE-Physics Overview
Dark Matter / Antimatter Interaction
C. Smorra et al., Nature 575, 310 (2019)
30-fold improvement compared to previous measurement
Proton:
Antiproton:
First limits on dark matter / antimatter coupling, orders of magnitudes mo stringend than astrophysics limits.
80-fold improved limits on directly constrained antiproton lifetime
FIP detection
J. Devlin et al., Phys. Rev. Lett. 126, 041301 (2021)
Single particle detection systems used to constrain the volume of dark matter radio (in a narrow mass band)
Testing CPT invariance with single particles in Penning traps / protons and antiprotons

## Slide 3: Measurements in Precision Penning traps
Cyclotron Motion
Larmor Precession
Determinations of the q/m ratio and g-factor reduce to measurements of frequency ratios -> in principle very simple experiments –> full control, (almost) no theoretical corrections required.
g: mag. Moment in units of
nuclear magneton
S. Ulmer, A. Mooser et al. PRL 106, 253001 (2011)
S. Ulmer, A. Mooser et al. PRL 107, 103002 (2011)
simple
difficult
High Precision Mass Spectrometry
High Precision Magnetic Moment Measurements

## Slide 4: Superconductivity in BASE
Single particle detection systems
Magnetic Shielding and Shimming
Developers of world class detectors
Developers of excellent shielding systems
Superconducting Magnets
Users of ultra stable persistent devices

## Slide 5: Single Particle Detection Systems
Particle oscillates in a Penning trap
Oscillation induces image currents, that produce voltage drops over resistors (fA currents)
Use superconducting inductance to compensate parasitic capacitance of the trap system.
Requires high-Q superconducting inductors.
Concept allows test of fundamental symmetries on the parts per trillion level
Experience on frequency ranges 100kHz to 100 MHz
Single particle
FFT
Amp
Amp
Rp
Lp
Cp
resonator
Low noise electronics

## Slide 6: Technology Transfer & Advice
Frequency band which is under control is at a level of 100kHz to 100MHz
Detectors 100kHz to 1MHz with Q up to 500000 available
Design of toroid geometries with diameters up to 100mm
Recently: high Q tuneability device developed, with bandwidth of 350 kHz to 1MHz at Q>100000
Relevant for single particle experiments, axion searches, NMR pickups, ultra sensitive magnetometry etc.

## Slide 7: Future Projection
With a purpose-built experiment we should be able to improve sensitivity considerably
Parameter | Current | New | Factor
Temperature |  |  | 
Geometry |  |  | 
Peak Sens. | 1 |  | 
Parameter | Current | New | Factor
Temperature |  |  | 
Geometry |  |  | 
Peak Sens. | 1 |  | 
Technologies available to build such an experiment / discussion with IAXO started
Laser cooled
resonators
Bandwidth-gain: x 3000
Devlin et al., BASE,
Phys. Rev. Lett. 126, 041301

## Slide 8: Self Shielding coil (SSC)
l
d
A
Bsolenoid
Be
Flux conservation means that if the external field changes, the current in the solenoid has to change.
With the right choice of l/d, the total magnetic field along the solenoid axis at the particle position x0 vanishes
G. Gabrielse and J. Tan, J. Appl. Phys 63 (10)
Y=-0.25(l/d-0.876)
Inverse shielding factor of single solenoid
as a function of l/d
For a perfectly aligned coil, the cyclotron frequency shifts according to

## Slide 9: Performance for fields along AD direction
AD fluctuations along all 3 axes
Shielding of crane field
External field
change
change
Experiment does not stop working if crane moves
Performance with AD on/off compared to 2014
AD field noise not resolvable at 1.5 ppb level
limited
by
measurement
noise
Expertise in designing ML SSC systems
Persistent joints for SSC’s
Currently looking for methods to improve persistent joints for high current shim-coils.

## Slide 10: BASE Measurements – Proton to Antiproton Q/M
Result of 6500 proton/antiproton Q/M comparisons:
S. Ulmer et al., Nature 524 196 (2015)
Rexp,c = 1.001 089 218 755 (69)
Stringent test of CPT invariance with Baryons.
Consistent with CPT invariance
New measurement:
  Acquired 35000 frequency ratio measurements over 1.5 years, distributed over the sidereal year.
  Used two measurement methods, tunable axial detector to suppress systematics, and a rebuilt apparatus
Rexp,c,1 = 1.001 089 218 763 (23)
Rexp,c,2 = 1.001 089 218 7XX (20)
Final data analysis is work in progress
BASE, in preparation (2021)

## Slide 11: Summary and Outlook
In BASE technologies exist to develop high-Q detection LC circuits with Q>500000 at frequencies up to 1 MHz
Expertise with high-Q small scale detectors up to 100MHz (Q = 10000)
Self shielding systems with S > 500 developed
BASE 2016
BASE 2017

## Slide 12: Thanks for your attention