## Slide 1
The LHC: How does it work?
NNV Profielwerkstukreis 4 – 8 oktober 2021
Accelerating Science and Innovation Jan Uythoven, CERN
Notes: 1

## Slide 2
How does the accelerator work?
  Magnets
  Radio Frequency
  …
Energy in the beam
The future
Compact Muon Solenoid
Cern Control Centre

## Slide 4: The LHC
Very big
Very cold
Very high energy

## Slide 5: The LHC
Two beams of trillions of protons race around the 27 km ring at 0.999999991 times the speed of light in opposite directions…
So a particle goes around the LHC 11’000 times per second !

## Slide 6: LHC tunnel
Circumference = 26.7 km
Depth = 70-140 m
Slope = 1.4 %

## Slide 7: LHC Injector Chain
7
Normal operation with protons, but every year few weeks of operation with heavy ions (Pb82+)
New Linac4 in 2020: H-
0.16
2.0

## Slide 8: Where do the Protons come from?

## Slide 9: Basic ingredients of a particle accelerator
Magnetic field to
  Bend the beam around the circle (dipole magnets)
  Keep the particles together (quadrupole magnets = lenses)
Electric field to accelerate the particles
  Very fast varying electric fields = Radio Frequency cavities

## Slide 10: Dipole Magnets
Bend the beam around the circle
Number of dipoles 1232
Dipole field at 450 GeV 0.535 T
Dipole field at 7 TeV 8.33 T
Bending radius 2803.95 m
Main Dipole Length 14.3 m
Openings (full aperture) 56 mm
I
I
I
B
SUPERCONDUCTING! Cooled with superfluid helium at 1.9 K

## Slide 11: The superconductor
Strand
Filament
Cable
Used 1200 tonnes/7600 km of cable Single cable carries current up to 12 kA
Niobium-titanium Rutherford cable

## Slide 12: More than just some coils…
12

## Slide 13: During construction: Dipoles all over

## Slide 14: In the LHC tunnel
?
?
?
?
?

## Slide 15: Beam is divergent
Many particles many initial conditions
Vertical
displacement
Many different angles
 s
Quadrupole magnet

## Slide 16: Quadrupole magnets
A quadrupole magnet will focus in one plane and de-focus in the other.
Convention: a “focusing” quadrupole focuses in the horizontal plane

## Slide 17: Alternate gradient focusing
(and similarly for the vertical plane y)
The general linear magnet lattice can be parameterized by a ‘varying spring constant’, K=K(s).
K(s) describes the distribution of focusing strength along the lattice and is periodic.
This is Hill’s equation.
s
x

## Slide 18: Squeeze
Beam 1
Beam 2
Focus beam down to very small sizes in the experiments using quadrupole magnets

## Slide 19: Accelerating the Particles
LHC: beams with an energy of 6.5 TeV
=
6 500 000 000 000 V
Tera Giga Mega kilo

## Slide 20: Radio Frequency Cavities
RF = Oscillation of field at 400 MHz (Radio Frequency)
Use the Electrical Field at each passage
4 cavities/module - 2 modules/beam - 16 MV (5.5 MV/m)
Superconducting to reduce Beam Impedance
4 Cavity RF Module

## Slide 21: Lots of bunches
25 ns = 7.5 m
In 2017 the LHC operated with 2300 bunches per beam, separated by 25 ns
Transverse size typically 1 mm

## Slide 22
12 micron
Up to 50 collisions per crossing
11’000 crossings per second
2200 bunches per beam (2016)
1 Billion Collissions Per Second  GRID

## Slide 23: Luminosity

## Slide 24: Energy in the Beam
Electric Energy (RF cavity)  Kinetic energy
E-beam | 6.5 TeV = 6.5e12 eV
1 eV | 1.6e-19 Joules
Number of bunches | 2300
Number of protons per bunch | 1.3e11 protons
Energy | 311 MJoules
What would be the speed of a car to have the same kinetic energy ?

## Slide 25: Car Versus Beam
E-beam | 6.5 TeV = 6.5e12 eV
1 eV | 1.6e-19 Joules
Number of bunches | 2300 (for 2016)
Number of protons per bunch | 1.3e11 protons
Energy | 311 MJoules
Electric Energy of the beam  Kinetic energy
Mass car | 1800 kg
Kinetic energy | 306 MJoules
V | 583 m/s
V | 2100 km/h
Kinetic Energy of the car
But at the size smaller than a hair ….

## Slide 26: Don’t break the machine!
Energy per beam up to 360 MJ
British aircraft carrier at 12 knots
Thread through a very cold, very dark, very small hole...
26
26

## Slide 27: Beam dump block (TDE)
700 mm  graphite core, with graded density of 1.1 g/cm3 and 1.7 g/cm3
12 mm wall, stainless-steel welded pressure vessel, at 1.2 bar of N2
Surrounded by ~1000 tonnes of concrete/steel radiation shielding blocks
0.7 m
3.5 m
3.5 m
1.7 g/cm3
1.1 g/cm3
1.7 g/cm3
beam
27
27

## Slide 28: It is all about Luminosity
2018

## Slide 29: Luminosity
N | Number of particles per bunch
kb | Number of bunches
f | Revolution frequency
σ* | Beam size at interaction point
F | Reduction factor due to crossing angle
ε | Emittance
εn | Normalized emittance
β* | Beta function at IP

## Slide 30: Quench Limit of LHC Super-Conducting Magnets
Beam
360 MJ
SC Coil: quench limit
5-30 mJ/cm3
56 mm
Nominal design at 7 TeV

## Slide 31: Collimation
beam
1.2 m
Almost 100 collimators and absorbers.
Alignment tolerances < 0.1 mm to ensure that over 99.99% of the protons are intercepted.
Primary and secondary collimators are made of reinforced graphite – robust.
31
31

## Slide 33
Beam dumps
RF
Collimation
Collimation
1720 Power converters
> 9000 magnetic elements
7568 Quench detection systems
1088 Beam position monitors
~4000 Beam loss monitors
120 tonnes of Helium, down to 1.9 K
360 MJ stored beam energy per beam
11 GJ total stored energy in magnetic systems
LHC: big, cold, high energy
Injection B2
Injection B1

## Slide 34: Machine Elements
Magnets: guidance and transverse ‘stability’
  Dipoles, Quadrupoles, Sextupoles, Octupoles
Radio Frequency – Longitudinal motion
  Acceleration
  Feedback
Injection and Beam Dumping Systems
  Fast Pulsed Magnets (‘Kicker Magnets’)
  Septum Magnets
  Beam dump block
Machine Protection
  Collimation System, other absorbers, Interlock Systems
Beam Diagnostics & Protection
  Beam Position, Beam Loss Monitors, Tune Measurement, Synchrotron Light Measurements, Beam Size Measurements
Cryogenics & Vacuum

## Slide 35: Operational cycle
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours
Turn around from stable beams to stable beams - 2 to 3 hours on a good day, followed by Stable Beams, average 6 hours.

## Slide 36
Luminosity
Beam intensity

## Slide 37: Machine Performance 2018

## Slide 38: Magnet Training to reach 7 TeV Beam Energy
During the training after LS2 (2021) we needed 3x a sector warm-up – delay of about 3 months each time, partly in parallel
Present Operation
‘Nominal’
6.5 TeV = Operation <= 2018
6.8 TeV

## Slide 39
Number of quenches needed to reach 7 TeV
A total of about 65 magnet quenches (corresponding to about 55 circuit quenches) are still needed to bring S23 and S78 to 6.8 TeV.
A total of about 340 magnet quenches (corresponding to about 280 circuit quenches) are still needed to bring the remaining 5 sectors from 6.8 to 7 TeV.
We calculated a 63 % probability for another sector warm-up if we continue training to 7 TeV  Experiments want to run  Run at 6.8 TeV
 | 12 | 23 | 34 | 45 | 56 | 67 | 78 | 81
#Q to reach 11600 A (6.8 TeV) (including flat-top quenches at 11600 A) | 0 | 23 | 0 | 0 | 0 | 0 | 42 | 0
#Q to reach 11950 A (7 TeV) (starting at 11600 A) | 0 | 70 | 0 | 0 | 71 | 54 | 67 | 53
#Q at 11950 A flat-top | 0 | 6 | 0 | 1 | 5 | 5 | 5 | 4
We have had 274 magnet training quenches from 2008-2018 and 614 magnet training quenches in 2021.

## Slide 40: Magnet Training to reach 7 TeV Beam Energy
During the training after LS2 (2021) we needed 3x a sector warm-up – delay of about 3 months each time, partly in parallel
Present Operation
‘Nominal’
6.5 TeV = Operation <= 2018
6.8 TeV
6.8 TeV

## Slide 41: What’s Next ? High-Luminosity LHC
Injectors upgrade and LHC civil engineering
HL-LHC upgrade
13.6 TeV

## Slide 42: HL-LHC
Luminosity so far

## Slide 43
11 T dipoles (compared to 8.3 T)

## Slide 44: In Two Weeks from Now
Beams again in the LHC after > 2.5 years
Two week long beam test period:
Machine checkout : 3 days (estimated).
Beam operation : 11 days, end 01.11.2021 @ 6AM followed by radio protection survey.

## Slide 45: Beam test outline
Nominal bunch setup
Circulate both beams
Instrumentation and tools setup
Optics meas. & correction
Collimation setup & global aperture
Collision setup
Local apertures
Machine tests
Collisions
6-7 days
Collisions build on setup work, expected around day 7
Interleaved data taking & machine activity periods
3-4 days
Little flexibility on workflow
Activities must follow defined order
Assumes availability  70-80%

## Slide 46: The Future @ CERN after the HL-LHC

## Slide 47
15 T  100 TeV in 100 km
20 T  100 TeV in 80 km
FCC (Future Circular Colliders)
80-100 km tunnel infrastructure in Geneva area – design driven by pp-collider requirements
with possibility of e+-e- (TLEP) and p-e (VLHeC)

## Slide 49: CLIC near CERN: e+e- Collider
Tunnel implementations (laser straight)
Central MDI & Interaction Region

## Slide 51
Bedankt voor jullie aandacht !
Accelerating Science and Innovation
Notes: 51

## Slide 52: SPARE SLIDES

## Slide 53: CMS: heavier than the Eifel tower

## Slide 54: ATLAS: large as a building of 5 floors

## Slide 55: ALICE: very sensitive, optimised for ion collisions

## Slide 56: LHCb: asymmetric, B-physics

## Slide 57: Aim of the game
We want to deliver maximum number of collisions at the maximum beam energy for maximum physics reach
E = m c 2

## Slide 58: The Higgs field gives mass to other particles

## Slide 59: Why is the Higgs so special?

## Slide 60: Reduced Energy – the history
10th September 2008: First circulating beams – all smiles

## Slide 61: Reduced energy – the history
19th September 2008: electrical arc ruptured bus-bar interconnection during tests without beam – violent He blow-off

## Slide 62: Reduced energy – the history
Major damage over a few hundred meters. Back in operation 1 year later.

## Slide 63
2013 – 2014: Long Shutdown to repair defective connections between superconducting magnets
2015: Restart with beam energy of 6.5 TeV

## Slide 64: Next 10 years
The LHC has a long future ahead ….
Followed by many years of HL-LHC running

## Slide 65: The HL-LHC Project
New IR-quads Nb3Sn (inner triplets)
  New 11 T Nb3Sn (short) dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Major intervention on more than 1.2 km of the LHC

## Slide 66
High Luminosity LHC Participants

## Slide 67
29 Countries – over 70 Institutes
Accelerator collaboration
Detector collaboration
Accelerator + Detector collaboration
CLIC Collaboration

## Slide 68: CERN: Particle Physics and Innovation
Interfacing between fundamental science and key technological developments
CERN Technologies and Innovation
Detecting particles
Accelerating particle beams
Large-scale computing (Grid)
Notes: 68

## Slide 69: Medical Application as an Example of Particle Physics Spin-off
Combining Physics, ICT, Biology and Medicine to fight cancer
Accelerating particle beams
~30’000 accelerators worldwide
~17’000 used for medicine
Hadron Therapy
Leadership in Ion Beam Therapy now in Europe and Japan
Tumour Target
Protons
light ions
>70’000 patients treated worldwide (30 facilities)
>21’000 patients treated in Europe (9 facilities)
X-ray
protons
Detecting particles
Imaging
PET Scanner
Clinical trial in Portugal for new breast imaging system (ClearPEM)
Notes: 69

## Slide 70
CERN Education Activities
Scientists at CERN
Academic Training Programme
Young Researchers
CERN School of High Energy Physics
CERN School of Computing
CERN Accelerator School
Physics Students
Summer Students
Programme
CERN Teacher Schools
International and National Programmes
Latin American School
Natal, Brazil, 2011 Arequipa, Peru, 2013
NEW:
Asia-Europe-Pacific School of High-Energy Physics
Fukuoka, Oct 2012
India, 2014
CERN School of Physics Hungary, June 2013

## Slide 71
2008
2009
2010
2011
LHC Timeline
September 10, 2008
First beams around
September 19, 2008
Disaster Accidental release of 600 MJ stored in one sector of LHC dipole magnets
August 2008
First injection test
August, 2011
2.3e33, 2.6 fb-1
1380 bunches
October 14 2010
1e32
248 bunches
November 2010
Ions
March 30, 2010
First collisions at 3.5 TeV
1380
June 28 2011
1380 bunches
November 29, 2009
Beam back
2012
18 June, 2012
6.6 fb-1
to ATLAS & CMS
6 June, 2012
6.8e33
4 July, 2012

## Slide 72
The highlight of a remarkable year 2012

## Slide 73
Nobel Prize in Physics 2013
The Nobel Prize in Physics 2013 was awarded jointly to François Englert and Peter W. Higgs "for the theoretical discovery of a mechanism that contributes to our understanding of the origin of mass of subatomic particles, and which recently was confirmed through the discovery of the predicted fundamental particle, by the ATLAS and CMS experiments at CERN's Large Hadron Collider”.

## Slide 74
The Worldwide LHC Computing Grid
Tier-1: permanent storage, re-processing,
analysis
Tier-0 (CERN): data recording, reconstruction and distribution
Tier-2: Simulation,
end-user analysis
> 2 million jobs/day
~250’000 cores
173 PB of storage
nearly 160 sites, 35 countries
10 Gb links
An International collaboration to distribute and analyse LHC data
Integrates computer centres worldwide that provide computing and storage resource into a single infrastructure accessible by all LHC physicists

## Slide 75: Verification of Dump Protection
Switch off the RF
  Debunching fills the abort gap
Dump Beam
  Loss in point 6 on absorber elements
  Some losses collimation
  Clean at experiments: factor 1 : 10 000
Dump
Collimation
Rest of the machine is clean
Measured Beam losses around the whole Machine
Image of the dumped beam
75
75

## Slide 76: Only one way to safely get rid of the beam
LHC Beam Dumping System
Extraction Kickers 2 x 15 Systems
TCDQ
TCDS
10 Dilution kickers MKB
76
76

## Slide 77: Beam dump block (TDE)
700 mm  graphite core, with graded density of 1.1 g/cm3 and 1.7 g/cm3
12 mm wall, stainless-steel welded pressure vessel, at 1.2 bar of N2
Surrounded by ~1000 tonnes of concrete/steel radiation shielding blocks
0.7 m
3.5 m
3.5 m
1.7 g/cm3
1.1 g/cm3
1.7 g/cm3
beam
77
77

## Slide 78: Extraction kicker – Abort Gap
Synchronised dump trigger
3.0 ms
particle-free
abort gap
Extraction kicker MKD deflection
LHC
Beam
Within 3 turns of dump request
78
78

## Slide 79: At every dump: Check the Extraction Kickers
3 µs ‘Abort Gap’ without beam
79
79

## Slide 80: At every dump: Check the Dump Pattern
80
80

## Slide 81: At every dump: Check the Beam Losses
81
81

## Slide 82: Protection against ‘Kicker Sweep’
Beam in the Abort Gap
Asynchronous beam dump  quench or damage
  Several failures possible (synchronisation, MKD erratic)
Precautionary measures include:
  TCDS (fixed) – 6 m long diluter protects extraction septum
  TCDQ/TCS (mobile) – 7 m long diluter kept at about 7-8 s from the beam at all times
82
82