## Slide 1: Cern Week 2 Report:
Kostantin Andreas Jacoby

## Slide 2: Goals For Past Week
Investiagte and Validate K-omega model
Introducing Viscous Heating and Full Boyancy Effects
Introduce 3D Model
Introduce Cern Material Values

## Slide 3: Full Buoyancy Effects
On
Off
K-e model are two equation models: Kinetic Energy and Dissipation equations, full buoyancy effects introduces bouyancy into the dissipation equation (very recent update, not fully understood and not stable or considered valid) .

## Slide 4: Limitations of k-e

## Slide 5: K-epsilon vs K-omega
Convergence issues possibly due material value limitations:
Allow for values outside of range (above 150 [K] or bellow 83.9 [K]) (extrapolation with given polynomial)
Use other material relations if possible outside calculated limits (Boussinesq if non constant)
Alter Relaxation Factors

## Slide 6: K-epsilon vs K-omega (if forced convection dominates)

## Slide 7: Material Values
Limited to 145 [K]

## Slide 8: Forced vs Natural Convection
Forced
K-epsilon
K-omega
Natural
Scale-Adaptive Simulation (SAS)
Detached Eddy Simulation (DES)
Large Eddy Simulation (LES)
Relationship for External Flows:
Mills

## Slide 9: 3D Model Mesh: Tetra to Polyhedral Mesh

## Slide 10: Surfaces for 3D Model

## Slide 11: Goals for this Week
Run 3D model
Adjust Surfaces for 3D Model
Impliment Internal Heating into 3D model
Possible Difficulties:
Resolving an adiquate mesh requires large RAM 125GB
Implementing walls that allow fluid to pass is very difficult, best solution might be implementing a volumetric heat source (requires external functions and 3rd party software – not very easy)