## Slide 1: Beam Generation for Test Beams
Alexander Gerbershagen

## Slide 2: Overview
  Introduction: Purpose and users
  Examples of test beam facilities
  Targets and particle production
  Secondary/tertiary beam lines

## Slide 3: Introduction: Purpose and Users

## Slide 4: Purpose and Users
Secondary Beam Areas (SBA) are hosting:
FT experiments: COMPASS,NA61, NA62, NA63, NA64, CLOUD, …
  Precision studies (QCD, standard model, BSM physics)
  Stable beam conditions for weeks and weeks
Radiation facilities: PARTREC, HiRadMat, Charm, Irrad, GIF++
Test beams:
  Detector prototype tests
  Detector calibration
  e.g. for LHC, linear colliders, space & balloon experiments
  Outreach
  Usually require a large spectrum of beam conditions within few days

## Slide 5: Examples of test beam facilities

## Slide 6: East Area – after renovation

## Slide 7: East Area
Area under renovation
-> See presentation by E. Montbarbon/J. Bernhard
Test Beams after LS2
Secondary beams:
  T9: < 0.5 GeV/c – 15 GeV/c
  T10: < 0.5 GeV/c – 12 GeV/c
  Horizontal momentum selection
Particle types and intensity
  Pure electrons, hadrons, muons
  Max. ~5·106 particles per spill
Spill structure from PS
  400ms spill length
  Typically 1 spill every 18s (15bp), more on request
telescope AZALEA in T10
Quick access from control room to experimental area (< 1 minute)
Short cables
CHARM
IRRAD
T11
T10
T9

## Slide 8
CERN North Area Beamlines
T6
T4
T2
T2 wobbling
T4 wobbling
T10
NA62
NA61
H2
H4
H6
H8
M2
P42
P6
K12
NA64
COMPASS

## Slide 9: North Area beamlines characteristics
Primary mode Secondary mode
Parameters | T2 |  | T4 | 
Beam Line | H2 | H4 | H6 | H8
Maximum Momentum [GeV/c] | 400 / 360 | 400 / 330 | - / 205 | 400 / 360
Maximum Acceptance [µSr] | 1.5 | 1.5 | 2 | 2.5
Maximum Δp/p [%] | ± 2.0% | ± 1.4 % | ±1.5% | ±1.5%
Maximum Intensity / spill * (Hadrons / Electrons) | 107/105 | 107/106 | 107 **/105 | 107 **/105
Available Particle Types | Primary protons*** OR pure electrons OR mixed hadrons (pions, protons,kaons) |  |  | 
Other / Special requests | sba-physicists@cern.ch & sps.coordinator@cern.ch |  |  | 
* Imposed by Radio Protection, and not available to every zone
** In some zones can be elevated up to 108 subject to certain restrictions
*** Not available in H6
Nota Bene : The particle momenta in H2/H4 and in H6/H8 are coupled. Send your beam request and discuss in advance with the SPS coordinator and the responsible liaison physicists.

## Slide 10: PARTREC – Accelerator and Facility
Superconducting AGOR cyclotron is a multi-particle, variable energy AVF-cyclotron
Operational since 1996
3 halfwave RF cavities, 24 - 62 MHz; h = 2, 3 or 4
Three external ion sources (two ECR sources for heavy ions, multi-cusp source for light ions) are axially injected
Extraction
  300 - 500 turns depending on harmonic mode
  extraction radius 870 - 890 mm depending on E/A
  turn separation at extraction 2 - 3 mm ~ beamwidth

## Slide 11: PARTREC – Beam Delivery
AGOR can deliver beams of all elements up to Xe
 | Protons | Ions
Kinetic energy (MeV/amu) | ≤ 190 | ≤ 90 for C and O ≤ 30 for all up to Xe
Attainable flux (particles per s) | > 1013 | ≤ 1013 for Ne ≤ 1011 for heavier ions
Field size (cm2) | ≤ 10 x 10 (scanned beam) ≤ 8 x 8 (scattered beam) | ≤ 7 x 7 for light ions (scanned beam) ≤ 3 x 3 for heavy ions (scanned beam)
Field homogeneity | ± 2 % (scattered beam) ± 1 % (scanned beam) | ± 2 % (scattered beam) ± 1 % (scanned beam)
Beam requests: irradiations.partrec@umcg.nl

## Slide 12: Targets and particle production

## Slide 13: Targets and particle production
Principle taken from cosmic radiation
  Primary proton beam initiating hadronic cascade
  Always followed by an electro-magnetic cascade

## Slide 14: Targets and particle production
Principle taken from cosmic radiation
Particles are produced in a large momentum range
SPS beam

## Slide 15: Target length and production rates
Beryllium has
  radiation length X0 = 35.3 cm,
  nuclear interaction length λI = 42.1 cm,
    => high X0/λI ratio
  low density (1.848 g/cm3)
  high melting point (1560 K)
The e/π ratio increases approx. linearly with the target length
Hadrons
  are produced via p + N -> hadron (rate ~ L)
  reabsorbed (rate ~ e-L)
  => Overall rate ~ Le-L (maximum at L≈ λI)
Electrons are mainly produced via
  p + N -> π0 -> γ γ (rate ~ L)
  γ converts to e+ + e- (rate also ~ L)
  reabsorbed (rate ~ e-L)
  => Overall rate ~ L2 e-L (maximum at L ≈ 2λI)
Chart: 
  Le-L
  L2e-L
  Length of beam propagation in material (L)
  Production rate

## Slide 16: Targets and hadron production
Atherton parameterisation (CERN 80-07):
with primary momentum p0 and production angle q
Flux per solid angle [steradian], per interacting proton, and per dp [GeV/c]
q = 0 mrad
Note: Valid for primary interactions only! Extrapolation for momenta below 60 GeV/c

## Slide 17: Secondary / tertiary beam lines

## Slide 18: Beamlines
Experiments and test beams require “clean” beams with high purity (one particle type) and small momentum spread
Beam lines design (“optics”)
  Collect produced particles from target
  Select momentum
  Select particle type
  Transport beam to experiment
  Select beam spot size for experiment

## Slide 19: NA beamline design considerations
NA beams were originally (end of 1970’s) designed for the fixed target experiments. Design considerations were
    Muon range (absorb underground)
    Charged pion lifetime
    Momentum selection (2∙10-4)

## Slide 20: NA secondary beamline - layout
Basic beam design
momentum selection in the vertical plane
two sets of bending magnets
  Upstream BENDs
    Between the primary target and the momentum slit
    Vertical focus of monochromatic beam at the momentum slit
  Downstream BENDs
    the main spectrometer for the beam momentum definition

## Slide 21: Secondary beamline - collimators
  TAX (Target attenuator)
    Define initial acceptance of the beam line
  Acceptance collimators
  Cleaning collimators
    Absorb secondary particles produced on the jaws of acceptance collimators
Cleaning collimator
Acceptance predefined by TAX
Acceptance collimator

## Slide 22: Secondary beamline - intensities
Basic beam design
Selection of particle types
Intensities
Primary
Target (Be)
Secondary
Target
Primary beam
400 GeV/c p
Few 1012 ppp
Secondary beam Mixed (e+h+m)
Typically ~100 GeV/c
Flux ~ 107 ppp
Tertiary beam
Typically 10-80 GeV/c Flux up to 104 ppp, e.g.
~4 mm Pb: 1Xo, <<1 lI: ‘pure’ electrons
~40 cm Cu: 3 lI, ~30 Xo: hadrons
Tertiary beam
Pure hadrons
Absorber
(few mm Pb)
x . 1012 ppp
< 108 ppp
< 104 ppp

## Slide 23: Selection of particle type - Converter
Primary Target
Converter
Hadrons, muons, electrons
Primary protons
Electrons from γ conversion
or hadrons from K0 or Λ-decay
Collimator
- polarity
+ polarity
Neutral beam
Collimator
Protons
Electrons
or hadrons
Experiment
Where to find at CERN:
North Area: H2, H4
East Area: T9 (starting 2021)

## Slide 24: Selection of particle type - Absorber
Primary Target
Collimator
Absorber (e.g. 6 mm Pb)
e-
e+
Hadrons, muons
Hadrons, muons, electrons
Primary protons
Both bends set to the same beam momentum
Large energy loss for electrons, very little for hadrons and muons
Experiment
Where to find at CERN:
North Area: H2, H4, H6, H8
East Area: T9, T10 (starting 2021)

## Slide 25: Selection of particle type - Filter
Example: +300 GeV/c beam filtered with 3m polyethylene
Initial flux 5∙108 particles
Drawbacks:
  Small suppression factor for unwanted particles
  Big losses with low efficiency
Differential absorption:
Beam through filter
Enrichment = single particle attenuation ai over total beam attenuation
Particles | % initial beam | % filtered beam | Flux
Protons | 92.5 | 73.4 | 7.9 106
Pions | 5.8 | 19.1 | 2.1 106
Kaons | 1.7 | 7.5 | 8 105

## Slide 26: High-energy electron beams
Synchrotron radiation
(for one full revolution)
E.g. e± at 200 GeV lose in 1° bending magnet of 1 T field 590 MeV
  => With beamline momentum acceptance of Δp/p < 0.3 % it is possible to separate them from (heavier) hadrons and muons. So set up the following bends either
    at the constant energy to select heavier particles or
    scale it with energy loss of electrons.
    Works only for pe > 120-150 GeV/c

## Slide 27: Selection of particle type - Radiator
Secondary electrons (e)
Radiator
(e.g. 1 mm Pb, Cu, W)
Electrons (e’),
Photons are created via Bremsstrahlung
Electrons
Profile monitor
Time resolution - electron by electron
Transverse position gives information on e- momentum
pγ = pe – pe’
Result : tagged photon beam
p2 < p1
p1
p3 < p2
Experiment
Photons
Where to find at CERN:
(Ad hoc installation, but usually used at)
North Area: H2, H4
East Area: T9

## Slide 28: Secondary beamline – beam optics
Optics of a beam line (H8)

## Slide 29
H2-H4 coupling via wobbling in T2 target
P(H2) in GeV
P(H4) in GeV

## Slide 30
Wobbling in T4 target
Three beams
=> stronger constraints

## Slide 31
North Area – beam instrumentation
Profile monitors
  XWCA(M) for higher fluxes (> 104 per spill)
  XDWC for lower fluxes (< 104 per spill)
Fiscs
Intensity counters
  Scintillators for lower fluxes (< 107 per spill)
  XION for higher fluxes (> 106 per spill)
Cherenkov detectors
  XCET (Threshold counter)
  CEDAR
SEM counters at the target
  BSI for beam intensity
  BSP split foil for beam symmetry
  BSM and SEM grid for angle set up
  BBS (fisc like)

## Slide 32: Summary
PARTREC has a high-intensity test beam complex with primary proton and ion beams
CERN has a test beam complex
  East Area
    Momentum : 0.5 GeV/c – 15 GeV/c
  North Area
    Momentum: 10 GeV/c – 400 GeV/c
  Capable to provide
    Protons
    Electrons
    Hadrons
    Pure pions
    Muons
    Tagged photons
  Diverse instrumentation for various purposes

## Slide 33
Questions?