## Slide 1
ND280_SFGD Box Envelope
US ECAL
SFGD Envelope definition
Connections to the Basket structure

## Slide 2
ND280 new configuration @ JParc
SFGD box size depends on:
  some existing detectors (ECAL, vertical TPC..)
  space left by POD removal
  New Upgrade detectors (TOF, HA-TPC)
  Mounting steps (see later)
  Side electronics (readout Crates and Cables)

## Slide 3
Basket size & measurement @ J-PARC
Measurement campaign in October 2018 @ J-PARC (Japan)
Focusing on the “POD area”, for ND280 Upgrade (SFGD, HA-TPC and TOF)
Final precision assumed to be +/-2mm (Laser + access issues)
Good match / CAD model at (2 to 3mm differences).
More checks @ J-PARC to come (as requested by ND280 community)
Basket structure
Laser system
POD area
6930mm
2480mm
Up ECAL
TPC
?
y
z
x

## Slide 4
Basket size & measurement @ J-PARC
Some tricks used to get access to the ECAL/TOF external parts (extensions)
In red the real measurements (+3mm / CAD along beam axis)
UpECAL includes bolt heads… not easy!
Top view
Top view

## Slide 5
First step: CAD model correction
Upstream ECAL / TPC moved by a few mm to comply with the measurements
Checked / bracket design (slotted holes) onto the Basket (quite coherent)
TPC
UpECAL
UpECAL
x
z
y

## Slide 6
With corrected CAD model
Including final CAD models for HA-TPC and TOF
Here after the main relevant steps regarding SFGD envelope definition
SFGD Box assembly steps
Step1: D_TOF installation
Step2: HA-TPC1 installation
Step3: SFGD Box insertion
Step4: SFGD electronics assembly
SFGD Box

## Slide 7
Side Electronics is removed for clarity
SFGD Box assembly steps
Step5: HA-TPC2 installation
Step6: U_TOF insertion
z
x

## Slide 8
Next steps are for TOF completion
SFGD Box assembly steps
Step7: Top and Bottom TOF fixation
Step8: Side_TOF installation
y
z
x

## Slide 9
4 TOF modules and SFGD electronics will stick out from Basket
Some clearance / magnets have been defined by measurement
Magnet closed: 200mm at the bottom is left / 240mm on other axes
Envelope respect to Magnets

## Slide 10
Back to STEP3 in more details….
Seen from top
Assuming all the MPPC cables are folded back onto the sFGD box, and safely stored
The top side is free for cable storage (plus holder, protections…)
SFGD Box envelope

## Slide 11
Back to STEP3 in more details….
Installation in 2 steps: first the BOX and then the side electronics
2 movements to get to final location for BOX :
  Down+ Horizontal along Z towards TPC
  > 90mm clearances all in all … quite acceptable for insertion.
  75mm is left for later U-TOF insertion.
2 movements
SFGD Box Clearances & Envelope

## Slide 12
SFGD box
SFGD box
Envelope for MPPC cables and others
Above the SFGD box area
Clearances respect to U-TOF
SFGD Box Clearances & Envelope

## Slide 13
Top cables envelope
SFGD
SFGD
Calibration system
(partly displayed)
sFGD Clearances
Clearances / Upgrade detectors (TOP and Bottom sides)
10mm minimum with respect to HA-TPC’s
Note that Top HA-TPC can move further up (by +28mm)
In yellow, the MPPC cable envelopes

## Slide 14
Summary on the clearances
SFGD Box Clearances & Envelope
Item | uTOF | dTOF | HA-TPC (bottom) | HA-TPC (Top) | Basket beam (X axis)
Clearance (mm) / SFGD | 20 | 17 | 10* | 10* | 10
Corresponding to a SFGD box volume of:
  Z axis: 1973mm
  X axis: 2310mm
  Y axis: 711mm
* + 28mm could be shared between 2 HA-TPC

## Slide 15
Backup slides

## Slide 16
BOX assembly into the Basket
Step 1 is the SFGD BOX fixation (4 corners)
Fixed corner (Ref.)
Adjustable corner (slotted holes / brackets)
Some shimming may be necessary between pieces (SFGD brackets, Basket)

## Slide 17
CRATE assembly into the Basket
Step 2 is the CRATE integration into the Basket

## Slide 18
CRATE assembly into the Basket
Step 2 is the CRATE integration into the Basket
Clearance / Bracket
Crate frame fixation
Crate fixation
6mm clearance in total respect to both SFGD corner brackets
Try to squeeze a bit more the CRATE assembly along beam line!

## Slide 19
CRATE assembly into the Basket
Step 3 is the CRATE Cabling sequence (seen from the bottom)
No interference with the top / bottom TPC’s

## Slide 20
MPPC to CRATE Cabling
MPPC
CRATE
MPPC
MPPC Harnesses are staggered
Envelope optimization
Extra length storage
Half mockup (cables + Crates)

## Slide 21
sFGD Clearances
Clearances / Upgrade detectors

## Slide 22
Clearances / Upgrade detectors (sFGD CRATE wrt side TOF)
8mm / side TOF (on a particular piece… which can be reduced by 3-5mm)
Or possibility to move a bit the TOF… (150mm / Basket beam…)
sFGD CRATES / Side TOF
TOF
13mm

## Slide 23
Basket modifications
Next slides for FEA validation

## Slide 24
Basket modifications
BabyBASKET to validate the modifications & installation process

## Slide 25
Basket modifications_FEA
SFGD
Modified basket beam
2x2 oblique beams removed to clear the access to side electronics
Replaced by 2x1 vertical beams in aluminum (FEA to analyze the impact)
Preliminary

## Slide 26
Basket modifications_FEA
Under completion… Results by the review