## Slide 1: The P3 project: A positron source demonstrator for FCC-ee
FCC-ee Week, 2 June 2022
Nicolas Vallis (PSI / EPFL) on behalf of FCC-ee Injector WP6

## Slide 2: The P3 project PSI Positron Production
1. Introduction 2. Key technology 2.1. Adiabatic Matching Device 2.2. RF Structures 2.3. Solenoids around RF structures 2.4. Beam diagnostics 3. Current project status
          3.1 Latest simulation results
          3.2 Main task status

## Slide 3: The P3 project PSI Positron Production
1. Introduction 2. Key technology 2.1. Adiabatic Matching Device 2.2. RF Structures 2.3. Solenoids around RF structures 2.4. Beam diagnostics 3. Current project status
          3.1 Latest simulation results
          3.2 Main task status

## Slide 4: P-cubed (WP6) in context

## Slide 5: P-cubed (WP6) in context
Design and perform a proof-of-principle experiment for the FCC-ee positron source:
    Provide first experimental measure of the FCC-ee e+ Yield
    Develop and test novel approach technology for e+ production
    Contribute to future accelerators and e+ sources

## Slide 6: The FCC-ee Injector complex
P. Craievich et al.

## Slide 7: The FCC-ee Injector complex
P. Craievich et al.
e+ production & capture LINAC
Cavity 2
Cavity 3
…
Cavity N
Cavity 1
solenoids surrounding RF cavities
6 GeV e-
e+e-
Matching Device
200 - 500 MeV
e+e-

## Slide 8: P3 concept design
Adiabatic Matching Device
2 RF Structures
4 solenoids around
Beam Diagnostics
Target
6 GeV e- beam
from SwissFEL linac
Spectrometer
P. Craievich et al.

## Slide 9: Positron Yield
High yield =
  High capture efficiency
  All particles in one bucket
  Small energy spread
e+ beam at target:
  Extremely large emittance
  No time structure
  Extremely large energy spread
E
t
+/- 3.8 %
t.b.d.
1.54 GeV
Representation of e+ distribution at DR input
And DR acceptance window

## Slide 10
State of the art: SuperKEKB
Yield ≈ 0.51
FCC-ee requirement
Yield = 1, w/ safety margin of 21
Preliminary simulation studies: FCC-ee and P-cubed
Yield > 5
1Chaikovska et al., 2019

## Slide 11: The P3 project PSI Positron Production
1. Introduction 2. Key technology 2.1. Adiabatic Matching Device 2.2. RF Structures 2.3. Solenoids around RF structures 2.4. Beam diagnostics 3. Current project status
          3.1 Latest simulation results
          3.2 Main task status

## Slide 12: P3 concept design
Adiabatic Matching Device
2 RF Structures
4 solenoids around
Beam Diagnostics
Target
6 GeV e- beam
from SwissFEL linac
Spectrometer
P. Craievich et al.

## Slide 13: e+ production at SwissFEL
SwissFEL is a free electron laser facility at PSI
The SwissFEL linac can provide similar beam as FCC-ee injector linac: 6 GeV, highly coherent and collimated
Dedicated extraction line to be installed at SwissFEL
Amorphous tungsten
6 GeV e-
e+e- pairs
Very high yield at target (~13) BUT:
Extremely high divergence, energy spread and no time structure = No beam!
Such distribution needs to be captured, transported and measured.

## Slide 14: Adiabatic Matching Device (AMD)
AMD is a strong solenoid lens (up to 17 T in P-cubed studies) surrounding the target.
Field is tapered adiabatically, target is placed downstream from the peak field. higher yield w.r.t. flux concentrator.
Extremely high H field (thus yield) high temperature superconductors (HTS).
6 GeV e-
AMD
e+e- pairs

## Slide 15: AMD (II): Beam dynamics
Before the AMD
    Similar time structure of primary e+
    Large divergence
    Large energy spread
After the AMD
    No time structure
    Still large emittance
    Still large energy spread
Energy [MeV]
z [mm]
Higher solenoid fields do not necessarily imply higher yield.

## Slide 16: AMD (III): Target handling
72 mm
Y. Zhao
R. Zennaro

## Slide 17: RF Cavities
R. Zennaro and A. Magazinik
Length | 1.2 m
RF Frequency | 2.9988 GHz
Gradient | ≈ 20 MV/m
N cells | 21
Q-factor | ~21000
R/L | 18.4 MOhm/m
Aperture | 40 mm
Mode Separation | 3.5 MHz (pi mode)
Standing wave, S-band Cavities

## Slide 18: RF(II): Phase tuning
Phi2
Phi1
e+ in “first” bucket
e+ in “second” bucket

## Slide 19: RF(III): Second bucket
Energy [MeV]
z [mm]
Longitudinal phase space
Captured particles
4 cavities
1
2
3
4

## Slide 20: RF(III): Second bucket

## Slide 21: RF(III): Second bucket
The beam is decelerated to almost zero during first cells
Beam deceleration is a well-known technique to reduce the energy spread

## Slide 22: RF(IV): First bucket

## Slide 23: RF(V): Best working point
Higher yield:
  Higher capture efficiency
  Lower energy spread
  More particle concentration in main bucket
More stable working point (phi1, phi2 scan)
Easier to measure
2nd Bucket
1st Bucket

## Slide 24: Solenoids around RF structures
The captured e+ beam is extremely divergent
A solenoid field needs to be applied along the RF structures in order to maintain high capture efficiency.
In order to provide a high yield, the field needs to be:
    Strong
    Flat
Cavity 2
Cavity 1
6 GeV e-
Magnetic field around
cavities is not zero!
AMD
solenoids

## Slide 25: Solenoids (II): Strength
Solenoid strength around cavities [ T ]
25%
72%
0.3 T as NC
reference point
1.5 T as SC
reference point
Capture efficiency after at 200 MeV

## Slide 26: Solenoids (III): Separation
Cryostat
Space for waveguide and cooling
Space for assembly

## Slide 27: Solenoids (IV): Capture efficiency after 10th cavitiy
Optimized separation (15 cm) between cavities
Large separation (40 cm) between cavities
~75%
~35%

## Slide 28: Beam diagnostics: Faraday Cup
25 Ohm Faraday cup
1050
250
650
25 Ohm Faraday cup
Vacuum chamber
Location of the spectrometer
Spectrometer Magnetic field
e+
e-
B
R. Zennaro

## Slide 29: Beam Diagnostics (II): pz profile reconstruction
e+
Vertical strip probe (2 mm width)
B
Measure different Trajectories of the beam
Sweep magnetic strength of the spectrometer
Latest pz reconstruction
(work in progress)

## Slide 30: Beam Diagnostics (III): Broad band pickup
Longitudinal distribution of the P3 beam
E. Ismaili and F. Marcellini
The use of pick-ups for time structure measurement has been proposed. 60 GHz sampling with coaxial pick-ups is currently under investigation.
The use of a fast BPM has been proposed. Successful precedent settled at SuperKEKB

## Slide 31: The P3 project PSI Positron Production
1. Introduction 2. Key technology 2.1. Adiabatic Matching Device 2.2. RF Structures 2.3. Solenoids around RF structures 2.4. Beam diagnostics 3. Current project status
          3.1 Latest simulation results
          3.2 Main task status

## Slide 32: Status of main tasks
 | Target | Concept design defined.
 | RF Structures | Ready for copper purchase.
Magnets | AMD | HTS tape to be purchased shortly. Design of cryostat in progress.
 | Solenoids around RF structures | Feasibility study of NC and SC options ongoing.
Beam diagnostics | Faraday Cups | Concept design defined.
 | Broad-band pick-ups | 
 | Spectrometer | Baseline design complete. Mechanical modification of existing dipole in progress.
Installation | Radioprotection | Fluka simulations in progress
 | Extraction line at SwissFEL | Location, layout and components defined.
Purchase phase
Main ongoing task
Concept design

## Slide 33: Istallation at SwissFEL
M. Schaer and D. Hauenstein

## Slide 34: The P3 beam

## Slide 35: Yield estimation
…
Cavity 10
Cavity 1
6 GeV e-
10 MeV
e+e-
Matching Device
200 MeV
e+e-
LINAC1
Particle Tracking with ASTRA
Analytical transformation
Geant4
1.5 GeV
e+
DR filter

## Slide 36: Extended simulation (e+ yield)

## Slide 37
FCCIS: 'This project has received funding from the European Union's Horizon 2020 research and innovation programme under the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754.'
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch
Special thanks go to
Prof. Dr. Mike Seidel (EPFL/PSI), thesis advisor;
Dr. Paolo Craievich (PSI), co-advisor;
Dr. Riccardo Zennaro (PSI), supervisor;
and the P3 and FCC-ee Injector team

## Slide 38: Backup: NC Solenoids
Solenoid strength | Mean power consumption (4 solenoids, cooling power not included)
0.3 T | 48 kW
0.5 T | 136 kW
0.7 T | 268 kW
Mean power consumption of 2 cavities = 25 kW

## Slide 39: Backup (III): Size-optimized AMD
Original arrangement: 22 coils
Downsized version: 5 coils.
Thanks to J. Kosse and M. Duda