## Slide 1: Transport requirements
gratefully acknowledging the contributions of J. Bauche, J. Osborne, T. Otto and FIML
02/06/2022 / FCC Week 2022
C. Colloca – R. Rinaldesi

## Slide 2: Table of contents
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Requirements for underground transport and handling of magnets
Requirements for underground transport of people
Boundary conditions
Open points

## Slide 3: Requirements for underground transport and handling of magnets1
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
1 FCC-ee magnets only are considered at this stage
Manufacturing-> Transport to FCC sites -> Storage
Lowering -> Underground transport
Unloading

## Slide 4: Requirements for underground transport and handling of magnets
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Collider ring
Booster ring

## Slide 5: Requirements for underground transport and handling of magnets
Collider ring
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Type | Dipoles | Quadrupoles | Sextupoles
Number | 5800 | 2900 | 3560
Length [cm] | 1200 | 340 | 170
Width [cm] | 45 | 60 | 30
Height [cm] | 30 | 70 | 50
Weight [kg] | 3700 | 5500 | 600

## Slide 6: Requirements for underground transport and handling of magnets
Magnets will be installed as follows:
5800 single dipoles
492 single quadrupoles
1256 units made up of quadrupole-sextupole and supporting girder (Q-S)
1152 units made up of quadrupole-sextupole-sextupole and supporting girder (Q-S-S)
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Collider ring
Unit | Q-S | Q-S-S
Length [cm] | 520 | 700
Width [cm] | 60 | 60
Height [cm] | 100 | 100
Weight [kg] | 6620 | 7400

## Slide 7: Requirements for underground transport and handling of magnets
Booster ring
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Type | Dipoles | Quadrupoles | Sextupoles
Number | 5888 | 2944 | Unknown
Length [cm] | 1140 | 170 | 70
Width [cm] | 30 | 50 | 30
Height [cm] | 30 | 70 | 50
Weight [kg] | 2500 | 2000 | 200

## Slide 8: Requirements for underground transport and handling of magnets
Data about collider ring have been defined based on existing design;
Data about booster ring have been derived by scaling the collider ones;
No specific requirements concerning the max allowed acceleration and tilt angle;
Max tunnel slope: 0.5%
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022

## Slide 9: Requirements for underground transport of people 1/2
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Vehicle shall be used to transport personnel
with material and evacuate them in case of emergency;
Minimum capacity: 6 people - 500 kg (possibly a bit more)
Materials payload: 1000 kg
Total capacity: 1500 – 2000 kg
Max speed: 30 km/h (lower for material);
Battery powered;

## Slide 10: Requirements for underground transport of people 2/2
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Possibility for autonomous drive to be investigated;
Vehicles connected between them and/or with a centralized system;
Modular design allowing the mounting of different platforms;
Hosting equipment for autonomous
or remote interventions (minimise human access to the tunnel).

## Slide 11: Boundary conditions
Vehicle design shall take into account the interaction with the surrounding environment, in particular:
Vehicle-vehicle crossing (especially for people vehicle)
-> if this shall be possible anywhere, a rail-bound system is not possible;
Vehicle-people crossing;
Presence of alcoves;
Dedicated areas for vehicles parking;
Passage through fire protection doors in fire partitions.
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022

## Slide 12: Open points 1/2
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Same vehicle for all types of magnets?
Number of shafts dedicated to magnets’ handling
Magnets design:
  Connection design;
  Installation procedure and time;
  Number of support points.

## Slide 13: Open points 2/2
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
Number of people/sector present at each stage (installation of the machine, operation i.e. technical stops, dismantling)
Installation schedule and sequence of magnets, technical services and fire protection doors
Information about components
to be installed in the klystron gallery
Klystron Gallery
Machine tunnel

## Slide 14: Open points per phase
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022
 | Installation | Operation (technical stops) | Dismantling
Different types of vehicles | x | x | x
Number of shafts for magnets’ handling | x |  | x
Magnets design: Connection design Installation procedure and time Number of support points | x | x | 
Number of people/sector | x | x | x
Installation schedule and sequence of magnets, technical services and fire protection doors | x |  | x
Information about components to be installed in the klystron gallery | x |  | x

## Slide 15: Thank you for your attention.
15
C. Colloca – R. Rinaldesi
02/06/2022 / FCC Week 2022