## Slide 1: 3D Compton polarimeter
Aurélien MARTENS (IJCLab Orsay)
On behalf of FCC-ee FS EPOL group
https://indico.cern.ch/category/8678/

## Slide 2: Introduction: Physics requirements
Blondel et al., arXiv:1909.12245
Beam-based measurements in real time, including beams energy with resonant depolarization
High reproductibility of measurements for various sqrt(s) is critically needed
Extract as much information as possible from physics experiments themselves (crossing angle, luminosity, sqrt(s) spread)
24/7 operable measurement of depolarization

## Slide 3: Resonant depolarization
LEP legacy
Assman et al., Eur. Phys. J. C 6, 187–223 (1999), Blondel et al., arXiv:1909.12245; Baier & Khoze, Sov. J. Nucl. Phys. \textbf{9}, 238-240 (1969)
Scan spin precession frequency with magnetic kicker
Detect beam depolarization at resonance
beam energy spread too large for colliding beams
(smeared spin resonances)
24/7 operable Compton polarimeter for pilot bunches
Use pilot bunches instead

## Slide 4: Precision experiments and Pz
Precision EW physics is sensitive to longitudinal polarization (Pz)
few 10-5 accuracy on EW asymmetries require that Pz is known at 10-5 level !
High precision polarimetry in all directions AND accurate spin propagation desired for colliding bunches too
Can the same polarimeter be used for both colliding (accurate P measurement)
and pilots bunches (accurate E measurement from P) ?

## Slide 5: The Compton process
Klein O. and Nishina Y., Z. Phys. 52(1929) 853; Ginzburg I. et al., Nucl. Instr. Methods in Phys. Research 219 (1984) 5, V. B. Berestetskii, E. M. Lifshitz, L. P. Pitaevskii (1982). Quantum Electrodynamics. Vol. 4 (2nd ed.)
Compton x-section
~0.3b (Ee~45GeV)
Kinematic edge

## Slide 6: Compton polarimeter layout
Blondel et al., arXiv:1909.12245
Redundancy: measure both electrons and photons

## Slide 7: Compton cross-section
Berestskii & Lfshitz QED textbook
The Compton cross-section averaged over scattered particles spins:
Differential cross-section
Electron beam polarization independent
Electron beam polarization dependent
Transverse laser polarisation: nuisance parameter to minimize and keep under control
Transverse electron beam polarisation: intervenes as an asymmetry in the transverse plane
⚠️ But small opening angle of scattered particles:
  Electrons  spectrometer
  Photons  difficult to measure asymmetric distribution of a narrow spot  long lever arm needed

## Slide 8: QED corrections
QED corrections<0.001 @ 45 GeV
Denner & Dittmaier Nucl. Phys. B 540 (1999) 58, Swartz Phys. Rev. D 58 014010 (1998), Veltman Ophys. Rev. D 40 2810 (1989), Veltman Phys. Rev D 42 1856E (1990)
Involved processes e𝛾 e𝛾, e𝛾eee, e𝛾 e𝛾𝛾
Scattered electron energy
Need to be eventually included in simulations…

## Slide 9: Transverse distributions
Realistic detector specifications to be drawn
Based on measurement of scattered particles transverse distributions (pixelized detectors)
Open questions: detector spatial resolution, longitudinal sampling, rates, combined fits, laser polarization flips,…
in a few seconds for pilots
Blondel et al., arXiv:1909.12245
Beam energy may be extracted too!  redundancy
All components extracted with ~0.001 precision in few seconds

## Slide 10: Laser helicity asymmetries
Reproductible and well known laser helicity flip is required
Blondel et al., arXiv:1909.12245

## Slide 11: Laser injection
Some constraints
  Small crossing angles are preferred (cross-section, beam jitters) few mrad typically
  Vertical crossing angle is preferred (space and synchrotron in horizontal plane)
  beam impedance
  beam induced currents in metallic parts
  mechanical stability
  ease of maintenance works
Blondel et al., arXiv:1909.12245
Fully vertical scheme  not very convenient ?
sun

## Slide 12: Laser injection: some inspiration
Gamma Factory SPS proof of principle optical cavity mechanical design could be adapted ?
Interaction point
Beam shield
Laser system and diags below ground
(in excavation) or send them up in a dedicated room
Vertically asymmetric drilling
Gamma Factory Proof of Principle LOI SPSC-I-253

## Slide 13: Laser injection: some inspiration
To be removed in present case
Impedance and currents shield
Cantilevered support (not drawn) directly on ground
Decoupling to pipe
Deport beam aside
Maintenance port
Gamma Factory Proof of Principle LOI SPSC-I-253

## Slide 14: Schematic layout of laser system
Box with rough temperature control
Box with rough temperature control
laser
Polarisation &
beam shaping
Position, pointing control and monitoring
Polarisation independent intensity monitoring
Optical spectrum monitoring possible
Polarisation monitoring
Duplicated at injection
Add Position and pointing monitoring
Rough design based on past experience, similar to other polarimeters
Some comments
  usual scheme for polarization control and monitoring rely on DC measurements
  actual figures for beam size are constrained by integration related issues (inputs needed)
  Laser polarization flipping rate ?
R&D path: photo-elastic modulators allow to measure polarization with FFT or lock-in detection techniques (synergy with SuperKEKB upgrade)
24/7 operable laser system, with full monitoring, remote control
S. Barneljee, M. Roney et al., Upgrading SuperKEKB with a Polarized Electron Beam

## Slide 15: Scattered photon rate
Laser-beam single pulse energy
Photon rate
Compton cross-section
Electron bunch charge (25nC or 6nC)
Geometrical factor
Laser photon energy
(2.4eV for 0.5µm wavelengths)
Transverse beam sizes:
  =300µm
  200µm, =25µm, mm
pilots

## Slide 16: Some possible laser systems
Laser param. | 1 pilot | 1 pilot v2 | All colliding bunches (at Z)
Repetition rate | 3 kHz | 3 kHz | 50 MHz
Pulse energy | 1 mJ | 1 mJ | 100 nJ
Pulse duration | 5 ns | 5 ps (**) | 5 ps (**)
Average power | 3 W | 3 W (***) | 5 W (***)
Scattering rate | 4x105/s (*) | 2x106/s (****) | 2x106/s (****)
Scattering rate per bunch | 4x105/s (*) | 2x106/s | 1.7x102/s
Nikolai’s baseline
(*) Large piwinski contribution, nearly scales as crossing angle, very dependent on laser beam size (was 2x106/s in ref. paper)
(**) Short pulse duration  broader laser spectrum, energy measurement from threshold more difficult
(***) Can be increased to typically ~100W (nowadays) but requires operational validation, management of thermal effects…
(****) not limited by Piwinski contribution  significantly increases when decreasing laser beam size
Same oscillator may be used but two different amplification schemes

## Slide 17: Conclusion
High precision beams energy calibration
High precision beams polarimetry
24/7 operable Compton polarimeter for pilot and colliding bunches
24/7 operable laser system, with full monitoring, remote control
Seems technically achievable with present day technology
Statistical precision compatible with physics requirements
Design being prepared within FCC-FS
A lot of work ahead still (laser design and polarimeter detector design and performance)