## Slide 1: Optics correction studies
Tessa Charles 1,2, Bernhard Holzer 3, Katsunobu Oide 3,4, Dmitry Shatilov, Frank Zimmermann 3
Rogelio Tomas 3, Leon Van Riesen-Haupt 3, and the entire FCC-ee optics team
1. University of Liverpool
2. Cockcroft Institute
3. CERN
4. KEK
FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s H2020 Framework Programme under grant agreement no. 951754.

## Slide 2: FCC-ee Emittance Tuning: Challenges & Constraints
Challenges:
Large beta function values makes us sensitive to field and misalignment errors
Small beta* means strong FF magnets, which in turn requires strong sextupoles for local chromaticity correction.
Small emittance ratio makes us sensitive to any coupling between the horizontal and vertical motion.
Tessa Charles
CEPC workshop 2021
IP
Notes: Beta* = 0.8 mm

## Slide 3: Natural chromaticities for a range of low emittance storage rings
Tessa Charles
Many thanks to:
Rohan Dowd (AS), Masamitsu Aiba (PSI), Katsunobu Oide (KEK), Thorsten Hellert (ALS), Ilya Agapov (DESY), Pedro Fernandes Tavares (MAX IV), Kent Wooton (APS), Bastian Härer (KIT), Liu Lin (LNLS), Simone Di Mitri (Elettra), Jeff Corbett (SLAC), Bernhard Holzer (CERN), Ian Martin (Diamond), David Amorim (SOLEIL)
CEPC workshop 2021
Notes: Here we compare FCC-ee to other low emittance SR around the world, including a number of existing and planned upgrades.
You can see that FCC-ee is pushing towards low emittance whilst battling high chromaticity.

## Slide 4: Context
“The actual value of the tolerances will not be the cost driver. The size of the machine will be the main cost driver.” - H. Mainaud
“Given the size of the FCC-ee, we will not be able to perform standard alignment and to use standard techniques in such a machine: we will need alignment sensors at least for the girders of the arcs quadrupoles and sextupoles. So applying a factor 2 on tolerances should not increase the cost by two.” - H. Mainaud
- FCC-ee tuning & alignment mini-workshop 11 & 12 May 2022

## Slide 5: Context
“Probably, we need to prepare for the fact that we will have to reduce misalignments and errors several times (factor 5?!).
Of course, this increases the cost of the positioning system, but it must be compared with the total cost of the collider. If the total cost increases by a few percent, and the luminosity by fifty, then it probably makes sense.” - D Shatilov
FCC-ee tuning & alignment mini-workshop 11 & 12 May 2022

## Slide 6: LOCO studies at PETRA III
Elaf Musa (DESY) has begun investigating LOCO for FCC-ee. Beginning by using PETRA III to demonstrate LOCO in simulations, and will then investigate the feasibility of LOCO for FCC-ee.

## Slide 7: Correction tools
Orbit correction:
  MICADO & SVD from MAD-X
    Hor. corrector at each QF, Vert. corrector at each QD
  1598 vertical correctors / 1590 horizontal correctors
    BPM at each quadrupole
  1598 BPMs vertical / 1590 BPMs horizontal
Vertical dispersion and orbit:
  Orbit Dispersion Free Steering (DFS)
Linear coupling:
  Coupling resonant driving terms (RDT)
    1 skew at each sextupole
Beta beating correction & Horizontal dispersion via Response Matrix:
  Rematching of the phase advance at the BPMs
    1 trim quadrupole at each sextupole

## Slide 8: Tuning simulations
File generation
Lattice initialisation
Corrections
as sextupole strength increase
Final corrections
Analysis
Tuning simulation

## Slide 9
File generation
Lattice initialisation
Corrections
as sextupole strength increase
Final corrections
Analysis
x 100
Inputs:
MAD-X template file
Errors values (yaml file)
Bash template
(for HT condor submission)
Python simulation configuration
(specify number of seeds [default 100])
generates
100 madx files,
100 bash files, and,
1 HT condor submission file
Tuning simulation

## Slide 10
File generation
Corrections
as sextupole strength increase
Final corrections
Analysis
Lattice initialisation
Tuning simulation
Correction macros defined
Insert bpms, correctors, skew quads, trim quads.
VOLTCA1 = 0.0; VOLTCA2 = 0.0;
Sextupoles turned off
Introduce field errors
Beta beating correction (Python)
Introduce arc misalignments
Girder misalignments (Python)
Add BPM roll angle (rotation of coordinate system before and after BPM) (Python)
Corrections applied:
  tune re-matched
  orbit correction
  beta-beat correction (Python)
  coupling correction (Python)
Introduce IR misalignments
Further correction:
tune re-matched, orbit correction, beta-beat correction, and coupling and
dispersion correction

## Slide 11
File generation
Final corrections
Analysis
Lattice initialisation
Corrections
as sextupole strength increase
Sextupoles set to 10% of their design strength
  Orbit correction
  Combined coupling and dispersion correction (Python)
  Beta-beating correction applied (Python)
  Sextupole strengths increased by 10%
Iterated over many times.
Constant checking of the tunes and orbit avoids running into resonances, or failure to find the closed orbit.
Tuning simulation

## Slide 12
File generation
Analysis
Lattice initialisation
Corrections
as sextupole strength increase
Final corrections
Final correction (at 100% design sextupole strength)
  Additional coupling, dispersion and beta-beating correction applied.
  Step through corrections until beta beating threshold is reached.
  Vary SV cut off values
  Chromaticity correction
Lattice sequence saved.
Lattice sequence file, error tfs file, copied to eos.
Tuning simulation

## Slide 13: Misalignments and field errors
Tessa Charles
  Misalignments are randomly distributed via a Gaussian distribution, truncated at 2.5 sigma.
  This table is not the final set of tolerances.
Notes: This table summarises the current set of misalignments. That’s not to say that this wont’ change. This talk is an update on going work.
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}ccccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$DTHETA & $\Delta$DPHI & Field Errors\\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) & \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 50 & 50 & 300 & 150 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
Arc sextupoles* & 50 & 50 & 300 & 150 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 & $\Delta B /B = 2 \times 10^{-4}$\\
\hline
Girders & 150 & 150 & - & 1000 & - & - \\
\hline
IR quadrupole & 100 & 100 & 250 & 250 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
IR sextupoles & 100 & 100 & 250 & 250 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
\hline
\end{tabular}
\end{table}

## Slide 14: Assigning girder misalignments
Tessa Charles
  - 2 independent DX and DY misalignments for each end of the girder, and which can be used to calculate DTHETA and DPHI.
(not to scale)
dipole
girder
sextupoles/ quadrupoles
dipole
girder
Notes: And actually we have misalignments on top of misalignments. Within the arcs, we have sextpoles and quadrupoels on a girder.

## Slide 15: Misalignments and field errors
Tessa Charles
  Misalignments are randomly distributed via a Gaussian distribution, truncated at 2.5 sigma.
  This table is not the final set of tolerances.
  Distributions of arc quadrupoles and sextupoles, total DX and DX misalignments:
Notes: This table summarises the current set of misalignments. That’s not to say that this wont’ change. This talk is an update on going work.
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}ccccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$DTHETA & $\Delta$DPHI & Field Errors\\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) & \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 50 & 50 & 300 & 150 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
Arc sextupoles* & 50 & 50 & 300 & 150 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 & $\Delta B /B = 2 \times 10^{-4}$\\
\hline
Girders & 150 & 150 & - & 1000 & - & - \\
\hline
IR quadrupole & 100 & 100 & 250 & 250 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
IR sextupoles & 100 & 100 & 250 & 250 & 100 & 100 & $\Delta k /k = 2 \times 10^{-4}$\\
\hline
\end{tabular}
\end{table}

## Slide 16
FCC-ee emittance tuning results
without BPM errors and without chromaticity correction
ttbar (182.5 GeV) 4IP lattice,
after correction strategy:
Important to note:
BPM errors not included and chrom correction not included.
Radiation not included in correctors and trim and skew quads.
Also note:
Despite well corrected linear optics, the DA is still greatly reduced.
RMS misalignment and field errors tolerances:

## Slide 17
Chromaticity correction:
No chromaticity correction:
Chromaticity correction added

## Slide 18
Chromaticity correction:
No chromaticity correction:
Chromaticity correction added
Highest 8 emittances removed, to better view lower end of distribution.

## Slide 19
Tessa Charles
Adding chromaticity correction
Chromaticity correction corrects chromaticity well, but increases coupling.
Applying additional coupling correction changes the chromaticity -> An iterative procedure is necessary.
RMS horizontal orbit and max orbit distortion, after corrections (without BPM errors):
Notes: Why does this happen? Chromaticity corr changes sextupole strengths.
Improved orbit correction would help, but it’s already good.

## Slide 20
Tessa Charles
After corrections, ttbar 4 IP lattice:
Notes: Need to develop and model IR optics tuning knobs

## Slide 21
Summary
The correction algorithms developed in this context represent a powerful correction tools and lead to successful convergence for a large majority of the applied errors seeds. And, most importantly, the lead to values of coupling and emittances that lie within the requirements of the machine design. For a standard set of misalignments, the final median vertical emittance achieved is 0.332 pm rad and horizontal emittance of 1.497 nm rad. The reduced DA needs dedicated investigation.
This work is ongoing.
Tessa Charles
21
Notes: %$\epsilon_{x, \textrm{rms}} = 2.271$ nm rad \\
%$\epsilon_{y, \textrm{rms}} = 0.180$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.0078$ $\%$ \\
Fontsize: 18

## Slide 22: Thank you for your attention.