## Slide 1
ESRF tuning algorithms
History of ESRF tuning  60mm mag-mag tolerances,
       simulated survey replace girder-to-girder
 align on existing survey
New tuning techniques tests  NOECO (Non-linear optics from Off-Energy Closed Orbit
FCC-ee tuning simulations  10mm no IP , NOECO
S.M.Liuzzo, A.Franchi, D.Martin, G.Gatta, et al. , FCC Week, Paris June 2022
Outline Conclusions

## Slide 2: Current ESRF, Accelerator Chain Layout and main parameters
ERSF
Storage ring
C=844 m
E=6 GeV
t= 5-26 h *
VRF= 6 MV
ex=134 nm rad
ey= 10 pm rad
I = 40-200 mA *
(*) according to filling mode
0-200MeV
0.2-6GeV
6GeV
1994-2018 and 2019-??
Compute error tolerances for the SR upgrade

## Slide 3: Tolerance estimates objective
TARGET
Septum
>10h
Touschek Lifetime
@ 200mA uniform, 5pm
Injected
beam
2 main parameters to achieve,
Absolute values depend on facility layout.
-10mm (-8.1mm @INJECTION)
~100% Injection Efficiency
Also :
Emittance variation < 2pm
Feasible correction strengths
Orbit < 100um rms
etc…

## Slide 4: Outline: 90 DAYS to get stable-STORED-BEAM
days 1-30, 2 shifts/day
days 31-60, 2 shifts/day
GUN, LINAC, Transfer Line to Booster
Booster Tr. Line Booster  SR
SR : inject beam
make first turn : lattice steerers, BPM, CT, beam losses ...
few turns -> RF on, beam accumulation (few mA)
orbit, tunes, BPM-QUAD offsets, chromaticity
Response matrix (optics/coupling)
Resonance knobs, sextupoles
specific optics adaptations
beam tuning for users
optimize injection efficiency / lifetime
Wait for vacuum, close collimators
Repeat:
Compute DA, lifetime, injection efficiency, etc…
From EBS MAC 2017

## Slide 5: What is simulated in Commissioning-like beam tuning procedures
GUN, LINAC, Transfer Line to Booster
Booster Tr. Line Booster  SR
SR : inject beam
make first turn : lattice steerers, BPM, CT, beam losses ...
few turns -> RF on, beam accumulation (few mA)
orbit, tunes, BPM-QUAD offsets, chromaticity
Response matrix (optics/coupling)
Resonance knobs, sextupoles
specific optics adaptations
beam tuning for users
optimize injection efficiency / lifetime
Wait for vacuum, close collimators
Repeat: in an optimal order
Compute DA, lifetime, injection efficiency, etc…
days 1-30, 2 shifts/day
days 31-60, 2 shifts/day
Many days to simulate a fraction of the activity to be done in few days only!
1
3
6
6
4
3
2
4
5
6
5
0
Assign lattice errors: magnetic centers + alignment survey
7
Most difficult and neglected
dedicated simulations, not included in the loop
Not included in commissioning-like simulations

## Slide 6: Example of one step of the commissioning-like tuning loop: First Turns (beam threading)
From beam threading till accumulation
Injection on axis (static bump) or off axis (fit injected beam oscillation) available. Start from injection off-axis.
All magnets at their nominal working point
Power orbit steerers to achieve first turn (from simulations, beam survives about 3-4 cells without orbit steering, if magnets & alignment within tolerances).
Measure and correct tune based on few turns data (most relevant for off-axis injection)
Switch on RF, search for optimal frequency and phase
Beam accumulation
Video: first turn correction simulations for beam injected on axis. Large BPM offsets (500mm) are included.
Preparation of the EBS beam commissioning
S M Liuzzo et al 2019 J. Phys.: Conf. Ser. 1350 012022
Measurements here:
Use in commissioning here: https://doi.org/10.1103/PhysRevAccelBeams.24.110701
Not included in tuning simulations as it, but could be done. Usually before step 4, AT is able to provide a closed orbit and tunes.

## Slide 7: Procedure for optics correction
Fit of “measured” partial Orbit Response Matrix (slow)
 FITTED OPTICS MODEL
Computation of normal and skew quadrupoles RDTs + dispersion and correction
 Normal and skew quadrupole correction strengths
This is LOCO equivalent (+ RDTs)
Linear problem + generalize potentially different fit and correction locations
Commissioning-like sequence of corrections is implemented using matlab accelerator toolbox.

## Slide 8: LifEtime and dynamic apertures vs error sources
10h
17h
DA=-10mm
Lifetime = 10h
A CLUSTER is crucial for this analysis. Each error set to analyze requires 1CPUx4h
CAoPAC Workshop l GSI, Darmstadt 10-13 March 2015 l S.M.Liuzzo
How to determine the ”tolerance” ?  DRAW A LINE (relative impact of each error), RESCALE globally.
The line where I should have placed it.
The line where I should have placed it.
Sext. Alignment do more on DA than on TLT ;
Moderate gradient are irrelevant compared to high gradient ;
Etc. etc.

## Slide 9: Tolerable random errors
Each error, on each magnet family, is studied individually looking at the dependence of DA, lifetime, emittances and all relevant parameters vs error amplitude.
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
This table represents only magnetic centers errors.
No alignment survey errors.

## Slide 10: Alignment survey errors, option 1 (the old school): Girder Errors
(g) Stands for girder errors,
no (g), are quadrupole and sextupole individual misalignments
10h
17h
Hor. DA @ QFI, X0.81 to scale at S3,
8mm required at S3, 10mm accepted at QFI
In terms of DA girders and magnet alignment approx. sum up. In terms of lifetime, magnets+girder have a stronger impact.
Girders+Magnets
Girders+Magnets
GOOD
BAD
Girders only
girders

## Slide 11: Alignment survey errors, option 2 (the long one): long range error waves
Impact of error “waves” on horizontal orbit
At a wavelength of L/128~6m
30um errors amplitude give
30 um residual orbit distortion.
At a wavelength of L/2~422m
7mm errors amplitude give
30 um residual orbit distortion.
26/07/2013
SLOW, LARGE VARIATIONS HAVE LIMITED IMPACT ON THE OPTICS

## Slide 12: The measured position of the lattice
nominal
current
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.

## Slide 13: Alignment survey errors, option 3 (the modern way): simulated surveys (replacement of existing SR)
Simulated survey errors about the current position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
26/07/2013
50 cases
WHERE WILL THE SR BE
if we remove it and reinstall it?
horizontal
Longitudinal (electrons path)
vertical
DATA from ALIGNMENT GROUP
D.Martin, G.Gatta
D.Martin, G.Gatta
D.Martin, G.Gatta
Idea by P.Riamondi

## Slide 14: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.6h
range:[16.4 17.1]
26/07/2013
MEASURED SURVEY + simulated alignment errors
SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the blue curve

## Slide 15: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.6h to about 12h with many lost seeds and increasing range.
As above + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
Increasing random errors
TARGET
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.

## Slide 16: In practice
We have no specific beam dynamics interest in the girder-girder tolerance themselves.
Those are not precisely defined among different groups and may lead to lack of understanding.
From beam dynamics, we can say that: large, slow, smooth, variations of position are not detrimental.
In order to model the lattice at the location where it will be installed, we included in all “predictive” (DA, LT, IE,etc) simulations the Simulated Survey Position provided by the alignment group.
From a beam dynamics point of view, as long as magnet-magnet tolerances (actually, single magnets rms position errors) are achieved at every location in the machine, including between magnets standing on neighboring girders, we will get the foreseen Dynamic Aperture and LIFETIME.
We let the alignment group decide how to achieve this requirement.
For ESRF-EBS It worked extremely well, largely exceeding expectations/simulations.
Expected magnet-to-magnet
60-70 mm
From steerers/orbit data
Achieved magnet-to-magnet
25-55 mm
rms DX DY
alignment

## Slide 17: Tolerable random errors
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
GIRDERS
SAME AS worst case MAGNET-MAGNET
What girder-girder tolerances did you use?
60
Many simulations for 1 number needed
Long range
Simulated Survey
How far can be two magnets on opposite sides of the ring?
girder-girder error simulations are useless.
All relative tolerance are as expectable from theory. Alignment will be based on a single value. Why running infinity of simulations? Just use a single number.
Long range error simulations are useless.

## Slide 18: NOECO: sextupoles tuning to maximize lifetime
After commissioning,
Improve measurement based tuning compared to the schemes used in commissioning-like simulations.

## Slide 19: NOECO correction at ESRF, MEASUREMENTS with BEAM
Function developed based on:
A.Franchi,
Data: 24th Jan 2022
Data: Jan 24 2022
Compute SEXTUPOLE correction strengths based on off-energy Fast-RM and dispersion measurement
Proof of principle: OK
SF
Preliminary, to be confirmed in future MDTs

## Slide 20: Start from a bad SD
The specific SD sextupole corrector is NOT found.
Nevertheless, the correction applied recovers the lifetime.
Preliminary, to be confirmed in future MDTs
Data: 19th Apr 2022

## Slide 21: Random sextupole correctors giving ~10h lifetime
40h
10h
10h
30h
The specific random sextupole corrector pattern is NOT found.
Nevertheless, the correction applied recovers the lifetime.
Zero correction strengths are better then 1 iteration of NOECO correction
Empiric sextupoles optimization
NOECO
Preliminary, to be confirmed in future MDTs
Data: 19th Apr 2022

## Slide 22: FCC-ee
Apply the same tuning strategy for FCC-ee.
Not trivial!
Yet not comparable to existing studies (see T. Charles presentation)

## Slide 23: Lattice converted By Felix CARLIER
Parameters table
222.
222.
Add
1 BPM at each quadrupole
1892 BPMs
Consider
Each quadrupoles is an H/V steerer and a skew quad. (1862 correctors)
FCC-ee Z V10 MADX->AT by Felix Carlier

## Slide 24: Lattice tuning functions adapted
Errors:
Correction matrices
No multipole errors
Grouped trying to follow family naming
Derivatives for optics fit, on computing cluster
Correction strategy:
+ matrices for RDT correction
SOME MAGNETS ARE described with “slices”: MUST MOVE TOGETHER For now, do not move

## Slide 25: Commissioning like correction sequence completed for 3 seeds with limited errors.
--------------------------------------------------
------ total std corrector values applied --------
------ --------
HK (1892) [1/m]: 0.00e+00 -> 9.67e-08
VK (1892) [1/m]: 0.00e+00 -> 6.64e-08
SK (1892) [1/m2]: 0.00e+00 -> 1.11e-06
QK (1892) [1/m2]: 4.17e-07 -> 5.14e-06
------ --------
------ residual orbit and dispersion --------
------ --------
OH (13363) [m]: 4.29e-04 -> 1.99e-05
OV (13363) [m]: 2.23e-04 -> 1.60e-05
DH (13363) [m]: 9.43e-02 -> 1.25e-01
DV (13363) [m]:7.39e-02 -> 5.36e-03
BBH (13363) %: 2.9 -> 1.6
BBV (13363) %: 116.7 -> 2.4
PhH (13363) : 2.28e-02 -> 1.22e-02
PhV (13363) : 8.48e-02 -> 3.30e-02
------ --------
------ tune and emittance --------
------ --------
Qx [222.172]: 222.176 -> 222.175
Qy [222.400]: 222.387 -> 222.402
Cx [-0.070]: -0.354 -> -0.065
Cy [-0.123]: -13.748 -> -1.718
EX [705.313 pm]: -183082.420 -> 787.625
EY [0.000pm]: -3340463.956 -> 0.105
------ --------
--------------------------------------------------
SEQUENCE OF CORRECTIONS
10 um rms (truncated at 2.5sigmas)

## Slide 26: Dynamic aperture and momentum acceptance with errors
This is only a preliminary plot, only showing that we can compute DA and MA for FCC-ee with errors and correction.
We need to work more time on it!
1/3 seeds failed completing the loop.
Assume the recent updates in AT
Tune the correction parameters (singular values cuts)
Tune the correction loop steps (tune, orbit, etc)
Start with COMMISSIONING OPTICS
Preliminary, more tuning of commissioning-like scripts for FCC-ee is needed
Preliminary, more tuning of commissioning-like scripts for FCC-ee is needed
The correction loop is unstable above 20-30 um (no IP errors). In most cases a closed orbit is found but tunes are NaN. May be fixed including an estimate of tunes from few turns, not presently available in the matlab AT toolkit.

## Slide 27: NOECO Simulations (Fit & correction) FOR FCC-ee
Top: Retrieve (large) sextupole error.
Right: computed momentum acceptance (over 600 m only) & Touschek lifetime
Test with one large sextupole error (50%)
FCC-ee ideal lattice
only ± 25 Hz RF freq. shift possible w/o making optics unstable

## Slide 28: NOECO Simulations (Fit & correction) FOR FCC-ee
Top: Retrieve (large) sextupole error.
Right: computed momentum acceptance (over 600 m only) & Touschek lifetime
Test with one sextupole with inverted polarity
FCC-ee uncorrected lattice with random quad. & sext. misalignments (RMS 0.1 mm)

## Slide 29: NOECO Simulations (Fit & correction) FOR FCC-ee
Top: Retrieve (large) sextupole error.
Right: computed momentum acceptance (over 600 m only) & Touschek lifetime
Test with one sextupole with inverted polarity
FCC-ee uncorrected lattice with random quad. gradient errors (RMS 3x10-5 m-2)

## Slide 30: Conclusions
Commissioning-like simulations do not include many of the steps that are actually done during commissioning. Space for future developments.
For EBS tuning was not the real issue. It was rather to set the most correct and realistic errors.
  Only one number is necessary for magnetic centers tolerances (for EBS 60 um). All other values are useful only if locally this value may not be achieved.
  Use simulated survey rather than girder-to-girder tolerances: more information, more realistic, easier to simulate.
NOECO has been tested in MDT and shows good potential, even if it does not improve compared to our best optimized settings for operation.
Contrary to EBS, FCC-ee optics tuning with errors is not trivial at all. Even without radiation!
The matlab AT tuning procedure used for EBS is being adapted to FCC. Seen the amount of changes needed till now and the speed at which AT is developing, it is likely that the work will start over using pyAT. This activity is synergic with several other laboratories working on python AT commissioning like simulations.
NOECO has been used in simulations also for the FCCee lattice, recovering the local momentum acceptance also in presence of errors.
Commissioning optics are being prepared and translated to AT. Dipoles will be sliced prior to the correction.

## Slide 31: BACKUP

## Slide 32: First-turns trajectory correction progress on tbt BPMs
BPM #
Number of turns
21h38
21h22
0
1
2
3
4 (first turn)
5
6
7
8
9
10 (few turns)
11
12
Stored beam
Sextupoles and octupoles ON
DATA
October 2018
Preparation of the EBS beam commissioning
S M Liuzzo et al 2019 J. Phys.: Conf. Ser. 1350 012022

## Slide 33: low intensity tuning (phase 1)
Response matrix (ORM) measurements is used for:
Precise orbit control (full, not compulsory)
Optics and coupling tuning (partial)
Check magnet calibrations
It is possible to use AC steerers for a fast partial response measurement. At ESRF this was only possible after the initial SLOW measurements, for calibration.
Optics tuning/correction
response matrix
beam-based alignment
tune working point
emittances
chromaticity
dynamic apertures
specific optics tuning (ex: phase advance between sextupoles)
Separated simulations for BBA, DA and special tunings.
For BBA in the tuning loop we assume it is possible by reducing BPM offsets from 500 to 50 um. (not as trivial as it sounds, as changing the offset the orbit has to be re-corrected)

## Slide 34: Comparable tolerance table
DQ (combined function dipoles) behave as quadrupoles concerning errors. Evident the impact on vertical dispersion compared to the other quadrupoles (defocussing quadrupoles).
Quadrupoles have large impact on orbit and horizontal dispersion, also in this case, lifetime and DA are strongly affected. QF6 and QF8 are dominant.
Sextupoles have the largest impact on DA, they are also the strongest source of beta-beating and emittance as expected.
Octupoles influence is limited compared to quadrupole and sextupoles, nevertheless they do have an impact on DA. Their effect on lifetime is very small.
Rotations up to 100urad have impact on the various parameters but limited.
How tolerances were defined
In RED
The worst crossing of the “line” for each performance parameter

## Slide 35: Correction of realistic errors (100um) , no RADIATION
Last simulations with errors only in arcs and of 30um rms.
Now 100 um rms errors in all the elements, a part IP magnets (50um)

## Slide 36: Matrices for correction steps
Long quads, small kicks (not integrated 1/m)!
orbit
Trajectory (Threading)
Optics correction

## Slide 37: Trajectory correction, fails due to missing correctors at the beginning of the lattice.
Solution:
add more correctors : NOT OK. The corrector indexes look correct, first corrector before first BPM. Nevertheless the first block of the Trajectory response is ZEROS, thus the trajectory correction never starts.
Trajectory correction Response Matrix
RECOMPUTE TRAJECTORY RM.

## Slide 38: Beam threading is running ok
All magnets ON at their nominal strengths.
Steerers powered as soon as there is beam on the next BPMs
Steering till one turn and closure of the orbit with the last 2 steerers.
Allow for 0.5mm trajectory amplitude accepted. May be this has to be revisited.

## Slide 39: Closed orbit correction
Once a closed orbit is found, correct it using all available H/V steerers.
No limits set to steerers for now.
Truncation of SVD to 500 singular vectors / >1800, to keep forces required to a minimum.
There is a closed orbit but tunes are several units different from nominal.

## Slide 40: Correction loop continues with tune and chromaticity correction
TO DO: Add orbit in in all functions, it must be given to atlinopt, atfittune, atmatch, …

## Slide 42: Try reduced errors and simplified orbit correction (2 steps only)

## Slide 43: Girder Errors
Girder displacements and rotations
Girder displacements and rotations
+ random errors Quad. and Sext.
4 girders, BPMs are moved with the girder.
l 30-31 May 2014 l S.M.Liuzzo
How GIRDER
tolerances were defined

## Slide 44: Dynamic aperture @S3 septum vs errors for s28A + RDT correction
-20%
l WP1 ESRF upgrade l May 2014 l S.M.Liuzzo
26/07/2013
How GIRDER
tolerances were defined
All is NOT the sum of each error

## Slide 45: error values for a reduction of 20% of Hor. Dynamic Aperture @S3
No influence on emittances
Strong impact of quadrupole errors
RDT correction
How GIRDER
tolerances were defined

## Slide 46: Summary Table of Girder Errors
(g) Stands for girder errors, no g, are quadrupole and sextupole individual misalignments
How GIRDER
tolerances were defined
Commissioning-like correction sequence to get these data
Cluster, Average over several (10) error seeds.
Computing cluster

## Slide 47: The measured position of the lattice
nominal
current
How GIRDER
tolerances were excluded
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.

## Slide 48: Survey errors PLUS random errors
Random Gaussian DX DY in quadrupoles and sextupoles on top of the survey errors.
The blue curve represents the current ESRF storage ring position.
The x symbols are the interpolated positions on this curve for the S28A lattice.
BPM are positioned on the same curve.
DX and DZ and girder rotations are applied.
Errors are ramped in steps of 20% up to the nominal value.
Added random errors to account for unknown magnetic center position
l ESRF Upgrade l June 2014 l S.M.Liuzzo
How GIRDER
tolerances were excluded
D.Martin, G.Gatta

## Slide 49: Long range errors
Error “waves” applied to the lattice: DX, DY, Rotations for quad and sext.
Correction performed for each frequency and amplitude set as:
Open trajectory correction
Orbit correction
RDT correction
storage ring survey data
simulated 1st harmonic,
Simulations performed on the OAR asd cluster, 8h-600cpu
26/07/2013
How GIRDER
tolerances were excluded

## Slide 50: displacements and global tilt
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.06e-04
VK (288) [1/m]: 0.00e+00 -> 1.19e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.08e-05
VKL (288) [rad]: 0.00e+00 -> 8.25e-06
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 3.78e-05 -> 9.02e-06
OV (288) [m]: 1.48e-04 -> 9.05e-07
DH (288) [m]: 3.80e-04 -> 1.18e-04
DV (288) [m]:1.38e-03 -> 3.33e-04
BBH (288) %: 0.9 -> 0.3
BBV (288) %: 0.6 -> 0.3
PhH (288) : 2.09e-02 -> 1.75e-02
PhV (288) : 1.70e-02 -> 1.07e-02
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.580 -> 0.580
Qy [0.620]: 0.619 -> 0.619
EX [147.528 pm]: 147.506 -> 147.545
EY [0.000pm]: 0.986 -> 0.049
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.51, 0.99,
corrected (ex, ey): 147.54, 0.05,
Freq 1, every 32

## Slide 51: every 8 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.37e-04
VK (288) [1/m]: 0.00e+00 -> 1.63e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.54e-05
VKL (288) [rad]: 0.00e+00 -> 1.14e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 8.79e-05 -> 1.31e-05
OV (288) [m]: 1.35e-03 -> 1.67e-06
DH (288) [m]: 2.59e-03 -> 2.61e-04
DV (288) [m]:1.02e-02 -> 3.12e-03
BBH (288) %: 3.9 -> 0.5
BBV (288) %: 2.2 -> 0.5
PhH (288) : 2.95e-02 -> 6.91e-03
PhV (288) : 2.13e-02 -> 5.69e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.574 -> 0.580
Qy [0.620]: 0.612 -> 0.619
EX [147.528 pm]: 147.077 -> 147.596
EY [0.000pm]: 67.039 -> 4.014
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.08, 67.04,
corrected (ex, ey): 147.60, 4.01,
Freq 4, every 8 cells

## Slide 52: Misalignment pattern, every 2 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.05e-04
VK (288) [1/m]: 0.00e+00 -> 5.10e-05
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.07e-05
VKL (288) [rad]: 0.00e+00 -> 6.21e-06
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 4.93e-05 -> 8.49e-06
OV (288) [m]: 3.13e-05 -> 1.60e-06
DH (288) [m]: 5.04e-04 -> 3.98e-04
DV (288) [m]:3.92e-04 -> 1.69e-04
BBH (288) %: 1.1 -> 0.6
BBV (288) %: 0.8 -> 0.2
PhH (288) : 7.76e-03 -> 2.97e-03
PhV (288) : 9.02e-03 -> 3.40e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.582 -> 0.579
Qy [0.620]: 0.616 -> 0.622
EX [147.528 pm]: 147.483 -> 141.513
EY [0.000pm]: 0.301 -> 13.404
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.48, 0.30,
corrected (ex, ey): 141.51, 13.40,
Freq 16, Every 2 cells

## Slide 53: Long range errors: error envelope function
Impact of error “waves” on horizontal orbit
At a wavelength of L/128~6m
30um errors amplitude give
30 um residual orbit distortion.
At a wavelength of L/2~422m
7mm errors amplitude give
30 um residual orbit distortion.
26/07/2013
How GIRDER
tolerances were excluded
SLOW, LARGE VARIATIONS HAVE LIMITED IMPACT ON THE OPTICS

## Slide 54: The measured position of the lattice
nominal
current
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 55: every 16 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.51e-04
VK (288) [1/m]: 0.00e+00 -> 1.68e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.54e-05
VKL (288) [rad]: 0.00e+00 -> 1.17e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 6.01e-05 -> 1.28e-05
OV (288) [m]: 2.61e-04 -> 1.31e-06
DH (288) [m]: 5.95e-04 -> 1.75e-04
DV (288) [m]:2.41e-03 -> 5.84e-04
BBH (288) %: 1.4 -> 0.5
BBV (288) %: 0.9 -> 0.5
PhH (288) : 1.77e-02 -> 1.28e-02
PhV (288) : 1.42e-02 -> 8.11e-03
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.579 -> 0.580
Qy [0.620]: 0.618 -> 0.619
EX [147.528 pm]: 147.487 -> 147.563
EY [0.000pm]: 2.806 -> 0.137
------ --------
--------------------------------------------------
Freq 2, evry 16 cells

## Slide 56: every 4 cells
--------------------------------------------------
------ total std corrector values applyed --------
------ --------
HK (288) [1/m]: 0.00e+00 -> 1.24e-04
VK (288) [1/m]: 0.00e+00 -> 1.63e-04
SK (288) [1/m2]: 0.00e+00 -> 0.00e+00
QK (514) [1/m2]: 0.00e+00 -> 0.00e+00
HKL (288) [rad]: 0.00e+00 -> 1.59e-05
VKL (288) [rad]: 0.00e+00 -> 1.14e-05
SKL (288) [T/m]: 0.00e+00 -> 0.00e+00
QKL (514) [T/m]: 0.00e+00 -> 0.00e+00
------ --------
------ residual orbit and dispersion --------
------ --------
OH (288) [m]: 6.11e-05 -> 1.40e-05
OV (288) [m]: 1.37e-04 -> 1.84e-06
DH (288) [m]: 7.00e-04 -> 2.83e-04
DV (288) [m]:1.72e-03 -> 3.68e-04
BBH (288) %: 3.8 -> 2.4
BBV (288) %: 1.8 -> 2.5
PhH (288) : 2.23e-02 -> 1.34e-02
PhV (288) : 1.19e-02 -> 1.38e-02
------ --------
------ tune and emittance --------
------ --------
Qx [0.580]: 0.583 -> 0.580
Qy [0.620]: 0.622 -> 0.620
EX [147.528 pm]: 147.809 -> 147.692
EY [0.000pm]: 1.477 -> 0.133
------ --------
--------------------------------------------------
----- ----- -- -- -- -- ------ -----
initial (ex, ey): 147.53, 0.00,
errors (ex, ey): 147.81, 1.48,
corrected (ex, ey): 147.69, 0.13,
Freq 8, every 4 cells

## Slide 57: Emittance, dispersion and beta-beating vs wavelength
How GIRDER
tolerances were excluded

## Slide 58: Comparison of various Error Sources to obtain 30 um orbit

## Slide 59: Comparison of various Error Sources (other parameters)

## Slide 60: DRAFT table of tolerable rms of error distributions
Error (S28 Table) | TDS value | New value
Dipole DPSI | 300 mrad | Splitted
Dipole DX | 50 mm | Splitted
Dipole DY | 50 mm | Splitted
Quadrupole DX | 50 mm | Splitted
Quadrupole DY | 100 mm | Splitted
Quadrupole DPSI | 350 mrad | Splitted
Sextupole DX | 50 mm | 70
Sextupole DY | 75 mm | 50
Sextupole DPSI | - | 500 mrad
Girder DX | 50 mm | Removed
Girder DY | 50 mm | Removed
Girder DPSI | 200 mrad | Removed
BPM X-offset | 50 mm | Separated
BPM Y-offset | 50 mm | Separated
Dipole DK0/DK0 | 10 10-4 | 10 10-4
Quadrupole DK1/K1 | 5 10-4 | 5 10-4
Sextupole DK2/K2 | 35 10-4 | 35 10-4
Error (S28 Table) | TDS value | New value
DL DPSI | 300 | 500 mrad
DL DX | 50 | 100 mm
DL DY | 50 | 100 mm
DL DS | - | 1000 mm
DQ and QF6-8 DPSI | 300 | 200 mrad
DQ and QF6-8 DX | 50 | 50 mm
DQ and QF6-8 DY | 50 | 70 mm
DQ and QF6-8 DS | - | 500 mm
Octupole DX | - | 100 mm
Octupole DY | - | 100 mm
Octupole DPSI | - | 500 mrad
Octupole DS | - | 1000 mm
Q [D-F] [1-5] DPSI | 350 | 500 mrad
Q [D-F] [1-5] DX | 50 | 100 mm
Q [D-F] [1-5] DY | 100 | 85 mm
Q [D-F] [1-5] DS | - | 500 mm
Sextupole DS | - | 1000 mm
DS = longitudinal displacement
DX = radial displacement
DY = vertical displacement
DPSI = rotation about beam axis
Girder errors replaced by smooth wave summing first 4 long wavelengths with 0.6mm amplitude.

## Slide 61: d.A. and lifetime: Table above + waves + Bpm errors 50 um rms
DA about 7mm at S3 septum.
Some seeds have bad DA and some are lost. Work in progress to recover them. this may change the above list of tolerable errors.
Lifetime is about 7h.
“Closed” continuous waves

## Slide 62: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.7h
range:[16.6 17]
IDEAL SURVEY SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the red curve
How GIRDER and LONG RANGE
tolerances were excluded

## Slide 63: Alignment survey errors, option 3 (the modern way): simulated surveys (ideal position)
Simulated survey errors about the nominal position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
PREVIOUS
horizontal
Longitudinal (electrons path)
vertical
D.Martin, G.Gatta
D.Martin, G.Gatta
DATA from ALIGNMENT GROUP
50 cases
WHERE WILL THE SR BE
after green field installation?

## Slide 64: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.7h to about 13h with many lost seeds and increasing range.
IDEAL SURVEY + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
Increasing errors
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.
Increasing random errors
nominal
current
On the red curve

## Slide 65
X-ray beam position at ID (60 meters) : decision to place the new SR where the old was.
All ID are assumed to be at 60m from the source.
The position of the beam after 60m is very similar for ESRF and S28A considering the current survey measurement.
The position if the ring was aligned on the reference circumference would be about (0,0) for al ID.
Current (simulated) position of the X-ray at the beamline
position of the X-ray at the beamline for S28A on the same survey
4TH APAC 2014
S28
ESRF
“on theory geom”.
Good choice. During commissioning (Jan2019): ALL beamlines but one could see the x-ray beam at the white beam viewers at very first Front End opening.

## Slide 66: Larger errors on more magnets
30 um rms (truncated at 2.5sigmas)
1/10 seeds failed

## Slide 67: Procedure for optics correction
Fit of “measured” partial Orbit Response Matrix (slow)
 FITTED OPTICS MODEL
Computation of normal and skew quadrupoles RDTs + dispersion and correction
 Normal and skew quadrupole correction strengths
This is LOCO equivalent (+ RDTs)
Linear problem + generalize potentially different fit and correction locations