## Slide 1: Status and plans for FCC-hh collimation
R. Bruce, A. Abramov, F. Cerutti, M. Giovannozzi, S. Redaelli, T. Risselada
CDR studies:
Y. Alexahin, W. Bartmann, A. Bertarelli, S. Arsenyev, I. Besana, F. Carra, A. Chance, B. Dalena, A. Faus-Golfe, M. Fiascaris, S. Gilardoni, E. Gianfelice-Wendt, G. Gobbi, J. Hunt, J. Jowett, A. Krainer, G. Lamanna, A. Langner, A. Lechner, R. Martin, A. Mereghetti, D. Mirarchi, N. Mokhov, J. Molson, A. Narayanan, L. Nevay, M. Pasquali, A. Perillo Marcone, E. Renner, M. Schaumann, D. Schulte, M. Serluca, E. Skordis, M.J. Syphers, I. Tropin, M. Varasteh, Y. Zou
29/06/2021 FCC week
Roderik Bruce
Space for additional logos

## Slide 2: Outline
Introduction and motivation
  Challenges with collimation in high-energy hadron colliders
  FCC-hh vs LHC
  Recap of collimation design for CDR
  Updates since CDR
  Outlook and needed future work
  Conclusions

## Slide 3: Collimation in high-energy colliders
High energy and intensity => Typically, very high stored beam energy
Need superconducting magnets to reach sufficiently high magnetic fields
  Cooled to cryogenic temperatures
  Sensitive to heating => Small temperature rise causes a quench (loss of superconductivity)
  Beam losses are unavoidable during regular operation
    Even a tiny loss could cause a quench, or even material damage
  Need collimation system to safely intercept and attenuate these losses

## Slide 4: Collimation challenge: LHC vs FCC
Cold aperture, superconductors
Beam: 680 MJ
collimator
HL-LHC
Loss power up to ~1 MW
Quench limit ~ 30 W/m
Cold aperture, superconductors
Beam: 8.3 GJ
collimator
FCC-hh
Loss power up to 11.6 MW
Quench limit ~ 100 W/m
Needed loss attenuation: factor ~3×104
Needed loss attenuation: factor ~105

## Slide 5: How much is 8.3 GJ?
0.6 MJ
LHC: 362 MJ - kinetic energy of
TGV train cruising at 155 km/h
FCC-hh: 8.3 GJ – kinetic energy of Airbus A380 (empty) cruising at 880 km/h
FCC-hh beams are highly destructive!!

## Slide 6: Outline
Introduction and motivation
  Challenges with collimation in high-energy hadron colliders
  FCC-hh vs LHC
  Recap of collimation design for CDR
  Updates since CDR
  Outlook and needed future work
  Conclusions

## Slide 7: FCC-hh collimation layout: CDR version
The following few slides are a summary of previous studies for CDR, references:
  R Bruce et al 2019 J. Phys.: Conf. Ser. 1350 012009
  Previous FCC week talks, FCC collimation meetings
  Long CDR (not yet published)
Separate betatron (PJ) and momentum cleaning (PF)
The FCC-hh collimation system is a scaled up version of the HL-LHC/LHC system (NIM, A 894 (2018) 96-106)

## Slide 8: Optics of collimation insertions: CDR version
IRJ (Betatron cleaning)
IRF (Momentum cleaning)
Scaled β-functions and insertion length by factor 5 from the LHC  2.8 km insertion length
Increased dispersion in momentum cleaning insertion

## Slide 9: FCC-hh multi-stage collimation system
As in the LHC, using a multi-stage system with primary and secondary collimators, shower absorbers, dispersion suppressor (DS) collimators
  DS collimators are placed in the cold region, in between dipoles where dispersion has risen
Similar layout as the LHC, but some modifications: DS collimators in many insertions, extra shower absorbers in extraction insertion, removal of skew primary
DS collimator

## Slide 10: Collimation performance – FCC-hh protons
Collimation performance checked with tracking studies using the SixTrack-FLUKA coupling and dedicated FLUKA simulations of exposed magnets
Collimation system is extremely efficient at absorbing horizontal and vertical losses – almost no losses on cold machine aperture, thanks to dispersion suppressor collimators
Collision, 50 TeV
Most loaded cold magnet
J. Molson
M. Varasteh

## Slide 11: FCC collimator design
Assuming LHC-type collimators, with some design modifications, following iterative simulations of tracking, energy deposition and thermo-mechanical response
Materials
  Primary collimators, and most loaded secondary collimator made of carbon-fiber-composite (CFC) for maximum robustness
  Remaining secondary collimators in MoGr with 5 μm Mo coating for a good compromise between impedance and robustness
Collimators would survive design losses in simulations, but some challenges remain: high temperature leading to potential outgassing, high deflection, load on cooling pipes
Horizontal primary
M. Varasteh
G. Gobbi, M. Pasquali

## Slide 12: Outline
Introduction and motivation
  Challenges with collimation in high-energy hadron colliders
  FCC-hh vs LHC
  Recap of collimation design for CDR
  Updates since CDR
  Outlook and needed future work
  Conclusions

## Slide 13: Updates since CDR
Tunnel layout updated – see talk M. Giovannozzi
  Need to revisit optics and layout of the whole ring
Symmetric 8-point layout, ring circumference decreased from 97.7 km to 91.1 km
Betatron collimation moved to shorter insertion: 2.1 km instead of 2.8 km
Momentum collimation in longer insertion: 2.1 km instead of 1.4 km
CDR
2022

## Slide 14: Updates to FCC-hh ring
New layout and optics under development – work in progress, but first results available (T. Risselada)
  Details shown in talk by M. Giovannozzi
Inserted collimators similar to LHC layout, including betatron and momentum collimation, tertiary collimators at experiments
  Some collimators still to be implemented (at beam dump, physics debris…)
IRA
IRB
IRD
IRF
IRG
IRH
IRJ
IRL
exp
exp
exp
exp
collim.
collim.
dump
RF

## Slide 15: Updates to betatron collimation layout
Scaling the original LHC collimation optics to new insertion lengths (T. Risselada)
Similar collimator layout as LHC, but including 3 dispersion suppressor collimators as CDR-version of FCC-hh
Insertion length and beta functions scaled by a factor ~4 compared to the LHC
Smallest collimator half gap (vertical primary) around 0.8 mm
  Compare: ~1mm in LHC
IRF

## Slide 16: Momentum collimation
For momentum collimation, LHC scaling used as starting point
First implementation of optics and layout available
Features high dispersion at primary collimator to give flexibility and independence between betatron and momentum cuts
DS collimators added
IRH

## Slide 17: Optimization of doglegs
Dogleg changes the distance between the beams in collimation insertion
  Separate primary beam from neutrals.
  Minimise flux of neutrals on the first superconducting magnet on right side of IP
  Needed separation depends on geometry of insertion
CDR layout: dogleg scaled from the LHC
New version: dogleg geometry worked out based on actual geometry in IRH
  290 mm separation proposed (compare 250 mm in the arc)
  To be confirmed with energy deposition studies
M. Giovannozzi

## Slide 18: Collimation in experimental insertions
Two pairs (horizontal-vertical) tertiary collimators on incoming beam
Two dispersion suppressor collimators on outgoing beam
Physics debris collimators still to be implemented
IRG

## Slide 19: Updates to aperture model
A detailed aperture model around the ring is crucial for collimation studies
First implementation of new aperture model, based on mapping from CDR lattice (A. Abramov)
  Including main magnets and collimators in insertion regions and arcs
To be refined in future iterations
Full ring
A. Abramov

## Slide 20: Aperture model in insertions
Apertures mapped from similar elements in CDR lattice – to be refined in future iterations
IRF (betatron collimation)
A. Abramov
IRH (momentum collimation)
IRG (experiment)
Preliminary result

## Slide 21: Simulations of collimation performance
Collimation performance simulated for latest version of FCC-hh using the SixTrack-FLUKA coupling
  Magnetic tracking using SixTrack, particle-matter interactions in FLUKA
Simulation assumptions
  1 μm impact parameter of generic halo on primary collimator – not simulating diffusion bringing halo onto collimators
  Same collimator settings in σ and materials as in CDR
Main beam
Impact parameter

## Slide 22: Simulated performance
Generally very good protection of the ring, losses localized on betatron collimation system
Rather high losses on tertiary collimators, with downstream leakage to cold magnets
  Potentially problematic, to be followed up in future iterations
Horizontal halo, beam 1, 50 TeV
Preliminary result
A. Abramov

## Slide 23: Simulated performance - IRF
Dispersion suppressor collimators essential for protecting the ring and the DS
Nevertheless losses in between them are well above the assumed quench limit
  Further iterations are needed to optimize collimation performance
Energy deposition should be evaluated with dedicated studies at critical locations – future work
  Compare power load in magnet coils with quench limit
  Note: Particle showers not seen in the loss map plots, which show only proton losses
Horizontal halo, beam 1, 50 TeV, Zoom in IRF
Preliminary result
A. Abramov

## Slide 24: High-β optics for collimation
Small collimator gaps might lead to problematic impedance (to be evaluated)
Could be mitigated through an optics with larger β-functions
Such an optics could also give significant gains in cleaning efficiency
  As for LHC studies in IPAC’21 paper
First exploratory studies carried out for new FCC-hh layout (T. Risselada)
  To be followed up with impedance and cleaning performance studies
T. Risselada

## Slide 25: Outline
Introduction and motivation
  Challenges with collimation in high-energy hadron colliders
  FCC-hh vs LHC
  Recap of collimation design for CDR
  Updates since CDR
  Outlook and needed future work
  Conclusions

## Slide 26: Next steps
Need to repeat work from CDR for new layout
Explore optimizations of optics and collimator settings
Study performance of momentum cleaning
Study impedance
Energy deposition studies to quantify risk of quench for design losses
Maybe new thermo-mechanical studies of most loaded collimators
Study outgassing and cooling of the most impacted elements in collimation insertion
Study failure scenarios
Collimation for Pb ion operation
  Energy deposition studies of collimation insertion and dispersion suppressor, possibly including imperfections
  Further studies of secondary beams from collision points
Imperfection studies?
Think of possible HiRadMat tests?
  Potential alternative: Laser-induced mechanical shock – possible synergies with tests carried out at GSI facility?

## Slide 27: Conclusions
An excellent collimation performance is crucial to keep the FCC-hh safe, and to operate smoothly without quenches
  8.3 GJ stored beam energy, 11.6 MW beam loss power
Fairly mature design presented in CDR, new iterations needed with latest layout
  Shorter insertion length for betatron collimation
  First new optics and collimation layout developed for betatron and momentum cleaning insertions
    Work in progress
First studies of cleaning performance with new lattice performed
  Generally good performance, but some bottlenecks need further study and performance improvements
    Tertiary collimators
    IRF dispersion suppressor

## Slide 28: Thank you for your attention.
28
Space for additional logos
Name of the speaker/author
Date / Name of the event