## Slide 1: SRF Baseline Cavity Designs for the Z and W Working Point of the FCC-ee
by Sosoho-Abasi Udongwo
Supervisors: Dr. Shahnam Gorgi Zadeh, Dr. Rama Calaga, Prof. Dr. Ursula van Rienen

## Slide 2: Content
SRF Overview
W working point
  Previous Design and Design Update
Z working point
  Previous Design and Design Update HOM Coupler (W Working Point)
Summary

## Slide 3: SRF Overview
The previous RF baseline presented in the CDR [1] considers:
  1-cell 400 MHz cavities– Z working point,
  4-cell 400 MHz cavities - W and H working points and
  Hybrid system 4-cell 400 MHz and 5-cell 800 MHz cavities - ttbar working point [2]
A detailed study [1] of the W working point showed strong higher-order mode (HOM) effects in the 4-cell cavities which can limit the operation of the cavities in terms of HOM power and beam stability requirements
A 2-Cell accelerating cavity and HOM coupler have been designed for the W RF working point of the FCC-ee with special attention to the HOM performance of the cavity
The present update to the RF layout considers:
  2-cell 400 MHz cavities - W working point
  1-cell cavities 400 MHz – Z working point (Updated Design)
[1] M. Boscolo et al., “FCC-ee machine design overview”, in FCC week, Amsterdam, 2018.
[2] S. Gorgi Zadeh, “Accelerating cavity and higher-order mode coupler design for the Future Circular Collider”, Ph.D. thesis, Theoretische Elektrotechnik, Universität Rostock, 2020;http://purl.uni-rostock.de/rosdok/id00003023

## Slide 4: W Working Point
Machine parameter | Z
Beam energy [GeV] | 80
Beam current [mA] | 147
Beam RF voltage [GV] | 0.750.44
SR loss/turn [GeV] | 0.34
No. of bunches/beam | 2000
Bunch intensity [ | 1.5
Bunch SR length [mm] | 3.0
Bunch BS length [mm] | 6.0
Luminosity [] | 28
Machine parameter | Z
Beam energy [GeV] | 80
Beam current [mA] | 
Beam RF voltage [GV] | 
SR loss/turn [GeV] | 0.34
No. of bunches/beam | 2000
 | 1.5
Bunch SR length [mm] | 3.0
Bunch BS length [mm] | 6.0
 | 28

## Slide 5: W-Working Point – Cavity Design
[1] P. Ylä-Oijala and et al. Multipacting Analysis and Electromagnetic Field Computation by the Boundary Integral Equation Method in RF Cavities and Waveguides. 1999.
Wakefield Results
Design
Multipacting Analysis with Multipac [1]
Variable | Value
[mm] | 73.52
[mm] | 131.75
[mm] | 106.25
[mm] | 118.7
[mm] | 369.6322
[mm] | 150
[mm] | 187
[˚] | 107.23
[] | 152.80
[] | 3.0e4
[-] | 2.05
[mT/MV/m] | 6.39
Variable | Value
 | 73.52
 | 131.75
 | 106.25
 | 118.7
 | 369.6322
 | 150
 | 187
 | 107.23
 | 152.80
 | 3.0e4
 | 2.05
 | 6.39
Niobium (Nb)
Copper (Cu)
Longitudinal and transverse wakefield impedance plots C3794 vs 4-Cell baseline cavity
Longitudinal and transverse wakefield impedance plots for designed cavity (C3794)
[1] P. Ylä-Oijala and et al. Multipacting Analysis and Electromagnetic Field Computation by the Boundary Integral Equation Method in RF Cavities and Waveguides. 1999.
Peak operating field
(W working point)
With a multi-objective shape optimization, a low longitudinal impedance cavity geometry was found.

## Slide 6: HOM Coupler Design
Result
Design
[MHz] | S3(1)2(1) [dB] | S3(2)2(1) [dB] | [dB]
400.79 | na | na | -110.99
488 | -3.32 | -28.03 | na
520 | -0.03 | -19.76 | na
 | S3(1)2(1) [dB] | S3(2)2(1) [dB] | 
400.79 | na | na | -110.99
488 | -3.32 | -28.03 | na
520 | -0.03 | -19.76 | na
Transmission curve of the HOM coupler
S3(3)2(1)
S3(1)2(1)
S3(2)2(1)
Port 2
Port 3

## Slide 7: HOM Coupler Mounting – 2-, 3-, 4-Hook Coupler Systems
Result
2HC1FPC
3HC1FPC
4HC1FPC

## Slide 8: 4-Hook Coupler System
Result
[MHz] | 486.19 | 516.36 | 555.88
[] | 8.89 | 16.81 | 0.32
[-] | 424.50 | 120.13 | 1115.09
[k/m] | 19.22 | 10.93 | 13.04
 | 486.19 | 516.36 | 555.88
 | 8.89 | 16.81 | 0.32
 | 424.50 | 120.13 | 1115.09
 | 19.22 | 10.93 | 13.04
Longitudinal wakefield and lossy eigenmode impedance plots C3794
Transverse wakefield and lossy eigenmode impedance plots C3794
Configuration

## Slide 9: Z Working Point
Machine parameter | Z
Beam energy [GeV] | 45
Beam current [mA] | 1390
Beam RF voltage [GV] | 0.1
SR loss/turn [GeV] | 0.036
No. of bunches/beam | 16640
Bunch intensity [ | 1.7
Bunch SR length [mm] | 3.5
Bunch BS length [mm] | 12.1
Luminosity [] | 230
Machine parameter | Z
Beam energy [GeV] | 45
Beam current [mA] | 
Beam RF voltage [GV] | 
SR loss/turn [GeV] | 0.036
No. of bunches/beam | 16640
 | 1.7
Bunch SR length [mm] | 3.5
Bunch BS length [mm] | 12.1
 | 230

## Slide 10: Z Working Point Cavity Design and Proposed Design Update Slide courtesy of Shahnam Gorgi Zadeh
Variable | FCCUROS1.0 (Z current) | LHC
[mm] | 156.0 | 150.0
[mm] | 120.0 | 160.0
[mm] | 70.0 | 104.0
[mm] | 70.0 | 104.0
[mm] | 25.0 | 25.0
[mm] | 25.0 | 25.0
[mm] | 350.574 | 344.398
[MHz] | 529.61 | 502.95
[MHz] | 528.76 | 542.03
[Ω] | 79.0 | 88.1
[Ω] | 2.3 | 6.3
[Ω] | 27.8 | 21.2
[°] | 102.8 | 109.5
[-] | 3.0 | 2.3
[] | 6.4 | 5.1
[MV/m] (for | 8.1 | 6.2
[mT] (for | 17.2 | 13.6
[kΩ2] | 15.5 | 22.2
[V/pC] | 0.116 | 0.146
Variable | FCCUROS1.0 (Z current) | LHC
 | 156.0 | 150.0
 | 120.0 | 160.0
 | 70.0 | 104.0
 | 70.0 | 104.0
 | 25.0 | 25.0
 | 25.0 | 25.0
 | 350.574 | 344.398
 | 529.61 | 502.95
 | 528.76 | 542.03
 | 79.0 | 88.1
 | 2.3 | 6.3
 | 27.8 | 21.2
 | 102.8 | 109.5
 | 3.0 | 2.3
 | 6.4 | 5.1
 | 8.1 | 6.2
 | 17.2 | 13.6
 | 15.5 | 22.2
 | 0.116 | 0.146
FCCUROS1.0 : Single-cell cavity designed by Shahnam [1]
The cavity was designed with a 156 mm aperture radius for FCCUROS1.0 so as to have a uniform radius with the previous 4-cell 400 MHz cavity designed for the W and H working points
Update motivation:
  Replicating similar longitudinal impedance properties as with the cavity designed for the W working point.
  Uniform iris radius with the cavity for the W working point
FCCUROS1.1 (Proposed update)
150
187
79.189
70
90
60
349.0943
518.89
531.98
81.25
4.77
24.81
-
2.36
5.99
6.3
12.74
17.47
0.117

## Slide 11: Proposed Design Update -
Highlights of the design update
Iris radius of 150 mm to match with the iris radius of the 2-cell cavity for the W working point
Absence of high-impedance longitudinal HOM
Having dipole modes closer to each other has two advantages:
  The design of coaxial HOM couplers is simpler
  The transmission curves of the coaxial HOM couplers can have a larger bandwidth around the resonances and are thus more robust against perturbations

## Slide 12: Power Requirement – Z and W Working Points
- Optimum loaded quality factor
Relevant formulas for the calculation of the presented parameters can be found in [2]
Working point | [MV/m] |  | [MV] |  | [kW]
Z* (Current Design 1-cell) | 5.7 |  | 2.1 | 0.712 | 808.3
Z (Potential update 1-cell) | 5.7 |  | 2.1 | 0.692 | 808.3
W* (Previous Design 4-cell) | 12 | 6 | 18.0 | 9.6 | 816.1
W (Current Design 2-cell) |  |  | 9.0 | 12.9 | 408.0
Working point |  |  |  |  | 
Z* (Current Design 1-cell) | 5.7 |  | 2.1 | 0.712 | 808.3
Z (Potential update 1-cell) | 5.7 |  | 2.1 | 0.692 | 808.3
W* (Previous Design 4-cell) | 12 |  | 18.0 | 9.6 | 816.1
W (Current Design 2-cell) |  |  | 9.0 | 12.9 | 408.0
[2] S. Gorgi Zadeh, “Accelerating cavity and higher-order mode coupler design for the Future Circular Collider”, Ph.D. thesis, Theoretische Elektrotechnik, Universität Rostock, 2020;http://purl.uni-rostock.de/rosdok/id00003023

## Slide 13: Summary
A new cavity has been designed for the W working point of the FCC-ee
The HOMs impedance of the designed cavity-hook-coupler system for the W working point fall below the impedance stability limit
A design update is proposed for the Z working point to have uniform cavity iris radius for the Z and W working points