## Slide 1
Summary of the Infrastructure Sessions
K Hanke, CERN
FCC week 2022, Paris

## Slide 2: Summary of the infrastructure sessions
K Hanke, CERN
FCC week 2022, Paris

## Slide 3
Infrastructure Sessions
K Hanke
FCC week 2022

## Slide 4
Geodesy and Survey
K Hanke
FCC week 2022

## Slide 5
S Guilleaume, Geodesy for Science and Society (remote)
K Hanke
FCC week 2022
Introduction to problematic and concepts of geodesy
Determination of position of objects
Determination of gravity field and its geometry
Density variations can perturb measurement
Choice of coordinate system is essential
Different techniques how to determine the gravity field

## Slide 6
A Ryf, Experience from the Gotthard Base Project (remote)
K Hanke
FCC week 2022
Longest railway tunnel in the world 57 km
Tolerance 25 cm for position and direction, 12 cm for height (achieved 8 cm in direction, 1 cm height)
Survey at the surface (e.g. dams) is needed
FCC monitoring will be necessary

## Slide 7
J A Koch, Gravity Field Modelling (remote)
K Hanke
FCC week 2022
A gravity field model allows the computation of the
Gravity potential (Geoid)
Gravity acceleration g
Deflection of the Vertical
Available gravity field model
Available model is insufficient!
Instrument absolute gravimeter
Gravity corrected height differences
Is an issue for FCC

## Slide 8
M Varga, Coordinate Reference and Networks
K Hanke
FCC week 2022
CRS Coordinate Reference System
Existing situation at CERN needs clarification
Proposed conceptual solution for FCC
Geodetic networks
Taking into account local constraints

## Slide 9
B Weyer, Handling Geodetic Challenges at CERN
K Hanke
FCC week 2022
Geographic Information System
Accuracy is key
Adapting prodecures for FCC in collaboration with ETHZ
Historic origin, coordinate system center in the PS
MAD coordinates vs coordinate system
From MAD-X to real world

## Slide 10
RF Points for FCC-ee
K Hanke
FCC week 2022

## Slide 11
K Hanke, The RF System for FCC-ee – General Considerations
Infrastructure Constraints
Physics Constraints
W, Z, H: Single RF point
ttbar: two RF points, do not need to be opposite points
Exclude experimental points and point B
L and H fit nicely integration wise, accessibility and infrastructure
F is not preferred (large lateral displacement of access shaft)
K Hanke
FCC week 2022

## Slide 12
F Valchkova-Georgieva, Integration of FCC-ee RF Sections
TLSS length: 2160 m
RF Section tunnel integration
K Hanke
FCC week 2022

## Slide 13
L Delprat, Update on the cryogenic design for the FCC-ee machine
K Hanke
FCC week 2022
Updated inventory of cryo needs and architecture (has much evolved since CDR)
Point L settled, point H options under investigation
RF point L
RF point H
Option 1: all cryo installed in a dedicated cavern at the LSS center
Option 2: half of cryo installed in a dedicated cavern at the LSS center
Option 3: all cryo installed in the usual service cavern
3 different options studied due to access pit location geographical constraints

## Slide 14
K Hanke
FCC week 2022
Electricity and Cooling

## Slide 15
J P Burnet, Update of the Power Demand for FCC-ee
K Hanke
FCC week 2022
Big Five:
RF
Cryo
Booster Magnets
Collider Magnets
Cooling & Ventilation
Plus others: general services, computing, …
 |  | Z | W | H | TT
Beam energy (GeV) |  | 45.6 | 80 | 120 | 182.5
Magnet current |  | 25% | 44% | 66% | 100%
Power ratio |  | 6% | 19% | 43% | 100%
PRF EL (MW) | Storage | 146 | 146 | 146 | 146
PRFb EL (MW) | Booster | 2 | 2 | 2 | 2
Pcryo (MW) | Storage | 1 | 7 | 17 | 50
Pcryo (MW) | Booster | 0.01 | 0.08 | 0.19 | 0.56
Pcv (MW) | all | 33 | 34 | 36 | 40.2
PEL magnets (MW) | Stroage | 6 | 17 | 39 | 89
PEL magnets (MW) | Booster | 1 | 3 | 5 | 11
Experiments (MW) | Pt A & G | 8 | 8 | 8 | 8
Data centers (MW) | Pt A & G | 4 | 4 | 4 | 4
General services (MW) |  | 36 | 36 | 36 | 36
Power during beam operation (MW) |  | 237 | 257 | 293 | 387
Average power / year (MW) |  | 143 | 154 | 174 | 225
Updated power demand for FCC-ee per working point

## Slide 16
K Hanke
FCC week 2022
J P Burnet, Update of the Power Demand for FCC-ee
Lots of ideas how to reduce power consumption being explored!

## Slide 17
M Parodi, Update on FCC Electrical Network and Grid Connection
K Hanke
FCC week 2022
Updated load estimate (has much evolved since CDR)
Adaptation to the 8-points new layout
Confirmation of n. 3 connection points to RTE grid:
  n. 2 HV connections at RF points
  n. 1 HV connection at point D (preferred) or point F (possible)
Internal closed 132 kV transmission loop
  Balanced power flow
  High reliability
  Existing control and protection technologies suitable for the topology
  Adapt to move towards FCC-hh
  Cost of investment Vs. FCC RAMS requirement: analysis to be performed
Collaboration with French electricity provider RTE
The overall power demands justifies a connection to RTE 400 kV (or alternatively 225 kV) grid
The first step (exploratory study) is free of charge and not binding. Data Collection Sheet available online.
The further study and execution phases need investment and commitment from both parties
The technical solutions include upgraded to RTE upstream infrastructure where required

## Slide 18
G Peon, Cooling and Ventilation Systems for the new FCC-ee Configuration
K Hanke
FCC week 2022
Updated inventory of water cooling power needs
Ventilation:
Heat loads in air collected (surface and underground)

## Slide 19
K Hanke
FCC week 2022
Transport and Safety

## Slide 20
C Colloca, Transport Requirements
K Hanke
FCC week 2022
Updated inventory considering FCC-ee (Booster and collider) magnets!

## Slide 21
M Schmidt, First Thoughts on Transport Options
K Hanke
FCC week 2022

## Slide 22
T Otto, The FCC Safety Feasibility Study
K Hanke
FCC week 2022
Hazard Register for HL-LHC

## Slide 23
O Rios, Robots for Safety in FCC
K Hanke
FCC week 2022

## Slide 24: Thanks to all speakers and chairpersons!