## Slide 1
Programs and projects
at GANIL-SPIRAL2

## Slide 2
1976 Creation of GANIL
(Grand Accélérateur national d’ions lourds)
1983 First experiment
2001 SPIRAL1 exotic beams
2006 SPIRAL2 Project signature of convention for construction Inclusion on European Strategy Forum for
Research Infrastructures (ESFRI) roadmap
  2016 SPIRAL2 ESFRI Landmark
  2019 Start of the commissioning of SPIRAL2
  2020 First neutron beams
  2021 First NFS experiments (Neutron For Science)
A brief history of GANIL
GANIL 1980
GANIL 2020

## Slide 3
Some numbers
France
Italie
Pologne
USA
Allemagne
Espagne
Japon
Corée
Royaume Uni
Belgique
Inde
Russie
Suède
Roumanie
Canada
• 230 permanent staff members (CEA and CNRS researchers, engineers, technicians) + 40 temporary staff (15 PhD, 5 postdocs)
+ CIMAP = 24 permanent staff + 15 PhD + 8 postdocs
• An international scientific community of ≈ 1000 members
A major facility for heavy ions in the world
with GSI/FAIR (Germany), RIBF/RIKEN (Japan), FRIB/MSU (USA), ISOLDE (CERN)…

## Slide 4
Programs
at GANIL-SPIRAL2

## Slide 5
GANIL: a multidisciplinary and multi-users laboratory
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics
~ 3300 radioactive isotopes produced and studied at accelerator facilities
~ 3000 more predicted by nuclear models (produced in reactions in stars)
Nuclear Physics@GANIL: study of exotic nuclei
Main questions to be answered :
What are the limits of existence of nuclei ?
What are the underlying fundamental interactions ?
How regular patterns emerge in the intrinsic structure of complex many body nuclei ?
Z=2
Z=8
Notes: 288 noyaux stables

## Slide 6
Fission dynamics
2p
radioactivity
Clusters
Pairing Correlations
Nuclear matter
Equation of State
Superheavy
nuclei
Nuclear shapes and coexistences
Shell effects
Coupling to continuum
Halo nuclei
Nuclear astrophysics
Fundamental interactions
GANIL: a multidisciplinary and multi-users laboratory
Nuclear Physics@GANIL: study of exotic nuclei
Are there more unexpected new phenomena to be discovered ?
  Shell structure modification and new magic numbers
  Halo nuclei
  New radioactivities
  ????
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics

## Slide 7
GANIL: a multidisciplinary and multi-users laboratory
Nuclear astrophysics:
How nuclei have participated and still participate in the creation of elements in the universe?
Renewed interest since the discovery of gravitational waves : EM counterpart of GW170817 is the strongest evidence of heavy elements nucleosynthesis through the r-process.
Arnould et al,
Physics Reports 2007
Observations
Strong shell closure
Shell quenching
r-abundance curve
A
B. Pfeiffer, et al., NPA 693 (2001) 282
r-process
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics
Notes: 288 noyaux stables

## Slide 8
Astrochemistry:
Role of cosmic rays and stellar winds on ices for the appearance of
molecules in the universe
IGLIAS setup to mimic interstellar ices exposed to radiation
fragmentation/destruction
formation of molecules
Desorption / Sputtering /implantation
In-situ gas deposition
3 spectrometers (UV-visible, FTIR, QMS)
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics
GANIL: a multidisciplinary and multi-users laboratory
Notes: une partie importante des demandes de faisceaux lors de l’IPAC est l’irradiation de glaces d’intérêt astrophysique.
Les glaces sont présentes partout dans l’espace que ce soit sur les lunes, les poussiéres, les cométes, les nuages moléculaires, les objet transneptuniens, ….et elles sont soumis à des flux de particules ionisantes. Cela peut induire des transitions de phases, de la radiolyse et donc la destruction de certaines molécules., D’&utres au contraire peuvent se former par réaction entre radicaux et voir ainsi former des molécuiles plus complexes.
On a développé pour cela un dispositif sous ultra vide permettant le dépôt de mélange gazeux pour former des glaces, leur irradiation et le suivi in-situ des modifications chimiques par spectroscopie IR ou UV visible.
What is the role of cosmic rays and stellar wind on ices and silicates for the appearance of molecules in the universe? To answer this question, GANIL is a precious and unique tool to perform laboratory experiments in particular to understand the production and the radio-resistance of newly formed molecules during ice irradiation, an important topic for the understanding of emergence of life.
Ices are ubiquitous in space. They can be found on dust grain in dense molecular clouds in the interstellar medium (ISM), on comets and on the Jovian moons like Europa in the solar system for example. These icy mantles are mostly composed of small molecules (H2O, CO, CO2, NH3, ...) and are permanently irradiated by cosmic rays or stellar wind. Irradiation leads to radiolysis: mother molecules are broken and radicals are formed. These radicals may then react inside the ice with neighboring molecules and produce new molecules leading to the chemical modification of the initial ices. More complex organic molecules can thus be produced which is in agreement with the fact that amino acids, as glycine, have been observed in space (Rosetta mission 2014-2015) on the 67P/Tchourioumov-Guérassimenko also know as “Tchouri”.
On the other, more than 200 molecules have been identified in the interstellar medium and organic complex molecules have been observed in planetary atmospheres such as Saturn moons. Many experiments are devoted to the ion collision induced molecular complexification inside carbonated molecules clusters and compared to theoretical calculations. These studies show the particular role played by ion collisions in the molecular synthesis in space due to the specific interaction of heavy particles with matter. GANIL is specially well adapted to tackle this important topic of understanding the building up of complex molecules in space.
Dans les parties denses de l’espace (comètes, planètes) Molecules se condensent dessus la glace. Implantation des ions dans les glaces, ou inverse sputtering, radiolyse,
Reproduire ce qui se passe dans l’espace: substrat à 10 K; in situ buse injection gaz, on dépose, puis on irradie puis on tourne fait spectro IR => évolution des liaisons chimiques
QMS,
iGLIAS soit IRRSUD, ARIBE
MCT= détecteur IR

## Slide 9
9
1500 µm
5 µm
surface
100 µm
ARIBE
Materials under irradiation/Nanostructuration
- Materials study
- Contribution to improving the
nuclear power plants safety
(fuel tubes, nuclear packaging)
Studies perfomed by scientific community related to CIMAP/CIRIL
GANIL: a multidisciplinary and multi-users laboratory
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics
Notes: Explication complète qu’il faudra bien sur simplifier: IRRSUD= produite de fission, HE= permet radiobio et simuler les alpha, SME = maximum de TEL
Grâce à la variété d’ions disponibles, ces différentes gammes d’énergie donnent accès à un grand domaine de pouvoir d’arrêt. Ce graphique représente le transfert d’énergie linéique en keV/µm en fonction de l’énergie de ions en MeV/A. Ce TEL dépend de la masse de l’ion projectile. Le carbone, élément léger, aura un TEL beaucoup plus faible que le plomb. Les zones vertes représentent les gammes d’énergie couvertes par nos 4 lignes de faisceaux. Il y a une zone énergétique non couverte par les lignes disponibles à Caen. Cette zone est couverte par la plateforme JANNUS à Saclay. Le pouvoir d’arrêt nucléaire domine le pouvoir d’arrêt électronique. A basse énergie, les mécanismes dominants étant l’excitation et la capture électronique, les systèmes les plus étudiés ont été, pendant les 20 dernières années, des atomes, molécules et agrégats en phase gazeuse. Depuis quelques années, grâce à l’amélioration des performances des sources ECR, les ions de basses énergies sont également un outil pour étudier la surface des matériaux (glace, métaux, semiconducteurs). Sur IRRSUD, l’énergie des ions est en moyenne de 1 MeV/A. Le dépôt d’énergie se fera essentiellement à gauche du pic de Bragg. La gamme d’énergie disponible en SME correspond au pic de Bragg alors qu’à haute énergie, la perte d’énergie se fait après le pic de Bragg. La profondeur atteignable dans le cas d’IRRSUD est de 5 à 10 µm alors que pour la HE elle est de l’ordre que 0.1 mm a plus d’1 mm. Selon les contraintes imposées par les méthodes de caractérisation des matériaux il sera plus judicieux de choisir telle ou telle ligne

## Slide 10
New hadrontherapy center nearby GANIL
GANIL: a multidisciplinary and multi-users laboratory
Radiobiology
- New radioisotopes for medicine (211At)
- pre-clinical studies and
innovative methods for
hadrontherapy
Nanostructuration
Materials under irradiation
Radiobiology
Astrochemistry
Nuclear Physics
Nuclear Astrohysics

## Slide 11
GANIL-SPIRAL2
Facility

## Slide 12
VAMOS
AGATA
EXOGAM
ACTAR TPC
MUGAST
LISE SPECTROMETER
INDRA + FAZIA
Experimental rooms
Sample holder for irradiation
CYCLOTRON
GANIL CYCLOTRONS
SOURCES
GANIL Cyclotrons and experimental equipment
Beams : 12C to U
Energy : from <1 MeV up to 95MeV/nucleon
Up to 4 experiments in parallel

## Slide 13
Convertor room
LINEAR accelerator (LINAC)
ION SOURCE
EXPERIMENTAL ROOM S3 (SUPER SEPARATOR SPECTROMETER)
EXPERIMENTAL ROOM NFS (NEUTRONS FOR SCIENCE)
Time of Flight room
SPIRAL2 and the new experimental rooms
EXPERIMENTAL ROOM DESIR (Desintegration,
Excitation and Storage of Radioactive Ions)
Beams :
33 MeV protons
40 MeV deutons
<14,5 MeV/A heavy ions

## Slide 14
● Neutron Beam at 0°
● Collimator beam quality
● Size (Lⅹl) ≃ (28m ⅹ 6m)
- TOF measurements
- free flight path
● Ion and neutron induced reactions
● Irradiation station (n, p, d)
Collimator
LINAC
Beam
New experimental room : Neutron for Science
Physics case
Fundamental physics
Astrophysics
New generation of reactor
Fusion technology
Radioisotopes production for medical applications
Biology (cells irradiation..)
Development and characterization of new detectors
Study of the single-event upsets

## Slide 15
● Neutron Beam at 0°
● Collimator beam quality
● Size (Lⅹl) ≃ (28m ⅹ 6m)
- TOF measurements
- free flight path
● Ion and neutron induced reactions
● Beam line extension
● Irradiation station (n, p, d)
Collimator
LINAC
Beam
New experimental room : Neutron for Science
Physics case
Fundamental physics
Astrophysics
New generation of reactor
Fusion technology
Radioisotopes production for medical applications
Biology (cells irradiation..)
Development and characterization of new detectors
Study of the single-event upsets
Li converter
Rotating
converter
Irradiation station
Pneumatic transfer system

## Slide 16
● Neutron Beam at 0°
● Collimator beam quality
● Size (Lⅹl) ≃ (28m ⅹ 6m)
- TOF measurements
- free flight path
● Ion and neutron induced reactions
● Beam line extension
● Irradiation station (n, p, d)
Collimator
LINAC
Beam
New experimental room : Neutron for Science
Physics case
Fundamental physics
Astrophysics
New generation of reactor
Fusion technology
Radioisotopes production for medical applications
Biology (cells irradiation..)
Development and characterization of new detectors
Study of the single-event upsets

## Slide 17
Neutrons beams
Flux at 5 meters :
8.107 n/s/cm2
at 15 MeV : 5.106 n/s/cm2/MeV
at 30 MeV : 6.105 n/s/cm2/MeV

## Slide 18
Target system
High power rotating targets
3 × M-dipoles
Large H & V gaps
E-Dipole
20 cm gap & +/- 300 kV
Open slit in the anode
SC Multipoles
Dispersive zone
Open RT magnet & beam dump & Movable fingers
Infra / Interface
LEB
SIRIUS
SMT, PSS, Coldbox & LTC
DSSD, SSD, FEE/BEE, DAQ & Diagbox
LEB @ LPC & GISELE Laser Lab
Cooling system, Laser room …
: the Super Separator Spectrometer
Fundamental research in Nuclear & Atomic physics
High selectivity > 1013 beam rejection
High efficiency 50%
Mass resolution > 350
Versatility : high resolution, high transmission, high beam rejection modes…
Unique instrumentation : SIRIUS for p, a, electron and g spectroscopy, and S3-LEB with gas catcher, RFQ and MR-ToF-MS
Notes: MR-ToF-MS: multi reflection ToF mass separator

## Slide 19
152
Eshell
Calc.: A. Sobiszewski
120
114
108
162
184
1 particle A
= 6.2 x1012 particles/s
S3-SIRIUS day 1 pre-proposals
Very heavy and super heavy nuclei
Limit of the nuclear existence
Shell correction effects
Reaction mechanisms
  K-isomers
  Single particle states
  New isotopes – limits of stability
  Odd-Z nuclei
  Reaction mechanism
  N=152, 162
Limits of stability / isomers
250,249,…No
Search for new isotopes
252Rf
Odd Z isotopes – nuclear structure
fermium region
Isomers
254Rf, 260Sg
“day 1”
with injector1
2024
beyond
with NEWGAIN
2028
+ SC source
2030
SIRIUS: Spectroscopy and Identification of Rare Isotopes Using S3
tracking detector
Si detector box
Ge detectors

## Slide 20
Octupole deformation
in U region ?
Evolution of N=126 shell closure with increasing Z ?
How relativistic effects affect the
architecture of the periodic table?
Measure IP in Rf and Db ?
Spectroscopic information on the heaviest nuclei ?
Fm (isomers, shapes, moments)
Nucleon-Nucleon interaction around 100Sn?
Effective Single particle energy levels: 101Sn, 99In
T = 0 T = 1 Pairing interaction: 98In
Spin-aligned coupling scheme: 94Ag, 90Rh
How deformation emerge from microscopic
configuration ?
Q in Sn chain
Evolution of deformation around 80Zr
Binding energies and Wigner term ?
From 80Zr-100Sn
rp-process
S3-LEB day 1 pre-proposals
N=Z region: shell evolution, nucleosynthesis, symmetries
Heavy neutron-deficient refractory elements: shapes/shape coexistence, exotic decay modes
Heavy and Super Heavy Element region: single-particle versus deformation, atomic physics
Laser spectroscopy
Mass measurement
Decay spectroscopy
PILGRIM
(MR-Tof-MS)
Observables :
Mass (100keV)
Observables :
Decay
spectroscopy
Half-life
Tape station
REGLIS3
Observables :
Nuclear magnetic
dipole moment
Nuclear Electric
quadrupole moment
Mean charge radii
Spin
Notes: REGLIS3: Rare Elements in Gas-Laser Ion Source and spectrocopy at S3
The physics cases for the S3 LEB experimental program have been updated in 2018 and 11 pre-proposals have been submitted by the collaboration. They cover experiment campain studying systems with extreme proton to neutron balance on the N=Z line including the doubly magic 100Sn, and systems with extreme masses in the actinide and super heavy region.

## Slide 21
Colloque GANIL 2021
Beam purification
and preparation
(Cooling/Bunching/Trapping)
Ion trapping
DETRAP
Laser
Spectroscopy
LUMIERE
Decay
Spectroscopy
BESTIOL
S3-LEB beam
SPIRAL1 beam
b-delayed charge part.
Full absorption spectroscopy
(Trap/Laser-assisted) decay spectroscopy
Collinear laser spectroscopy
Laser polarization (decay spectroscopy, b-NMR, …)
Precise mass measurements
In-trap decay spectroscopy
b-n angular correlations
HRS
UHRS
Construction will start after « Modification autorisation » procedure (ASN, MSNR) and public inquiry => Spring-summer 2023
First beams: 2027
Low-energy radioactive-ion-beam facility
Beams from SPIRAL1 and S3
Important beam preparation and purification capabilities
High resolution/precision experiments
Experimental room under project:

## Slide 22
Scientific Program
Collinear laser spectroscopy
b-delayed g spectroscopy
b-n angular correlation
Mass measurement
b-delayed charge part., b-n emission
(Trap-assisted) b-decay, full absorption spectroscopy
S3-LEB
SPIRAL 1 Upgrade
LUMIERE
DETRAP
BESTIOL
A~150
Very (super)-heavy
N~Z
Fundamental
interactions
Nuclear structure
near closed shells
b-n
  Fusion-evaporation
  (Multi-)nucleon Transfer
  Beam & target fragmentation
Decay properties
Deformation

## Slide 23
beam injector1 (injector2)
intensities 2023 2028 2030
2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
first
beam
time line
Ions | Intensity (pµA) Phoenix V3 RFQ A/Q≤3 | Intensity (pµA) Phoenix V3 RFQ A/Q≤7 | Intensity (pµA) SC Ion Source RFQ A/Q≤7
18O | 80 | * | 375
19F | >15 | >40 | >40
36Ar | 16 | 70 | 45
40Ar | 3.6 | 70 | 45
36S | 2.3 | * | *
40Ca | 2.9 | 10 | 20
48Ca | 1.2 | 10 | 20
58Ni | 1.1 | 4 | 8
84Kr | 0.1 | 10 | 20
139Xe | 0.001 | 7 | >10
238U | <<0.001 | 0.1 | 6
* -> no estimation
Measured
Estimated
White Book
https://www.ganil-spiral2.eu/scientists/ganil-spiral-2-facilities/accelerators/newgain/
Study Phase
Construction Phase
New injector for SPIRAL2: NEWGAIN
Floorplan, design intensities and time line

## Slide 24
GANIL-SPIRAL2
medium/long term perspectives

## Slide 25
Vision for the future of GANIL: Expert Committee report
Expert committtee Chair : Michel Spiro
Members: Maria Jose Garcia Borge (CSIC), Paolo Giubellino (FAIR), Ulli Köster(ILL), Hiroyushi Sakurai (RIKEN),
Boris Sharkov (JINR), Brad Sherill (MSU), Johanna Stachel (Univ. Heidelberg)
Three steps for the future of GANIL
Until 2030:
-finalisation of ongoing projets : S3, DESIR, NEWGAIN
-cyclotrons and LINAC operation, refurbishing of cyclotrons
-new target station for test of radioisotopes production
-test gas cell for fragment production via MNT (multi-nucleon transfer)
2) Until 2035
-renovation or replacement of CIME cyclotron
to reach 100 MeV/nucleon
-building for production of n-rich exotic nuclei by fission of UCx target.
-Dedicated target station for radioisotopes production
-Dedicated beam line for pluridisciplinary research
3) Until 2040
-Construction of an electron accelerator (synchrotron or ERL) for a new generation of experiments : electron-exotic nuclei scattering
« Vision to keep GANIL at the forefront of nuclear
science globally for many decades to come »

## Slide 26
Vision for the future of GANIL: Expert Committee report
GANIL 2040 ????

## Slide 27: Thank you for your attention

## Slide 28: Back up slides

## Slide 29
Nuclear Physics :
Some examples of latest results

## Slide 30
Study of very neutron rich light nuclei : 7H
ACTAR active target : the detector gas constitutes the target material
  Thick target to compensate for low beam intensity
  Vertex and energy measurement
  Low particle thresholds
  Large range of center of mass angles
  Very high efficiency
  Excitation function
Application to 7H ground state properties investigation by missing mass method M. Caamano et al, Phys. Lett B829 (2022)
ER=
GR=
½+ ground state

## Slide 31
The AGATA project : THE ultimate spectrometer
180 (60 triple-clusters) 36-fold segmented crystals
Amount of germanium: 362 kg
Solid angle coverage: 82 %
Singles rate >50 kHz
Efficiency: 43% (Mγ=1) , 28% (M γ = 30)
Peak/Total: 58% (M γ =1), 49% (M γ = 30)
Angular Resolution: ~1º
S. Akkoyun et al., Nucl. Instrum. Methods Phys. Res., Sect. A 668, 26 (2012).
E. Clément et al., Nucl. Instrum. Methods Phys. Res., Sect. A 855, 1 (2017).
AGATA@GANIL
Combination of:
segmented detector
pulse-shape analysis
tracking the g rays
digital electronics
The project timeline is to complete the 4p by 2030

## Slide 32
2015-2017
2018
2019-2021
AGATA@GANIL: many sub-campaigns
AGATA coupled with VAMOS, FATIMA, PARIS
AGATA coupled with NEDA- DIAMANT
AGATA coupled with VAMOS MUGAST
AGATA coupled with VAMOS, EXOGAM, 2nd Arm, LEPS
2021

## Slide 33
N=Z isotopes: study p-n (iso-scalar) pairing correlations
Nucleons can form strongly correlated pairs which impact strongly on nuclear structure.
Only in N=Z nuclei will the p-n (isoscalar) pairing be important, as protons and neutrons occupy the same orbit.
 N

Z
88Ru: 44 protons and 44 neutrons (near proton dripline)
B. Cederwall et al., PRL 124, 062501 (2020)
Rotating deformed nucleus with strong
ISO-SCALAR
p-n pairing !

## Slide 34
Fission Studies in inverse kinematics @ VAMOS
238U @ 6 AMeV
transfer
reaction
fission
SPIDER:
Recoil
A, Z, E, angle
recoil
evaporation
target
  Inverse Kinematics using beams of 238U around Coulomb Barrier
Access to « exotic » fissionning systems heavier than 238U
  Surrogate reactions (transfer induced fission)
Selection of the fissionning system
Measurement of the excitation energy
  VAMOS Magnetic Spectrometer
Direct and Complete isotopic fission fragment yields
VAMOS A,Z
PISTA
239U
D. Ramos et al PRL (2019)​​

## Slide 35
Nuclear Physics
and dark matter

## Slide 36: The neutron lifetime puzzle
W. Pattie et al, Science 360 (2018) 6389
How could the remaining 1% be explained ?
Decay of neutron into particles of Standard Model (other than p) : excluded
n → dark matter : Fornal and Grinstein, PRL120(2018)191801 -> shortening of the apparent lifetime in the bottle
  n → dark particle(s) to be searched for
  Neutrons loosely bound in nuclei may also decay by the dark channel, if allowed by energy conditions
Discrepancy
Counting remaining neutrons :
Counting emitted protons :
tn(s)
Year of experiment
Notes: Voir les manipes UCNA et UCN

## Slide 37
Search for dark decay of neutrons in 6He
(H. Savajols et al. June 2021)
Branching ratio estimate from bottle/inflight decays B = 1.2 × 10−5
Allowed energy window : M < Mn - 975.45 keV
Combining other results 937.992 MeV < M < 938.589 MeV
Pfutzner and Riisager, PRC 97, 042501(R) (2018)
6He1+ SPIRAL1 world-record intensity (2×108 pps)
Neutron multidetector TETRA with 50% efficiency
Search of an excess of neutrons in the decay of 6He
➔ The final analysis provides a stringent
upper limit for this dark decay
Standard decay
Dark decay ?
Time (10ms)
Time (10ms)
3x T1/2
TETRA

## Slide 38
Nuclear Physics and
Physics beyond the Standard Model

## Slide 39
Nuclear beta decay as a laboratory for weak interaction
b: Search for Tensor Interactions in nucLear bEta Decay (bSTILED)
  Searching for exotic tensor currents via a b correlation measurement to the 10-4 level
Matter’s Origin from RadioActivity (MORA)
  searching for CP violation in nuclear b-decay via a D correlation measurement to the 10-5 level
Measurement of Ft values (half-lifes, branching ratios) of superallowed decays for tests of CVC to the 10-4 level and the search for exotic scalar currents
Two complementary approaches:
High energy frontier
« Direct » observation of new particles at high energy colliders (LHC)
Precision/intensity frontier
Look for tiny deviations from SM predictions
  Non zero EDMs
  n oscillations
  Search for WIMPs
  Dark decay of neutron
  …
  Correlation measurements in nuclear beta decay
   exotic couplings
  of electroweak interaction
Linked through EFT

## Slide 40
Materials under irradiation

## Slide 41
H. Vázquez et al.
Carbon 114 (2017) 511
L. Madauß et al.
Nanoscale 9 (2017) 10487
Collaboration:
Universities of
Helsinki and Aalto, Finland
Nottingham, UK
Duisburg-Essen, Germany
Wien, Austria
Science and Technology MISiS, Russian Federation
CIMAP, France
Ruder Boskovic Inst., Croatia
Helmholtz-Zentrum Dresden-Rossendorf, Germany
Application:
Desalination of sea water
Project NU TEGRAM
Flagship Graphene
Pores diameter as a function of time
Experiment
Simulation
Pore diameter as a function of stopping power
Graphene/polymer nanoporous membranes
Notes: Les ions font trou de petite taille dans le graphene (dépendant du pouvoir d’arret des ions) et comme le graphene est sur un polymere on peux ensuite faire attaque chimique pour révéler les trou dans polymeres
Sur image le « flou » est la zone avec graphene. On voir les trous dans polymere mais en regardant de plus pres on peut voir trou dans graphene. Et taille trou simulé marche bien avec observation
Sel tout petit donc trou très petit, qq couches de graphnèe sur polymère, puis trou sur polymère . Eau passe, sel reste sur graphène

## Slide 42
Radiobiology

## Slide 43
Clonogenic assays: comparison between X-rays and C-ions (+/- PARPi)
Cell survival (%) is a mean +/- SD of 3 independent experiments performed in triplicate
Chondrosarcoma / pre-clinical experiments
Chondrosarcoma
malignant tumor of cartilage with bad prognostic - highly radio-resistant => use of hadrontherapy ?
Comparison of C-ions and X-rays:
Relative Biological Effectiveness 2,95
M. Cesaire, J. of bone oncology 17 (2019) 100246
Notes: Comparaison des courbes en bleu: montre que ions C plus efficace que X rays (pas de cellules survivante à 6 Gy alors qu,’il en reste aux RX). Si on rajoute des agent radiosensibilisant (ici des inhibiteur de PARP pour limiter la réparation) on augmente encore l’efficacité des ions carbone.
Cartilage, résistante aux rayonsX, une indication hadronthérapie
PARPi: inhibiteur de PARP, protéine qui permet réparation ADN. Injection au patient, empêche que l’aDN se répare avant radiothérapie
Ions C 3 fois plus efficaces que X, et plus localisé.
Intérêt d’avoir labo de bio juste à côté + nécessité d’avoir planning qui ne bouge pas (ajout de PARPI 2 heures avant irradiation)

## Slide 44
Astrochemistry

## Slide 45
Role of cosmic rays and stellar winds on ices for the
appearance of molecules in the universe
IGLIAS setup to mimic interstellar ices exposed to radiation
fragmentation/destruction
formation of molecules
Desorption / Sputtering /implantation
Compactation / Amorphization
In-situ gas deposition
3 spectrometers (UV-visible, FTIR, QMS)
Notes: une partie importante des demandes de faisceaux lors de l’IPAC est l’irradiation de glaces d’intérêt astrophysique.
Les glaces sont présentes partout dans l’espace que ce soit sur les lunes, les poussiéres, les cométes, les nuages moléculaires, les objet transneptuniens, ….et elles sont soumis à des flux de particules ionisantes. Cela peut induire des transitions de phases, de la radiolyse et donc la destruction de certaines molécules., D’&utres au contraire peuvent se former par réaction entre radicaux et voir ainsi former des molécuiles plus complexes.
On a développé pour cela un dispositif sous ultra vide permettant le dépôt de mélange gazeux pour former des glaces, leur irradiation et le suivi in-situ des modifications chimiques par spectroscopie IR ou UV visible.
What is the role of cosmic rays and stellar wind on ices and silicates for the appearance of molecules in the universe? To answer this question, GANIL is a precious and unique tool to perform laboratory experiments in particular to understand the production and the radio-resistance of newly formed molecules during ice irradiation, an important topic for the understanding of emergence of life.
Ices are ubiquitous in space. They can be found on dust grain in dense molecular clouds in the interstellar medium (ISM), on comets and on the Jovian moons like Europa in the solar system for example. These icy mantles are mostly composed of small molecules (H2O, CO, CO2, NH3, ...) and are permanently irradiated by cosmic rays or stellar wind. Irradiation leads to radiolysis: mother molecules are broken and radicals are formed. These radicals may then react inside the ice with neighboring molecules and produce new molecules leading to the chemical modification of the initial ices. More complex organic molecules can thus be produced which is in agreement with the fact that amino acids, as glycine, have been observed in space (Rosetta mission 2014-2015) on the 67P/Tchourioumov-Guérassimenko also know as “Tchouri”.
On the other, more than 200 molecules have been identified in the interstellar medium and organic complex molecules have been observed in planetary atmospheres such as Saturn moons. Many experiments are devoted to the ion collision induced molecular complexification inside carbonated molecules clusters and compared to theoretical calculations. These studies show the particular role played by ion collisions in the molecular synthesis in space due to the specific interaction of heavy particles with matter. GANIL is specially well adapted to tackle this important topic of understanding the building up of complex molecules in space.
Dans les parties denses de l’espace (comètes, planètes) Molecules se condensent dessus la glace. Implantation des ions dans les glaces, ou inverse sputtering, radiolyse,
Reproduire ce qui se passe dans l’espace: substrat à 10 K; in situ buse injection gaz, on dépose, puis on irradie puis on tourne fait spectro IR => évolution des liaisons chimiques
QMS,
iGLIAS soit IRRSUD, ARIBE
MCT= détecteur IR