## Slide 1: The lpGBT: from concept to a radiation-tolerant high-speed communication ASIC for the HL-LHC upgrade
Adithya Pulli, CERN
Pedro Vicente Leitao, CERN
Stefan Biereigel, CERN
on behalf of the lpGBT team
EP-ESE Seminar, https://indico.cern.ch/event/1065136
28th June 2022

## Slide 2: Outline
Introduction [Pedro]
UVM Verification [Adi]
Testing / Validation [Stefan]
Conclusions [Stefan]

## Slide 3
The lpGBT Collaboration
The lpGBT wouldn’t have been possible without our collaborators!
AGH UST
Poland
Marek Idzik
5 engineers
CTU
Czech Republic
Miroslav Havranek
2 engineers
CERN
Switzerland
Paulo
Moreira
15 engineers
1 technician
KU Leuven
Belgium
Paul
Leroux
3 Engineers
UNL
Portugal
Nuno
Paulino
2 Engineers
SMU EE/PH
USA
Ping Gui /
Jingbo Ye
8 engineers
CERN
Coordination
3

## Slide 4: lpGBTv1 Timeline
Dates of interest:
Specs frozen: 2015
lpGBT V0 submission: 07/2018
lpGBT V0 prototypes: 11/2018
lpGBT V0 extensive testing: Q4/18 - Q3/19
27/Sept/2021
TWEPP 2021
Public presentation
03/2021
lpGBT v1 submission
Functional validation
and
characterization started
Start large scale testing
09/2021 Prototypes @ CERN
TID @ CERN
Proton irradiation @ PSI
Heavy Ion @ UCL
In house testing
&
deliveries to the users
ESE seminar on the lpGBT
28 June 2022
Today!
Wafers on their way to CERN!
Mar
Apr
May
June
July
Aug
Sept
Oct
Nov
Dec
Jan
Feb
Mar
Apr
June
July
Aug
Sept
Oct
Nov
Dec
Jan
2022
2023
May
02/2022
63 Wafer Ordered
3089 die/wafer
194k devices
Start large scale
packaging
End of Production
Feb
Mar
In house testing
2000 ASICs (reserved)
Industrial testing
8k ASICs
2021
Neutron irradiation VLDB (VTRX+)
Target: 1014 n/cm-2

## Slide 5: lpGBT Link Architecture
On-Detector
Radiation Hard Electronics
Off-Detector
Commercial Off-The-Shelf (COTS)
lpGBT
TIA
LD
PD
LD
Custom ASICs
Timing & Trigger
DAQ
Slow Control
Timing & Trigger
DAQ
Slow Control
FPGA
No or small radiation doses
High radiation doses
LHC: up to 100 Mrad (1014 1MeV n/cm2) HL – LHC: up to 1 Grad (1016 1MeV n/cm2)
Short distance optical links: 50 to 300 m
Electrical links to the frontend modules. Lengths: cm to few m
Custom optoelectronics

## Slide 6: What’s the lpGBT? [user point of view]
Data transceiver with fixed and “deterministic” latency for both up and down links
  Clocks and Data
Downlink
  2.56 Gbps
  FEC12
  eLinks
    Bandwidth: 80/160/320 Mbps
    Count: 16/8/4
Uplink
  5.12 Gbps or 10.24 Gbps
  FEC5 or FEC12
  eLinks
    Data rates: 160 /320 / 640 / 1280 Mbps
    Count:
      FEC5
        Up to 28 @ 160 Mbps
        Up to 7 @ 1.28 Gbps
      FEC12
        Up to 24 @ 160 Mbps
        Up to 6 @ 1.28 Gbps
Experiment control/monitoring functions
  10-bit ADC
  12-bit voltage DAC
  8-bit current DAC
  Temperature sensor
  Three I2C masters
  Programmable parallel port: 16 x GPIO
Package
  9 mm x 9 mm x 1.25 mm (pitch: 0.5 mm)
  Pin count: 289 (17 x 17)
ROC
ROC
ROC
lpGBT
Data rate: 160 Mbps to 1.28 Gbps
Length: cm to meters
Data rate: Rx: 2.56 Gbps Tx: 5.12 and 10.24 Gbps Length: <200 m
Notes: Update the footer
Add disclaimer for temperature sensor and mention that

## Slide 7: LpGBT System Block Diagram (Simplified)
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase – Shifter
Clocks
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
lpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM
PUSM
BOD/POR
Notes: lpGBT is communication hub on hybrid – mention to introduce PUSM, brownout, POR

## Slide 8: Specifications summary [radiation]
The lpGBT is designed in 65 nm CMOS process
Targets [not only] the innermost layers of the HL-LHC detectors
  Total Ionizing Dose (TID)
    200 Mrad (two times safety factor)
  Non Ionizing Energy Loss (NIEL) radiation
    ~ 1015 1 MeV neq/cm2 (mainly a concern for the optoelectronics components)
  [Over a 10 years lifetime]
Operation robust to Total Ionizing Dose
  Designed with ELT (enclosed-layout-transistor) whenever possible
Operation robust to Single Events Upsets
  Triple Modular Redundancy (TMR) used in the State Machines and the “low-frequency” section of the Data Path
  Forward Error Correction used in the “high-frequency” section of the data path and over the optical links
  Use of an LC-VCO architecture for increased SEU-Tolerance and low jitter.
  Clock triplication at the output of the PLL
Notes: Move last bullet about ELT to TID section
Align TID spec between Stefan and Pedro

## Slide 9: lpGBT - Verification
Adithya Pulli, CERN
on behalf of the lpGBT team
EP-ESE Seminar
28 June 2022 – CERN

## Slide 10: Verification - Introduction
What?
  ASIC verification is one of the crucial steps of ASIC design process which ensures that the design specification is preserved in the actual design implementation
  It can consume as much as 70-80% of the total ASIC design time
Why?
  Humans tend to make mistakes
  Cost of finding and fixing a mistake (AKA bug) increases significantly over project lifetime
How?
  Build a realistic world (AKA verification environment) around a design (AKA Design Under Test - DUT)
  Exercise the DUT in all possible ways* using the verification environment
  Check all the outcomes of the DUT are as expected

## Slide 11: Verification - Introduction
*Catch
  It is impossible to exercise DUT in all possible ways in a reasonable amount of time
  Algorithmically, verification is a PSPACE-complete problem
What now?
  Rely on constrained random stimulus to maximize the design space exercised
  Use a methodology which supports efficient implementation of constrained random tests
  Use metrics to gain confidence in the verification effort
    Quis custodiet ipsos custodes? (Who will guard the guards themselves?)
    Coverage, regression testing, bug-rate etc.
Verification reduces the risk of finding a bug after fabrication. It cannot assure absence of any bugs

## Slide 12: lpGBT Verification
lpGBT verification landscape
  Unit-level directed (and random) tests written in System Verilog and cocotb which mainly served as design sanity tests
  Top-level directed tests written in System Verilog which mainly exercised debug features
  Top-level highly random tests written in System Verilog following UVM methodology
lpGBT UVM environment
  The verification infrastructure built around lpGBT DUT to drive its inputs and observe its outputs
lpGBT UVM tests
  11 tests were defined for lpGBT. 8 tests are very simple tests which mainly focus on checking the sanity of the environment
  lpgbt_reg_rw_test exhaustively verifies register instantiation and connectivity from all configuration ports of lpGBT
  lpgbt_fuse_burning_test exercises and verifies fuse burning process
  lpgbt_rand_test randomly exercises most of the features of lpGBT

## Slide 13: lpGBT UVM Environment
Key design considerations
  Modularity
  Ease of randomization
Supports RTL, triplicated RTL (tmr) and netlist (impl) versions of DUT
Partially synthesizable drivers which are reused in post-si test setup
SEE aware checkers
Register Access Layer (RAL) with support for accesses through different interfaces

## Slide 14: lpGBT Rand Test
Simulate a catastrophic event by injecting a sequence of operations which trigger frame-aligner/lock-filter/PLL/DLL/channel to unlock
Sequence blocks until chip recovers and reaches ready state
Data integrity checkers are disabled during this phase
Number of operations and their order
Thresholds for filters and timeout actions
Enable/disable of watchdog actions
Operations include:
  Lock-filter unlock
  Frame-aligner unlock
  PLL timeout
  PLL watchdog
  DLL watchdog
  DLL timeout
  Channel timeout
  Brownout
  State machine force override through configuration
Status of state machines
Action counter values
Continuous uplink/downlink data
I2C masters
Programmable IO
Random register accesses with error injection
Induce correctible FEC errors
Random variables:
Number of operations and their order
Config access mechanisms
Configuration values
clock phase and jitter
Data integrity checks
Clock frequency and phase checks
Reset out check
I2C master transaction check
Dedicated checks for each operation
  Data checks for I2CM
  IO values for PIO tests
  Expected register values after random reg access with error injection
Check status registers values of critical state machines
Action counter values
Mode: simplex_rx, simplex_tx, transceiver
Boot config: fuses, ROM, none
TX datarate: 5.12Gbps, 10.24Gbps
TX FEC modes: FEC5, FEC12
E-groups configuration: datarates, channels enabled etc
CRC error injection in fuses
config_mechanism: fuses, ROM, IC, EC, I2C
Program PLL and datapath
Trigger lpGBT to boot and get to a ready state
Description
Random variables
Checks
Legend
boot up
regular actions
catastrophic events
regular actions
regular actions
Reports an error if the chip doesn’t get to ready state in expected duration

## Slide 15: lpGBT Rand Test
 | Full injection | Partial injection | No injection
Fault injection scope | All nodes | Only triplicated modules | No faults injected
Checkers | Relaxed (allow up to 8 consecutive bits of data corruption in downlink and up to 3 consecutive frames corruption in uplink) | Strict (doesn’t tolerate any corruption of uplink and downlink data) | Strict (doesn’t tolerate any corruption of uplink and downlink data)
Fault injection frequency | Fclk/2 | Fclk/2 | -
boot up
regular actions
catastrophic events
regular actions
regular actions
boot up
regular actions
catastrophic events
regular actions
regular actions
boot up
regular actions
catastrophic events
regular actions
regular actions

## Slide 16: lpGBT Signoff
Tools and techniques
  Massive parallel regression testing using Oracle Grid Engine (OGE) batch system
  Gitlab for content and project management using issues and merge requests
  tmake based build system
  vManager for regression management and metrics tracking
Metrics
  Regression pass-rate (98.24%)
    10k simulations on the final netlist
  Code coverage (94.35%)
  Functional coverage (100%)
  Fault coverage (100%)
    >2k SEU/node, 200 SET/node

## Slide 17: lpGBT verification timeline
Chart: Bugs found
| 43983 | 43997 | 44004 | 44011 | 44018 | 44025 | 44032 | 44039 | 44046 | 44053 | 44060 | 44067 | 44074 | 44081 | 44088 | 44095 | 44102 | 44109 | 44116 | 44123 | 44130 | 44137 | 44144 | 44151 | 44158 | 44165 | 44172 | 44179 | 44186 | 44193 | 44200 | 44207 | 44214 | 44221 | 44228 | 44235 | 44242 | 44249 | 44256 | 44263
Bugs found | 0 | 0 | 0 | 1 | 1 | 3 | 1 | 2 | 2 | 0 | 2 | 0 | 1 | 1 | 0 | 4 | 1 | 5 | 2 | 6 | 4 | 2 | 1 | 2 | 2 | 1 | 0 | 1 | 0 | 0 | 0 | 2 | 3 | 2 | 0 | 1 | 2 | 2 | 2 | 0 | 2
Lines of code | 494 | 1562 | 1850 | 3100 | 3647 | 3930 | 3798 | 4170 | 3562 | 4260 | 4260 | 5810 | 5810 | 6161 | 6017 | 6584 | 6267 | 6267 | 6267 | 8369 | 8503 | 8890 | 9817 | 9896 | 10292 | 11004 | 11161 | 11154 | 11154 | 11154 | 11154 | 11375 | 11018 | 11018 | 11157 | 11988 | 11306 | 12672 | 12774 | 12774 | 12774
01-Jun-2020: Start of verification framework development
June/July-2020: Verification environment bring-up Configuration sequences First functional tests
early August 2020: Setting up verification flow (vmanager, fault simulations)
~21-Aug-2020
First version of
lpgbt_rand_test
Oct-2020
Catastrophic events test phase
added to lpgbt_rand_test
Jan-2020 to Mar-2020: Fault campaigns and netlist simulations
Mostly SEE vulnerabilities
Dec-2020
SEE tolerance built into checkers

## Slide 18: lpGBT Verification – Key takeaways
Verification can only show presence of bugs, but cannot prove their absence
Start early! Verification is a resource intensive activity
Before embarking on verification, define a verification strategy which considers
  Functional verification
  SEE verification
  Netlist verification
Use constrained random verification approaches. Randomize as much as possible
Benefit from already existing verification IPs and verification productivity tools. Don’t reinvent the wheel

## Slide 19: lpGBT - Validation and Testing
Stefan Biereigel, CERN
on behalf of the lpGBT team
EP-ESE Seminar
28 June 2022 – CERN

## Slide 20: lpGBT - Testing Ecosystem
Complex, rad-hard mixed-signal ASICs require extensive silicon validation efforts
The „lpGBT tester“: dedicated, FPGA-based test system [1], enabling:
  Lab characterization (functional tests & electrical characteristics)
  Environmental testing (temperature)
  Heavy Ion / Laser SEE testing
  X-ray total ionizing dose testing
  Automated volume production testing
Based on high performance Xilinx Virtex 7 FPGA Reference Board (Xilinx VC707)
Supplemented by further testing hardware (VLDB+ Demo Board, lpGBT characterization PCB)
[1] J. Mendes et al: "lpGBT Tester: an FPGA based test system for the lpGBT ASIC", TWEPP2019

## Slide 21: lpGBT – Functional & Performance Characterization
Extensive validation performed on lpGBTv0, functionality & performance OK for most features
Remaining functional & performance issues identified successfully addressed in lpGBTv1
  I²C Master yield issue fixed
  Clock & data latency determinism now at ps-level
  Phase shifter performance improved
    Two channels had degraded performance: fixed
    Improved low-voltage + TID performance
  Deterministic jitter significantly reduced
    Improvement about 2x
Remaining issue: Reliability of eFuses
  eFuses are foundry IP blocks
  Fuse burning process unreliable in lpGBTv0 + v1
  Fuses also degrade with TID (discussed later)
  General advisory: Do not use eFuses, baseline other configuration mechanisms (ROM, I²C, IC, EC)
  Mitigations
    Chip ID will be stored redundantly for mass production chips
    Per-chip calibration data will be delivered through online database
Deterministic Jitter Performance of lpGBTv0 and lpGBTv1 (Credit J. Troska)

## Slide 22: Single-Event Effects Testing

## Slide 23: Single-Event Effects Testing – General Information
High complexity makes SEE testing challenging
  Limited test time available
    Exercise & monitor all modes/subsystems
  Capture a-priori unknown chip failure behavior
Testing of lpGBTv0 revealed several issues
  Systematic design issue in configuration memory
    Corruption of ASIC configuration
  Critical part of clock distribution not TMR-protected
    Bursts of errors on high speed link
  SEE sensitivity of LC-VCO inductor
    Transients of clock phase in PLL mode
Known issues were addressed in lpGBTv1 design
Qualification HI campaign in 2021 @ CRC HIF (Louvain-la-Neuve, Belgium)

## Slide 24: Single-Event Effects Testing – General Information
Scope of lpGBTv1 SEE qualification
  Key modes of operation (Simplex RX, TRX modes)
  Key high speed link modes (5 Gbps, 10 Gbps, FEC5, FEC12)
  Different ePort/eLink configurations (data rate & group combinations)
  Clock phase stability (eClock + Phase Shifters)
  Slow-Control, power-up state machine (Configuration Memory, I²C Slave, I²C Master, IC, EC, config ROM, ...)
Analog peripherals out of scope
  Glitches & single conversion errors in ADCs & DACs to be expected, presence or magnitude not studied
Similar expectations for all digital I/Os (Data, Clock, GPIOs, …)
  Part of their signal path is necessarily unprotected
lpGBTv1 installed in HIF Louvain, BE

## Slide 25: Single-Event Effects Testing – General Information
Dedicated Slow Control Testing
Exercised with single ion at UCL HIF CRC: LET = 32.4 MeV cm²/mg
Power-up + configuration sequence w/ beam over 1 hour: no issues
Exercised I²C Masters over 1 hour: no issues
Saturation HI cross section for both subsystems < 2x10-8 cm²
Power consumption
Monitored throughout all tests
No latch-up sensitivity found
Data path testing
Some data errors expected, since part of data path is not fully redundant
  Some correctable: HS link protected by FEC
  Some uncorrectable: eLink and associated logic cannot be fully protected
Goal: Enable conservative estimates of in-experiment error rates
  Using LET between 1.3 and 32.4 MeV cm²/mg - constrain threshold LET and saturation cross section
  1 hour per ion, 11 minutes per mode (TRX 5G FEC5, TRX 5G FEC12, TRX 10G FEC5, TRX 10G FEC12, TX 10G FEC12)

## Slide 26: Single-Event Effects Testing – Data Path
Data Path Reliability
Key observation: Improved clock generator now fully robust against unlocks
  In GBTX, BER is dominated by PLL unlocks producing long bursts of errors
Link errors now dominated by single- and multi-bit errors
  Originating in different parts of the data path
lpGBT data path architecture

## Slide 27: Single-Event Effects Testing – Data Path
Downlink Data Path
Only small amount of downlink bit errors observed during 16 hours of testing
Three main SEE signatures
  FEC-correctable link errors: no impact
  SET in eLink output driver: Single bit errors affecting one eLink
  SET in deserializer: Frame corruption, simultaneous single errors in multiple groups
Conservative estimate for high-fluence regions (e.g. CMS tracker): BER < 4x10-14 @ 1.28 Gbps
Heavy ion cross section for data errors on high-speed downlink

## Slide 28: Single-Event Effects Testing – Data Path
Uplink Data Path
BER cross section depending on link data rate and FEC mode
Similar SEE signatures
  FEC-correctable link errors: no impact
  Single-bit errors: affecting non-TMR'd parts of ePortRxGroup, scale with data rate
  Frame errors: corrupt data of multiple links/groups in a single frame
Conservative estimate for high-fluence regions (e.g. CMS tracker): BER < 1x10-14 @ 8.92 Gbps
Heavy ion cross section for data errors on high-speed uplink

## Slide 29: Single-Event Effects Testing – Inductor SEE Sensitivity
Inductor SEE Sensitivity (1/2)
New type of radiation sensitivity, discovered during tests of lpGBTv0
  Not reported in literature before
Affects inductor used in 5.12 GHz VCO of lpGBT clock generator
  Long-lived frequency shift (up to 100 ppm, depending on LET) of oscillator
  Stimulates temporary phase shift of lpGBT clock generator in PLL mode
  Large sensitive area (approaching 10-3 cm²)
Mechanism not yet fully understood (various studies underway), so only system-level mitigations available
Inductor
Micrograph
Heavy Ion
Sensitivity Map
Qualitative visualization of transient phase errors

## Slide 30: Single-Event Effects Testing – Inductor SEE Sensitivity
Inductor SEE Sensitivity (2/2)
Impact assessment performed
  Dedicated 200 MeV proton test @ PSI
  No danger to data transmission in any mode of operation
  Concern only for timing derived from lpGBT clocks when in simplex TX mode
  Effect suppressed in RX/TRX mode by higher CDR bandwidth
Mitigation strategy
  New default clock generator settings, minimize magnitude of effect
  Recommendation: prefer clocks from transceiver-mode-lpGBTs for precision timing
200 MeV p+ cross section characterized for recommended settings
Results & recommendations published in Application Note [2]
[2] lpGBT team: "Application Note: Single-Event Effect Clock Phase Transients in Simplex Transmitter Mode", 2021

## Slide 31: Total Ionizing Dose Testing

## Slide 32: lpGBT X-ray TID Testing - Introduction
TID design spec for lpGBT: 100 Mrad (200 Mrad with safety factor)
Common development makes qualification difficult
  Large variability of use cases: expected lifetime dose, operational chip temperature
  TID degradation highly dependent on dose rate, die temperature, bias conditions
  Annealing behavior another important aspect
Chosen approach
  Small user survey carried out to identify application environments
  Irradiation of 7 samples performed in different conditions (temperature, ultimate dose)
  Dose rate: approx. 3 Mrad/h to limit the test time
Caveat for data presented here
  Due to high dose rate used, optimistic by 2x - 4x compared to in-experiment dose rates
  Extrapolating the data to different temperatures is not straight forward

## Slide 33: lpGBT X-ray TID Testing - Introduction
Extensive X-ray campaign
  Total test time: 4 weeks
  Chips 1-6 irradiated deeply into failure in different conditions, to study TID margins of various blocks
  Chip 7 irradiated up to 50 Mrad at room temperature, to study annealing behavior after low doses
Main goals
  Identify key failure mode and dose
  Characterize degradation behavior of analog peripherals
 | Mode | Die Temp (°C) | TID (Mrad) | Annealing with bias
CHIP1 | 10G FEC5 | 30 | 340 | -
CHIP2 | 10G FEC5 | 30 | 400 | 1 week
CHIP3 | 5G FEC12 | 30 | 350 | -
CHIP4 | 5G FEC12 | 30 | 400 | 1 week
CHIP5 | 10G FEC5 | -5 | 560 | -
CHIP6 | 10G FEC5 | 0 | 620 | -
CHIP7 | 10G FEC5 | 30 | 50 | 3+ weeks
TID test samples & test conditions

## Slide 34: lpGBT X-ray TID Testing – General Information
Configuration (Config Memory, EC, IC, I²C, ROM, CRC, PUSM)
No problems found during testing
Power Consumption
Degrades gracefully, reducing during irradiation
Changes in Ptot smaller than variation over supply voltage range
eFuses
Tend to lose information with TID
High variability from chip to chip
Once again: Strong advisory against using the eFuses!

## Slide 35: lpGBT X-ray TID Testing – Data Path
TID failure mode in all tested chips: Data transmission
Uplink datapath is critical component
  High speed serializer
    Initially introduces correctable errors, gradually reducing link margin
    At some point, too many errors are produced → user data corruption
  Uplink eLinks (ePortRxGroup)
    Fail to sample/forward data through uplink data path → user data corruption
First failures always observed at low supply voltage
  100 Mrad difference between failures at 1.08 V and 1.20 V
  No failures observed at 1.32 V
  ASIC specification: 10% supply voltage variation → failures reported at 1.08 V
Downlink data path did not experience any failures during testing
 | Temp | UL Errors (Correctable) | Data Errors @ 160 Mbps | Data Errors @ 320 Mbps | Data Errors @ 640 Mbps
CHIP3 | 30 °C | 270 Mrad | 335 Mrad | 310 Mrad | 310 Mrad
CHIP4 | 30 °C | 285 Mrad | 355 Mrad | 320 Mrad | 320 Mrad
Uplink data path failure (10 Gbps, VDD = 1.08 V)
 | Temp | UL Errors (Correctable) | Data Errors @ 320 Mbps | Data Errors @ 640 Mbps | Data Errors @ 1280 Mbps
CHIP1 | 30 °C | 140 Mrad | 210 Mrad | 220 Mrad | 210 Mrad
CHIP2 | 30 °C | 200 Mrad | 285 Mrad | 285 Mrad | 190 Mrad
CHIP5 | -5 °C | 385 Mrad | 455 Mrad | 470 Mrad | 320 Mrad
CHIP6 | 0 °C | 415 Mrad | 520 Mrad | 500 Mrad | 325 Mrad
Uplink data path failure (5 Gbps, VDD = 1.08 V)

## Slide 36: lpGBT X-ray TID Testing – Data Path
Room temperature annealing after large TID
  Chip 1/3 without bias
  Chip 2/4 with bias
Degradation observed when annealing with bias
  Data path failures occur during annealing even at 1.2 V
  Not seen for samples without bias
Operational recommendation: Do not power lpGBTs when detectors are warmed up
For low-dose sample, no failures observed during long-term annealing with bias
Uplink data path failures during annealing

## Slide 37: lpGBT X-ray TID Testing – Analog Peripherals
Bandgap Reference Generator
Reference for all analog peripherals (VRef = 1 V)
Drift over TID larger than calibration accuracy (ΔVRef ~ -15 mV)
Results obtained with X-ray irradiation, i.e. no DD effects
Degradation observed during neutron testing: ΔVRef ~ -4 mV at 2.8 x 1014 n/cm^2

## Slide 38: lpGBT X-ray TID Testing – Analog Peripherals
On-Chip Temperature Sensor
Sensor is based on bandgap-like circuit structure
Output voltage is affected by TID
Leads to uncertainty of up to 30 K across 200 Mrad TID spec
Not useful for absolute measurements, but valuable for detecting transient changes
Current DAC
Foreseen for PT1000-based temperature measurements
Output current sensitive to VDD and TID
Combined uncertainty of 20-30 K across 200 Mrad TID+VDD spec
Similar performance as on-chip T-sensor

## Slide 39: lpGBT X-ray TID Testing – Analog Peripherals
ADC/DAC
Continuously characterized during X-ray irradiation
Both very well-behaved
When accounting for VRef drift
  Offset/slope changes limited to a few LSBs
Performance limited by reference voltage drift

## Slide 40: Conclusions
Silicon validation of lpGBTv1 successful
All critical issues identified in lpGBTv0 successfully mitigated
  Includes performance, SEE, TID issues
SEE qualification campaign
  Big leap in reliability compared to previous generation of high speed links
  Extensive SEE verification one of the keys to success
  Novel radiation sensitivity of inductor characterized and mitigated to possible extent
Very reassuring TID response
  High confidence of meeting demands of experimental environments
  Provided operational recommendations to experiments to maximize device lifetime
Volume testing commencing this year
  Awaiting arrival of production wafers at CERN
  Next steps: packaging and testing at the contractor

## Slide 41: Finding Information
Official schedule
  https://ep-ese.web.cern.ch/content/lpgbt-vl-dcdc-schedule
lpGBT user manual
  https://lpgbt.web.cern.ch/lpgbt
LpGBT-FPGA core
  https://gitlab.cern.ch/gbt-fpga/lpgbt-fpga
Contact and support
  lpgbt-support@cern.ch
  https://lpgbt-support.web.cern.ch

## Slide 42: Backup

## Slide 43: lpGBT team and contributors
lpGBT Design team
CERN, Geneva: Sophie Baron, Stefan Biereigel, Jose Fonseca, Rui Francisco, Iraklis Kremastiotis, Thanushan Kugathasan, Szymon Kulis, Pedro Leitao, Paulo Moreira, David Porret, Adithya Pulli, Ken Wyllie
AGH-UST, Cracow: Jakub Moroń, Krzysztof Swientek, Marek Idzik, Miroslaw Firlej, Tomasz Fiutowski
KU, Leuven: Bram Faes, Jeffrey Prinzie, Paul Leroux
FCT/UNL, Lisbon: João Carvalho, Nuno Paulino
SMU Physics, Dallas: Datao Gong, Di Guo, Dongxu Yang, Jingbo Ye, Quan Sun, Wei Zhou
SMU Electrical Engineering, Dallas: Ping Gui, Tao Zhang
lpGBT Test team
CERN, Geneva: Sophie Baron, Stefan Biereigel, Eduardo Brandao De Souza Mendes, Jose Fonseca, Nour Guettouche, Daniel Hernandez, Szymon Kulis, Pedro Leitao, Julian Mendez, Paulo Moreira, David Porret
Macrocell contributors
Czech Technical University, Prague: Miroslav Havranek, Tomas Benka
CERN, Geneva: Alessandro Caratelli, Iraklis Kremastiotis, Stefano Michelis

## Slide 44: Configuration
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 45: Programming the lpGBT (1/2)
The lpGBT is a highly flexible device:
  Transceiver modes / Locking modes / Uplink data rate / FEC coding / Clock frequencies / Clock phases / Number of active eLinks / Phase-aligner modes / Pre-emphasis / Equalization / Driving strengths / … / …
It won't simply work by just having it installed in your system…!
It needs to be configured!
There are:
  11 configuration pins to be “hardwired”;
  320 registers to be programed (240 R/W/F + 80 R/W + 142 R (status));
Configuration pins define the “basic” operation mode;
Configuration registers “customize” for the user application:
  Some of them also affect the basic operation (e.g. PLLs, DLLs, startup procedure, etc.);

## Slide 46: Programming the lpGBT (2/2)
Several options are available to read / write the configuration registers:
  I2C port, always possible;
  IC channel, only possible in Transceiver mode;
  EC port, only possible in simplex TX or RX modes;
  Access mode needs to be configured [pin “SC_I2C”].
Optionally, the user’s configuration can be “burned into” the ASIC on a bank of “eFuses” and copied at startup into the configuration registers
  Requires additional 2.5 V supply voltage during the programming cycle.

## Slide 47: Electrically Interfacing with the Frontends
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 48: eLinks Electrical “Standard”
CLPS “CERN Low Power Signalling”
  [This should] avoid any confusion with LVDS or SLVS;
Link type:
  Point – to – point
  Multi – drop transmitter
Max data rate:
  1.28 Gbps (NRZ)
Max clock frequency:
  1.28 GHz
Programmable signalling level:
  100 mV to 400 mV (single-ended PP amplitude)
  200 mV to 800 mV (differential PP amplitude)
Common mode voltage:
  600 mV (nominal)
Load impedance:
  100 W
Vout+
Vout-
Single-ended PP amplitude:
  max(Vout+) – min(Vout+)
Differential PP amplitude:
  max(Vout+ - Vout-) – min(Vout+ - Vout-)
Vcm:
Termination load close to the last receiver in the transmission line
100 W transmission line, twisted pair, etc.
Common mode in the middle of the supply (Vdd/2) for best tolerance to ground fluctuations between modules;

## Slide 49: eLink Line Receiver (eRx)
Specs
  Data rate:
    Up to 1.28 Gbps
  Common mode voltage range:
    70 mV – 1.13V
  Differential input voltage:
    140 mV – 450 mV
Programmable
  ON/OFF receiver (for power saving)
  Data polarity (to simplify routing)
  ON/OFF termination (100 W)
  ON/OFF common mode setting (for AC coupling, Vdd/2)
  Programmable equalization:
    Optimized for cables with bandwidths of “infinite” (equalization off), 448, 299 and 224 MHz
Off chip capacitors if AC coupling needed!
Remember: AC coupling introduces a zero at f = 1/(2p × Cc × 100 W) reducing the number of consecutive zero and ones that can be sent over the line reliably (DC base wander).
An external termination can be used to improve this but will certainly complicate your layout.
in+
in-
Rail-to-Rail Receiver
invertData
enableRx
enableTermination
eq[1:0]
setCommonMode
100 W
VCM
Cc
Cc
Macro cell, available for front-end designers (upon request)

## Slide 50: Using the eRx(s)
Equalization:
Should only be used if needed (low bandwidth transmission line)
Only effective for the high bit rates
Equalization has (only) three coarse settings
User must choose the most appropriate!
This requires a verification / scanning procedure from the user:
  Ideally the front-end designer implements a PRBS7 that the lpGBT can automatically verify;
  The user verifies the transmitted data at the counting room;
  A detailed scan procedure will also be proposed by the lpGBT team…
eRx Check list:
Turn ON the receivers corresponding to the eLinks in use.
  Obviously the others should be OFF
Choose the polarity (non-invert / invert)
Turn on the termination:
  Most likely the case (unless the chip in a multiple drop configuration – unlikely, or AC coupling to be optimized)
Enable the internal bias, if using AC coupling
Choose the appropriate equalization setting

## Slide 51: eLink Data Sampling and “Deserialization”
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 52: Up eLink – Phase Alignment
The phase of the incoming data signals is “unknown” in relation to the internal sampling clock!
There are up to 28 eLinks inputs (potentially) all with random phase offsets
The solution:
  “Measure” the phase offset of each eLink input
  Delay individually each incoming bit stream to phase align it with the internal sampling clock
eLink “i”
eLink “j”
Good sampling instants
LpGBT internal clock
Bad sampling instants
LpGBT
Clock (explicitly) provided to the front-end by an eLink clock.
Clock embedded in the data, CDR needed at the front-end
Phase relationship between the received data and the internal clock unknown!

## Slide 53: Phase-Aligner Block Diagram
Delay Line (reference)
PD
CP
LPF
Delay Line (replica)
bitRateClock
MUX
Phase Selection Logic
trackMode [2:0]
phaseSelectChannel [3:0]
Q D
CK
(x4)
(x1)
dataRate[2:0]
enableChannel
trainChannel
resetChannel
dllConfig [3:0]
dllReset
Input Data (unknown phase)
Resampled Data
Reference DLL

## Slide 54: Phase - Selection
T/8
Automatic, semi-automatic or or user driven procedures:
“Examine” all the eLink phases
Detect where the data “edges” are in relation to the clock;
Choose the phase that has the edges better centred around the clock
In automatic mode:
  Once aligned, the PA can track the data phase wanders that cover virtually a full clock cycle:
  To allow for this, the delay line covers more than one bit period: 1.75 × Tbit
  And, during initialization only phases 4 to 11 are allowed
-3/8 T
+3/8 T

## Slide 55: Using the Phase-Aligner(s)
There are 8 phase-aligners in the lpGBT:
  7 serve 28 data eLinks;
  1 serves the EC eLink.
A phase-aligner serves 4 eLink channels:
  Called an eLink Group.
The four channels in a Group share a calibration DLL;
User must setup:
  The calibration DLL
  The individual phase-aligner channels corresponding to the eLinks in use.
Phase Aligner Check list:
Set the group data rate;
  This sets the maximum number of eLinks per group (see next slides);
Configure the DLL parameters;
Reset the DLL;
Set the phase alignment mode:
  Static phase selection:
    User intervention needed.
  Initial training with learned static phase selection:
    User intervention needed
  Automatic phase tracking;
Enable and reset the channels in use;

## Slide 56: eLink Rx Groups
eLinks are “clustered” in groups of 4:
  Simply called groups.
The number of available groups is determined by the FEC uplink code in use;
The number of available eLinks within a group is determined by the Group data rate;
The possible data rates depend on the uplink bandwidth (5.12 or 10.24 Gbps)
The data rate of each group can be set independently:
  A couple of [over complicated] examples:
    uplink 5.12 Gbps & FEC12: 8 eLinks x 160 Mbps + 4 eLinks x 320 Mbps + 2 eLinks x 640 Mbps
    uplink 10.24 Gbps & FEC5: 8 eLinks x 320 Mbps + 4 eLinks x 640 Mbps + 3 eLinks x 1.28 Gbps
Input eLinks (uplink) |  |  |  |  |  |  |  |  |  |  |  | 
uplink bandwidth [Gbps] | 5.12 |  |  |  |  |  | 10.24 |  |  |  |  | 
FEC coding | FEC5 |  |  | FEC12 |  |  | FEC5 |  |  | FEC12 |  | 
Bandwidth [Mbps] | 160 | 320 | 640 | 160 | 320 | 640 | 320 | 640 | 1280 | 320 | 640 | 1280
Maximum number | 28 | 14 | 7 | 24 | 12 | 6 | 28 | 14 | 7 | 24 | 12 | 6

## Slide 57: Note about eLink Input Pin Names
EDINGCP
eLink
Data
Input to the lpGBT
Group number: 0, 1,… 6 (there are 7 groups)
Channel number within a group: 0, 1, 2 or 3 (there are 4 eLinks associated with every group)
Pin Polarity: P – Positive, N – Negative
(Remember: polarity can be inverted at the output of the corresponding eRx)
Example: EDIN32N – eLink data input group 3 channel 2 negative polarity pin

## Slide 58: The EC “Group”
The EC “group” is a special case!
It is composed of a single eLink!
It only works at 80 Mbps!
EC channel eLink Functionality is only available in Transceiver mode;
In transceiver mode it is always available independently of the other Groups activity;
Its mission is to implement an “experiment control” link, however it can be used as a general purpose link;
[As seen before, this input can be used to control the ASIC in the simplex modes (TX / RX) but not in transceiver mode]
Pins:
  EDINECP (eLink Data In EC channel Positive pin)
  EDINECN (eLink Data In EC channel Negative pin)

## Slide 59: eLink Deserialization
eLink inputs receive serial data from the frontend devices;
These data is de-serialized and inserted in the uplink frame to be transmitted to the counting room (more on this soon):
  The frame is processed in parallel in the chip before it is itself serialized for uplink transmission.
In the case of transmission at 5.12 Gbps an eLink Group is always associated with the same 16-bits in the frame, the group bits.
The same is true for 10.24 Gbps but in this case the group bits are 32 (the uplink frame is twice as long)
The user knows from the position of the bits in the frame from which eLink group the data belongs to!
Moreover, depending on the data rate, a specific eLink is identified by the position of the corresponding bits within the “group bits” (or simply, the position within the frame).
After the eLinks input data is de-serialized, scrambling, FEC coding, interleaving header insertion and high-speed serialization takes place in the uplink data path…

## Slide 60: Uplink Data Path
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 61: High – Speed Uplink Frame
The LpGBT supports the following uplink data rates:
  5.12 / 10.24 Gbps
Data is transmitted as a frame composed of:
  Header
  The data field
  A forward error correction field: FEC5 / FEC12
The data field is scrambled to allow for CDR operation at no [additional] bandwidth penalty
Efficiency = # data bits/# frame bits
 | uplink |  |  | 
 | 5.12 Gbps |  | 10.24 Gbps | 
 | FEC5 | FEC12 | FEC5 | FEC12
Frame [bits] | 128 |  | 256 | 
Header [bits] | 2 |  | 2 | 
Data [bits] | 116 | 102 | 232 | 204
FEC [bits] | 10 | 24 | 20 | 48
Correction [bits] | 5 | 12 | 10 | 24
Efficiency | 91% | 80% | 91% | 80%
H
Message
FEC
Forward Error Correction
(Allows to correct transmission errors)
Header
(Delimits the frame boundaries)
Data
(User data payload)

## Slide 62: Example: 5.12 Gbps FEC5 Uplink Frame
IC[1:0]
EC[1:0]
D[63:48]
D[47:32]
D[31:16]
D[15:0]
FEC[9:0]
D[79:64]
D[95:80]
D[111:96]
112 bits
G0
G1
G2
G3
2 bits
10 bits
2 bits
128 bits
G4
G5
G6
7 groups of 4 input e-Ports
Number of data ports:
28 eLinks @ 160 Mbps
14 eLinks @ 320 Mbps
7 eLinks @ 640 Mbps
H[1:0) = 2’b10
2 bits
Frame | Function | I/O Group
FRMUP[9:0] | FEC[9:0] | 
FRMUP[25:10] | Data[15:0] | 0
FRMUP[41:26] | Data[31:16] | 1
FRMUP[57:42] | Data[47:32] | 2
FRMUP[73:58] | Data[63:48] | 3
FRMUP[89:74] | Data[79:64] | 4
FRMUP[105:90] | Data[95:80] | 5
FRMUP[121:106] | Data[111:96] | 6
FRMUP[123:122] | EC[1:0] | EC
FRMUP[125:124] | IC[1:0] | 
FRMUP[127:126] | H[1:0] = 2'b10 | HFH[1:0] = 2'b10
Note: This is how you will see the uplink frame after it has been processed by the lpGBT-FPGA receiver but not how it is actually transmitted by the lpGBT …

## Slide 63: Uplink data path
Scrambler
FEC
Coding
Interleaving
Serializer
data[N:0]
header
serialData
The order of operations is important
We avoid the details here since you will not have to worry with them, they will be “handled” by lpGBT-FPGA
128-to-1 @ 5.12 Gbps
Or
512-to-1 @ 10.24 Gbps

## Slide 64: High-Speed Line Driver
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 65: Line – Driver Topology
Accommodate the large capacitive load
RC delay to generate the pre-emphasis pulse
Pre-emphasis current driver
On-chip 100 Ω matching
Buffer Stage
Imax = 12 mA
Imax = 8 mA

## Slide 66: Line driver simulations (@5.12Gbps)
Im
Ipre
Iout
= +
“long” delay
“short” delay
Advantage:
Pre-emphasis is made by subtracting the “bit stream” to itself after inversion and scaling!
No narrow pulses required (as needed for the eTx scheme)
Disadvantage:
The pre-emphasis is done by reducing the amplitude rather than peaking the signal during the pre-emphasis phase.
The driver consumes in permanence Im + Ipre.
Icc = 40 mA
Imod = 12 mA
Ipre = 8 mA
Cout = 500 fF
Process: SS_100C_1.2V

## Slide 67: Using the Line Driver
The user must:
Enable the line driver for Transceiver and Simplex Transmitter modes:
Enable the pre-emphasis if needed;
Set the amplitude of the:
  Modulation current;
  Pre-emphasis current.
Set the pre-emphasis pulse duration;
It is possible to invert HS output polarity to simplify the PCB design:
  The inversion is done @40M (before the Serializer) at the frame level.

## Slide 68: High-Speed Line Receiver / Equalizer
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 69: The Equalizer in the LpGBT
To be used in case of “low bandwidth” downlink
  “Bypassed” by default.
If needed, user programs the positions of the zeros of the four CTLE stages (and the 1st stage attenuation)
It is an iterative process in a “case-by-case” basis
Passive attenuator: allows to handle signals as high as 1 V
Attenuation: 0, -3.5 and -9.5 dB
Four equalizing stages allow
to flexibly control the shape of the transfer function.
75 cm of Low Bandwidth Coaxial Cable

## Slide 70: Eye Opening Monitor
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 71: Eye Opening Monitor
Y-axis:
  31 points, step = ~20 mV (covers from VDD/2 up to VDD)
X-axis:
  64 points, step = ~6.1 ps in typical
Operation:
  Controlled through the I2C interface
  Eye reconstruction at the "backend”
DFF
CML
CMOS
Phase
Interpolator
data+
DAC
data-
Vof+
Vof-
clk5G12
clk2G56pi
toCounter
comp
Vof+
Vof-
polarity
vSel[3:0]
compQ
selPhase[5:0]
Notes: The DAC is designed with a resistive network plus passgates

## Slide 72: PLL / CDR and Clock Manager
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 73: Clock Syntheses
This circuit generates all the clocks needed by the ASIC:
  40 MHz, 80 MHz, …, 5.12 GHz
  The 10.24 Gbps Serializer uses a DDR scheme
Simplex TX:
  A 40 MHz external reference is needed
Simplex RX and Transceiver:
  The downlink serial stream is used as a clock reference
CDR Locking modes:
  External reference aided
  Reference-Less Locking
PLL / CDR
+
Clock Manager
40 MHz
2.56 Gbps
40 MHz
160 MHz
5.12 GHz
80 MHz
320 MHz

## Slide 74: Down Link Data Path
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 75: Downlink Data Path
DeScrambler
FEC
DeCoding
(error detection /correction)
DeInterleaving
CDR &
DeSerializer
data[N:0]
header
serialData
The order of operations is important
[Once again] We avoid the details here since you will not have to worry with them, they will be “handled” by lpGBT-FPGA
2.56 Gbps CDR circuit

## Slide 76: eLink Groups and Serialization
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 77: eLink Tx Groups & Serialization
Tx eLinks are “clustered” in groups of 4 (similar to RX eLinks):
The data rate of each group can be set independently:
80 / 160 or 320 Mbps
The number of available eLinks within a group is determined by the Group data rate;
[Similar to the uplink] Tx eLinks are associated with specific bits within the downlink frame (geographical addressing):
  The user knows, from the position of the bits (and the selected data rate) in the frame, to which eLink the data will be serialized to.
EC outputs (pins: EOUTECP / EOUTECP) are fixed data rate (80 Mbps) that can be used for Experiment Control in Transceiver mode or participate in the control of the ASIC itself in Simplex TX or RX modes
Output eLinks (down-link) |  |  | 
Bandwidth [Mb/s] | 80 | 160 | 320
Maximum number | 16 | 8 | 4

## Slide 78: eLink Tx “Mirror” function
To help implementing broadcast of data to the frontends, a “mirror” function is implemented for the Tx eLinks:
  Call it “buffering” if you prefer!
Since the number of active Tx eLinks depends on the selected data rate, “unused” transmitters can be used to “repeat” the data of the active channels
This called “mirror” function
The possibilities are:
  80 Mbps:
    No mirroring
  160 Mbps:
    Each channel is [can be] available on 2 outputs
  320 Mbps:
    Each channel is [can be] available on 4 outputs

## Slide 79: eLink Line Transmitter (eTx)
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 80: eLink Driver
Data rate:
  Up to 1.28 Gbps
Clock frequency:
  Up to 1.28 GHz
Driving current:
  Programmable: 1 to 4 mA in 0.5 mA steps
Receiving end termination:
  100 W
Voltage amplitude in 100 W:
  100 mV to 400 mV (SE PP amplitude)
  200 mV to 800 mV (DIFF PP amplitude)
Common mode voltage:
  600 mV
Selectable polarity
Pre-emphasis:
  Driving current: 1 to 4 mA in 0.5 mA steps
  Pulse width:
    Externally timed
    Self timed: 120 ps to 960 ps in steps of 120 ps
    Clock timed: T bit / 2
Pre-emphasis logic
Macro cell, available for front-end designers (upon request)

## Slide 81: eTx Functionality
Programmable delay line allows to generate pre-emphasis pulse widths between 120 and 960 ps
Pre-emphasis amplitude
programmable
Pre-emphasis mode selectable
Pre-emphasis self-timed pulse width selectable
Half bit period pre-emphasis pulse width
Pre-emphasis pulse
Controls the polarity of the driver

## Slide 82: eTx – Pre-Emphasis
No Pre-Emphasis
Driver Strength = 2 mA
Pre-Emphasis Strength = 0 mA
Pulse width = n.a.
With Pre-Emphasis
Driver Strength = 2 mA
Pre-Emphasis Strength = 2 mA
Pulse width = T/2
Data: PRBS 7
Data rate: 2.56 Gb/s
CL = 2 x 5 pF

## Slide 83: Note about eLink Output Pin Names
EDOUTGCP
eLink
Data
Output from the lpGBT
Group number: 0, 1, 2 and 3 (there are 4 groups)
Channel number within a group: 0, 1, 2 or 3 (there are 4 eLinks associated with every group)
Pin Polarity: P – Positive, N – Negative
(Remember: polarity can be inverted at the output of the corresponding eTx)
Example: EDOUT32N – eLink data output group 3 channel 2 negative polarity pin

## Slide 84: eLink Clocks
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 85: eLink Clocks
Same drivers as for the Tx data eLinks, thus:
  Programmable: polarity, driving strength and pre-emphasis
4 programmable Phase/Frequency clocks:
  4 independent
  Phase resolution: 50 ps
  Frequencies: 40 / 80 / 160 / 320 / 640 / 1280 MHz
eLink Clocks:
  28 independent
  Fixed phase
  Frequency programmable
  Frequencies: 40 / 80 / 160 / 320 / 640 / 1280 MHz

## Slide 86: Experiment Control and Environment Monitoring
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mbps port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mbps to
1.28 Gbps ports
LpGBTIA
LpGBLD
LpGBT
eLink
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gbps
5.12 Gbps or 10.24 Gbps
EOM

## Slide 87: Digital
Three I2C Masters:
  Three general purpose masters
    But one typically dedicated to control the laser driver (LDQ10)
  Transfer rates: 100 KHz, 200 KHz, 400 KHz, 1 MHz
  7-bit and 10-bit addressing standards
  Single-byte and multi-byte I2C read/write bus operations
  Masters themselves controlled by:
    The I2C slave port (always possible)
    The IC – channel (only possible in transceiver mode)
    The EC – port (Only possible in Simplex RX or TX mode)
General Purpose I/O
  16-bit I/O port
  Optional internal pull-up / pull-down resistors
  Controlled by the same means as the I2C masters
Output reset pin
  Active low
  Programmable pulse duration

## Slide 88: Analogue Peripherals
10 bit ADC
  Core: fully differential SAR
  8 channels (single ended or differential)
  Voltage amplifier (x1 .. x32)
  Sampling rate up to ~ 1MSps (limited by the control channel)
  Monitoring of internal signals (like VDD)
12 bit voltage DAC
8 bit current DAC
  can be attached to any analog input
  range: 0-1mA (8bit)
Temperature sensor
ADC
Input[7:0]
InPSel[3:0]
x1-x32
GainSel[1:0]
Vref/2
InNSel[3:0]
Vref generator
Vref/2
dataOut[9:0]
Vref
Current MUX
8-bit
Current DAC
12 bit
voltage DAC
DACout
Temp
Sensor

## Slide 89: Example: Using an External Temperature Sensor
ADC
InPSel[3:0]
x1-x32
GainSel[1:0]
Vref/2
InNSel[3:0]
Vref generator
Vref/2
dataOut[9:0]
Vref
Current MUX
8-bit
Current DAC
12 bit
voltage DAC
DACout
Temp
Sensor
ADCX
X = 0, 1, … 7
PT100
I
DV

## Slide 90: Package
Small Footprint BGA package:
  Size: 9 mm x 9 mm x 1.25 mm
  Fine Pitch: 0.5 mm
  Pin count: 289 (17 x 17)
Routing of high speed signals optimized and simulated
  Very small loss @ 10GHz
  Models used for line driver simulations

## Slide 91: lpGBT FPGA
The lpGBT-FPGA provides a back-end counterpart to the lpGBT ASIC
Warning:
  “Strategy” departures from that used for the GBT-FPGA
  Not a single generic “block”;
  But a set:
    Of modules;
    Of implementation examples;
    Of reference notes.
  To help the user designing its own system!

## Slide 92: lpGBT Simulation Model
The lpGBT model (will be) available to the users:
  To simplify the design and verification of front-end (ASIC) and back-end (FPGA) systems
Contains all essential features related to the data transition and slow control interfaces:
  Some of the chip’s analogue features are not modelled:
    e.g.: pre-emphasis, equalization, analogue I/O (ADC,DAC), pull up/down resistors;
“Distributed” as one System Verilog file, compatible with:
  Cadence Incisive
  Mentor Questa
  Synopsys VCS

## Slide 93: lpGBT UVM Agents

## Slide 94: lpGBT tests
AliveTest
EcAliveTest
IcAliveTest
I2cAliveTest
FuseAliveTest
RalTest
I2cMastersTest
RegRandRwTest
PioTest
FuseBurningTest
RandTest

## Slide 95: lpGBT – Functional & Performance Characterization
Data path validation
  High speed links (5G/10G, FEC5/FEC12)
  RX / TX ePort characterization (BER testing, phase aligners, data jitter, ...)
  Equalization / pre-emphasis on high-speed optical link and eLinks
Clock performance testing
  PLL and CDR clock quality, deterministic and random jitter, clock latency
  High-Resolution clock phase shifter
Analog peripheral characterization
  Bandgap reference
  Voltage ADC
  Current DAC
  Voltage DAC (linearity, noise, stability, temperature)
Configuration/Start-Up/Watchdog Testing
  Power-Up state machine
  Configuration flows: I²C, EC, IC, ROM, eFuses, CRC, …
  I²C Master, GPIOs
List not exhaustive!

## Slide 96: Single-Event Effects Testing – Clock Glitches
Glitches on Clock Signals
eClocks are not fully redundant all the way through the chain
  Short (100s of ps) SETs might appear on the clock outputs
eClock and PSclock were monitored during irradiation
  Sensitive to pulses longer than 100 ps
Frequency of occurrence characterized
  No further data collected (typical length of individual pulses unknown)
Heavy ion cross section for glitches on eClocks and phase programmable clocks

## Slide 97: lpGBT X-ray TID Testing – eClock and eLink Delay
Clock and Data Delay
Clock and data delay through chip varies with VDD and TID
  Variations across supply range on the same level as drift over TID
Achieves excellent repeatability across power cycles
  Only long-term drift needs to be accounted for
Degradation of different eClocks is consistent
Evolution of eClock delay with TID

## Slide 98: lpGBT – Functional & Performance Characterization
Data path validation
  High speed links (5G/10G, FEC5/FEC12)
  RX / TX ePort characterization (BER testing, phase aligners, data jitter, ...)
  Equalization / pre-emphasis on high-speed optical link and eLinks
Clock performance testing
  PLL and CDR clock quality, deterministic and random jitter, clock latency
  High-Resolution clock phase shifter
Analog peripheral characterization
  Bandgap reference
  Voltage ADC
  Current DAC
  Voltage DAC (linearity, noise, stability, temperature)
Configuration/Start-Up/Watchdog Testing
  Power-Up state machine
  Configuration flows: I²C, EC, IC, ROM, eFuses, CRC, …
  I²C Master, GPIOs
List not exhaustive!

## Slide 99: Single-Event Effects Testing – Clock Glitches
Glitches on Clock Signals
eClocks are not fully redundant all the way through the chain
  Short (100s of ps) SETs might appear on the clock outputs
eClock and PSclock were monitored during irradiation
  Sensitive to pulses longer than 100 ps
Frequency of occurrence characterized
  No further data collected (typical length of individual pulses unknown)
Heavy ion cross section for glitches on eClocks and phase programmable clocks

## Slide 100: lpGBT X-ray TID Testing – eClock and eLink Delay
Clock and Data Delay
Clock and data delay through chip varies with VDD and TID
  Variations across supply range on the same level as drift over TID
Achieves excellent repeatability across power cycles
  Only long-term drift needs to be accounted for
Degradation of different eClocks is consistent
Evolution of eClock delay with TID