## Slide 1: Novel cavity with ultra low R/Q for CLIC DR RF system
Alexej Grudiev, Themis Mastoridis
22/09/2021

## Slide 2: 380 GeV CLIC DR parameters (PRAB22, 091601)
Parameter of DR |  | value | unit
Energy | E | 2.86 | GeV
Circumference | C | 373.7 | m
Revolution frequency | f0 | 802 | kHz
RF frequency | fRF | 2 | GHz
Harmonic number | h | 2493 | 
Energy loss per turn | eVA | 5.8 | MeV
RF voltage | VC | 6.5 | MV
RF stable phase | φ | -26.8 | o
Bunch population | Ne | 5.7 | 1e9
Number of bunches per train | Nb | 352 | 
Number of trains | Nt | 1 | 
Peak beam current | Ib | 1.8 | A
Strict specifications on the bunch spacing variation: δφb < ±1o at 2 GHz (±400μm) for Luminosity loss < 1% (CLIC-Note-1138)
This is difficult to maintain due to strong transient beam loading effects caused by large difference between peak and average beam power values of 10.4 MW and 1.5 MW, respectively
1%
±400μm

## Slide 3: Current baseline summary (NIMA V985, 164659)
Cavity type | ARES
Cavity R/Q [Ω] | 7.5
Number of cavities | 32
Cavity Q0 | 55000
BL compensation method | feedforward
Beam phase variation [o] | ~1
Peak input power [kW/cavity] | 405
Cavity power loss [kW] | ~50
Total peak input power [kW] | 12960
Very high peak power
Larger klystron bandwidth
Strong peak power modulations on each turn
Inefficient due to most of average power lost

## Slide 4: Transient beam loading effects (CLIC-Note-879)
VC
δVC
Re{V}
Im{V}
VA
φ
δVB
δφ1
δφ2
δV1
δV2
TR
t
Tb
Ib
VC
δVC
VA
<< 1
<< 1

## Slide 5: Estimate of required R/Q for RF system with large enough stored energy to maintain small beam phase variation
Bunch phase variation versus cavity voltage variation due to transient beam loading: δφb = 1o => δVC/VC = 7.1e-3
Relationship between voltage and stored energy: δU/U = 1.4e-2
Variation of stored energy due to transient beam loading: δU = 1.86 J
Required stored energy: U = 133 J
Required R/Q of the DR RF system (all cavities): R/Q = 12.6 Ω
This estimate neglects input and reflected power
There is factor 2 margin in the case of linear variation of ±1o peak-to-peak => 2o linear variation

## Slide 6: Verification of the estimate by LLRF model: Results for R/Q = 12.6 Ω= 0.48 Ω/cav * 26 cavities
For an R/Q = 0.48 Ω per cavity the beam phase variation is 0.87 degree.
For an R/Q = 0.55 Ω per cavity the phase variation is exactly 1 degree.
Cavity voltage
In this case total R/Q = 0.55*26 = 14.3 Ω
δφb = 0.87o
Beam
phase

## Slide 7: Example of conventional elliptical pillbox: a/λ=0.2
TM011 | 
a [mm] | 30
f [GHz] | 2
a/λ | 0.2
Lc [mm] (0.01Hmax) | ~200
R/Q [Ω] | 42.5
Emax/Vacc [1/m] | 26.1
Hmax/Vacc [mA/Vm] | 49.0
a
Bmax limit: 100 mT
Hmax = 80kA/m
Emax = 42 MV/m
Vmax = 1.6 MV
Umax = 2.4 J
E- and H-fields for 144J
Looking at R/Q , even one cavity is ‘too many’: R/Q is ~x4 higher than specs
Looking at Vmax 4 cavities are necessary to get nominal total RF voltage of 6.5 MV

## Slide 8: Design philosophy for Ultra low R/Q RF cavity
Increase cavity aperture to reduce loss factor => reduce R/Q per cavity
Increase cavity length to reduce transit time factor => reduce R/Q per cavity
Optimize cavity wall shape to minimize H-field to reach largest stored energy per cavity under the H-field limit of 80 kA/m (100 mT, private communication, W. Venturini, 2021) => reduce number of cavities
R/Q per cavity X N of cavities must be below Total R/Q: 14.3 Ω

## Slide 9: Novel cavity: Barrel Cell Cavity (BCC) geometry
Rcav
Beam axis
a
Rarc
Large aperture => low R/Q
Long cell: ~λ => low transit time factor
Low field on the cavity wall
E-field

## Slide 10: Design of the cavity for total R/Q=14.3Ω
E- and H-fields for 144J
Hmax limit: 80kA/m
Vmax = 0.275 MV
Umax = 5.0 J
Emax = 8.7 MV/m
TM011 | 
a [mm] | 52
f [GHz] | 2
a/λ | 0.347
Lc [mm] (0.01Hmax) | ~520
Rarc [mm] | 307
Rcav [mm] | 61.95
R/Q [Ω] | 0.6
Emax/Vacc [1/m] | 31.6
Hmax/Vacc [mA/Vm] | 291
To get this design parameters,
two conditions must be met:
R/Q per cavity is 14.3Ω/Ncav
Vmax per cavity is 6.5MV/Ncav
AND
See next slide

## Slide 11: Optimization of the cavity for total R/Q=14.3Ω
R/Q=0.6Ω
24 cavities
R/Q and Hmax/Vacc of the cavity can be changed by varying Rarc
Ncav to get total R/Q=14.3 Ω
Hmax for Vacc from the top plot
Vacc per cavity =
6.5 MV / Ncav
Bmax < 100 mT
Lowest number of cavities with Bmax < 100 mT
Optimum value of Rarc = 307 mm

## Slide 12: Potential way to reduce number of cavities Higher Bmax: 100 => 200 mT
Bmax [mT] | 100 | 100*2=200
Hmax [kA/m] | 80 | 160
Emax [MV/m] | 8.7 | 17.4
Vmax [MV/cav] | 0.275 | 0.55
Ncav | 24 | 12
Pin [kW/cav] | 60 | 120
Umax [J/cav] | 5.0 | 20.0
Bunch phase variation [o] | 1 | ~0.5
R/Q=0.6Ω
Imagine that we could get 2 times higher Bmax = 200mT
which is still lower than recently demonstrated value of 210mT
=> Factor 2 less cavities, worth making prototype
E-field
B-field
E-field
B-field

## Slide 13: Monopole wake: a=52mm, R/Q=0.6Ω
CST wakefield solver
Indirect interfaces
FFT
Only operating
Fundamental
TM011 mode
is trapped
All HOMs are above cut off and are not trapped: a = 52 mm is adjusted to have
TM01 WG mode cutoff at 2.2 GHz < 1st HOM
Lowest HOM: TM01 waveguide cutoff mode

## Slide 14: Dipole wake: a=52mm: R/Q=0.6Ω
TE111 mode: E-field
CST wakefield solver
Indirect testbeams
FFT
Lower Order Mode
(LOM) TE111is trapped and require damping
TE11 WG mode cutoff: 1.69 GHz

## Slide 15: Damping TE111 LOM, Cornell cavity approach The magic flute helps to damp dipole LOM
One of the BCC beam pipes is ‘fluted’ using 4 longitudinal grooves to reduce TE11 WG mode cutoff from 1.69 GHz to lower value and let TE111 mode at f=1.59 GHz escape.

## Slide 16: Damping TE111 mode
damping
The dipole wake is well damped
The slop is numerical artefact, require special treatment but does not change the conclusion about damping
Lower Order Mode
LOM TE111 mode
is well damped

## Slide 17: An idea for RF frequency tuning
Longitudinal Corrugations used for damping dipole LOM can also be used to deform (reduce or increase) the ‘fluted’ beam pipe cross-section
Although it is not the cavity itself it will impact the cavity fundamental mode frequency depending on how close is the deformation to the cavity

## Slide 18: Another way to reduce number of cavities: Less conservative specification for bunch phase variation: R/Q = 28.6Ω
Total R/Q = 14.3 Ω results in 1o peak-to-peak linear variation
The specification for the bunch phase (bunch spacing) variation is given as δφb < ±1o.
The total variation is 2o peak-to-peak
Assuming linear scaling of the phase variation with the R/Q we can estimate R/Q for 2o peak-to-peak phase variation: 14.3 * 2 = 28.6 Ω
It is basically factor 2 larger due to taking off the factor 2 margin we had before
This is less conservative but on the other hand it will be better for most of the bunches, so integrated effect over the full bunch train is expected to be less than ±1o.
To be confirmed by the beam dynamics

## Slide 19: Cavity design for total R/Q=28.6Ω
E- and H-fields for 144J
Hmax limit: 80kA/m
Vmax = 0.47 MV
Umax = 4.3 J
Emax = 11.7 MV/m
TM011 | 
a [mm] | 50
f [GHz] | 2
a/λ | 1/3
Lc [mm] (0.01Hmax) | 500
Rarc [mm] | 160
Rcav [mm] | 63.55
R/Q [circuitΩ] | 2.04
Emax/Vacc [1/m] | 24.86
Hmax/Vacc [mA/Vm] | 170

## Slide 20: Optimization of the design for total R/Q=28.6Ω
R/Q=2.04Ω
14 cavities

## Slide 21: Damping TM01n HOMs, => a=50mm
Only operating
Fundamental
TM011 mode
is trapped
Lowest monopole HOM: TM012

## Slide 22: Damping TE111 mode
damping
Lower Order Mode
LOM TE111 mode
is well damped
The dipole wake is well damped
The slop is numerical artefact, it requires special treatment but does not change the conclusion about damping

## Slide 23: Summary table
Case | 1 | 2 | 3 | 4
Cavity R/Q [Ω] | 0.6 |  | 2.04 | 
a [mm] | 52 |  | 50 | 
Lc [mm] (0.01Hmax) | 520 |  | 500 | 
Rarc [mm] | 307 |  | 160 | 
Rcav [mm] | 61.95 |  | 63.55 | 
Total R/Q [Ω] | 14.3 | 7.15 | 28.6 | 14.3
Bunch phase variation [o] @2GHz | 1 | 0.5 | 2 | 1
Ncav | 24 | 12 | 14 | 7
Cavity input power Pin [kW] | 60 | 120 | 103 | 206
Bmax [mT] | 100 | 200 | 100 | 200
Hmax [kA/m] | 80 | 160 | 80 | 160
Emax [MV/m] | 8.7 | 17.4 | 11.7 | 23.4
Cavity voltage Vc [MV] | 0.275 | 0.55 | 0.47 | 0.94
Cavity stored energy Uc [J] | 5.0 | 20.0 | 4.3 | 17.1

## Slide 24: Fundamental power coupler limit (Eric, FCC2021)
At 2 GHz
P [kW] = 100 (SOTA)
P [kW] = 200 (FCC goal)

## Slide 25: Dual coupler cavity geometry for case 4
In case 4:
Pin = 206 kW per cavity
If the limit is 100 kW per coupler
Two couplers may be used

## Slide 26: 2-cell BCC operating at 2π-mode for case 1
2 GHz: λ=150mm;
Conventional multi-cell periodic structure is based on π-mode, cell length: λ/2=75mm.
This does not work here since cell is significantly longer: ~200mm
Novel multi-cell periodic structure based on 2π-mode, cell length: λ=150mm is proposed
200mm
2π-mode 2-cells BCC
~150mm
Case 1 need 24 cavities
Potentially it can be reduced by x2 by going to 2-cell cavities of novel shape

## Slide 27: LLRF simulation results for cases 1 - 4
Design | Δf (Hz) | QL | Peak power per klystron (kW) | Total peak power (MW) | φb | Δφ
1 | -514 | 983e3 | 62.2 | 1.49 | -26.8° | 0.99°
2 | -257 | 1962e3 | 125 | 1.49 | -26.8° | 0.49°
3 | -1020 | 496e3 | 107 | 1.49 | -26.8° | 1.99°
4 | -510 | 990e3 | 213 | 1.49 | -26.8° | 0.98°
Due to the very high cavity filling time, the closed-loop response of the RF/LLRF system is slow.
In addition, there is a 350 ns delay in the RF loop. Very small klystron power modulation

## Slide 28: Comparison: baseline vs new proposal
Current baseline
New proposed design #1
Cavity type | ARES | BCC
Cavity R/Q [Ω] | 7.5 | 0.6
N of cavities | 32 | 24
Peak input power [kW/cavity] | 405 | 60
Total peak input power [MW] | 13 | 1.5
RF power match the average beam power => efficient
No klystron power modulation => no large bandwidth
Peak power requirements are SIGNIFICANTLY reduced => cost, size

## Slide 29: Summary and outlook
Novel shape cavity for ultra low R/Q is proposed
It allows to implement RF system with small variation of stored energy enough to maintain beam phase variation below the specified value of 1 degree with ‘classical’ slow feedback LLRF
The RF system based on this cavities requires significantly less (x9) RF power and has higher RF-to-beam efficiency compared to current baseline
The number of cavities can also be reduced or even significantly reduced depending on the final design choice
Several designs are proposed. The final design choice depends on:
  Cavity performance in terms of achievable surface B-field.
  Beam dynamics requirement for the beam phase variation of all bunches in the train considering that it has linear distribution at the exit of DR.
BCC has much lower max surface E-field to B-field ratio. This type of cavity can be useful for testing B-field limit with less of a concern about field emission