Experience with the Linac4 RFQ Breakdown Protection and Automatic Recovery System
Rolf Wegner, Bartosz Bielawski
Andy Butterworth, David Glenat, David Landre, Pablo Martinez Yanez, Simone Chicarella, Ylenia Brischetto

---
Outline
Introduction
Implementation of Protection and Automatic Recovery,
adjustments made
Illustration of Inspector panels and typical events
Comparison of accumulated Breakdowns 2019 to 2021
Interlocking RFQ on Tuning faults
Conclusions

---
Introduction
Plenty of craters from RF discharges = breakdowns (BD) seen in the L4 RFQ endoscope inspection.
Picture from CLIC high gradient study (T24).
Discharges occur in high gradient RF structures. They can be isolated in time (single BD) or occur in clusters.
A BD protection system has been developed to intervene on BD clusters.

---
BD Detection and Protection
Detection and Protection:
detection: reflected power > adjustable threshold level (100 kW)
=> fast interlock stops the RF pulse within ~60 μs (pulse ~1000 μs)
=> RF and Beam stopped
Software auto-reset of interlock for the following pulses - assuming an isolated BD
BD cluster detection:
Bin 1 (BD cluster): 3rd BD within 25 pulses
=> Recovery Level 1 (trying a quick recovery ~1 min)
Bin 2 (high BDR): 8th BD within 9’000 pulses (3 hours, BDR ~ 1e-3)
=> Recovery Level 3 (sensitive recovery ~30 min)
Traceability
alarms are generated on interlocks (LASER) + Timber logging

---
Recovery from Breakdowns
General remarks, Beam inhibition:
Recovery: RF field in cavity lowered and slowly ramped-up to nominal level
RFQ needs to be pulsed without beam to avoid beam loss
BIS interlock is kept active during recovery (RFQ BIS user_permit = FALSE)
=> a small but important change was required to separate the RF pulse permit and BIS interlock (both were linked originally)
implementation: RFQ BIS user_permit = AND (original logic, extra FESA bit)
In recovery beam stopper is automatically activated to keep source pulsing

---
Recovery from Breakdowns
Recovery algorithm:
synergy with CLIC high gradient structure conditioning / BD recovery
in Recovery Mode the LLRF Feed-back is opened (open loop).
5 normal levels with different amplitude reduction factors and ramp-up speeds.
Level 1 / 2 shall quickly bring back the RFQ into operation, ~1 / 5 min, deeper levels ramp-up slower from lower amplitudes.
If more than a certain number of BDs are detected during a Recovery Level, the next, more sensitive Recovery Level is entered.
When the nominal amplitude is reached, LLRF feedback is closed and the RFQ is pulsed for a certain time before going back to operational mode.
If too many BDs occur, the RFQ is stopped (Locked state).

---
Recovery from Breakdowns
Level	new amplitude	# pulses hold	ΔA / A / ramp-up	# pulses FB closed	sum pulses	approx. time	allowed BDs
1	95% * Anominal	2	0.5%	20	40	1 min	2
2	95% * Acurrent	4	0.25%	50	130..210	~5 min	3
3	95% * Acurrent	10	0.1%	200	700..1700	15 to 35 min	5
4	75% * Anominal	10	0.1%	500	3000	60 min	7
5	to keep RFQ pulsing while expert is contacted
	65% * Anominal	10	0.1%	1000	4500	90 min	11
locked	emergency stop
=> Refinement intended after first experience in operation

---
Recovery from Breakdowns
Level	new amplitude	# pulses hold	ΔA / A / ramp-up	# pulses FB closed	sum pulses	approx. time	allowed BDs
1	95% * Anominal	2	0.5%	20	40	1 min	2
2	90% * Acurrent	4	0.25%	50	210..280	4..6 min	3
3	90% * Acurrent	6	0.1%	200	800..1600	16 to 32 min	5
4	75% * Anominal	8	0.1%	250	2250	45 min	7
5	to keep RFQ pulsing while expert is contacted
	65% * Anominal	10	0.1%	1000	4500	90 min	11
locked	emergency stop
=> 1st Refinement, 11.12.2020

---
Inspector Panel, normal operation

---
Inspector Panel, in Recovery

---
Illustration
normal operation => 3 BDs => Recovery Level 1
2 BDs in Level 1 => Level 2 (early implementation error ≥ 2 BDs instead of > 2 BDs)
~14:05 feed-back closed, ~14:06 back to normal state = ready to accelerate beam
[blue curve: amplitude factor (gain), red spikes: BDs,
yellow curve: state of recovery class: 10 = normal, 20 = Recovery Level 1, 21 = Rec. Level 2]

---
Illustration
Sa 5 Sep. 2020: Operator increased pulse length by accident => many BDs
Recovery down to Level 5 (very short Level 1) [blue: amplitude factor, red: BDs]
29 BDs in total, 4 more and RFQ would have stopped pulsing (locked state)

---
Illustration
Waveform of a good pulse (green) and pulse where BD protection interlocks (yellow).
Time axis (abscissa) in sample number, 1’400 samples <=> 1’000 μs.
Interlock stops the feeding RF power in about 60 μs.

---
Breakdowns 2019 to 2021
2019 no BD protection, nominal amplitude 3.03 MV
2020 BD protection, re-calibration, nominal amplitude 3.06 MV => running above nominal
=> number of BDs significantly reduced by avoiding BD clusters - even with higher amplitude
BD clusters dominated by external events (RFQ tuning [glitches, water cut])

---
Breakdown-rate
The BD Protection and Automatic Recovery system was introduced before the start of the 2020 Run.
It worked so well that the decision could be taken to operate the RFQ above the design level (10% in power).
Despite the higher amplitude, the Breakdown-rate decreased by nearly 1 order of magnitude.

---
Breakdown Clusters
5. Sep. 2020 (Saturday): Operator by accident increased pulse length => very high BDR,
protection went to Level 5 (a few BDs left to reach the emergency stop), 29 BDs in total
25. Sep. 2020 (Friday evening): RFQ tuning stopped => 16 BDs + 7 BDs when switching back on
23. Oct. 2020 (Friday evening): RFQ tuning stopped => 11 BDs + 6 BDs when switching back on
3. Dec. 2020: “normal” BD caused a cluster of 18 BDs, recovery down to Level 3
6. Dec. 2020: “normal” BD caused a cluster of 9 BDs, recovery down to Level 2
8. Dec. 2020: “normal” BD caused a cluster of 33 BDs, recovery down to Level 4
----------------------------------------
12. Mar. 2021: (undeclared) CV intervention, tripped RFQ tuning => a lot of BDs due to detuning, 28 BDs
17. Jun. 2021: electric glitch, RFQ tuning tripped => recovery down to Level 4, 19 BDs
4. July 2021: “normal” BD caused a cluster of 8 BDs
7. Aug. 2021: electric glitch, RFQ tuning tripped => recovery down to Level 4, 36 BDs

---
RFQ tuning - interlocking
The RFQ tuning consists of a body circuit supplied by CV and stabilised to ±0.1 K and a circuit for the vanes for each of the 3 segments. This later circuit is chilled by CV (stabilised to ±0.5 K) and precisely re-heated (to ±0.1 K) by a PLC system in responsibility of RF. This precision system keeps the RFQ on tune.
The design philosophy was to optimise the performance by the precision system but still be able to run without it as degraded, back-up solution.
However, increasing the RFQ amplitude above the design amplitude increases the risk of BDs and hence a deterioration in tuning can quickly cause BDs and
BD clusters.
It is too much demanded from operators to survey the RFQ tuning on top of their other duties so that interlocking the RFQ on interruptions of the tuning system is seen as a good solution (RF + OP)
a) to protect the RFQ and
b) to make the operator aware of the issue (manual reset required for restart).

---
Feedback from OP
Feedback from OP (Piotr Skowronski):
“In my view, the RFQ protection system works very well and it does not act too often. I believe the amplitude can stay like this.”
[ amplitude 3.20 MV instead of 3.06 MV nominal (+5% in amplitude, +10% in power) ]
“I think beam operation should be blocked if RFQ is not tuned. I guess it would be safer if power would be limited until the tuner shows OK state.”

---
Conclusions
A system to detect Breakdowns (BDs) and to interlock within concerned pulses has been implemented.
On isolated BDs the interlock is automatically cleared to continue beam operation.
On BD clusters or high BDRs the RFQ is switched automatically into a Recovery mode.
Beam is inhibited during Recovery via RFQ BIS user_permit=FALSE.
5 Recovery Levels with different amplitude reduction factors and ramp-up functions recondition the RFQ.
If still too many BDs occur, the RFQ will stop pulsing.
During the 2020 and 2021 runs the Protection and Automatic Recovery system intervened several times and acted as designed.
The RFQ is seen to be well protected, so that the decision could be taken to run the RFQ about 10% above the nominal power level in order to reduce the H- beam loss inside the RFQ.
Despite the higher amplitude, the Breakdown-rate decreased by nearly an order of magnitude compared to previous runs thanks to the BD Protection and Automatic Recovery system.
In order to further decrease the Breakdown-rate, an interlock mechanism on the tuning system state is being implemented.

---
RFQ parameter
“Linac4 RFQ Design, Contruction, Commissioning, and Operation”
(presentation, Carlo Rossi)
https://indico.cern.ch/event/754020/