## Slide 1
Measurement of absolute quantum efficiency
Method: measure DC photocurrent for monochromatic illumination. Normalize light intensity with a photodiode of known quantum efficiency.
The set-up is suited for any kind of photodetector (PMT, MA-PMT, MCP-PMT, HPD) up to 5 inch diameter which can stand a DC photocurrent of several 10 nA and allows for direct electrical contact with the photocathode.
Xe arc
discharge lamp

## Slide 2
Measurement procedure
Discussion of principle and components (15’)
Familiarize with monochromator, picoampmeter and control software (10’)
Measure IPD(l) for 200 < l < 800 nm
Measure IDUT(l) for 200 < l < 800 nm
Subtract dark currents (if any)
Calculate QE
Optional: Perform measurement in centre and edge of photodetector
Discussion of result, error sources, precision
Depending on used degree of automation, the whole measurement can be completed in 1- 1.5h.
The set-up can be used by max. 3 students .
Special technical requirements: cooling water for Xe lamp (just tap water)