## Slide 1
Detection developments at n_TOF
a quick tour through the challenges and n_TOF solutions to (n,*) measurements
Carlos GUERRERO
Universidad de Sevilla, Seville, Spain
Centro Nacional de Aceleradores (CNA), Seville, Spain

## Slide 2: Detection developments at n_TOF
Disclaimer:
No time to include every single detector system
No space to include the corresponding references
Limited to detection systems. Analysis methods and techniques not covered
(n,f)
(n,g)
(n,chp)
Day-to-Day cross sections measurement
Others …
Dealing with high radioactivity
Pushing the high En limits
The challenges
The reaction channels
The n_TOF solutions!

## Slide 3: Every detector is connected to the n_TOF DAQ
n_TOF Phase 1: one of the firsts of its kind
~54 flash-ADC (FADC) channels with 8-bit and 1 GS/s with 8 MB memory
Digitized movies stored permanently (CASTOR) for offline Pulse Shape Analysis (PSA)
n_TOF Phase3 Upgrade:
8 => 10-12 bits && 8 => 64 MB && 1 => 10 Gb/s (PCIeX4)
More performant and versatile PSAs

## Slide 4
(n,f)
challenges and (n_TOF) solutions

## Slide 5: Current day-to-day fission cross sections
The challenge
The n_TOF solution
Need of a stable, robust, easy to use/analyze fission detector
[for s(n,f) and beam monitoring]
Mesh
Anode
traise~20ns
FWHM~150ns
n_TOF Micromegas MGAS (micro-mesh gaseous structure) detectors:
Minimal material (almost ”transparent” for neutrons)
High detection efficiency (100% in fission studies)
Radiation durability - important for highly radioactive samples
Fast response & time resolution
MGAS@n_TOF ===> Beam monitoring with 235U(n,f) + s(n,f) of 230Th, 240,242Pu + …

## Slide 6: Pushing the high En limit
n_TOF Parallel Plate Avalanche Counters (PPAC) detectors:
Low (1-10mb) pressure: fast ion mobility => excellent timing (200 ps resolution)
Thin anode/cathode (1-2 um Al-Mylar): transparent => low sensitivity to g-flash
Position sensitivity: 2mm pitch gives 300mm resol. => measure angular correlations
The challenge
The n_TOF solution
MGAS
few MeV
1 1 1
2 2 2
3 3 3
PPAC@n_TOF ===> Beam monitoring + s(n,f) and ang. corr. of natPb, 209Bi, 233U, 232Th (1 GeV!)

## Slide 7: Seeing all fission observables simultaneosuly
The challenge
The n_TOF solution
Fission is very rich in observables!
Fission fragments:
    A and Z yields
Prompt emission of:
    gammas: energy and multiplicity
    neutrons: multiplicity (Nubar)
Main axis ( 1 & 2)
e- detectors for FF ToF (10 mbar C4H10):
  MCP start + MWPC stop
IC (100 mbar C4H10,15 segments)
Secondary axes (3 & 4)
e- detector for FF timing
  MCP only
IC (100 mbar C4H10 isobutane)
Scintillators: Array of NaI and LaBr3 detectors
FF@Bragg
prompt g
STEFF@n_TOF ===> 235U and 239Pu experiments
STEFF:
SpecTrometer for Exotic Fission Fragm.

## Slide 8: Measuring relative to 1H(n,p) at high En
The challenge
The n_TOF solution (II)
235U(n,f) standard only up to 200 MeV,
how can it be extended above 20 MeV? masure abve 200 MeV
2 silicon detectors 300 μm thick
4 plastic scintillators
=> 5, 30, 60 and 60 mm thick
Radiator - C2H4
E detector
ΔE detector
proton
Pyramidal shape
plastic scintillators (EJ-204)
PRT@n_TOF: 235U(n,f) combined with PPAC

## Slide 9
(n,g)
challenges and (n_TOF) solutions

## Slide 10: Neutron sensitivity
The challenge
The n_TOF solution
Neutron scattering (sample→ detector) background
n
n
n
g
g
g
g
g
Al/SS→Carbon Fiber
g
Total Energy Detectors (TED):
Condition I: Low efficiency detectors egi<<1
Condition II: The efficiency is proportional to Eγ
  (by means of the ¿accurate? PWHT)
C6D6@n_TOF: 35Cl, 53Mn, 54,57Fe, 58Zn, 62,63Ni, 90,91,92,93,94,96Zr, 69,71Ga, 72,74,76Ge, 80Se, 89Y, 88Sr, 140Ce, 147Pm, 171Tm, 203,204Tl, 204,206,207Pb, 209Bi, 236,238U, 242Pu, 244,246Cm

## Slide 11: Pushing the high En limit (@EAR2?)
The challenge
The n_TOF solution
The upper En limit for (n,g) at EAR2 is due to:
High counting rate
Huge g-flash
C6D6
(1”x1”x3”)
sTED@n_TOF ===> beam tests ongoing
n_TOF segmented Total Energy Detector (sTED)
Physical segmentation reduces the large energy deposition due to the flash and the counting rate in individual each detector, while keeping the overall efficiency.
Smaller readout devices (PMTs and or SiPMs) for mitigating the interaction of the flash with the device itself
200 keV
12 keV

## Slide 12: Low signal to background cases
The challenge
The n_TOF solution
Everything but g-rays from the sample is background!
True Capture Event
Backgound event
GAMMA IMAGING
Total Energy Detector with g-ray imaging capability (i-TED)
4 detector modules: scatterer (15 mm) + absorber (25 mm)
LaCl3 scintillators
Position sensitive SiPM with PETsys readout electronics
iTED@n_TOF: tests at EAR1 and EAR2, 79Se in 2022
4 iTEDs

## Slide 13: Unstable isotopes: low-mass & high-activity
The challenge
The n_TOF solution
Activity and limited mass of the radioactive isotopes of interest in nuclear technology (actinides) and astrophysics (branching points).
=> Require high efficiency
=> Require background reduction
TAC@n_TOF: 233, 234, 238U, 237Np, 240Pu, 241,243Am
Neutron energy
Deposited energy
Multiplicity
n_TOF Total Absorption Calorimeter (TAC):
40 BaF2 15 cm thick crystals => multiplicity mcr
95% solid angle coverage => en,g≈100% & info on Esum
S/B enhancement via conditions on the event’s Esum and mcr.

## Slide 14: Fission background
The challenge
The n_TOF solution
Fission competes with capture, with more and more energetic g-rays emitted in fission than in capture.
=> g-ray background from fission
TAC@n_TOF: 233U, 235U and, soon, 239Pu
Fission tagging system for the TAC
Compact: cylindrical chamber Ø9 cm × 12 cm
Up to 14 samples/detectors
Minimum material: 10 µm Al backing + 20 µm Al anodes per target
Fast signals (34 ns FWHM using CF4) for high α-count rates (>1 MBq per anode)

## Slide 15
(n,chp)
challenges and (n_TOF) solutions

## Slide 16: Day-to-day (n,chp) cross sections
The challenge
The n_TOF solution
The challenge
The n_TOF solution
Need of a stable, robust, easy to use/analyze detector
for s(n,p/a/t) and beam monitoring]
Mesh
Anode
MGAS@n_TOF ===> Beam monitoring with 10B(n,a) + s of 14N(n,p), 33S(n,a), 35Cl(n,p)

## Slide 17: Pushing the high En limit
The challenge
The n_TOF solution
MGAS
few MeV
16O(n,a)
235U(n,f)
n_TOF DFGIC with gated Charge Sensitive Preamplifier (CSP)
A twin Double Frisch Grid Ionization Chamber
Gas in the chamber acting as a gaseous 16O target
PS triggered switch applied to the CSP
Results from nELBE
Gated DFGIC@n_TOF: tests ongoing for 16O(n,a)

## Slide 18: Dealing with high radioactivity in (n,a/p)
The challenge
The n_TOF solution
Silicon detectors in the neutron beam
3x3 cm2 active area, 140 μm thickness
2 7Be targets with ∼18 GBq each (∼1.4 μg)
det 1
det 2
det 3
det 4
sample 1
sample 2
neutrons
α
α
α
α
Dealing with the activity from GBq targets.
=> Unambiguous identification of the reaction products.
E
neutrons
p
ΔE
Silicon detectors OFF the neutron beam
3x3 cm2 active area, 20 and 140 μm thickness
7Be target with ∼1 GBq each (∼0.1 μg)
Discriminate background 7Be γ and 7Be(n,p)
Discriminate background 7Be γ and 7Be(n,a)

## Slide 19: Summary
Pourpose | Challenge | n_TOF solution
Monitoring | Beam intensity | SiMon & MGAS
 | Beam profile | XY-MGAS / Timepix / StrippedSili
(n,f) | Original day-to-day s(n,f) | FIC-0,1,2,JRC
 | Current day-to-day s(n,f) | MGAS
 | Pushing the high En limit | PPAC
 | Measuring relative to 1H(n,p) at high En | 2 x Proton Recoil Telescope
 | Look for all fission observables | STEFF
(n,g) | Neutron sensitivity | Carbon fiber C6D6
 | Low S/B | iTED
 | Low mass + High radioactivity | TAC
 | Fissile targets | Fission tagging
 | Pushing the high En limit | sTED
(n,chp) | Current day-to-day s(n,chp) | MGAS
 | Pushing the high En limit | DFGIC with switch
 | Dealing with high radioactivity | Si-sándwich
Thank you for your attention
*Not exhaustive