## Slide 1
Event Overlay Tools
September 27, 2010
Christian Grefe, Peter Schade
CERN
Notes: 1

## Slide 2
Introduction
Need to study impact of machine induced backgrounds:
  Incoherent pairs, γγ -> hadrons, parallel muons, …
Signal and background events are simulated separately
Study different background conditions -> need flexible overlay tools
Merging of LCIO files after full simulation and before digitization
  Merge collections
  Displace hits/entries in time
  Variable number of BX
  Multiple background files (different kinds of background)

## Slide 3
LCIO Merge
Command line tool with basic functionality
Assumes identical content in both (or more) files
Or with an input file to steer the overlay process
lcio merge -f file1.slcio -f file2.slcio -o file3.slcio
inputFile.txt :
/path/to/file1.slcio, nEvt, time offset, time between two events
/path/to/file2.slcio, nEvt, time offset, time between two events
...
lcio merge -i inputFile.txt

## Slide 4
Marlin Overlay
Processor inside Marlin with almost same functionality
Possibility to add random number of background events
Parameters:
Automatically rewinds overlay samples if they run out of events
InputFileNames (StringVec) – list of background LCIO files
NumberOverlayEvents (int) – Number of events taken from each background file
runOverlay (bool) – instead of setting number of overlay events, use all background events from a run
expBG (double) – add additional background events based on poisson statistics
CollectionMap (StringVec) – pairs of collection names to be merged

## Slide 5
Marlin OverlayBX
Processor inside Marlin with very special functionalities for VTX and TPC collections
Expects a background file per BX
Parameters:
BackgroundFileNames (StringVec) – list of background LCIO files
MaxNumberOfEventsPerFile (int) – Number of signal events merged with the background
BunchCrossingTime (float) – time between two BX
TPCDriftvelocity (float) – displace TPC hits
MaxBXsTPC (int) – maximum numer of BX overlayed in TPC
PhiRotateTPCHits (bool) – randomly rotate background TPC hits in phi
VXDLayerReadOutTimes (FloatVec) – Integration times of different VTX layers
TPCCollection (StringVec) – Name of TPC collection
VXDCollection (String) – Name of VTX collection
RandomSeed (int) – Random seed for phi rotation
MergeCollections (StringVec) – pairs of collection names to merge

## Slide 6
LCSim OverlayEvents
Based on the Marlin Overlay processor
Parameters:
Automatically rewind background files if they run out
Currently still in lcsim-contrib, will move to lcsim soon
lcioFile (String) – adds an overlay file (can be used multiple times)
bunchCrossings (int) – number of background events to merge into the signal
bunchSpacing (double) – time between two BX
convertCollection (StringVec) – pair of collection names (only use if not identical in signal and background files)
mergeOnlyCollections (StringVec) – list of collections to merge
ignoreCollections (StringVec) – list of collections not to merge
outputFile (String) – the output lcio

## Slide 7: Status
Overlay tools exist in both framework
  Basic functionality available: merging of different types of collections
  Most studies can already be done
Possible improvements:
  Make a clean interface
  Let digitization drivers/processors steer the overlay for their input collections
  Respect the full bunch train structure (especially for CLIC)
    Study differences in when the signal event takes place
    Include backscatters and late hits from everything that happened before

## Slide 8: Possible User Interface
Number of bunch crossings in a train
Time between bunch crossings
Time of signal event (user defined or random)
Multiple lists of background files
  Each list represents one source of background events
  One event represents one BX, could introduce weight, then n events are taken instead of 1 per BX
Mapping of collection names
Which collections to overlay
One integration time per hit collection
Treat layers within one hit collection differently
Handled by the digitization

## Slide 9: How to read out a bunch train?
Not all subdetectors are read out at the same time
Readout times are shifted by time of flight (to the actual hit)

## Slide 10: How to read out a bunch train?
The actual readout window is selected by the signal event

## Slide 11: How to read out a bunch train?
Late hits from earlier background events have to be taken into account
Everything after the readout window can be omitted
What if signal event spills over to the next time window?

## Slide 12: Outlook
Implement modified overlay processors in Marlin & org.lcsim
  Simple and streamlined interface
  Remove multiple definitions of same values -> use digitization
  Digitization drivers have to register with a digitization handler or with the overlay processor and have to provide accessor functions