## Slide 1
Jan Buytaert
Preliminary ideas on ECS.

## Slide 2: Subjects:
High & low voltage systems.
Detector temperature monitoring.
Interlock system.
Motion, cooling and vacuum.
FE electronics configuration & monitoring.

## Slide 3: HV & LV
Plan to reuse the current ISEG (HV) and CAEN (LV) for VELOpix.
  same number of detector stations.
  similar power consumption
  Very flexible programmable supply voltages.
  Remote control by CAN bus (ISEG) and ethernet (CAEN).
    Keep for the upgrade.

## Slide 4: Detector temperature monitoring.
Currently: 6 temperature boards (64 channels/board).
  Read NTC installed on modules (2) & repeater boards (2).
Can be reused for the upgrade.
On board ELMB with CAN bus remote control.
Hardware detection of alarm conditions. Cabled to interlock system.

## Slide 5: Interlock system.
Central handling of all alarm conditions.
  Cabled input/ouput from/to all systems : module temperature, vacuum, cooling, motion, emergency button.
Pure hardware logic.
  No ‘software’, only FPGA firmware.
  Currently no remote monitoring. (-> LED’s and web camera)
    Could be implemented in future.

## Slide 6: Motion, vacuum and cooling.
Based on PLC system.
Will be reused for the upgarde.
No plan to change the remote control interface.

## Slide 7: FE electronics configuration & monitoring.
Currently this is done through 16 ‘Control boards’.
  Control:
    TFC Timing adjustments.
    Beetle configuration (I2C)
    Test pulse & reset generation,
    Power-on/off of frontend supply voltages.
  Monitoring:
    FE supply voltages and over-current state.
  Remote control by specs slave.
Will not be reused.
  Hopefully will be done by GBT-SCA.

## Slide 8: VELO upgrade.
Total of 2x26=52 modules in full system.
1 GBT ‘downlink’ per module for ECS and TFC.
Vacuum tank
< 48 Diff Cu lines @3.2Gb/s ~ 1m
Low mass
vacuum feed-throughs
Electro-optical
< 48 optical links
@3.2Gb/s ~60m
½ Tell 40
10Gb interface
Module readout concept :
1 optical down link
ECS & TFC

## Slide 9: FE electronics configuration & monitoring.
GBT SCA remarks:
  Radiation hardness ? On module we need 370Mrad !
    If not sufficient, then it must be outside vacuum tank on electro-optical boards.
  Temperature and voltage monitoring with built-in ADC’s.
  I/O levels must be directly compatible with FE asic.
    LVDS (1-1.6V) comaptible with Vdd=12.V ?
  I2C. OK
    16 channels available: one I2C per ASIC.
    Addressing capability : RAL indirect addressing mode ?
    Block read and write is a must for pixel configuration !
      O(10bit) per pixel -> O(1Mbyte) per asic->O(12Mbyte) per module .
  We will not used:
    Memory bus and parallel I/O bus.
    JTAG.
  Use digital output for test pulse, resets, power on/off.
  Optical link monitoring/control ? i2c ?