## Slide 1: East Area Beam Commissioning Update
M. Fraser on behalf of the PS commissioning team
132nd EATM 14/9/2021

## Slide 2: Extraction Setup Status
High-level parameters used to adjust extraction rate (e.g. PSBEAM/QH_PFW)
Septa (SEH23 and SMH57) aligned with beam and spiral step maximised (within H aperture limit apparently in SS41)
Extraction beam loss acceptable from RP perspective (below acceptable limits for maximum proton flux)
Loss optimisation studies to get underway: higher beam loss at start of spill in ring and upstream part of line: to be understood
Fast extraction setup and ready for BCT / XSEC BI calibrations
  Successful test to increased slow bump 57 amplitude to reduce fast extraction beam loss
SEH23 anode/cathode movement interlock perturbed by beam induced noise on AD cycle (masked for now, ABT investigating)

## Slide 3: East Area Primary Transfer Line Status
Reverted to pre-LS2 quadrupole settings (using new magnet transfer functions) to improve transmission, permitting steering to T8:
  What should be the beam spot size, do we have BTV references from the past?
East Area shielding validated with RP:
  All destinations (East Dump, T8, T9 and T10/11) tested up to 50e10 ppp
  Now increasing number of cycles in super-cycle up to flux limit of 6.6e10 p/s
Inversion F62.DHZ02 <-> F62.DVT02
  Update needed in Layout Database
ZT8.BHZ03 is non-PPM was pulsing on T9 and T10/11 when both destinations played:
  T8 in super-cycle with other destinations, not obvious on BLM but on RP monitors
Realignment of IRRAD made set-up and steering tricky:
  Beam noticeably lower vertically on BTV with lower beam loss and high transmission
Hysteresis effects clearly visible when switching F61.BHZ01 to the East Dump:
  Effect can be mitigated, tested with EPC by pushing magnet into saturation after switching to the dump… to be checked and tested when in physics and producing secondary beams

## Slide 4: East Area Beam Instrumentation
BLM’s working well, also publishing time dependency of beam loss
Spill monitor (BCCGA) working well (we have 2.5 kHz)
  Take care: its signal is dominated by beam loss at extraction
XSEC needed for transmission estimation, commissioning on-going:
  BE-EA provided calibration factors for sensors
  First XSEC is giving very high count rate: further checks needed by SY-BI
Fast BCT’s being tested using the fast extracted beam:
  Ringing of the signal (possible reflections) being investigated by SY-BI
  XSEC fast acquisition system ready for cross-calibration
IRRAD BPM’s now working well
IRRAD BTV working best when lights are OFF in the zone
CHARM MWPC: gas connection during the TS, ready for beam from Friday

## Slide 5: Longer term activities and follow-up
Implementation of AutoSpill (development from SPS)
Optics measurements in F61/62/63 using BTV’s
Implementation of stray fields in extraction simulations to assess impact on initial beam parameters
Systematic cross-calibration of BI devices
Ion cycle setup
Low energy slow extraction set-up with protons (2 GeV) in MD
  Repeated for ions in MD
Implementation of COSE
Implementation of empty bucket channelling