## Slide 1: TCLPX – TCTPXH – TCSPM Bake out systems
L. Gentini
WP5.2 Technical meeting

## Slide 2
TCLPX heating JACKETS
Pump jackets
Body jackets
Bellow jackets
The jackets must be installed on the collimator before to put the collimator on its support.
7 electrical lines are used on the hypertac.

## Slide 3
BODY JACKETS ASSEMBLY - LHCTCLPX_T0001
25 mm thickness.
Just one single jacket for the bottom side and the two lateral sides.
For space matters on jacket has just one electrical connector.
ION PUPM JACKETS - LHCVEJEC0006
25 mm thickness.
The two jackets of the ion pumps are connected in series to reduce the number of electrical connections on the hypertac.
BELLOW JACKETS - LHCTCLPX_T0019
10 mm thickness.
TCLPX heating JACKETS

## Slide 4
Pump jackets
Body jackets
Bellow jackets
The jackets must be installed on the collimator before put the collimator on its support.
7 electrical lines are used on the hypertac.
TCTPXH heating JACKETS

## Slide 5
BODY JACKETS ASSEMBLY - LHCTCLPX_T0011
25 mm thickness.
Just one single jacket for the bottom side and the two lateral sides.
For space matters on jacket has just one electrical connector.
ION PUPM JACKETS - LHCVEJEC0006
25 mm thickness.
The two jackets of the ion pumps are connected in series to reduce the number of electrical connections on the hypertac. (Same of TCLPX)
BELLOW JACKETS - LHCTCLPX_T0019
10 mm thickness.
Same design of TCLPX
TCTPXH heating JACKETS

## Slide 6
2nd beam jackets
Body jackets
The jackets must be installed on the collimator before put the collimator on its support.
6 electrical lines are used on the hypertac.
TCTPXV heating JACKETS

## Slide 7
BODY JACKETS ASSEMBLY - LHCTCTPX_T0001
25 mm thickness.
Two jackets for the bottom side and the two lateral sides.
2nd BEAM JACKETS – LHCTCTPXV_0104
20 mm thickness.
TCTPXV heating JACKETS
EXTREMITY JACKET NECESSARY ?

## Slide 8
BODY JACKETS ASSEMBLY – LHCTCSPM0105
6 electrical lines are used on the hypertac.
DESIGN IMPROVEMENT
A lot of eating is lost in the pick-up area:
There is not heating on the tank between the pick-up
There is not heating on the pick-up flanges.
SOLUTION 1
Remove the aperture between the pick-up.
Close the gap between the pick-up (20 mm of jacket). This solution does not change the design
SOLUTION 2
Remove the aperture between the pick-up.
Put a collar on the lateral jacket to heat also the pick-up flanges. For this solution, the pick-up of the cartridge must be moved by 10 mm.
TCSPM bake out system improvement 1
SOLUTION 1
SOLUTION 2

## Slide 9
MKT CHAIN SYSTEM
By conduction, the extremities of the tanks are cooled down.
A solution could be to add tow thermal insulating plates between the MKT system and the tank (2 or 3 mm) as we have done on the IR collimators.
To do not decrease the stroke of the MKT, the space must be obtained on the thickness of the MKT plate. The MKT system must be slightly modified.
TCSPM bake out system improvement 2

## Slide 10: Thank you for your attention

## Slide 11
Hypertac – bake out connector