## Slide 1: CERN's accelerator complex Connecting the dots…
Rende Steerenberg
15 February 2022

## Slide 2: Content
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 3: Content
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 4: The CERN Accelerator Complex

## Slide 5
Linac 4
H- ion source at 95 keV
Accelerates beam up to 160 MeV
The chopping scheme allows removing some of the Linac bunches to make the beam fit into the PS Booster RF buckets
Pulse rate 1.2 s

## Slide 6
PS Booster
1st Synchrotron with 4 superposed rings
Circumference of 157 m
Proton energy from 160 MeV to 2 GeV
Can cycle every 1.2 s
Each ring will inject over multi-turns, using charge exchange injection
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil

## Slide 7: The CERN Accelerator Complex

## Slide 8: PS
The oldest operating synchrotron at CERN
Circumference of 628m
  4 x PSB circumference
Increases proton energy from 2 GeV to max. 26 GeV
Cycle length ranges from 1.2s to 3.6s
Many RF systems allow for complex RF gymnastics
Various types of extractions:
  Fast extraction
  Multi-turn extraction (MTE)
  Slow extraction

## Slide 9: SPS
The first synchrotron in the chain at ~30m under ground
Circumference of 6.9 km
  11 x PS circumference
Increases proton beam energy up to 450 GeV with up to ~5x1013 protons per cycle
Provides slow extracted beam to the North Area
Provides fast extracted beam to LHC, AWAKE and HiRadMat

## Slide 10: The CERN Accelerator Complex

## Slide 11: LHC
Situated on average ~100 m under ground
Four major experiments
Circumference 26.7 km
Two separate beam pipes going through the same cold mass 19.4 cm apart
150 tons of liquid helium to keep the magnets cold and superconducting

## Slide 12
LHC
1232 main dipoles of 15 m each that deviate the beams around the 27 km circumference
858 main quadrupoles that keep the beam focused
6000 corrector magnets to preserve the beam quality
Main magnets use superconducting cables (Cu-clad Nb-Ti)
12’000 A provides a nominal field of 8.33 Tesla
Operating in superfluid helium at 1.9K

## Slide 13: Content
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 14: The LHC Cycle
6.5 TeV
450 GeV
Time
Injection
Ramp
Squeeze
&
Adjust
Stable beams for physics
Dump
&
Ramp down
= Field in main magnets
= Beam 1 intensity (current)
= Beam 2 intensity (current)

## Slide 15: Filling the LHC & Satisfying Fixed Target users
1.2 seconds
PSB
PS
SPS
Time
= Field in main magnets
= Proton beam intensity (current)
= Beam transfer
To LHC clock-wise or counter clock-wise
450 GeV
26 GeV
1.4 GeV

## Slide 16: Content
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 17: The LEIR Accelerator as Example
Building 150

## Slide 18: Make Particles Circulate
Main Dipoles
Main Dipoles
Main Dipoles
Main Dipoles

## Slide 19: Deviating Charged Particles
Magnetic Lorentz Force:
Moving charged particles are deviated
in a magnetic field

## Slide 20: Oscillatory Motion in the Horizontal Plane
Horizontal motion
Different particles with different initial conditions in a homogeneous magnetic field will cause oscillatory motion in the horizontal plane  Betatron Oscillations
Particle B
Particle A
2π
0
Horizontal
displacement
Machine circumference
Two charged Particles in a homogeneous magnetic field
Particle A
Particle B

## Slide 21: Oscillatory Motion in the Vertical Plane
The horizontal motion seems to be “stable”…. What about the vertical plane ?
Many particles many initial conditions
Vertical
displacement
Many different angles
 s

## Slide 22: Focusing Particle Beams, a bit like a lens
Force on particles
Focusing Quadrupole
De-focusing Quadrupole
Rotated by 90º
QF
QD
QF

## Slide 23: Focusing Particle Beams in LEIR
Main Dipoles
Main Dipoles
Main Dipoles
Quadrupoles

## Slide 24: Accelerating Particles, Using Electrical Fields
Accelerating
Cavity

## Slide 25: Radio Frequency Cavity
Charged particles are accelerated by a longitudinal electric field
The electric field needs to alternate with a harmonic of the revolution frequency

## Slide 26: ….and quite some more…
Beam instrumentation to measure beam properties
  Beam intensity
  Beam size
  Luminosity
Possible limitations
  Machine imperfections
  Collective effects and instabilities

## Slide 28: ISOLDE / HIE-ISOLDE
The PSB proton beam impinges on a target producing a range of isotopes
Two mass separators (GPS & HRS) allow selection of isotopes
The post acceleration of isotopes is being extended
  REX, normal conducting accelerating structures
  HIE-ISOLDE, super conducting LINAC

## Slide 29: AD-ELENA
Receives fast extracted proton beam from PS at 26 GeV/c on a target
Every million protons yields about one usable antiproton at 3.5 GeV/c.
AD decelerates beam in stages down to 5.3 MeV
ELENA will further decelerate down to 100 keV
Experiments:
  ASACUSA, ALPHA, AEGIS, BASE, GBAR

## Slide 30: LHC: Luminosity
Maximise Luminosity:
Bunch intensity
Transverse beam size
Beam size at collision points (optics functions)
Crossing angle
Machine availability
Intensity per bunch
Beam dimensions
Number of bunches
Geometrical
Correction
factors