## Slide 1: Dr. Andrew Grimshaw Lancium Compute Emeritus Professor of Computer Science, University of Virginia September 8, 2022
Decarbonizing Scientific Computing

## Slide 2: Agenda
The message
The renewable transformation of the Texas electricity markets
The challenges of renewable power
Addressing the challenges
Lancium
OSG/CMS and CVMFS

## Slide 3: The Message
Renewables are the least expensive way to produce power in the world today.
The pace of renewable deployment is staggering.
  And gated only by the ability of electrical grids to safely absorb the power
Controllable loads, particularly loads that can be rapidly reduced, are critical to maintaining grid stability in the presence of non-constant solar and wind power.
Computation can be used as the controllable load.
If we, as a community, can adapt a bit, there are gigawatts of very inexpensive, green, electricity available.
1: “Renewables 2020: Analysis and forecast to 2025”, International Energy Agency
2: Lazard, Levelized Cost of Energy and Levelized Cost of Storage – 2020

## Slide 4: The Renewable Transformation - Texas

## Slide 5
Notes: Note, this is peak production, guaranteed never to exceed

## Slide 6: ERCOT’s Rapid Renewable Generation Growth...
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Coal | 0.37 | 0.37 | 0.37 | 0.4 | 0.39 | 0.34 | 0.37 | 0.36 | 0.28 | 0.29 | 0.32 | 0.25 | 0.2 | 0.18 | 0.19
NatGas | 0.45 | 0.43 | 0.42 | 0.38 | 0.4 | 0.45 | 0.41 | 0.41 | 0.48 | 0.44 | 0.39 | 0.44 | 0.47 | 0.46 | 0.43
Other | 0.02 | 0.02 | 0.02 | 0.01 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Nuclear | 0.13 | 0.13 | 0.14 | 0.13 | 0.12 | 0.12 | 0.12 | 0.12 | 0.11 | 0.12 | 0.11 | 0.11 | 0.11 | 0.11 | 0.1
Solar | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01 | 0.01 | 0.01 | 0.02 | 0.04
Wind | 0.03 | 0.05 | 0.06 | 0.08 | 0.09 | 0.09 | 0.1 | 0.11 | 0.12 | 0.15 | 0.17 | 0.19 | 0.2 | 0.23 | 0.24
Coal
Natural Gas
Other
Nuclear
Solar
Wind
25% renewable
Percent Energy (MWh) Generated in ERCOT by Fuel Type
Source: ERCOT - Market Data

## Slide 7: West Texas Installed Capacity by Technology
18
In 2021, West Texas load averaged 6GWs with installed capacity at 35GWs (24GWs Wind, 7GWs Solar, 4GWs NatGas)
ERCOT Annual Load Statistics by Zone
Installed Capacity by Technology for Each Zone
West Texas Supply
Wind: 24GWs
Solar: 7GWs
NatGas: 4GWs

## Slide 8: Challenges with Wind/Solar

## Slide 9
Congestion – the load (people, industry) is far from the generation.
They are variable and intermittent.
  Solar is (obviously) diurnal, varies with the seasons, and can change rapidly due to clouds.
  Wind varies constantly, though has trends:
    Stronger in winter than summer. Stronger at night.
As load approaches generation, frequency starts to drift (called an excursion). If load not reduced, or generation increased, generators can be destroyed. The grid operator will not let this happen. They are taken offline to prevent damage. This can lead to blackouts to reduce load.
  Because of this grid operators (ERCOT) keep a significant amount of reserve capacity that can come on-line very quickly (~15s), quickly (~15 minutes), slowly (~3 hrs).
  They pay for this .. It is called an “ancillary” service.
  “Capacity” can be increases of generation OR decrease of load.
In the absence of massive (and expensive) energy storage systems, or the ability to rapidly shed load, or increase production, the amount of renewable power the grid can absorb is limited without risking instability and blackouts.
Challenges

## Slide 10: Addressing the Challenges

## Slide 11: To address congestion and variability we need:
To move load close to production.
  There are many industries that consume huge amounts of power: aluminum, steel (arc furnaces), heavy manufacturing, computing (think about training large models).
  But most require significant infrastructure and logistics to operate. Computation does not.
A controllable load. We need to be able to ramp the controllable load down when the renewable resources are not producing enough – or are forecast to be unable to produce.

## Slide 12: Scientific Computing
Computing meets the criteria
  All we need is power and fiber …
  Most machines can be remotely managed
    Still need hands
Scientific computing specifically
  The bulk of applications are “batch” and have no interactions with humans.
  Users are already used to queueing delays … suspending a job for a bit is not the end of the world.
  Need the ability to stop/start, persist/restart, and migrate. More on this tomorrow.

## Slide 13: Lancium Compute
Unhook Computation from fossil fuels by dancing with the grid.

## Slide 14: Lancium Compute Offerings
HPC PaaS
Custom HPC System
(BYODC)
Custom HPC PaaS
HPC PaaS Offering: Pre-configured HPC Clusters to focus your efforts on HTC and loosely-coupled parallel jobs
Just Bring your Workloads and Data: We make it easy to launch your workloads and retrieve the results for analysis
Customize HPC PaaS: Modify the HW infrastructure of our HPC PaaS to suit your workload needs (and leverage our SW Stack)
Just Bring your Workloads and Data: Leverage our state-of-the-art HPC Software Stack to obtain the PaaS benefit on custom HW Config
Customize HPC: A data center to suit the specific requirements of your HPC environment and business model (HW, SW, cooling, space design etc..)
Carbon-Free Environment: Our clean campuses are powered 100% by renewable energy to host and maintain your HPC Infrastructure
300 MW at Ft Stockton, TX, January 2023.
200 MW in Abilene, TX in May 2023.
Another 1 GW at Abilene approved.
Another 1 GW in approval process in Childress, TX.

## Slide 15: PaaS “run a container” service
Singularity based.
Users can upload their own images or use provided images.
  Users specify the job resource requirements, e.g., 8GB of memory, 8 vCPUs, and the command line to run, files to stage in and out, e.g.,
CLI, API, browser
Single node codes and low-degree parallel MPI – currently up to 96 nodes
lcli job run --name "BLAST Tutorial job” --command "blastp –query \ cow_db_small/cow.1000.protein.faa -db human_db/human.1.protein.faa –evalue 1e-5 \
-max_target_seqs 1 -num_threads 4" --image lancium/blast --cores 4 --mem 8 \
--input-file cow_db_small.tar.gz --input-file human_db.tar.gz

## Slide 16: Lancium Compute Today
Providing ~ 1M vCPU hrs/week for Open Science Grid .. 42M+ vCPU hours so far.
Have run CERN/CMS jobs for US CMS.
Running low-degree parallel MPI CFD jobs for commercial customer– less than 100 nodes.
Rendering for Grid Markets.
Financial & business analytics – essentially ML/AI.

## Slide 17: OSG/CMS and CVMFS
To port OSG onto we Lancium Compute we installed Squid and mounted CVMFS on all compute nodes, and then bound it into Singularity container instances.
  Initially only a single centralized Squid instance.
  Later we went hierarchical with caches on each head node.
  Getting CVMFS operational was pretty easy.
To support CVMFS we installed Frontier everywhere.

## Slide 18: Conclusion

## Slide 19: Our vision is to build geographically dispersed data centers.
In the “wind belt”.
When the wind does not blow in Texas, we’ll migrate north to the Dakota’s, or somewhere else where the wind is blowing, the sun is shining, and the electricity is cheap and carbon-neutral.
Further, with decent forecasting we can begin migrations before the power levels shift, particularly with jobs that are being scheduled for the first time.
Great Plains wind belt.

## Slide 20: END
I believe we are at the beginning of a new industrial revolution; just as oil, gas and coal replaced water and animal power as the power sources of industry, wind and solar will gradually yet surely replace oil and gas as the primary power source.
And just as in the first industrial revolution, it is the efficiency of the new technology that is the main driver in the transition. While it is true that it is in our collective best interest to turn away from carbon-emitting energies, it is the fact that electricity is simply cheaper when generated from renewables that is securing a carbon-free, or carbon-reduced, future.
Lancium is at the center of this transformation.

## Slide 21: Texas West Load Zone
Negative Prices
Breakeven prices for gas

## Slide 22
134-198-248
0-147-147
40-140-210
0-147-147
86-192-142
14-36-71
64-63-64
151-162-182
221-227-236
Batteries and load flexibility can provide short-term balancing throughout the day
Hourly balancing challenge for ERCOT – March 18, 2022 – March 20, 2022
Sources and Notes: ERCOT
Chart: 
GW’s
Solar
Wind
Non-Renewable
3-18-22
3-19-22
3-20-22
61%
39%
6%
94%
11AM
10PM
53%
47%
67%
22%
78%
12PM
8PM
2PM
33%

## Slide 23: Wind power production functions
On the right is data from a small, 150MW, facility in the panhandle near Lubbock.
One rarely gets the full capacity out of a wind system.
Below that is a graph that shows what % of time you get a certain amount of power.
Wind power can vary very rapidly.

## Slide 24
Wind and Solar are complimentary

## Slide 25: Frequency Stability

## Slide 26: Frequency & Inertia
As demand approaches supply
  Frequency starts to drop
  As frequency starts to drop current starts to rise on spinning generators.
  As current starts to rise, so too does temperature and R
  If it goes to far, generators “trip-off”.
  This causes supply to drop – potentially causing a chain reaction.
  To prevent collapse, load is shed by turning off load zones, i.e. blackouts.
Immediate response to stabilize is “Primary Frequency Response”, must be done very rapidly. Typically within 15 seconds.
Longer term response, e.g., within 15 minutes is called “Load Response” or LR. This is addressed by adding more generation or reducing load. Increases and decreases are controlled by the grid operator using computer generated “set points”.
If you can vary your load rapidly, and in response to grid operator signals or price signals, you can be paid for it in the “ancillary markets”.
  This can significantly reduce the price you pay for electricity.

## Slide 27: ….Causing Increased Prevalence of Negative Power Prices…
Depressed power prices can inhibit the buildout of new renewable generation
134-198-248
0-147-147
40-140-210
0-147-147
86-192-142
14-36-71
64-63-64
151-162-182
221-227-236
Frequency of negative real-time pricing
0%
10%
20%
2021
2013
Source: Lawrence Berkeley National Laboratory – Energy Markets & Policy – Frequency of negative locational marginal prices at nodes in the seven organized wholesale markets in the United States
2017
Lancium founded

## Slide 28: Controllable Loads Are the Best Application of Grid Flexibility
Technological options and solutions for flexibility
 |  |  | Flexibility |  | Economy | Quantity | Emissions
Resource designation | Resource type | Start-up time | Run-time | Rampability | Start-up cost (USD/MWh) | Minimum load (% of nominal power) | Emissions intensity
Baseload fossil generation | Generation | 1–10 h | Continuous (Subject to frequent outages) |  | 55 - > 100 | 25–50% | High
Natural Gas Peaker | Generation | 5 min | ~ Days |  | < 1 (excludes degradation) | 20% per unit | High
Batteries | Storage | Seconds | < 4 h |  | 0 (excludes degradation) | 0% | Varies
Load - Traditional demand response | Load | Minutes | Continuous | ~ | N/A | 5–40% | N/A
 | Load | Seconds | Continuous |  | 0 | 0% | Low-Negative
4
Source: International Renewable Energy Agency

## Slide 29
Breakeven on fuel costs for Nat Gas

## Slide 30: Lithium is not the answer
Cost Projections for Utility-Scale Battery Storage: 2021 Update Wesley Cole, A. Will Frazier, and Chad Augustine, National Renewable Energy Laboratory, NREL/TP-6A20-79236 June 2021. For non Li, see https://ambri.com/technology/


At $100/KWh, one GWh of storage costs $100M

## Slide 31: Energy storage (batteries) produced per year (GWh).
https://www.iea.org/reports/energy-storage 2022-09-07