## Slide 1: FCC-EE Multipole Kicker Injection Studies
Patrick Hunchak and Michael Hofer
Thanks to Masamitsu Aiba
Sept. 21, 2021 – FCC-ee Injection #3
Patrick Hunchak

## Slide 2: Injection Into FCC-ee
Top-up injection is necessary to maximize the integrated luminosity of the collider.
Four options have been proposed:
 | On Momentum | Off Momentum
Conventional Orbit Bump |  | 
Multipole Kicker Injection (MKI) | Focus of this Work | 
Wienands, U. “Lepton Collider Operation with Constant Currents”. Proceedings of the 2005 Particle Accelerator Conference. doi:10.1109/pac.2005.1590385

## Slide 3: The FCC-ee Ring
Z-mode operation Parameters
Injection at Point PB
Layout has been updated recently. Shorter Circumference, longer injection straight.
Four operation modes ( Z, WW, ZH, & ) ranging in beam energy from 45.6 to 182.5 GeV.
Z-mode examined first for machine protection aspect (high stored beam energy).

## Slide 4: Machine Parameters
Full Machine
PB Injection Section
Optics matched to allow for both orbit bump and MKI on momentum.
Large at injection point to minimize effective size of the septum.

## Slide 5: Placement of Injection Magnets
MKI is a phase advance after the septum.
Compensation kicker (MKIC) is ahead of the septum.
Locations of the two identical kickers share similar . (191m vs 193m)

## Slide 6: Dynamic Aperture
3 mm eddy current septum
0.1 mm electro-static wire septum
The thinner septum reduces dynamic aperture req. but not previously used.*
Our simulations show plenty of DA for either septum.
Assume that injected emittance = stored emittance.
* M. Aiba “Top-up Injection Status and Next Steps” FCC Week 2021 https://indico.cern.ch/event/995850/contributions/4419415/attachments/2271652/3858072/FCC-ee_Injection_aiba.pdf

## Slide 7: Modelling the Multipole Kicker
MADX does not currently support arbitrary field elements.
Maximum of 20th order polynomial not a good fit.
Split into two fits, for interaction with stored/injected beam.
MKI has zero on-axis field to minimize disturbance of stored beam, large off-axis field to kick the injected beam.

## Slide 8: Simulating Injection
Injection at 20 horiz. phase, beam is off-axis at MKI. (90 phase advance)
MKI kicks injected beam and reduces its angle.
No losses during injection, with preliminary aperture model (no collimators included).

## Slide 9: Injection Effect on Stored Beam at Interaction Point
Without MKIC, increase in would result in factor of ~5 decrease in luminosity.
180 phase advance from MKIC to MKI allows for ‘-I transformation’ which counters effect on stored beam.
Stored beam at MKI location
Stored beam at IP

## Slide 10: Injection Effect on Stored Beam at Interaction Point
Without MKIC, increase in would result in factor of ~5 decrease in luminosity.
180 phase advance from MKIC to MKI allows for ‘-I transformation’ which counters effect on stored beam.
Stored beam at MKI location
Stored beam at IP

## Slide 11: Next Steps
Long term
Error studies – Misalignments, Kicker Misfires, etc.
Beam-beam effects
* M. Aiba “Top-up Injection Status and Next Steps” FCC Week 2021 https://indico.cern.ch/event/995850/contributions/4419415/attachments/2271652/3858072/FCC-ee_Injection_aiba.pdf
Short Term
Other optics (tuned for MKI or off-momentum)
Other operation modes
Other injection approaches (conventional orbit bump)

## Slide 12: Thank you for your attention.
Sept. 21, 2021 – FCC-ee Injection #3
Patrick Hunchak
Gitlab Repository of Project Work:
https://gitlab.cern.ch/phunchak/fccee-injection-studies

## Slide 13: Placement of kickers
FCCee_z_216_nosol_1.seq

## Slide 14
Colors
Backgrounds
Radiant Blue
Flash
Energy
Green
Red
Deep Blue
Use for Layout
Background Blue
Background Purple
Background Yellow
Background Grey

## Slide 15
Graphical Elements
Badges
Infographics
Separation lines 1.5 pt
Arrows
Use light badges on dark backgrounds
Use blue badges on light backgrounds
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!