## Slide 1: Hadron Accelerators
R.W. Aßmann
2011 CERN-Fermilab HCP Summer School Accelerator Beam Physics Group
Beams Department - CERN

## Slide 2: Acknowledgements
W. Fischer (RHIC)
T. Roser (RHIC)
R. Schmidt (LHC)
V. Shiltsev (Tevatron)

## Slide 3: Contents – Lecture 1
Introduction
  Scope of lecture. What is an accelerator? Tevatron, RHIC, LHC. Limits and high tech solutions
What are beams?
Collider goals: Energy, event rate and luminosity
Generating beams
Proton bending
Beam acceleration
Collimation
Beam dump
Colliding beams

## Slide 4: LHC Latest News: 1 fb-1 Produced
Goal for year 2011

## Slide 5: LHC Latest News: 1 fb-1 Produced
Goal for year 2011
LHC performance discussed in lecture 2!
First: Let’s get an idea of hadron accelerators!

## Slide 6: Introduction – Scope of Lecture
There are many hadron accelerators around the world:
  Hadron synchrotron colliders (Tevatron, RHIC, LHC)
  Hadron synchrotrons without collisions (SIS, …)
  Hadron linacs (SNS, UNILAC, medical applications, …)
  Hadron cyclotrons (PSI, medical applications, …)
Very broad field. Here focus on hadron colliders.
As we are at CERN: Particular focus on LHC, including latest news from the control room.

## Slide 7: What is an Accelerator?
The accelerator (“atom smasher”)
A scientific instrument that increases the kinetic energy of charged particles!

## Slide 8: Particle beams find many usages
Use particle beams:
  for scattering experiments (Transmission Electron Microscopy)
  to destroy cancer (medical accelerators).
  to produce high temperature, high density plasmas (plasma physics).
  to produce diamonds (high temperature – high pressure).
  to build a fusion reactor (high temperature – high pressure)
  to initiate a nuclear chain reaction or to get rid of nuclear waste (transmutation).
  to produce neutrons (neutron spallation sources – material science).
  to produce neutrinos (neutrino physics).
  to produce new particles in colliding beam experiments (high energy physics).
Use emitted light:
  for applied research (synchrotron light facilities).
  for lithography (microchip production).

## Slide 9: Accelerators
Beams of charged particles are a very powerful tool for science.
Many applications exist with new ideas coming up regularly.
Different types of accelerators: Protons, anti-protons, electrons, positrons, ions!
Hundreds of accelerators support scientific advance around the globe.
The future of accelerators will be very active and diverse.
RHIC – Collider for ion physics and polarized protons.
Tevatron – Discovery of the top. To be switched off in 2011.
LHC is the new flagship accelerator for high energy physics!

## Slide 10: Technology as Base for Innovation or: The Connection Between a Washing Machine and an iPhone
Steve Jobs:
  “We ended up opting for these Miele appliances, made in Germany... These guys really thought the process through. They did such a great job designing these washers and dryers. I got more thrill out of them than I have out of any piece of high tech in years. ” (1996)
  “We're both busy and we both don't have a lot of time to learn how to use a washing machine or to use a phone - you get one of the phones now and you're never going to learn more than 5 per cent of the features.” (Oct 2005)
Let’s look at the washing machines (accelerators) to make an iPhone (new territory in physics)!
2007

## Slide 11: Tevatron
V. Shiltsev

## Slide 12: Tevatron

## Slide 13: RHIC – a High Luminosity (Polarized) Hadron Collider
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
6:00 o’clock
PHENIX
8:00 o’clock
10:00 o’clock
Jet Target
12:00 o’clock
RF
4:00 o’clock
2:00 o’clock
Operated modes (beam energies):
Au–Au 3.8, 4.6, 5.8, 10, 32, 65, 100 GeV/n
d–Au* 100 GeV/n
Cu–Cu 11, 31, 100 GeV/n
p–p 11, 31, 100, 250 GeV
Planned or possible future modes:
U – U 100 GeV/n
Au – Au 2.5 GeV/n (~ SPS cm energy)
p – Au* 100 GeV/n (*asymmetric rigidity)
Achieved peak luminosities (100 GeV, nucl.-pair):
Au–Au 1551030 cm-2 s -1
p–p 501030 cm-2 s -1
Other large hadron colliders (scaled to 100 GeV):
Tevatron (p – pbar) 351030 cm-2 s -1
LHC (p – p, design) 1401030 cm-2 s -1
EBIS
2 superconducting 3.8 km rings
2 large experiments

## Slide 14: LHC: The Biggest Machine on Earth
Diameter: 27 km
Depth: ~ 100 m below ground surface
LHC: “collider”

## Slide 15: Limit: The Dipole Magnets
Hadron (p) circular collider
Limited by available bending field strength (even SC):
(increase momentum by increasing radius times bending field)
LHC: 8.3 T bending field from 1232 magnets!
56 mm holes for beams.

## Slide 16
At less than 1% of nominal intensity LHC enters new territory. Collimators must survive expected beam loss…
Limit: Power of the Beams
Entry and exit holes of an electron beam impacting on a spoiler
(courtesy P. Tenenbaum)

## Slide 17: High Tech Solutions
These and other challenges are addressed with high tech solutions.
Fundamental research as a driver for technology…

## Slide 18: RHIC: Siberian Snakes

## Slide 19: Tevatron: Electron Beam Lens

## Slide 20: LHC: SC Magnets

## Slide 21: LHC: Super-Conducting RF Cavities

## Slide 22: LHC: Collimators

## Slide 23: What Are Beams?

## Slide 24: The Charged Particle Beam
The accelerator generates, accelerates, transports and delivers beams to the user (e.g. HEP exp).
Beam are transported in ultra-high vacuum.
A beam can consist of individual bunches.
Each “bunch” is an ensemble of charged particles that are grouped together in space and carry the same (very similar) energy.
Radio-frequency fields are used to accelerate particles coherently and to group them together longitudinally.
Magnetic fields are used to guide the beam particles on well defined paths and to focus them into a small transverse area.

## Slide 25: Purpose of accelerators
Transverse area
Length of bunch
(packet)
 Increase kinetic energy of particles
More particles per bunch
Smaller transverse areas
Shorter bunches
 More bunches

## Slide 26: The choice of particle type
Hadron colliders
(p-pbar or pp or ions)
“Discovery” machines
LHC 2009
p-p: 2 × 7 TeV
Pb-Pb: 2 × 2.76 TeV
VLHC study
p-p: 2 × 20 TeV
2 ×100 TeV
Lepton colliders
(e-e+ or gg)
“Precision” studies
B factory upgrade studies
Linear collider study
e+e-: 0.5-1.5 TeV (eg, gg, e-e- options)
mm collider study
2 × 0.15/4.0 TeV
Plasma accelerators

## Slide 27: Tevatron: Anti-Proton Beam

## Slide 28: The LHC Beam
Transverse area
Length of bunch
(packet)
 Increase kinetic energy of particles (3.5 – 7 TeV)
 More protons per bunch (150,000 – 300,000 billion)
Smaller transverse areas (~ 30 mm – width of hair)
Shorter bunches (~ 7 cm)
 More bunches (~ 400 – 2808)

## Slide 29: RHIC: Polarized Proton Beams
Transverse area
Length of bunch
(packet)
UP
DOWN
Proton Spin
Goal: Fully polarized beam, e.g. all spins UP.
Manipulation of polarization vector needed!

## Slide 30: Collider Goals

## Slide 31: High & well-defined beam energies
Einstein’s famous formula:
Mass can be converted into energy!
Collide electrons (matter) and positrons (anti-matter):
If energy is high enough new particles can be produced…
Maximum beam energy
for
highest discovery potential!
electrons
positrons

## Slide 32: Example: Producing the Z-boson
Example from the LEP-ALEPH detector
The Z boson:
Discovered in the SppS with proton and anti-protons (nobel prize C. Rubbia and S. van de Meer 1984)  accelerator innovation!
Detailed studies at the LEP collider with electrons and positrons.

## Slide 33: The need for high event rate
proton
proton
Luminosity L
 Determines how long the PhD student has to wait for his data…
p+p+
p+p+

## Slide 34: Luminosity
Gaussian transverse distributions (neglecting effect of self-focusing of beams):
Neglecting geometric factor F…

## Slide 35: Generating Beams

## Slide 36: Fermilab Example

## Slide 37: Producing the LHC beams
H gas

## Slide 38: Proton bending (circular)

## Slide 39: Governed by Maxwell’s Equations
Very few acceleration issues require quantum mechanics (e.g. spin polarization).

## Slide 40: Lorentz Force F
Longitudinal electrical field to accelerate a particle
Transverse magnetic field to guide a particle

## Slide 41
The electron accelerator in your (past) living room
(1931)
(1938)

## Slide 42
Cathode Ray Tube (CRT) has the basic ingredients of a scientific accelerator:
Particle source
Acceleration scheme
Focusing scheme
Beam steering
Beam observation
Particle momentum p given by Lorentz Force:
dp / dt =

## Slide 43
Transverse deflections:
Transverse magnetic fields are used for beam deflections!
x
y
z
Proton
Depends on particle energy and transverse field
Focusing lattice
Bending (esp. circular)
De-magnifying
Steering
Transverse fields used for:

## Slide 44: The PSI Cyclotron
590 MeV protons, 1.3 MW
Fixed target physics
neutrons, muons

## Slide 45: Cyclotron Principle

## Slide 46: Limited in Energy Reach
Constant bending field B with time  Radius R will change during acceleration (increase of momentum p): p = R e B
Solution: Increase bending field synchronous with momentum gain  constant radius  large rings with a vacuum pipe become possible.
See also: Large accelerators (big R) are required to reach high momentum if bend fields are limited!
Large synchrotrons (LHC, …).

## Slide 47: Dipolmagnet Coils in Synchrotrons

## Slide 48
Strong focusing lattice  Quadrupoles
Built with quadrupole magnets…
x
y
Force is restoring in one, anti-restoring in the other plane.
More focusing (beam size larger) than defocusing!
Quadrupoles
Beam
Equation of particle motion:
g

## Slide 49
Fit the LHC ring into the LEP tunnel
8.3 T bending field from 1232 magnets!
56 mm holes for beams.
LHC

## Slide 50: Tevatron Magnet Technology
Two colliding beams in the same vacuum pipe!
V. Shiltsev

## Slide 51: Tevatron Ring
V. Shiltsev

## Slide 52: Tevatron Cooling System
V. Shiltsev

## Slide 53: Why Super-Conducting?
For LHC we need 12,000 A current to generate the bending fields required for 7 TeV protons!
A resistive magnet would just over-heat and melt.
We need to build super-conducting magnets: no resistance  high currents and fields are possible.
Magnets cooled to 1.9 K and some to 4.5 K  biggest refrigerator on earth (Helium).
CERN is the coldest place on earth (inside the magnets).

## Slide 54
54
High Beam Energy with Super-Conducting Magnets: Handle High Currents and Large Stored Energy
Each beam in a separate vacuum pipe!
Notes: 54

## Slide 56
1232 main dipoles +
3700 multipole corrector magnets
392 main quadrupoles +
2500 corrector magnets
Regular arc:
Magnets
R. Schmidt

## Slide 57
Regular arc:
Cryogenics
Supply and recovery of helium with 26 km long cryogenic distribution line
Static bath of superfluid helium at 1.9 K in cooling loops of 110 m length
Connection via service module and jumper
R. Schmidt

## Slide 58
Insulation vacuum for the cryogenic distribution line
Regular arc:
Vacuum
Insulation vacuum for the magnet cryostats
Beam vacuum for
Beam 1 + Beam 2
R. Schmidt

## Slide 60: Quench Limit of LHC Super-Conducting Magnets
Beam
362 MJ
SC Coil:
quench limit
12 - 41 mJ/cm3
56 mm

## Slide 61: If Resistance Develops…
61
Notes: 61

## Slide 62: Electrical arc between C24 and Q24
M3 line
V lines
Resistance  current cannot flow as foreseen  electrical arc!
Local material is destroyed by electrical arc.
Liquid Helium escapes and inflates.
What is not taken out by safety valves runs as pressure wave along the accelerator!
Pressure waves hit the vacuum barriers that are located every two cells.

## Slide 63
63
Magnet supports cannot handle pressure wave and buckle…
Consequences
All fixed
Notes: 63

## Slide 64: Beam Acceleration: RF System
Wideroe accelerator
Cylindrical cavity
E.g. d = lRF/2: lRF is the RF wavelength 
fRF = 400 MHz

## Slide 65: Multiple cavity structure
Iris
Smooth waveguide: vph > c
Obstacles (irises) to slow down accelerating wave for synchronous acceleration:
Bunch length shorter than lRF

## Slide 66: LHC RF systems: 400 MHz
400 MHz system:
16 sc cavities (copper sputtered with niobium) for 16 MV/beam were built and assembled in four modules

## Slide 67: Fitting Beam in RF Buckets
time
RMS bunch length 11.2 cm 7.6 cm
RMS energy spread 0.031% 0.011%
450 GeV 7 TeV
RF bucket
2.5 ns

## Slide 68: To get to 7 TeV: Synchrotron – circular accelerator and many passages in RF cavities
LINAC (planned for several hundred GeV - but not above 1 TeV, e.g ILC)
LHC circular machine with energy gain per turn ~0.5 MeV
acceleration from 450 GeV to 7 TeV takes about 20 minutes
....requires deflecting magnets (dipoles)

## Slide 69: Collimation
Shock beam impact: 2 MJ/mm2 in 200 ns (0.5 kg TNT)
Maximum beam loss at 7 TeV: 0.1% of beam (360 MJ) per second (assumed lower than Tevatron/HERA)
360 kW
Quench limit of SC LHC magnet:
~ 5 mW/cm3
 proportional to stored energy

## Slide 70
At less than 1% of nominal intensity LHC enters new territory. Collimators must survive expected beam loss…
Limit: Power of the LHC beams
Entry and exit holes of an electron beam impacting on a spoiler
(courtesy P. Tenenbaum)

## Slide 71
Examples of damage from beams
Tungsten collimator
in the SPS
Lead block accidentally put into a p beam
(courtesy G. Stevenson)
Damage of coating of a SLC collimator
Entry and exit holes of an electron beam impacting on a spoiler
(courtesy P. Tenenbaum)

## Slide 72
Examples of damage from beams
TEVATRON Dec 2003 Photographs courtesy D. Still

## Slide 73: Hearing Proton Beam…
Collimator
Beam Dump
450 GeV
3 1013 p in the beam
2 MJ
0.7 x 1.2 mm2
~ Tevatron beam
~ ½ kg TNT
Microphone
Proton beam…

## Slide 74: LHC Collimators: Dilute and Stop
Jaw 2
Jaw 1
Incoming: up to ~ 50 MJ/mm2 (primary collimator)
Quench limit: ~ 5 mJ/mm2 (any SC magnet)
Required “filter” factor:
1 × 10-10 = Leakage / Dilution
Leakage factor (inefficiency): 10-4
Dilution factor: 106
Cannot be achieved with single collimator  therefore multi-stage collimation for betatron cleaning (x, y, skew) and momentum cleaning.

## Slide 75: Multi-Stage Cleaning & Protection 3-4 Stages
Secondary halo
p
p
e
p
Primary
collimator
Core
Unavoidable losses
Shower
Beam propagation
Impact parameter
≤ 1 mm
Primary
halo (p)
e
p
Shower
p
Tertiary halo
Secondary
collimator
High Z coll
CFC
CFC
W/Cu
W/Cu
High Z coll
Super-conducting magnets
SC magnets and particle physics exp.
CFC collimator

## Slide 76: System Design
Momentum
Cleaning
Betatron
Cleaning
“Phase I”
108 collimators and absorbers in phase I (only movable shown in sketch)
Gaps: ± 6/7 s
2-3 mm

## Slide 77: Tunnel: Cleaning Insertion IR7
BEAM PIPES
COLLIMATOR
TRANSPORT ZONE
COLLIMATOR CABLE TRAYS
RADIATION-HARD CABLE PATH
WATER FEEDS
PHASE I/II
WATER
DISTRIBUTION

## Slide 78: Beam Dump: Disposing the Beam
 0.7m  7.7 m C cylinder

## Slide 79: Dilution with spiral sweep
108 cm sweep length
400 cm sweep length
Dilution kicker
  At 7 TeV would allow currents of ~4 A in distributed bunches

## Slide 80: Colliding the Beams

## Slide 81: Crossing Angles

## Slide 82: To be continued tomorrow…