## Slide 1: Monte Carlo Model of High-Gradient Conditioning and Operation
Lee Millar1, Walter Wuensch1, Graeme Burt2
1CERN SY-RF-MKS
2Cockcroft Institute, Lancaster University, Lancaster, United Kingdom
International Workshop on Breakdown Science and High Gradient Technology (HG2022), 18th May 2022

## Slide 2: Contents
Introduction.
Simulation Setup.
A Visual Example.
Results of the Model.
Conclusion.

## Slide 3: High-Voltage Conditioning
Well known that high-gradient structures (and high-power RF components) are often limited by breakdown.
To achieve stable high-power operation, they must first be conditioned.
At CERN a conditioning algorithm has now been developed to automate the process and offers a consistent and reproducible method of component testing [1,2].
Figure: Preliminary conditioning of several X-band structures tested at CERN.
“Typical” Behaviour

## Slide 4: So Why Model Conditioning?
The Physics Motivation:
Many attempts have been made to connect theory to the measurements (e.g. probabilistic behaviour of BDs, BDR dependency on gradient), but they generally only address a single facet of the problem. Real operation is more complex, the model is an attempt to combine theoretical explanations and connect them to results.
The Pragmatic Motivation:
Conditioning procedures are largely anecdotal. Despite being essential the conditioning process has yet to be optimised (tests require a long timeframe/significant expense, difficult to do experimentally).
The first attempt at a comprehensive integration of HG operation to address these issues.
Notes: Mention: Very nice study on the LES was also previously carried out however with some different objectives pertaining to field emitters.

## Slide 5: Contents
Introduction.
Simulation Setup.
A Visual Example.
Results of the Model.
Conclusion.

## Slide 6: Simulation Setup: Assumptions of the Model
Figure: Scaled gradient vs. cumulative no. pulses (top) and scaled gradient vs. cumulative no. breakdowns (bottom) for four different structures [3].
No. 2:
Structures condition on pulses (pulse count usually more comparable than BDs).
No. 1:
Asymptotic behaviour
(no indefinite conditioning)

## Slide 7: Simulation Setup: Assumptions of the Model
Figures: Cumulative breakdowns vs pulses for a TD26CC tested at CERN showing “staircasing”.
Figure: Probability distribution of the pulses between BDs for a structure tested at CERN and a two-exponential fit [4].
No. 3:
Breakdowns can improve or worsen the surface
(occur both individually or in groups).

## Slide 8: Simulation Setup: Assumptions of the Model
Field distributions often vary spatially, and the effect of breakdown is a local one, making a grid/mesh-based approach appropriate. We can then monitor each element individually.
E [V/m]
Surface electric field in an dipole-mode RF cavity.

## Slide 9: Simulation Setup: Assumptions of the Model
I have condensed the process into three key characteristics, although many other facets of operation exist. To summarise:
Each pulse improves (conditions) the surface elements.
Elements asymptotically approach a limit, above which no improvement takes place.
Breakdowns may worsen or improve a given surface element.
The model is built around the idea of progressive modification of the surface on a pulse-to-pulse basis. To do so, we have used a few terms…
Notes: Next, lets define a few terms…

## Slide 10: Simulation Setup: A Reminder
Figure: Preliminary conditioning of several X-band structures tested at CERN.
“Typical” Behaviour

## Slide 11: Simulation Setup: A Few Terms
Electric Field [MV/m]
Cumulative RF Pulses
Eoperate
ESat
EState
Figure: Visualisation of proposed quantities during conditioning. For illustrative purposes only.
BDR [bpp]
We have an operating field (EOperate).
The field level to which the device has been conditioned (EState).
There is a saturation point for EState for a given material (ESat).
There is a probability of breakdown for a given level of conditioning (PReference). Applies to the whole device i.e. all grid elements.

## Slide 12: Simulation Setup
Using these quantities, we have then derived appropriate equations to capture and quantify:
The conditioning effect.
The probability of breakdown for each element.
How breakdowns affect the grid elements.
Today I’d rather focus on the model’s capabilities and some results, so I have left the equations employed and the relevant justifications in the bonus slides. For now, I’ll show only a broad overview of the model.

## Slide 13: Summary: A (very) Simple Model Outline
Figure: Simplified block diagram of the model showing the equations implemented.
Conditioning Algorithm
(Determine characteristics of next pulse)
Calculate BDR
End Simulation
Pulse goal not met
Pulse goal met
Condition Surface
Input Values
Run
Append
Data
Increment Pulse Count
Modify BD Element
No BD
BD
Check Grid Elements for Arc

## Slide 14: Summary: A (very) Simple Model Outline
Figure: Simplified block diagram of the model showing the equations implemented.
Conditioning Algorithm
(Determine characteristics of next pulse)
Calculate BDR
End Simulation
Pulse goal not met
Pulse goal met
Condition Surface
Input Values
Run
Append
Data
Increment Pulse Count
Modify BD Element (Assign new ψ from Gaussian dist.).
No BD
BD
Check Grid Elements for Arc
PLACE YOUR MODEL HERE

## Slide 15: Contents
Introduction.
Simulation Setup.
A Visual Example.
Results of the Model.
Conclusion.

## Slide 16: A Visual Example: The CLIC Crab Cavity
Face of a single cell.
Breakdown locations superimposed on electric field distribution.
Cavity after high-power test and cutting.
Figure: Images from the post-mortem examination of the CLIC crab cavity [5].

## Slide 17: A Visual Example: The CLIC Crab Cavity
E [V/m]
Apply grid/mesh.
Relative Field Values are assigned.
Select Surface
Breakdown locations.

## Slide 18: A Visual Example: The CLIC Crab Cavity
Eop Values (Applied Electric Field)
Estate Values
Cumulative BDs
Can then monitor quantities accessible in experiments (EOp, global BDR) and others which cannot be directly measured (Estate, effect of breakdowns, etc.).

## Slide 19: A Visual Example: The CLIC Crab Cavity
And generate the more familiar plots…..
Eop Values (Applied Electric Field)
BD Accumulation
Probability Distributions

## Slide 20: Contents
Introduction.
Simulation Setup.
A Visual Example.
Results of the Model.
Conclusion.

## Slide 21: Result 1: CLIC Prototype Structure
Modelling each cell as an identical grid element (real structures vary in field and cell surface area).
Constant impedance example in the bonus slides.
Conditioned state for each cell.

## Slide 22: Result 1: CLIC Prototype Structure
Simulated conditioning in red (25 grid elements).
Notes: Probabilistic behaviour.

## Slide 23: Result 1: CLIC Prototype Structure
Previously described as a “double Poisson” or having a “two-exponential” fit (referring to primary and secondary breakdowns). Similar behaviour emerges in simulation using only a standard gaussian distribution.
Experimental Data
Simulation
More in the bonus slides!

## Slide 24: Contents
Introduction.
Simulation Setup.
A Visual Example.
Results of the Model.
Conclusion.

## Slide 25: Conclusion & Future Work
A discretised model of conditioning has been created and the results align well with HG test data. Ongoing studies include:
Spatially Resolved Conditioning.
Conditioning algorithm optimisation.
Multi-Structure arrangements.
Simulation of DC electrodes (to be compared with CERN Large Electrode System data).
Trialing alternative models/conditioning theories.
Currently being prepared for publication!
Figure: Additional ongoing Monte Carlo studies. DC Electrode clip courtesy of Ruth Peacock
Simulation
Real Data

## Slide 26
Thank you. Questions?

## Slide 27: References
[1] – B. Woolley, “High Power X-band RF Test Stand Development and High Power Testing of the CLIC Crab Cavity,” Lancaster University, United Kingdom, 2015.
[2] – L. Millar, “Conditioning and Operational Algorithms”, Presentation, Available online: https://indico.cern.ch/event/719535/
[3] – J. Giner Navarro, Breakdown Studies for High Gradient Rf Warm Technology in: CLIC and Hadron Therapy Linacs, University of Valencia, 2016.
[4] – Statistics of vacuum breakdown in the high-gradient and low-rate regime. Wuensch, W. et al. 10, s.l. : American Physical Society, 2009, Phys. Rev. Accel. Beams 20, 011007 – Published 25 January 2017, Available online: https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.20.011007
[5] – Enrique Castro, “CLIC Crab CavityPost-Mortem analysis” (presentation), Available online: https://indico.cern.ch/event/449801/contributions/1945273/
[6] – W. Wuensch, “The CLIC accelerating structure development program” (presentation),Available online: https://indico.cern.ch/event/106300/contributions/1306888/
[7] – T. Lucas et al., “HIGH POWER TESTING OF A PROTOTYPE CLIC STRUCTURE: TD26CC R05 N3”, Available online: http://cds.cern.ch/record/002642425

## Slide 28
Bonus Slides: Extra Results

## Slide 29: Result 1: CLIC Prototype Structure
Previously described as a “double Poisson” or having a “two-exponential” fit (referring to primary and secondary breakdowns). Similar behaviour emerges in simulation using a standard gaussian distribution.
Experimental Data
Simulation

## Slide 30: Result 1: CLIC Prototype Structure
Previously described as a “double Poisson” or having a “two-exponential” fit (referring to primary and secondary breakdowns), emerges naturally in simulation using an enhancement factor taken from a standard gaussian distribution.
Values tend towards stability.

## Slide 31: Result 2: A Constant Impedance Structure
Cells identical, E-field decreases.
Different BD accumulation.
Figure: Number of breakdowns accrued in each cell for different windows of pulses (millions) during the test of the CLIC crab cavity.
Different cells in the CLIC crab cavity (shown left) accumulated different numbers of BDs.
Figure: Field profile of the CLIC crab cavity.

## Slide 32: Result 2: A Constant Impedance Structure
Experiment
Simulation
Experimental and simulation data shows cells reach virtually the same field (~97%) but accrue different numbers of breakdowns.
Simulations agree!

## Slide 33: Result 3: Adjusting CERN’s Conditioning Algorithm
One of the goals was to examine changing the parameters in our conditioning algorithm.
In the test stands, we track an operator-selected BDR. Little data exists on changing this value.

## Slide 34: Result 3: Adjusting CERN’s Conditioning Algorithm
Simulation predicts that reducing the BDR setpoint can reduce the BDs accrued without significantly prolonging conditioning. Results agree with an existing experimental example.
Fewer BDs at lower setpoints.
Simulation
Offers an explanation for the results✔.
Experimental Data

## Slide 35
Bonus Slides: Model Details

## Slide 36: BONUS SLIDE - Definition of Model Terms
PReference = The instantaneous probability of breakdown for a given device operating at the level to which it has been conditioned. 5E-5 bpp selected as it is generally the max permissible BDR chosen in CERN structure tests.
EOperate = The electric field level in MV/m at which the device operates.
EState = The surface electric field level to which the device has been conditioned in MV/m. Operation at this field level results in a probability of breakdown which is equal to PBaseline.
ESat = The saturation point for a given material in MV/m. Operation above this level does not result in any further improvement in EState and thus, this is the maximum surface field attainable at the reference breakdown rate (5E-5 bpp) after the device has been fully conditioned. Typically ≈ 250 MV/m in our structures.

## Slide 37: Simulation Setup: Assumptions of the Model
EOperate = The electric field at which the device operates.
EState = The surface electric field level to which the device has been conditioned.
ESat = The maximum achievable value for Estate. The saturation point for a given material in MV/m.
Electric Field [MV/m]
Cumulative RF Pulses
Eoperate
ESat
EState
Figure: Visualisation of proposed quantities during conditioning. For illustrative purposes only.
BDR [bpp]

## Slide 38: Simulation Setup: Quantification of Conditioning
Assuming each element has a conditioning rate (CR), the surface state (EState) should asymptotically approach a limit (ESat):
However, to produce a significant conditioning effect the operating field (EOperate) must be close to the level to which the surface is conditioned (EState):
Electric Field [MV/m]
Cumulative RF Pulses
Eoperate
ESat
EState
Figure: Visualisation of proposed quantities during conditioning.

## Slide 39: Simulation Setup: Quantification of Conditioning
Adding a constant to facilitate tuning (), we can then modify the state of the surface every pulse i.e.
The surface state after N pulses is then given:
Figure: Visualisation of proposed quantities during conditioning.
Electric Field [MV/m]
Eoperate
ESat
EState
Cumulative RF Pulses

## Slide 40: Simulation Setup: Probability of Breakdown
In the CLIC structures the BDR scales strongly with the electric field. Some variance is present, but 30 is the frequently quoted exponent. Values measured in structure tests generally lie around this.
Figures: E30 fit to various HG structure test results [6,7].

## Slide 41: Simulation Setup: Probability of Breakdown
For the time being, it is assumed that changes in the operating field strongly affect the probability of breakdown (PBD) as:
However, the probability of BD decreases as we condition, hence:
Figure: Conditioning curve of a CERN structure.

## Slide 42: Simulation Setup: Probability of Breakdown
A reference probability is added to provide a reasonable BDR:
However, Preference applies to a whole device, not individual grid elements. The probability corresponding to each element in a grid of n elements is then:

## Slide 43: Simulation Setup: Probability of Breakdown
The probability of a BD occurring for each grid element is then:
Given that breakdown randomly improves or worsens the surface, a quasi-enhancement factor in the BD calculation for each element taken from a gaussian distribution as:

## Slide 44: Simulation Setup: Probability of Breakdown
On every pulse, each element is checked for the occurrence of a breakdown. If a breakdown occurs the relevant grid element is assigned a new ψ value.