## Slide 1: Power Combination of Magnetrons as compact X-band RF source
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Jiayang Liu on behalf of VED team in THU
May 19, 2022

## Slide 2: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Power combination of conventional magnetrons
Power combination of magnetrons with dual ports
Power combination of magnetrons with parallel cathodes
Summary

## Slide 3: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Motivations
Locking technologies
Power combination of conventional magnetrons
Power combination of magnetrons with dual ports
Power combination of magnetrons with parallel cathodes
Conclusions

## Slide 4: Motivations
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Advantages of X-band structures:
Compact size, light weight, high shunt impedance…
Advantages of magnetrons:
Compact size, low cost, high efficiency…
Bottleneck of miniaturization:
Peak power of magnetrons (2MW)
Longer structures
Lower dose rate
Power combination of the magnetrons seems to be a cost-effective solution
IPAC’19, THPMP038
X-band
S-band
Preferred for industrial and medical applications

## Slide 5: Locking Technologies
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
The frequency- and phase-locking of the magnetrons is critical for the power combination of magnetrons.
Peer-to-peer locking
Master-to-slave locking
Mm
Ms
Load
Load
M1
M2
Load
Load

## Slide 6: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Power combination of conventional magnetrons
Based on master-to-slave locking
Based on peer-to-peer locking
Power combination of magnetrons with dual ports
Power combination of magnetrons with parallel cathodes
Conclusion

## Slide 7: Master-to-Slave Locking
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
The power for phase locking was extracted from the master magnetron by utilizing a 15-dB coupler, and then fed into the slave magnetron through a 4-port circulator.
A phase shifter was employed in the locking circuit to adjust the phase difference between two magnetrons.
3-dB hybrid
Directional couplers
4-port circulator
Master magnetron
Phase shifter
6-MeV accelerator
15-dB coupler
Slave magnetron

## Slide 8: Master-to-Slave Locking
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
RF power source | Peak power (MW) | Pulse width (us) | Duty cycle (‰) | Dose rate (cGy/min) | Dose rate@1‰ (cGy/min)
Power combination | 2.37 | 3.5 | 0.070 | 113.3@1m | 1619@1m
2-MW magnetron | 2.0 | 3.8 | 0.076 | 88.8@1m | 1168@1m
f (MHz) | Um (kV) | Im (A) | Pm (MW) | Us (kV) | Is (A) | Ps (MW) | Pcomb (MW) | ηcomb (%) | ηtotal (%)
9304.3 | 38.8 | 80.3 | 1.39 | 38.9 | 77.8 | 1.10 | 2.37 | 95 | 39
Notes: 46%, 36%

## Slide 9: Peer-to-Peer Locking
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
The power for peer-to-peer locking circuit was picked up by two 10-dB couplers adjacent to the magnetrons.
3-dB hybrid
Directional couplers
4-port circulator
Magnetron 1#
Phase shifter
6-MeV accelerator
10-dB coupler
Magnetron 2#

## Slide 10: Peer-to-Peer Locking
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
f (MHz) | U1 (kV) | I1 (A) | P1 (MW) | U2 (kV) | I2 (A) | P2 (MW) | Pcomb (MW) | ηcomb (%) | ηtotal (%)
9304.4 | 38.6 | 89.0 | 1.66 | 38.9 | 88.1 | 1.61 | 3.09 | 94 | 45

## Slide 11: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Power combination of conventional magnetrons
Power combination of magnetrons with dual ports
Design and assembly
High-power experiments
Power combination of magnetrons with parallel cathodes
Summary

## Slide 12: Magnetron with Dual Ports
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Design
Pout
Pcoupler
Pout
105 A
1.8 MW
0.1 MW
108 A
2.2 MW

## Slide 13: Magnetron with Dual Ports
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Assembly
Mechanical design
Fabrication
Conditioning
Cold test
before welding
Cold test
after welding

## Slide 14: Magnetron with Dual Ports
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
High-power experiments
Asymmetric 3-dB hybrid with 0 and π phase characteristic was used to combine the power.
Port 1
Port 2
Port 3
Port 4
3-dB hybrid
Directional couplers
MGDP1
Phase shifter
MGDP2
Load

## Slide 15: Magnetron with Dual Ports
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Phase | f (MHz) | U1 (kV) | I1 (A) | P1 (MW) | U2 (kV) | I2 (A) | P2 (MW) | Pcomb (MW) | ηcomb (%) | ηtotal (%)
0 | 9303.4 | 40.3 | 87.2 | 1.75 | 41.0 | 88.7 | 1.73 | 3.39 | 97 | 47
π | 9303.5 | 40.3 | 86.0 | 1.74 | 41.0 | 87.5 | 1.70 | 3.27 | 95 | 46
~ 0.15 MW

## Slide 16: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Power combination of conventional magnetrons
Power combination of magnetrons with dual ports
Power combination of magnetrons with parallel cathodes
Design and simulations
Fabrication and assembly
High-power experiments
Summary

## Slide 17: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Design
Cathode 1
Cathode 2
Coaxial
cavities
Coupling
waveguide
Anode
resonators
Output port 1
Output port 2
Anode
resonators
Combined
port 2
Combined
port 1
L = 131.5 mm
Working mode: π-like mode
f = 9.300 GHz, Q0 ~ 15700
Parasitic mode: 0-like mode
f = 9.313 GHz, Q0 ~ 5600
Eigenmode simulation

## Slide 18: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Frequency-domain simulation
π-like mode in outer cavity: 9.300 GHz
0-like mode in outer cavity: 9.314 GHz
TE121 mode in two coaxial cavities: 9.387 GHz
π-like mode
in outer cavity
0-like mode
in outer cavity
TE121 mode in two
coaxial cavities

## Slide 19: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Particle-in-cell simulation
f = 9296.25 MHz, U1 = U2 = 40 kV, I1 = 110 A, I2 = 109 A
P1 = 2.29 MW, P2 = 2.07 MW, Pcomb = 4.36 MW, ηcomb > 99%, ηtotal = 50%
Conventional coaxial magnetron：
f = 9295.00 MHz, U = 40 kV, I = 112 A, P = 2.27 MW, ηtotal = 51%

## Slide 20: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Fabrication and assembly
Magnetron prototype(12.9 kg) + permanent magnet(12.2 kg) + asymmetric 3-dB hybrid(1.8 kg) ≈ 27 kg

## Slide 21: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
High-power experiments
Magnetron prototype
Asymmetric
3-dB hybrid
Directional coupler
Load

## Slide 22: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
High-power experiments
f (MHz) | U1 (kV) | I1 (A) | P1 (MW) | U2 (kV) | I2 (A) | P2 (MW) | Pcomb (MW) | ηcomb (%) | ηtotal (%)
9284.0 | 38.8 | 86.7 | 1.84 | 36.7 | 79.0 | 1.57 | 3.38 | 99 | 54
9286.3 | 38.9 | 85.0 | 1.80 | 36.7 | 79.8 | 1.57 | 3.34 | 99 | 54
9289.2 | 39.0 | 86.1 | 1.88 | 36.6 | 79.6 | 1.57 | 3.43 | 99 | 54

## Slide 23: Magnetron with Parallel Cathodes
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
High-power experiments
f (MHz) | U1 (kV) | I1 (A) | P1 (MW) | U2 (kV) | I2 (A) | P2 (MW) | Pcomb (MW) | ηcomb (%) | ηtotal (%)
9284.0 | 38.8 | 86.7 | 1.84 | 36.7 | 79.0 | 1.57 | 3.38 | 99 | 54
9286.3 | 38.9 | 85.0 | 1.80 | 36.7 | 79.8 | 1.57 | 3.34 | 99 | 54
9289.2 | 39.0 | 86.1 | 1.88 | 36.6 | 79.6 | 1.57 | 3.43 | 99 | 54

## Slide 24: Outline
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Background
Power combination of conventional magnetrons
Power combination of magnetrons with dual ports
Power combination of magnetrons with parallel cathodes
Summary

## Slide 25: Summary
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
The power combination of magnetrons based on conventional coaxial magnetron has been proven effective.
A peak output power greater than 3 MW has been achieved by the power combination of magnetrons.
Magnetron with parallel cathodes is compact and has prominent performance, which can be a possible candidate as the RF power source for the X-band linacs.

## Slide 26
International Workshop on Breakdown Science and High Gradient Technology (HG2022), May 16-19
Thanks for your attention！
This work was supported in part by the National Key Research and Development Program of China under Grand 2017YFC0111700 and the National Natural Science Foundation of China under Grant 11922504.

## Slide 27
S11
S22
S21
/
/
/

## Slide 29
9309MHz, TE121
TE121 mode
π-like mode