## Slide 1: The HEPiX IPv6 working group - an introduction
David Kelsey (STFC UKRI) HEPiX IPv6 WG meeting, virtual, 14-15 Oct 2021

## Slide 2: On behalf of all co-authors in the HEPiX IPv6 working group
Active in HEPiX IPv6 Working Group – last 12 months
M Babik (CERN), M Bly (RAL), T Chown (Jisc), D Christidis (U Texas/ATLAS), J Chudoba (Prague), C Condurache (EGI.eu), J Flix (PIC), C Grigoras (CERN/ALICE), B Hoeft (KIT), D P Kelsey (RAL), E Martelli (CERN), S McKee (U Michigan), R Nandakumar (RAL/LHCb), K Ohrenberg (DESY), F Prelz (INFN), D Rand (Imperial), A Sciabà (CERN/CMS)
Many more in the past, and others join from time to time
and thanks also to WLCG operations, WLCG sites, LHC experiments, networking teams, monitoring groups, storage developers…

## Slide 3: Outline
History (Phases 1 and 2)
Current status (see later agenda items for more details)
The future - Phase 3: IPv6-only networking
Summary

## Slide 4: Worldwide LHC Computing Grid (WLCG)
The WLCG is a global collaboration
more than 170 computing centres in 42 countries
Its mission is to store, distribute and analyse the data generated by the LHC experiments
Sites hierarchically arranged with three tiers:
  Tier-0 at CERN
  13 Tier-1s (mainly national laboratories)
  >150 Tier-2s (generally university physics laboratories)

## Slide 5: WLCG sites

## Slide 6
Why should WLCG use IPv6?

## Slide 7: Why IPv6?
Survey of 18 major HEP sites (Sep 2010) – IPv6 readiness
  National NRENs ready, Universities and Labs not ready
  Some reported lack of IPv4 address space, including CERN
HEPiX meeting – Cornell, Ithaca NY – Nov 2010
  Projected IANA IPv4 address exhaustion
  Sep 2010 – memo from US Federal CIO to all Exec depts (incl DOE)
Offers of opportunistic CPU resources which could be IPv6-only
  Experiments want to be able to use them
Recognition that much of our middleware, software and technology was not yet IPv6 capable
HEPiX decided to create a working group (started April 2011)
  No specific funding – but motivated, competent volunteers!

## Slide 8: Phase 1: 2011-2016
Phase 1 – full analysis of work to be done
  Applications, system and network tools, operational security
  Create and operate a distributed test-bed
    No interference with WLCG production data analysis!
  Propose timetable and plan for transition
CERN announces shortages of routable IPv4 addresses
  explosion of virtualisation
Active HEPiX IPv6 test-bed with ~ 12 sites
  engagement of all 4 LHC experiments
Testing regular data transfers across the testbed
Testing dual-stack services (in production) at Imperial College London
Concluded not able to support IPv6-only clients until at least 2014

## Slide 9: At CHEP2013 conference
> 2 PB data transferred over IPv6 in last 6 months
Success rate > 87%
Very High!
GridFTP IPv6 data transfer mesh

## Slide 10: 2013-14 Data Management
Testing the important data transfer protocols, technology and data storage/file systems
  For IPv6-readiness
GridFTP, DPM, dCache, xRootD, OpenAFS, FTS, CASTOR
  Found many problems needing work
    Worked closely with developer community
Concluded IPv6 support will be much later than 2014!

## Slide 11: Phase 2 – Dual-stack deployment – 2016-20
Most important IPv6 use case
  Sites, Clouds providing CPU (virtual machines)
  Opportunistic resources may be IPv6-only
  Need dual-stack federated storage services
  And dual-stack central WLCG and Experiment services
LHCOPN (Tier0-Tier1 private network)
    Encourage IPv6 peering everywhere
perfSONAR – end to end network monitoring – dual-stack
Move central services and central monitoring to IPv4/IPv6
Wrote guidance on IPv6 security for WLCG sites
Deployment timetable approved by WLCG Management Board (Sep 2016)

## Slide 12: WLCG – IPv6 deployment
Plan approved by WLCG Management Board
April 2017 – support for IPv6-only CPU starts
  Tier-1s to provide dual-stack storage (in testbed)
April 2018
  Tier-1 dual-stack storage in production mode
By end of LHC Run 2 (end 2018)
  A large number of Tier-2s to migrate storage to IPv6
  All requested to do this

## Slide 13
Growth of dual-stack hosts in the WLCG (Jan 2019)
~25%
Fraction of endpoints listed in the CERN central BDII (lcg-bdii.cern.ch) where the DNS returns a dual-stack IPv6-IPv4 (A+AAAA) resolution (green line) or an IPv6-only resolution (blue line). (http://orsone.mi.infn.it/~prelz/ipv6_bdii/).
All services, not just storage

## Slide 14: Problems & lessons learned
Many blocking issues outside of our own control
  Both software and site networking teams
Developers claim that software is fully IPv6-compliant!
Software/protocols fixed-size storage for IP addresses
Software/protocols assume single address (as in IPv4)
Performance differences between IPv4 & IPv6
  IPv6 must perform at least as well
Have to understand cases where fraction of IPv6 is smaller than expected
  Preference for IPv6 over IPv4 must be established
Can be lots of development effort and testing is not easy when no other positive change re functionality
Sys admins, operations staff, security team, developers
  All need TRAINING and experience

## Slide 15: IPv4/IPv6 and Tier-1 storage
Sep 2021 (GDB)
FTS servers at BNL, CERN, Fermilab and RAL all now work in dual stack
FTS transfers do happen via IPv6 at most Tier-1s (but not all transfers)
IPv6 transfers do not (yet) happen at RRC-KI but IPv6 is enabled
Experiment | Fraction of T1 storage accessible via IPv6
ALICE | 78%
ATLAS | 96%
CMS | 100%
LHCb | 94%
Overall | 96%

## Slide 16
IPv4/IPv6 deployment at Tier-2 sites
The deployment campaign was launched in November 2017
Steady progress (status)
  ~79% of Tier-2 sites have storage on dual stack
Experiment | Fraction of T2 storage accessible via IPv6
ALICE | 87%
ATLAS | 62%
CMS | 94%
LHCb | 75%
Overall | 77%

## Slide 17: Fraction of SRM/GridFTP FTS traffic over IPv6
Some FTS protocols, e.g. DAVS, not yet instrumented to monitor IPv6
these are excluded from this plot

## Slide 18: IPv6 traffic on LHCOPN/LHCONE at CERN
LINK to these plots
IPv6 traffic on LHCOPN/ONE as seen at CERN
~70% of all traffic is IPv6
> 50% from June 2019 onwards

## Slide 19: IPv4 transfers on LHCOPN/ONE?
Tier1s are dual-stack, but IPv4 can still be used for transfers
  Site/experiment issues - some storage end-points not yet dual-stack
    Old software stacks (legacy deployments) are still deployed
  both ends are dual-stack but configuration or request prefers IPv4
    Investigation of ATLAS/CMS IPv6 traffic has been proposed in UK
  transfers are to/from WN's and the WNs are still IPv4-only
    Difficult to monitor WN IPv6 traffic centrally – can sites monitor?
encourage all sites to deploy all WNs and all services as dual-stack
encourage all sites and all experiments to "prefer" IPv6 transfers

## Slide 20: IPv6 use cases
Main driver was and still is: “support IPv6-only CPU”
  Ongoing concern of lack of IPv4 addresses (at some sites)
Other (more recent) drivers
  Support packet marking in TCP for monitoring by RNTWG
    Research Networking Technical Working Group
      See WLCG GDB May 2021 – LHCOPN/ONE (E. Martelli) slide 15
      And report today from Marian Babik
  US Federal Government - 80% of services to be IPv6-only by 2025-26
    See report today from Phil DeMar

## Slide 21: Phase 3: From dual-stack to IPv6-only (CHEP2019) https://doi.org/10.1051/epjconf/202024507045
Planning for an IPv6-only WLCG
To simplify operations
  dual-stack infrastructure is the most complex!
Large infrastructures (e.g. Facebook, EE/BT) use IPv6-only internally
The plan - the goal we are working towards
  IPv6-only for the majority of WLCG services and clients
  With ongoing support for IPv4-only clients where needed
    e..g. via use of RFC 7755/7756
      Stateless IP/ICMP Translation for IPv6-only Data Centres
Timetable to be defined

## Slide 22: IPv6-only timetable
A possible first place to turn-off IPv4?
  LHCOPN (Tier0 and all Tier1’s are all dual-stack)
  When the amount of IPv4 traffic becomes very small
    Can we make LHCOPN IPv6-only?
    IPv4 traffic will flow via general internet links
  WLCG Management Board (July 2021) – “must not happen too early”
WLCG IPv6-only plan - is during LS3 and before start of Run 4 possible?
  MB still to agree date for end of “full support” for IPv4 on WLCG Clients
  Core services at that point can become IPv6-only

## Slide 23: WLCG MB Conclusions (July 2021)
Deployment of dual stack storage remains the priority
  this is a prerequisite to fully supporting IPv6-only WNs
All sites and regions should plan accordingly and as soon as possible
The final goal is agreed to be IPv6-only
  But the timetable to be agreed later!

## Slide 24: Summary
WLCG is ready to support use of IPv6-only CPU resources
  Good steady progress towards this goal!
Tier-1s should all have production storage accessible over IPv6
  >96% of Tier-1 storage is available via IPv6
Tier-2s ~80% sites done
  >75% of Tier-2 storage is dual-stack
WG Phase 3 - we are planning for move to IPv6-only services
message to new research communities - build on IPv6 from start

## Slide 25
Questions, Discussion?