## Slide 1: Target and first experiences after operation
R. Esposito (SY-STI-TCD)
n_TOF Collaboration meeting (25/11/2021)

## Slide 2: The n_TOF Target #3
150 mm
50 mm
Al-6082-T6 supporting structure
(anti-creep and N2 cooling channels)
N2 gas cooling to avoid Pb corrosion and contamination of the cooling circuit
More details: Phys. Rev. Accel. Beams 24, 093001 (2021)

## Slide 3: Target instrumentation
2 thermocouples  3 points = 6 thermocouples to monitor Pb surface temperature

## Slide 4: Target commissioning
n_TOF Vistar: https://insp.web.cern.ch/webviewer/application/CPS/n_TOF_Web_Vistar
First beam on target: July 19th 9:47 AM
Protons on target so far: ~8.11018 p+
All systems working correctly
  Thermocouples
  SEM grid
  Nitrogen and moderator systems
Faraday cup

## Slide 5: Target systems logging
All the monitored parameters are logged on NXCALS
Accessible from TIMBER
Snapshot configurations for each system

## Slide 6: Target design parameters
Design values
  Bunch intensity: 1013 ppb
  Average intensity: 1.671012 p/s
    1 pulse every 6 s on average
    6 pulses in a 36 s supercycle
  Beam size: 15 mm  15 mm (RMS)
  Momentum: 20 GeV/c
TOF-TAR-EP-0001 (EDMS 1581048), Beam Parameters for the n_TOF Spallation Target, 2016
TOF-TAR-EN-0001 (EDMS 1580996), Preliminary conceptual design of the n_TOF Spallation Target #3, 2016
TOF-TAR-ES-0003 (EDMS 2154581), n_TOF neutron spallation Target #3 – N2 cooled bare Pb core, 2019
Esposito R. and Calviani M., J. Neutron Res., 22, 221, 2020
https://indico.cern.ch/event/696196/contributions/2949603/attachments/1649528/2637499/2018-05-15-Updated_Beam_parameters_for_n_TOF.pdf
SEM grid was not available before commissioning
BTV images (not reliable) compatible with 1515mm2 size
SEM grid reveals beam size
16 mm  7 mm

## Slide 7: Test with new optics
Optics manipulation  Required beam
mGy/s
15 mm  15 mm 16 mm  7 mm
Up to factor 4 higher beam loss
Test run with 15x15 beam during August until mid-September
mm
 H
 V

## Slide 8: Dose rate in the FTN line after test
Target
PS beam
Hot spot
15mm15mm 16mm7mm

## Slide 9: Back to pre-LS2 optics
High dose in FTN with 15x15mm beam size  spread on the horizontal axis keeping the limitation on the vertical axis
15x15 mm2
27x7 mm2
Comparison of peak energy density ongoing
mm
 H
 V
mm
 H
 V

## Slide 10: Gas analysis
Before BEAM
N2
H2O
Ar
After BEAM
N2 (carrier gas) + Ar (2.7%)
H2O: this value is not accurate as H2O(g) is condensable and tends to accumulate in the mass spectrometer  H2O(g)= 1-2 ppm
Other impurities: O2 (20 ppm), H2 (20 ppm), CO2 (60-80 ppm)
Courtesy F. Dragoni
Faraday cup

## Slide 11: Gas analysis
Courtesy F. Dragoni
Before BEAM
After BEAM
He
Traces of organic components – 10-500 ppb
Secondary Electron
Multiplier

## Slide 12: Beam interlocks
Beam interlocked if average intensity > than 1.671012 p/s (computed over the last two supercycles)
If 3 high-intensity pulses (> 7.51012 p+) have wrong size or position (xv within +/- 3mm, v< 5mm, H < 25mm)
Number of pulses per supercycle accidentally high:
Beam interlock went off every time the average intensity increased too much

## Slide 13: Conclusions
The n_TOF Target #3 and all the related systems worked well during commissioning:
  Target instrumentation (thermocouples)
  Cooling system (nitrogen and moderator station)
  Beam size monitoring (SEM grid)
The target has already been impacted by 8.11018 p+ ( 1 million pulses).
The beam size assumed by design induces high dose in the beamline due to vertical aperture limitation: work ongoing to get the desired energy density by respecting the vertical limitation while spreading the energy along the horizontal axis.
The gas analyzer did not show variations in the cooling gas content so far.
Beam interlocks developed for beam size and position, in addition to pre-existing interlock on average intensity.

## Slide 14
Thank you for your attention!