## Slide 1: RADWG Activities Overview
Rudy Ferraro (BE-CEM-EPR)
RadWG Workshop – 13 October, 2021

## Slide 2: Radiation Test Service
BE-CEM-EPR provides, through R2E resources, the service of radiation testing of electronic components supporting the Radiation Working Group (RadWG)
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
19/1-019 Rapid Prototyping lab
107/1-A10 Main PCB Assembly Atelier
PSI Beam Line
CC60 Instrumentation

## Slide 3: 2021 in Numbers: Annual
112 requests collected
84 components & Systems tested
  New components but also a lot of system consolidation
12 Radiation campaigns done (9*PSI, 2*CC60, 1*ILL)
Other three planned: 1*PSI, 2*CHARM
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Breaking records:
  Highest number of campaigns
  Highest number of DUTs

## Slide 4: 2021 in Numbers: Monthly
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 5: 2021 in Numbers: User distribution
Basically the equipment groups in charge of new developments requested to qualify their selected components
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
  CIBU
  QPS
  LHC BPM
  DIOT Crate
  BATMON
  IOT Humidity Mon.
  Space RADMON
  LHC BLM
  R2E-HL-LHC(60;120)A
  VSC Conditioning Electronics (Penning, log etc…)
  RaToPUS
  BLM Crate
  Common building blocks
  FGPAs
  Opamps
  Regulators
  Etc…

## Slide 6: 2021 in Numbers: DUT distribution
Opamps
MOSFETs
Regulators
Most Tested Devices
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
We tested from the simplest component (BJT) to the most complex ones (FPGAs) and even complete systems.
Notes: Link to the radWG database

## Slide 7: 2021 in Numbers: DUT distribution
Opamps
MOSFETs
Regulators
Most Tested Devices
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Opamps
Regulators
MOSFETs
FPGAs
FPGA
Honorary title for FPGAs, which came in fourth place but represented a considerable effort.
We tested from the simplest component (BJT) to the most complex ones (FPGAs) and even complete systems.

## Slide 8: 2020-2021 in pictures
FPGAs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
PLLs
uControllers
FANS

## Slide 9: 2020-2021 in pictures
BJTs
More BJTs
ADCs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 10: 2020-2021 in pictures
PSI not meant for System level tests
But tests need due to urgency of the system qualification
Challenging due to size and setup limitations
“Nothing beats a CHARM Test”
BATMON
BE-BI
BE-CEM
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Space RADMON
BE-CEM

## Slide 11: 2020-2021 in pictures
In case of system testing we make use of Gafchromic film to cross-check the irradiated areas:
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
BATMON
BE-CEM
Space RADMON
BE-CEM

## Slide 12: Recent outcomes: 5 GHz PLLs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
5 GHz PLL testing in collaboration with SY-BI for new LHC BPM
  Challenging setup to keep signal integrity through 15 m of cables and multiples splitters
  Devices tested in active monitoring online SEE (SEU & Transients) and TID degradation (Phase Noise & Spectrum)
EDMS Reports: 2611501

## Slide 13: Recent outcomes: 5 GHz PLLs
5 GHz PLL testing in collaboration with SY-BI for new LHC BPS
  Challenging setup to keep signal integrity through 15 m of cables and multiples splitters
  Devices tested in active monitoring online SEE (SEU & Transients) and TID degradation (Phase Noise & Spectrum)
EDMS Reports: 2611501
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Single Event Effects:
  No events observed

## Slide 14: Recent outcomes: 5 GHz PLLs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
LMX2694
Phase-Noise jitter:
5 GHz PLL testing in collaboration with SY-BI for new LHC BPS
  Challenging setup to keep signal integrity through 15 m of cables and multiples splitters
  Devices tested in active monitoring online SEE (SEU & Transients) and TID degradation (Phase Noise & Spectrum)
EDMS Reports: 2611501

## Slide 15: Recent outcomes: 5 GHz PLLs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
LMX2694
Frequency Spectrum:
LMX2592
LMX2594
5 GHz PLL testing in collaboration with SY-BI for new LHC BPS
  Challenging setup to keep signal integrity through 15 m of cables and multiples splitters
  Devices tested in active monitoring online SEE (SEU & Transients) and TID degradation (Phase Noise & Spectrum)
EDMS Reports: 2611501

## Slide 16: Recent outcomes: Low Power N-MOSFETs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
MOSFETs tested at CC60 for SY-EPC (EDMS-2636745)

## Slide 17: Recent outcomes: Low Power MOSFETs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 18: Recent outcomes: Low Power MOSFETs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
BSS127 Best candidate from this campaign
While the SQ2398 can be used as ionizing dosimeter

## Slide 19: Recent outcomes: Low Power MOSFETs
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )
Best component from 2021 (BSS127) still ~3 times more sensitive than the best one found in 2016 (MGSF1N01LT1)
The MGSF1N01LT1 remains the best option in terms of N-MOSFET used as switch.
2021 N-MOSFET campaign:
2016 N-MOSFET campaign:
From: EDMS-1609725
From: EDMS-2636745

## Slide 20: Test results analysis and reporting
The website https://radwg.web.cern.ch/ embeds an User-Friendly database
  More than 490 reports from the 2011 up to 2021
180 users subscribed to the mailing list lhc-proj-radwg-members
It embeds also the TE-EPC component list and tests
The service produces reports in a common template for all the components tested
  Test reports template ensure a coherent reporting
databases accessible by all the equipment groups
https://radwg.web.cern.ch
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 21: Conclusions
BE-CEM-EPR provides the service of radiation testing of electronic components supporting the Radiation Working Group (RadWG)
Very intensive testing activity in 2021
  Highest number of test campaign
  Highest number of DUTs tested
CHARM restart this year, first component-level campaign planned next week!
Opamps and MOSFETs always among the three most tested components
  A lot of Instrumentation amplifier tested this year (report coming soon)
  No better N-MOSFET than the MGSF1N01LT1 found
Already preparing 2022 campaigns with SY-EPC and TE-MPE
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )

## Slide 22
Thank you for your attention!

## Slide 23: Recent outcomes
New FPGA qualifications: PolarFire & NanoXplore
[cm²/FF]
Chart: 
| FF | FF SET | FF TMR | FF TMR SET
ProASIC | 1.16e-13 | 9.6e-14 | 3.12e-15 | 4.09e-15
SmartFusion | 5.22e-14 | 7.86e-15 | 1.89e-15 | 3.51e-15
PolarFire | 4.4389e-15 | 9.0554e-15 | 3.5511e-16 | 1.4205e-15
NanoXplore | 1.09e-15 | 2.38e-16
DFF
FF
FFTMR
FF Logic
FF logicTMR
PolarFire Propagation delay increase [%]
5 kGy
  PolarFire SEE sensitivity one order less of magnitude wrt SmartFusion
  PolarFire programmability > 2.5 kGy !! (SmartFusion ~ 100 Gy)
  No increase of propagation delay up to 5 kGy !
  High sensitivity to thermal neutrons
  Reports: 2475661; 2319932; R2E presentation
  Research: Use of Benchmark test circuit for qualification
A.Scialdone ‘FPGA Qualification and Failure Rate estimation Methodology for LHC Environments Using Benchmarks Test Circuits’, oral RADECS2021
RADWG Activities Overview by R. Ferraro (BE-CEM-EPR )