## Slide 1: Synchrotron radiation (SR) studies for the FCC-ee arc with FLUKA
Barbara Humann (SY-STI-BMI)
Supervisor: Francesco Cerutti
FCCIS WP2 Workshop 2021 (09/12/2021)
Acknowledgments to J. Bauche, M. Benedikt, R. Garcia-Alia, G. Lerner, R. Losito, R. Kersevan & F. Valchkova

## Slide 2: Agenda
Simulation setup - reminder
Synchrotron radiation: spectrum
Dose levels in the tunnel
Si-1MeV neutron equivalent fluence
Conclusion & Outlook

## Slide 3: Simulation Setup
182.5GeV (ttbar): most challenging case for energy deposition studies
Representative arc cell (140m)  periodic re-insertion of the particles
  5 dipoles, 5 quadrupoles, 4 sextupoles
SR source (NEW!): e-, e+ in all magnets  direct approach
Different layouts performed:
  Absorbers: Tungsten (Inermet180) vs. copper (CuCrZr)
  Continuous shielding (comparable to LEP design): tungsten, 1cm around winglet
Tunnel layout by F. Valchkova-Georgieva (IOWG, 16.10.2019)
 | Tungsten | Copper
+ | Better absorption properties (higher Z and density) | Easier to manufacture, better behavior in vacuum
- | Brittle, harder to manufacture, cost | Less good energy absorption properties

## Slide 4: Model comparison: absorber vs continuous shielding
Absorbers (ABS):
CuCrZr or Inermet180
Length: 30cm
5-6m distance
Angled surfaces for even power distribution
Water cooled
25 ABS in each beam (MBs, MQs) (Design and initial placement by R. Kersevan)
Continuous shielding:
Equivalent to LEP layout
Continuous shielding around VC in MBs
  Space restrictions due to yoke and coils  no shielding in MQs and MSs.
Intermet180
Shielding thickness:
  Top/bottom: 1cm
  Sides: 1.3cm
z
x

## Slide 5: Source term – Synchrotron Radiation
SR Spectrum of primary electrons:
-2
ttbar-mode is most relevant for energy deposition studies
Energy loss ( | 
Critical energy () | 
Power whole ring | 
Power | 
Power whole ring | 
Electromagnetic radiation emitted tangentially with an angular spread by charged particles moving along a curved trajectory
The lighter the particle and the higher the energy, the stronger the effect:
SR related numbers in FCC-ee ():

## Slide 6: Power deposition comparison: Tungsten vs Copper vs Continuous
Chart: Copper Absorber
| Dipoles | Quads | Sext | Abs/Shield | Tunnel
 | 14.5221 | 1.5799 | 0.055628 | 76.8265 | 7.0158
Power | Tungsten |  | Copper |  | Continuous | 
Dipoles* | 7.8kW | 4.7% | 23.4kW | 14% | 3.5kW | 2%
Quads | 0.9kW | 0.5% | 2.6kW | 1.6% | 17.4kW | 10.4%
Sexts | 0.05kW | 0.03% | 0.09kW | 0.06% | 7.1kW | 4.3%
ABS, Shield/VC | 155kW | 92.3% | 131kW | 78% | 135kW | 81%
Tunnel | 4.1kW | 2.4% | 9.5kW | 7% | 3.5kW | 2.1%
Total | 168kW |  | 168kW |  | 167kW | 
Chart: Tungsten Absorber
| Dipoles | Quads | Sext | Absorbers | Other
 | 4.6729 | 0.52739 | 0.0288 | 92.3239 | 2.447
Peak heat load on ABS (hottest spot on the absorber)
In the (unrealistic) adiabatic assumption:
Tungsten: 280K/s
Copper: 100K/s
Continuous: 10K/s
* Without VC and shielding
Normalisation:
Current: 5.4mA
Energy: 182.5GeV
Runtime: 107s
Chart: Continuous
| Dipole | Quads | Sext | Shield | Tunnel
 | 3.5 | 17.4 | 7.1 | 135 | 3.5

## Slide 7: Power distribution on the absorbers and MBs
Highly impacted VC
Chart: Power per unit length in W/m
| YOKE | COILS | VCR | VCL | SHIELD B1 | SHIELD B2
Absorber Setup | 155.8585 | 29.4956 | 9.4658 | 8.9378
Continuous Shielding | 21.0893 | 8.5212 | 378.1095 | 356.4191 | 214.1597 | 201.2899
ABS (Copper)
`
Continuous
Comp. | Material
Yoke | Iron
Coils | Copper
VCR/VCL* | Copper
Shield | Inerm180
Power on ABS | Tungsten | Copper
Absorber | 97% | 94%
Cooling | 0.4% | 1%
BP | 2.6% | 4%
Percentage calculated from one representative absorber
Power on MB | Tungsten (1.7kW) | Copper (5.3kW)
Yoke | 64% | 72%
Coil | 24% | 21%
BP | 12% | 7%
Percentage calculated from one representative MB
* VC…Vacuum Chamber (right/left)
Power distribution on MB: ABS (Copper) vs continuous
Absorber (CuCrZr, 30cm): ~2.6kW
(W/m not meaningful)
Power comparison different ABS:

## Slide 8: Dose in the tunnel environment – y centre
COPPER
 | Tungsten | Copper | Cont.
Middle, ext. | 100kGy | 600kGy | 200kGy/1.2MGy
Middle, int. | 500kGy | 1MGy | 200kGy
HL-LHC arcs reference value: 1.4Gy (!)
TUNGSTEN
CONTINUOUS
(https://edms.cern.ch/ui/file/2302154/1.0/HLLHC_Specification_Document_v1.0.pdf)
Higher dose internally due to backscattering of particles on ABS
One order of magnitude higher dose than for tungsten (especially externally)
Higher dose internally
Peaks due to missing shielding in MQs
Externally higher dose values
On average lowest dose

## Slide 9: Dose in the tunnel environment – y above
COPPER
COPPER
 | Tungsten | Copper | Cont.
Top, Cent. | 100kGy | 300kGy | 120kGy
HL-LHC arcs reference value: 1.4Gy
TUNGSTEN
CONTINUOUS
(https://edms.cern.ch/ui/file/2302154/1.0/HLLHC_Specification_Document_v1.0.pdf)
Lowest obtained dose levels
Homogeneously distributed
Less effective ABS lead to higher dose
Lower dose level at z~5500cm due to absorber placed in MQ
Areas of higher dose due to MQs without shielding
Booster on top of collider
Shielding options for R2E are under study

## Slide 10: Fluence in the tunnel – ABS (Copper) layout
Neutron fluence:
Similar results for B1 and B2
Magnets are “transparent” for neutrons
Thermal neutrons (0.025eV)
Electromagnetic particles fluence:
B1: higher fluence obtained due to scoring at the outside of the tunnel
B2: particles absorbed in magnets
Electron & Photon Fluence (B1, B2)
-2
Scoring area
x
y

## Slide 11: R2E: Si-1MeV neutron equivalent fluence
ABS Copper
Continuous
ABS Tungsten
Similar levels for all case, different contribution levels on the level of neutrons and em particles
  Tungsten: high Z leads to lower production threshold for neutrons
  Copper: higher production threshold for neutrons, but stronger impact from em particles
   Total levels are similar
HL-LHC arcs reference: 1.6x1010cm-2

## Slide 12: Summary
Heat load:
  Tungsten absorbers have best absorption properties, but cost and manufacturing properties are disadvantageous;
  VC highly impacted in case of continuous shielding
Peak heat load on the absorbers:
  2.5x higher for tungsten absorber  cooling feasible, outgassing?
Radiation to electronics:
  Highest dose levels for the copper absorbers in the tunnel environment
  Lower dose levels on top of accelerator are favorable for booster placement
  Si-1MeV eq. fluence similar for all three cases but different levels of contributions from neutrons and em. particles
  Si-1MeV neutron equiv. fluence ~2 orders of magnitude higher than in HL-LHC, but bigger differences are obtained in dose levels (kGy instead of Gy  5 orders of magnitude!)

## Slide 13: Outlook
Radiation studies for possible shielding in the tunnel for R2E
  Test different materials (lead, concrete) & thicknesses (1cm, 3cm, 10cm)
Investigate lower beam energies to assess if they comply with radiation safe environment in the tunnel (<1Gy/year)
Gas bremsstrahlung simulation
  Lowest energy (Z pole  higher current)
  Constant beam-gas profile  find critical residual gas density
Other Fluka/FCCee related ongoing activities: Heat load
studies for the positron target
Shielding
Space for electronics

## Slide 14
Any questions?

## Slide 15: Backup slides

## Slide 16: Magnets
Magnets designed from scratch in Fluka. Technical drawings received from J. Bauche
Dipoles (MB):
Long: 24.64m (lmag) (Simulations were performed before 24m long model was abandoned)
Short: 21.44m (lmag)
56.6mT at 182.5GeV
Quadrupole (MQ):
2.9m (lmag)
3.2m (lmech)
Maximum gradient: 10.0T/m
Sextupole (MS):
1.4m (lmag)
No prototypes and technical drawings so far (ending of coils,…)
7cm
12cm
Vacuum chamber (VC):
Copper
2mm
Winglets
General: 30cm beam separation

## Slide 17: Absorber working & reflection
z
x
x
y
External beam: reflected particle  magnet yoke
Internal beam: reflected particle  tunnel
Compton scattering: photon collides with electron and is scattered into a different direction, dominant in the MeV range