## Slide 1: SPL cryomodule specification: Preliminary summary
V.Parma, TE-MSC

## Slide 2: issues
Keep possibility for testing cryomodule in a beam line. Where could it be tested?
Magnetic shielding
  1st shield cryo-perm: active cooling? What T? Dedicated circuit? Active solution of Spiral 2 cryomodule seems interesting
  2nd shield @ RT
“fast” cool down requirement (Q desease): 100 K/h as a goal though not a specif requirement yet (vertical tests will tell us)
No active cooling of inter-cavity bellows, but T measurement
HL measurements.
  Pressure gauge measurement rather than T helium, but having T cavity measured is useful (cryo), but no need for precision (could be in insulation vacuum)
  Flow-meter could be useful
T of thermal shield should be close to 50 K. This needs a dedictated line in SM18 or an artifact, to increase T to 50K. Dp is limited. To be checked with thermalshield geometry.
Make a specific table of T for the test bench in SM18
Heat Loads table: discussed and confirmed
Clarify warm-up means (boir-off of helium, followed by vac.degradation?)
Space allocation in bunker for cryogenic connection activity
Connection to cryo distribution line:.Confirmed:
  Welded solution for connection to the cryo distribution line
  Flexibility on connection to allow tilt change (0-2%)

## Slide 3: Other issues from CNRS
Magnetic shielding. Additional points:
  Definition of the interfaces:
    Tank and cavity support
    Instrumentation
Making a magnetic field map of SM18 bunker.
Evaluate the needs of maintenance actions on/in the cryomodule… (for design of windows)
  Frequency
  Type of maintenance
    On the experimental site
    In an intervention zone (= assembly zone)
 Yes, need access windows to access tuners (motor), HOM (there are 2), RF vac. Transitions ...frequency of intervention not discussed

## Slide 4: Issues
Instrumentation. Quite an exhaustive list presented by system responsible:
  Priority and Redundancy to be further discussed
Alignment budgets: cavity figures considered tight, but overall figures OK. Reconsider sharing?
Aligment monitoring (WPM or similar) is a must to confirm the new supporting concept
RF coupler “2-in1” concept. Suggested dedicated mock-up for testing the mechanics and of vacuum integrity (RF gasket). Yes!

## Slide 5: Other issues
Cryogenic scheme. SPL slope-specific.
Cryogenic valves/filling scheme is redundant, yes, but wanted. Aim is to test and eventually simplify.
Dark current measurements

## Slide 6: Thanks to all participants (especially speakers!) for the fruitful meeting