## Slide 1: Continuous Integration and the Automatization of the PLC Update Process
Vacuum Group – Interlocks Controls and Monitoring
Rodrigo Ferreira | rodrigo.ferreira@cern.ch

## Slide 2
The Vacuum Control System
(PLC Architecture of the LHC Vacuum ICS)
(EDMS 1576467)
SCADA
Servers
Technical Network
Master PLC
(S7-400 x 35)
Sector Valves
NEG + Ion Pumps
LSS Beam Gauges
( … )
VPG PLC
(S7-1200 x 220)
Pumping
Group
Penning + Pirani Gauges
LSS Gauge
Reading PLC
(ET200-SP x 18)
Arc Gauge
Reading PLC
(ET200-SP x 16)
Bypass
Valves
Cryogenic
Interlocks
LSS Insulation Vacuum Gauges
Cryogenic
Interlocks
Arc Insulation Vacuum Gauges
Arc Beam Vacuum Gauges
Profibus (mobile)
Mobile Devices
User Terminals
 | LHC | SPS | CPS + EXP
No. of PLCs | 292 | 21 | 29
Number of Vacuum PLCs per Machine
Siemens PLCs exclusively.
Global architecture updated during LS2 (only S7-400s remain from old ICS).
S4-400 PLCs will be replaced during LS3.
S7-400 projects are still SIMATIC Manager. All the rest are TIA Portal.
Profibus (fixed)
Notes: Demonstrating accountability - Parts of project under my responsibility
- Give credit for deployment + commissioning to ICM team
Working in teams
Show that the renovation was a process that the whole section was working towards

## Slide 3
The Vacuum Control System
(Vacuum SCADA Applications)
(EDMS 1576467)
Notes: Demonstrating accountability - Parts of project under my responsibility
- Give credit for deployment + commissioning to ICM team
Working in teams
Show that the renovation was a process that the whole section was working towards

## Slide 4
The Vacuum Control System
(Vacuum Framework)
(EDMS 1576467)
Master DB
Equipment definitions
Machine DBs
Machine Geometry
Equipment instances + Config
PLC Configuration
…
VacMaster
(WebApp)
VacDBEditor + Exporter
(WebApp)
Export Process
SCADA Configuration Files
Machine Geometry (synoptic generation)
Equipment instances
PLC Connections
Datapoint + DIP Configurations
…
PLC Configuration Files
Equipment Instances
(Instance + Global DBs)
DB Renumbering Lists
(DB Name <-> Number link)
Equipment Calling Functions
(FCs)
PLC Summary
(Global overview of PLCs)
Notes: Demonstrating accountability - Parts of project under my responsibility
- Give credit for deployment + commissioning to ICM team
Working in teams
Show that the renovation was a process that the whole section was working towards

## Slide 5
Vacuum Framework
(Updating PLCs)
Machine
DB
PLC Sources
PLC Project (TIA Portal)
Export
Find correct sources
Import into Project
Update time per PLC : 5~7 minutes
Complete LHC Update: > 3 FTE for 1 day
Repetitive, frustrating work
Hard to finish full update in a day
Will become worse with system growth
Compile DBs + FCs
Renumber Blocks
Production PLC
Vacuum Framework
Baseline Project
Copy Baseline
(if required)
VacPLC Repository
ICMDev Repository
(Production PLC Projects)
Checkout Production
PLC Projects
Updated PLC Project
Deploy
Commit
Notes: Managing self
Taking initiative to solve a problem
Solving Problems
Achieving results
Learning and sharing knowledge / Working in teams
- Code is open-source, available, and being used by BE/ICS)
Demonstrating flexibility
- Going for a new solution

## Slide 6
Automating Control System Updates
(Freeing resources and avoiding repetitive work)
TIA Portal Vacuum Updater
(Generic PLCs)
Automates all the main phases of a PLC update.
TIA Portal VPG Manager
(LHC VPG PLCs)
Integrates with CERN LanDB to configure VPG projects.
Available in CERN
repositories
Live Demo
(Applications + Implementation)
Notes: Managing self
Taking initiative to solve a problem
Solving Problems
Achieving results
Learning and sharing knowledge / Working in teams
- Code is open-source, available, and being used by BE/ICS)
Demonstrating flexibility
- Going for a new solution

## Slide 7
Continuous Integration
(Proposed Architecture)
PLC Compilation Server Windows 10
OpenStack VM
MS .NET Webservice Orchestrates update procedure.
Shared Folder SMB, dfs, CERNbox (TBD)
VacDBEditor + Exporter
(WebApp)
User
Trigger Update
PLC Sources
(REST)
Request project updates
TIA Portal (no UI)
Production
PLC Projects
Vacuum Framework Baseline (exported to xml)
Production PLC
Deploy
Functionality exists, but we don’t intend on automating deployment at this time.
Notes: Managing self
Taking initiative to solve a problem
Solving Problems
Achieving results
Learning and sharing knowledge / Working in teams
- Code is open-source, available, and being used by BE/ICS)
Demonstrating flexibility
- Going for a new solution