## Slide 1
Very high gradient RF Guns
(Task 7.4)
David Alesini, coord.
INFN-LNF (Frascati, Italy)
On behalf of the INFN-PSI Very High Gradient C band gun group

## Slide 2
OUTLINE
Goals, Responsibilities and Timeschedule of task 7.4 on Very high gradient RF Guns
Update on SW GUN Activities
Update on TW GUN Activities
Bunker Status@PSI for high power test

## Slide 3
RF Photo-injectors are widely used in FEL, as very low-emittance and high-brightness electron sources.
A laser pulse hits a cathode and the electrons are immediately accelerated by an intense RF E field (60-120 MV/m)
RF technology mostly used is the L or S-band (f=1.3 or 3 GHz).
The higher the peak electric field on the cathode, the better the quality of the beam emerging from the Gun.
RF PHOTO-GUNS
The frequency step-up from L/S-band to C-band can provide higher achievable cathode peak field as high as 160-180 MV/m.
Because of its higher efficiency a C-band RF Gun is also suitable for application requiring repetition rates in the 200 Hz÷1 kHz range.
The availability of a new state-of-the-art, electron injector would bring benefits to a large accelerator user community, (FEL radiation sources, Thomson/Compton photon sources and plasma based accelerators)

## Slide 4
Design, realization and high power test of two different C-band (5.712 GHz) RF electron guns operating at very high gradient cathode peak field (>160 MV/m): a Standing Wave (SW) gun and a Travelling Wave (TW) gun.
Comparison of the performances.
Beam dynamics simulations to exploit the device potentialities
Research Institutions involved: INFN (IT), PSI (SW);
Private Companies involved: VLD (NE), COMEB (IT)
GOALS AND TIMSCHEDULE OF TASK 7.4
SW GUN
TW GUN
Detailed Gantt well defined

## Slide 5
INFN: coordination, design and low power test SW Gun, solenoid design and procurement, design of the module to test the gun, providing the RF circulator.
COMEB: mechanical construction SW gun, mechanical supports and movable screen with magnetic corrector.
SW GUN
PSI: design, assembly, brazing and low-power characterization of the TW Gun, hosting and setting up the high-power test.
VDL: Machining of the cups and couplers of the TW gun.
TW GUN
RESPONSABILITIES
INFN and PSI: A comprehensive study and optimization of the beam dynamics aspects, to fully exploit the devices potentialities, will be led by

## Slide 6
SW GUN STATUS
RF gun
solenoid
Laser injection chamber
Laser injection chamber
New technology w/o brazing for RF gun realization (clamping and special gaskets)
e.m. design completed
Mechanical design: almost completed

## Slide 7
SW GUN: STRATEGY, PARAMETERS
RF gun
Mode launcher
Longitudinal electric field profile
2.5 cell
Powered with very short rf pulses (300 ns) of few tens of MW to reduce the pulsed heating (), BDR (5) and average dissipated power (allowing the high rep. rate operation);
Cathode peak field (Ecath)> 160 MV/m
4-port mode launcher (no quadrupole components, no pulsed heating)
New technology for its realization w/o brazing: hard copper
(Commercial) circulator is necessary: order done
Design compatible with 1 kHz rep. rate;
Parameter | value | 
Frequency [GHz] | 5.712 | 
Ecath/Pdiss [MV/(mMW0.5)] | 51.4 | 
Peak input power [MW] | 18 | 23
Cathode field [MV/m] | 160 | 180
Cathode type | copper | 
Rep. rate [Hz] | 1000 | 100
Quality factor | 11900 | 
Filling time [ns] | 166 | 
Coupling coefficient | 3 | 
RF pulse length [ns] | 300 | 
Esurf/Ecath | 0.96 | 
Mod. Poy. Vect. [W/m2] | 2.5 | 3.1
Pulsed heating [oC] | 16 | 20
Av.diss. Power [W] | 2300 | 300

## Slide 8
SW GUN: MAIN FEATURES
4 port mode launcher for quadrupole compensation and low pulsed heating
Coupling coefficient for short rf pulses
Dark current studies in progress;

## Slide 9: TW gun RF gun Design: NEW DESIGN
Started with the design by M Schaer (PR-AB19, 072001 (2016)).
Tolerance Studies demonstrated tight tolerance requirements for the cathode.
Concerns over chokes for the possibility of multipacting.
A new design was conceived based on tolerance studies.
A rigid (brazed) inner conductor on the coaxial couplers and a cathode threaded through the inner conductor which is removable.
All chokes were removed to prevent multipacting.
Misalignment in brazing can be fixed with a phase shift and adjustment of the cathode in z.
David Alesini– Task 7.4: Very high gradient RF Guns – Open Steering Committee 15-16 Nov 2021
Courtesy T. Lucas

## Slide 10: TW GUN: Dark Current Simulations
Field Enhance-ment Factor (β) | Effective area (Ae) [um^2] | Cathode Gradient [MV/m] | Charge arriving downstream (per 90ns RF pulse) [pC] | Capture Ratio | Total Field emitted charge (per 90ns RF pulse) [pC] | Peak Energy [MeV]
70 | 0.01 | 135 | 5.9 | 0.31 | 19.0 | 13.0
70 | 0.01 | 200 | 160.3 | 0.29 | 552.8 | 19.2
70 | 0.1 | 135 | 65.8 | 0.31 | 212.3 | 13.0
Simulations of dark current performed in CST.
Values of Ae and β taken from measurements of SwissFEL gun.
Dark current production less than 1 nC per RF pulse at 200 MV/m.
New design not expected to change this.
David Alesini– Task 7.4: Very high gradient RF Guns – Open Steering Committee 15-16 Nov 2021
Courtesy T. Lucas

## Slide 11: TW GUN: Thermal Simulations
Thermal Simulations performed in CST by coupling EM solver to Thermal Solver.
Heating from surface currents.
Convection coefficient for cooling water applied using empirical model.
No significant heating issues observed.
New design expected to perform better with a better thermal connection between end of cathode and cooling channels.
David Alesini– Task 7.4: Very high gradient RF Guns – Open Steering Committee 15-16 Nov 2021
TW GUN: SHORT TERM TIMELINE
Courtesy T. Lucas

## Slide 12: BUNKER@PSI: Status
HV klystron modulator is routinely running on C-band PSI loads (max power 50 MW)
Closure of the bunker: documents under preparation to get permission from BAG
Waveguide network: C-BOC and most of the RF components already at PSI
The bunker will be closed approximately at 19 m from the wall to ensure that he bunker meets safety standards with respect to emergency exits.
The bunker already has all water and electrical facilities installed
David Alesini– Task 7.4: Very high gradient RF Guns – Open Steering Committee 15-16 Nov 2021
Courtesy P. Craievich

## Slide 13
CONCLUSION
TIMESCHEDULE for SW, TW and BUNKER preparation well defined
DESIGN activities on both SW and TW guns started according to the established GANTT
NEXT STEPS:
    SW GUN: Concluding the mechanical design, solenoid design and its order
    TW GUN: Concluding the e.m. design and proceed with the mechanical one
    BUNKER: waiting for the authorizations (BAG) and work in parallel on control access, waveguides, etc…
MAIN CONTRIBUTORS
INFN-LNF: F. Cardelli, G. Di Raddo, A. Vannozzi, A. Giribono, L. Faillace, A.Gallo, L. Pellegrino (support on project management tools)
INFN-ROMA1: L. Ficcadenti, G. Pedrocchi, G. Castorina
PSI: P. Craievich, T. Lucas, R. Fortunati, R. Zennaro, M. Pedrozzi, F. Marcellini, W. Tron
David Alesini– Task 7.4: Very high gradient RF Guns – Open Steering Committee 15-16 Nov 2021
This project has received funding from the European Union’s Horizon 2020 Research and Innovation programme under GA No101004730.
THANK YOU FOR YOUR ATTENTION