## Slide 1: Welding lathe MFHX70-004 replacement
Laurent Prever-Loiri (EN-MME-FW)
26th November 2021

## Slide 2: Welding lathe for Ultra-High-Vacuum aluminium chambers
Specificities of this unique welding equipment & main applications
Design of the new welding Lathe
CE Certification Process
Planning of Manufacturing & cost of Fabrication

## Slide 3
Welding lathe MFHX70-004:
  Length. 3800 mm
Length: 3800 mm
Height of welding axis: 1200 mm
Aperture: 250 mm
Date of commissioning January 1960
Brackets
Base
Thermalized Clamping Tool
Aluminium Chamber
Synchronized
Rotary device

## Slide 4: Experiments aluminium chambers welding requirements
Clamping Tool + Thermal regulation
Segments of chambers
Cooling tubes
No tack welding
Contact force
Contact force
DC current Welding

## Slide 5: Examples of Welding Assembly Aluminium Chambers for detectors

## Slide 6: Modification of Beryllium Chamber VI ATLAS

## Slide 7: CMS HF CT2 Chamber

## Slide 8: CMS End Cap Chamber

## Slide 9: Double Aluminium Bellows for ALICE

## Slide 10: Why this equipment shall be consolidated?
Reliability issues (recurring failures e.g. driving system, control system)
Safety issues (danger of catching or entrapment)
Compatibility issues with UHV applications (risk of oil pollution, air stream perturbation)
Refurbishment would not be adapted, decision to replace the equipment
No similar equipment available on the market → in house design and fabrication

## Slide 11: Study of the new welding lathe
  Definition of technical requirements
  Standard components research
  Design of 3D model
  Integration of safety aspects

## Slide 12: Technical Requirements
Mechanical Characteristics:
Welding lathe shall have a synchronized a double rotary system to avoid a twist effect
The system shall guaranty a very good alignment between components to be welded
Compression device ensuring contact of the pipe before welding and allowing free dilatation and shrinkage during welding
Aperture diameter of motorization need to be large, more of 310 mm
Shall be compatible with existing clamping tools
Brackets shall be movable to allow extraction of chambers with specific shape
Dimension of base : 3500 mm x 600 mm x 400 mm
Height of the welding rotation axis: 1200 mm

## Slide 13: Technical Requirements
Operational Characteristics:
Compatibility with various welding sources
Welding lathe shall be compatible with UHV requirements
Shall be operated by one or two operators in direct contact with the moving parts
Possibility to work with one or two rotary system
Shall be easy to operate; intuitive HMI interface

## Slide 14: Call for tender motorisation + HMI
Technical Specification Supply of two of High Accuracy Large Aperture EDMS 2616612
DO-33019
Mechanical Characteristics | 
External dimensions | Maximum 550 mm x 550 mm x 120 mm
Aperture | Minimum 310 mm
Type of motorization | Direct-drive (permanent-magnet synchronous motor)
Positioning accuracy | ≤ ± 10 µrad
Bidirectional Repeatability | ≤ ± 5 µrad
Load capacity | Radial: ≥ 250 kg at 100 mm from the faceplate Axial: ≥ 250 kg
Maximum Torque | ≥ 200 Nm
Speed range | From 0.04 to 32 rpm
Position feedback | Incremental Encoder
Compact motorisation
Large aperture
High accuracy

## Slide 15: Human Machine Interface (Hardware)
Control panel with the following features:
  Two Emergencies stop buttons;
  A start cycle button;
  A stop cycle button;
  A potentiometer to adjust the rotation speed;
  A home button to return to home position;
  A Joystick to rotate the selected Stage(s) in a direction specified by the button.
Start cycle
Stop cycle
Home
Emergency stop
Joystick for manual rotation
Computer screen
/ HMI Tactile

## Slide 16: Human Machine Interface (Software)
  A simplified graphical user interface operating the controller. The screen shall include the following functions:
    Saving and loading of programs
    Welding diameter display and input
    Speed display and input;
    Angular position display and input;
    Selection of motor (left, right or both)
    A sector graph enabling variable speed for up to 8 sectors with the following information and inputs:
Welding Diameter (mm)
Speed (mm/s)
Rotation Angle (°)
Direction (+/-)
Nombre de secteurs
File
Home
Edit
3
Sector 3
Sector 1
Sector 2
Vitesse (mm/s)
1
2
3
Number of motor (L, R, Both)
Angle du secteur (°)
Angular Position (°)
Real Speed (mm/s)
Over Lapp (°)

## Slide 17: Design of a new Welding Bench
Two rails with 14 trolleys
Granit base
Centering tool
Centering tool
Articulated arm with a welding torch
and his setting system
Adjustable compression device
Two adjustable mounting brackets

## Slide 18: Design of a new Welding Bench
Rack with controllers
Articulated arm or pedestal with a HMI interface
Two synchronised motorisations

## Slide 19: Questions

## Slide 20: CE Certification Process

## Slide 21: CE Certification Process
  Risk analysis
  Risk mitigation and implementation in design
  Manufacturing of the welding lathe
  Drafting of the instruction manual
  Final conformity check
  CE Certification provide by CERN
  Decision to be assisted by a Notified Body : DEKRA

## Slide 22: Risk Analysis
    Risk analysis EDMS 2664483 “DEKRA report”

## Slide 23: Risk Analysis

## Slide 24: Risk Analysis: highlights

## Slide 25: Where are we now?
  Risk analysis: done
  Risk mitigation and implementation in design: ongoing
  Manufacturing of the welding lathe
    Complete 3D design (already done at 90%), detailed drawings: to be done
    Call for tender for the Motorisation and HMI procurement: done
    Cost estimate 256 kCHF, in accordance with ACC-CONS budget
  Drafting of the instruction manual: to be done
  Final conformity check

## Slide 26: Planning of Manufacturing
In line with ACC-CONS schedule

## Slide 27: Thank you

## Slide 29: Cost of Fabrication
Study: 30,000 CHF
Motorization with controllers and HMI: 140,000 CHF
Granit base: 8,000 CHF
Rails and trolley: 8,000 CHF
Frame + Mounting brackets + accessories: 50,000 CHF
CE Certification process including DEKRA support: 10,000 CHF
Welding lathe assembly & commissioning: 10,000CHF
Total cost: 256,000 CHF
In line with ACC-CONS budget