## Slide 1: HOM coupler modelling for SPL
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK
H.-W. Glock
Universität Rostock - Institut für Allgemeine Elektrotechnik
26.11.2010
5th SPL Collaboration Meeting, CERN, 25./26.11.2010

## Slide 2: What we are talking about:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
2
(drawing: Thierry Renaglia, CERN, 21.7.2010)
704-MHz-SPL-beta-1-Cavity
Dri = 140mm
Dle = 130mm
Dpipe = 80mm
power coupler port
D=90mm
"right" side HOM coupler port
opposed to power c., D= 36mm
"left" side HOM coupler port
rotated by 60° towards you
(not drawn)
Qsecure ≤ 105: HOM coupler not popular, but seem to be not to avoidable

## Slide 3: "Classical" LEP hook design as starting point (priv.com. WW)
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
3
coaxial 50-Ohm-port
(connector not modelled)
adjustable capacitive coupling
combined E-/H-field coupling,
capacity couples to outer conductor
support carries liquid helium
reminder

## Slide 4: E-field geometry @ 704 MHz
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
4
strong capacitive coupling between "hook" and outer conductor
capacitive coupling at hook determines notch resonance frequency
reminder

## Slide 5: Pure hook not tunable for 704 MHz => Modification of hook end in order to adjust fundamental mode notch filter
20.9.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
5
enlarge capacitive coupling at hook with additional surface element
reminder

## Slide 6: Waveguide(TM0)–Coax–Transmission blocked @ fundamental mode frequency => Tuning ok
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
6
reminder

## Slide 7: Some geometrical details
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
7
Penetration depth of the antenna/loop in the beam pipe could be increased, but:
risc of dark current heating,
impedance
Mechanical stability, esp. against oscillations, may be an issue.
But: LHC cavs. use similar concept (courtesy W.W.)

## Slide 8: Remarks about fundamental mode notch filter:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
8
1.) Tuning rather sensitive both against capacity surface AND rotation angle (~5 MHz/Degree 30 dB/Degree)
2.) => notch filter understood as combination of resonance AND "directional coupler"-effect: certain E-H-correlation causes cancelation
3.) This demands for external re-tuning capability after mounting (e.g. rotation)

## Slide 9: Why looking for a single S-parameter during tuning?:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
9
Fundamental mode is of TM0-type (no dependence on angle around axis).
Thus it directly couples only to TM01, TM02, ... waveguide modes, all below cut-off @ 704 MHz.
Neglecting all higher types than TM01 causes very small error but significantly reduces numerical effort.
TM01-Mode H-field

## Slide 10: Q-ext computations based on:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
10
CSC-coupling of 8 modes in D=130mm/140mm-coupler-cavity-connections (TE11,TM01, TE21,TM11,TE01)
right coupler both w/o power coupler (90mm coax, 50 Ohm, penetration depth freely chosen)
D=80mm beam pipes left open (but most below cut-off)

## Slide 11: Scattering parameter computation:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
11
Using "Fast-Resonant"-Solver of CST MicrowaveStudio© (ver. 2010-7)
taking S-parameter from multimodal Z-matrix using analytical waveguide impedance expressions (most secure way)
typical computation time: ~several hours; therefore during optimization use of tetrahedral grid, applied to few frequency points (=> ~fraction of hours/configuration)

## Slide 12: This (cst-computation, csc-concatenation) gives HOM1-HOM2 transmission:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
12
red: HOM coupler only, green with matched power coupler
presence of power coupler lifts transmission level and seem to decrease Qs
f/Hz
Shom1-hom2 /dB

## Slide 13: Put this in resonance-fit-algorithm in order to determine Qs:
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
13
red: HOM coupler only, green with matched power coupler
main power coupler helps significantly below 2 GHz; still Qs > 10^6 found
f/Hz
Log10(Q)

## Slide 14: Conclusion
26.11.2010
© 2010 UNIVERSITÄT ROSTOCK | FAKULTÄT INFORMATIK UND ELEKTROTECHNIK H.-W. Glock
14
23/02/2010
14
tuning successful, but: sensitive setup, 180° rotation seem to hinder "directional coupler"- effect
Q values w/o main power coupler computed, closer to 10^5, but not reached