## Slide 1: Task 2.6: Ions – operational scenario
  Recap: Updated operational scenario worked out and published (CERN-ACC-report and EPJ plus paper)
    However, in assumption of 50% OP efficiency, short of experiments’ targets (for Pb-Pb about 10% missing at worst IP for the best filling scheme, for p-Pb factor 2 missing at LHCb)
  Recent updates
    My talk at WP2 meeting
      Found ways to reach Pb-Pb targets: combinations of smaller β*, smaller crossing or beam-beam separation, higher levelling targets
      Found ways to reach p-Pb target at LHCb: strong increase of proton bunch intensity; solutions with both 25ns and 50ns proton beams; developed new realistic filling schemes
    Talk by Sofia: Can tolerate vertical crossing in both ATLAS/CMS for Pb-Pb
    Talk by Riccardo: Aperture is OK for proposed ALICE beam pipe upgrade
    Talk by Marta:
  Next steps:
    Consolidate and validate performance improvements
      Can we learn anything more now from beam-beam simulations, e.g. for p-Pb with higher proton intensity?
      Simulate V/V crossing for p-Pb?
    Ideally, need beam studies (aperture measurements, possibly beam-beam)- make overview of needed ion MDs in Run 3 and prioritize
      other high-priority items: BFPP quench test (to verify luminosity reach), collimation schemes and quench test (to verify intensity reach with crystals)
    Proposed strategy: use present baseline in 2022 (with optics similar to 2018), and do further studies to arrive at improved configuration for later runs
      Need anyway minor optics work to adapt 2018 optics to Run 3
    With conclusions on new scenario, develop new HL-LHC ion optics if needed (possibly for 2023 or 2024)
    With WP5: study and optimize collimation scenarios
    With WP10 and WP5: continue studies of collision products and their energy deposition, if resources are available (e.g. BFPP for Pb-Pb in IR8, p-Pb in IR2/8)
  timeline in Google doc for updated operational scenario looks too tight if we need inputs from 2022 beam tests

## Slide 2: Task 2.6: Ions – light ions for beyond Run 4
Reminder: present baseline has no ion runs beyond Run 4, but serious studies are ongoing to extend to Run 5/6…
  ALICE3 letter of intent under finalization
  Possibility to achieve higher nucleon-nucleon luminosity with lighter ion species than Pb
Previous estimates for LHC performance with various lighter species shown in yellow report
Recent update shown at WP2 meeting: including realistic injector limitations, we get much lower bunch intensities and LHC luminosity
  Explored also some paths for improved performance, but need to be demonstrated
Next steps: Further studies of performance improvements
  In collaboration with injectors, more detailed studies of collective effects in injectors
  In collaboration with injectors, possibly do beam studies in Run 3: several MDs proposed by Reyes
  We will hopefully learn a lot from the Run 3 pilot oxygen run
  Once we have an updated Pb scenario, we assume these machine settings for light-ion operation and update performance estimates
  With WP5, need to study limitations from losses (collimation efficiency, beam transmutation)
Write up and publish studies