## Slide 1: HL-LHC IT String Validation Program
D. Gamba
WP2/WP4 Meeting – 30th November 2021

## Slide 2: IT String Program is Being Finalized!
A series of meetings to discuss the IT String program took place during 2021 (see indico)
Main input/interest form WP2 (see indico) was linked to
  ground motion (measurement of ground-to-coldmass transfer function)
  flux jumps (no B-field measurement will be possible, but only voltages/currents logged to spot and possibly quantify the size/rate of flux jumps)
Additional “operational” tests where identified and summarized in the last presentation by Samer (see indico)
  E.g. FRAS and Q1A k-modulation tests
  See next slides for all planned WP2/OP tests
All planned tests are being summarized in HL-LHC IT String Validation Program - EDMS #2664290
  Test procedures will need to be written/validated early 2022
Question to WP2:
  is there some other test we should have asked for?

## Slide 3: WP2 and Beam Operation Tests
Requirement ID | Test Name | Items to Test | Goal of the Test | Warm or Cold
WP2 and Beam Operations |  |  |  | 
WP2-1 | Ground-to-Cold-Mass Transfer Function (TF) Tests | Q1 and Q2a | Validate the estimated transfer functions to determine the expected vibration of the triplets and the impact on luminosity and emittance blow-up for both Q1 and Q2a before and after interconnection. | W & C
WP2-2 | Alignment Tests | Cold masses alignment procedures and tolerances | Validate the procedures for the Fully Remote Alignment System (FRAS) and define the expected tolerances on which WP2 is relying the definition of the corrector strength. | C
WP2-3 | Alignment Tests during Powering | FRAS | Operation of FRAS with powered magnets (ideally at top energy, tbc) which might be requested for the commissioning of HL-LHC. | C
WP2-4 | K-modulation Powering | Triplet circuit | Validate the Q1a K-modulation at top energy with sinusoidal trim 35A which is required in optics commissioning in HL-LHC. | C
WP2-5 | Triplet Trim Powering | Triplet circuit | ±1% trim on Q1 and Q3 at top energy (sinusoid optional) which is required for optics commissioning. | C
WP2-6 | Triplet Trim Powering | Triplet circuit | Ramping the triplet with less current in Q1/Q3 and in Q2 (Amplitude to be defined in the order of 500 A) and trimming down the current in Q1/Q3 and in Q2 after reaching nominal. | C
Courtesy S. Yammine - indico

## Slide 4: WP2 and Beam Operation Tests
Requirement ID | Test Name | Items to Test | Goal of the Test | Warm or Cold
WP2 and Beam Operations |  |  |  | 
WP2-7 | Orbit Corrector Tuning Tests | RCBX circuits | Tuning of orbit correction knobs (in relation to the crossing angle, the crab cavity settings, etc.) which is required in normal operation. | C
WP2-8 | HOC Powering Combinations | HOC circuits | Relevant combination at max strengths and at both signs which is required for nominal operation. | C
WP2-9 | Tuning of D1 Powering | RD1 circuit | Trim of some tens of amps at top energy even if not foreseen in nominal operation but is considered as a potential back-up for operations. | C
WP2-10 | Orbit Feedback Tests | RCBX circuits | Validate the expected trims from the orbit feedback which is required for normal operation. | C
WP2-11 | Flux Jumps Measurements | Triplet circuit | Acquire data on the flux jumps and estimate the eventual impact on the magnets field and the power converter stability and control. | C
WP2-12 | Nominal Beam Cycle | All Circuits | Verification of the nominal performance of the circuits through nominal beam cycles (ramp-up, squeeze, collision and ramp-down). | C
Courtesy S. Yammine - indico