## Slide 1: Space Gravitational Wave Antenna DECIGO
Seiji Kawamura (Nagoya University) and DECIGO working group
Physics in LHC and Beyond
May 15, 2022 @Matsue, Japan

## Slide 2: Outline
Introduction
DECIGO
  Design and Science
  Update of design
B-DECIGO
  Design and Science
Summary

## Slide 3: Establishment of gravitational wave astronomy

## Slide 4: GW detector in space
Arm length: much longer than ground-based detectors (GBD).
Signal increases at low frequencies
－Longer interaction between GW and light
Noise decreases at low frequencies
－No seismic noise and less Newtonian noise
Sensitivity improves at low frequencies
Furthermore, expected GW signals larger

## Slide 5: Laser Interferometer Space Antenna (LISA)
LISA project

## Slide 6: What is DECIGO?
Deci-hertz Interferometer Gravitational Wave Observatory
Bridges the gap between LISA and GBDs
  Follow-up for LISA, Predictor for ground-based detectors
Low confusion noise -> Extremely high sensitivity
10-18
10-24
10-22
10-20
10-4
104
102
100
10-2
Frequency [Hz]
Strain [Hz-1/2]
LISA
DECIGO
GBDs
Confusion limiting noise
Moving above
LISA band
Moving into
GBD band
  Seto, Kawamura, Nakamura, PRL, 2001
  Kawamura et al., PTEP 2021

## Slide 8: Pre-conceptual design
Thruster
FP cavity
Drag-free spacecraft
Mirror
d: 1 m
M: 100 kg
Laser
P: 10 W
: 0.515 m
1,000 km

## Slide 9: Orbit and constellation (preliminary)
Sun
Earth
Record disk
Increase angular resolution
Correlation for primordial GW

## Slide 10: Target sensitivity and science
Primordial GW
Intermediate-mass BH
Frequency [Hz]
Correlation
(3 years)
Strain [Hz-1/2]
10-3 10-2 10-1 1 10 102 103
10-19
10-20
10-21
10-22
10-23
10-24
10-25
10-26
BH-BH
Coalescence
NS-NS (z=1)
1 cluster
PGW (GW~1×10-16)
BH-NS
(10 M z=1)
PBH related
(1000 M z=10)
5 years
3 months
Acceleration of expansion of Universe
Dark Matter
General relativity
  Seto, Kawamura, Nakamura 2001
  Yagi, Tanaka 2010
  Saito, Yokoyama 2009, 2011
PGW (GW~2×10-15)
  Design parameters:
  under optimization for PGW
Prediction of BNS coalescence
  Takahashi, Nakamura 2003

## Slide 11: Primordial GW
Direct observation of primordial GWs from inflation
  Whether Inflation really happened?
  Which inflation model is correct?
  Parity violation?（Clockwise and counterclockwise GW）
    Seto 2007
  Separation of Tensor, Vector, scalar mode
    Nishizawa, Taruya, Kawamura 2010

## Slide 12: Acceleration of Expansion of the Universe
NS-NS (z～1)
GW
DECIGO
Output
Expansion
Time
Strain
GW (No Acceleration)
Phase Delay～1sec (10 years)
Seto, Kawamura, Nakamura, PRL 87, 221103 (2001)
GW (with Acceleration)
＋Acceleration

## Slide 13: DECIGO and gamma-ray burst (GRB)
Prediction of NS-NS coalescence
  z<5; 5 years before coalescence
  Expected event rate: 106 /year (300 /day)
  Angular accuracy：1 arcsec
Assuming short GRB comes from NS-NS coalescence
  Assuming 1/30 of short GRB can be detected (beaming effect)
  Expected event rate: 10 /day
Frequent and detailed observation of GRB by electro-magnetic waves

## Slide 14: Gravitational waves as a probe of extended scalar sectors
Kakizaki, Kanemura, Matsui, PRD 92 (2015) 115007; modified by Kanemura
GW expected from strongly first order phase transition at the electroweak symmetry breaking
: related to amplitude of GW
: related to peak frequency
N: Number of additional scalar fields
ms: Mass of scalar field
Latent heat
1/Phase transition time

## Slide 15: Requirements
Force noise: 25 times more stringent than LISA
  Comparable in terms of strain; distance: 1/2500, mirror mass: 100
Sensor noise: 30 times looser than KAGRA
  Comparable in terms of strain; storage time: 30
KAGRA

## Slide 16: Update of PGW
Frequency [Hz]
Correlation
(3 years)
Strain [Hz-1/2]
10-3 10-2 10-1 1 10 102 103
10-19
10-20
10-21
10-22
10-23
10-24
10-25
10-26
1 cluster
PGW (GW~1×10-16)
PGW (GW~2×10-15)
The upper limit of PGW has been reduced by the Planck observations.
The target sensitivity of DECIGO should be improved to enhance the possibility of detection of PGW.

## Slide 17: Procedure of update of design
Step 1
  Optimization considering only quantum noise
Step 2
  Optimization including other noise sources
    Thermal noise
    Confusion limiting noise by GWs from double white dwarf (DWD) binaries
Step 3
  Optimization considering practical constraints

## Slide 18: Step 1: Optimization with quantum noise
Iwaguchi, et al., Galaxies 9 (2021) 9010009
Ishikawa, et al., Galaxies 9 (2021) 9010014
The following parameters are optimized for the best SNR for a given mirror radius
  Cavity length
  Reflectivity of mirror
  Laser power (up to 100 W)
Considering only quantum noise
Constant mirror mass is assumed

## Slide 19: Step 2: Optimization with thermal noise and DWD noise
Values/type for each model: 23 in total
Design parameters
For a given radius,
optimize the other parameters
Parameter | Range
Mirror radius | 0～1 m
reflectivity | 0～1
Laser power | 0～100 W
Arm length | No limit
Parameter | Value
Cut-off frequency | 0.07 Hz / 0.1 Hz
Pressure inside spacecraft | 10-8 Pa / 10-9 Pa
Mirror model | Constant mass (100 kg) / Constant thickness (0.5 m, 100 kg)

## Slide 20: Results
Cut-off frequency: 0.1Hz Cut-off frequency: 0.07Hz
Constant thickness
Constant mass
10-8 Pa
10-8 Pa
10-9 Pa
10-9 Pa
Kawasaki, et al., Galaxies 10 (2022) 10010025

## Slide 21: Step 3: Optimization with practical constraints
A dedicated team of experts inside the DECIGO working group is now being convened.
The team will soon start the final optimization, using the framework that was created in step 2.

## Slide 22: B-DECIGO: scientific pathfinder
Thruster
FP cavity
Drag-free spacecraft
Mirror
d: 0.3 m (1 m)
M: 30 kg (100 kg)
Laser
P: 1 W (10 W)
: 0.515 m
100 km
(1,000 km)
Orbit: TBD
(Heliocentric orbit)
# of clusters: 1 (4)
Aim to launch in 2034
* (for DECIGO)

## Slide 23: B-DECIGO: Target sensitivity and objectives
Frequency [Hz]
Strain [Hz-1/2]
10-3 10-2 10-1 1 10 102 103
10-19
10-20
10-21
10-22
10-23
10-24
10-25
10-26
BH-BH
Coalescence
NS-NS
(z=1)
Coalescence
BH-NS
(10 M z=1)
PBH related
(1000 M z=10)
5 years
3 months
Observation of NS-NS (BH) binary
  Prediction of timing of NS-NS (BH) coalescence
  100 /year
Revelation of origin of ~30 M BBH (Nakamura+ 2016)
Much better parameter estimation of binaries (Isoyama+ 2018)
Removal of foreground for DECIGO
Verification of technologies for DECIGO
PGW (GW~1×10-16)
1 cluster

## Slide 24: Progress on technologies for B-DECIGO
Bi-directional interferometer Low-noise thruster
High-power stabilized laser

## Slide 25: Related mission: SILVIA
Space Interferometer Laboratory Voyaging towards Innovative Applications
Small satellite mission by formation flight official WG at ISAS/JAXA in collaboration with DECIGO team and infrared interferometer team (and possibly X-ray interferometer team)
Objectives and scope
  Demonstration of the formation flying technologies
Recent progress
  Feb. 2020: SILVIA mission proposed to ISAS
  Aug. 2020: Approved to proceed to Pre-Phase A1b (Idea implementation process)
  Only SILVIA selected among seven missions that applied
Next step
  Review to judge for Pre-phase A2 (Mission definition)
  If approved, will become a candidate mission for the 5th or 6th small satellite mission

## Slide 26: Summary
DECIGO will accomplish a variety of amazing science including direct observation of primordial GW to reveal the secret of the birth of the Universe.
B-DECIGO will verify technologies for DECIGO as well as accomplish a variety of fruitful science including prediction of NS-NS coalescence to reveal its mechanism.
SILVIA will establish the essential technologies for B-DECIGO and DECIGO.
Image of
B-DECIGO
©NEC