## Slide 1
1 March 2022
SoLAr: an overview
Solar Neutrinos in Liquid Argon
Guilherme Ruiz Ferreira
PhD Student
The University of Manchester

## Slide 2
Detector Geometry
Motivation
Detector Readout
Conclusion
Presentation Outline

## Slide 3
SoLAr is a new concept for a liquid-argon neutrino detector.
The goal: extend the sensitivities to the MeV energy range by combining charge and light readout on one plane
The concept is also a possible technology choice for the DUNE “Module of Opportunity“.
SoLAr collaboration established March 2022
What is SoLAr?
arXiv:2203.07501

## Slide 4
SoLAr Novelty
The traditional wire planes used for LArTPCs are replaced by a modular pixel design
The readout unit will be a pixel tile that embeds charge readout pads and Silicon Photon Multipliers (SiPM).
Each tile produces signals corresponding to the charge of the electrons collected in each pixel and to the photons collected in the pixel frame, respectively.

## Slide 5
Motivation
Detector Geometry
Detector Readout
Conclusion
Presentation Outline

## Slide 6
Initial concept:
100mm x 100mm x 3mm square board
100 6mm x 6mm x 2mm SiPMs
500 3mm x 3mm x 0.5mm charge pixels
500V per cm drift field
Cathode at -5000V
SiPM negatively biased with ΔV=53V
How does the electric field behave?
Prototyping
Pixel
SiPM

## Slide 7
Using the Finite Element Analysis (FEA) software “COMSOL Multiphysics”, we modelled the electrostatic field in the TPC.
We started with a simple 2D model, then evolved to 3D with different variations of the charge pixel geometry and SiPM bias.
Which combination of geometry and bias yield the most efficient electric field?
Electric Field Modelling
10cm

## Slide 8
Using the Finite Element Analysis (FEA) software “COMSOL Multiphysics”, we modelled the electrostatic field in the TPC.
We started with a simple 2D model, then evolved to 3D with different variations of the charge pixel geometry and SiPM bias.
Which combination of geometry and bias yield the most efficient electric field?
Electric Field Modelling

## Slide 9
Version 1
3mm x 3mm x 0.5 mm rectangular charge pixel
3mm x 3mm x 3 mm charge pixel with rounded top (1.5mm x 1.5mm x 1.0mm dome)
Version 3
3mm x 3mm x 3 mm square charge pixel with rounded corners (0.5mm radius)
Version 2
Pixel Geometry Concepts
SiPM
SiPM
SiPM
Pixel
Pixel
Pixel

## Slide 10
3D visualization of the electric field is extremely hard
We made a number of cuts in the 3D object in different axis and coordinates to obtain 2D cross section plots
Each cut allows us to explore a different aspect of the TPC
Electric Field Visualization

## Slide 11
3D visualization of the electric field is extremely hard
We made a number of cuts in the 3D object in different axis and coordinates to obtain 2D cross section plots
Each cut allows us to explore a different aspect of the TPC
We focused on a plane through the centre of the pixels and SiPMs near the TPC centre
Electric Field Visualization

## Slide 12
Version 1
SiPM biased -300V on top and -247 on bottom
SiPM biased -100V on top and -47 on bottom
Version 3
SiPM biased -100V on top and -47 on bottom
Version 2
Best SiPM Bias Configuration (so far)

## Slide 13
COMSOL does not simulate drifting electrons.
As a proxy, we use the fraction of electric field lines passing through the SiPM top surface to calculate the loss of charge, and hence calculate the expected charge collection efficacy.
1) we define a surface cutting the anode slightly above the SiPM top but below the charge pixel top (2.05mm from PCB surface) and excluding the anode edges.
Charge Collection Efficacy (?)

## Slide 14
2) We define a surface the same size but at the centre of the TPC (50mm from the PCB and Cathode)
By integrating the Z-component of the electric field where Z ≥ 0 over each surface and calculating their ratio, we obtain the fraction of the electric field lines ending in the SiPM surface.
These would be the lines where electrons are not captured by the charge pixels.
Charge Collection Efficacy (?)

## Slide 15
Version 2
Version 1
Version 3
Efficacy ?%
Even though we are unable to use our proxy method to obtain an efficacy value, it is clear from the plots that this is the least efficient geometry and requires a larger SiPM bias.
Efficacy 96%
This version has the advantage over version 3 of having a simple geometry for real life production.
It also allows the SiPM to operate in a lower bias than version 1
Efficacy 99%
Despite of having a more complicated geometry for real life production, this version yields the best efficacy we obtained so far.
Charge Collection Efficacy Proxy

## Slide 16
Motivation
Detector Readout
Detector Geometry
Conclusion
Presentation Outline

## Slide 17
Q-Pix offers an innovation in signal capture with a new approach and measures time-to-charge (ΔQ), which Keeps the detailed waveform information from the LArTPC.
The readout follows the “electronic principle of least action”, i.e. don’t do anything unless there is something to do.
Total charge for any RTD = ΔQ
What is RTD?
The difference between sequential pixel resets, i.e. Reset Time Difference = RTD
RTD’s measure the instantaneous current and captures the waveform.
Small average current = Large RTD
Large average current (signal) = Small RTD
Q-Pix Readout Novelty

## Slide 18
The Q-Pix RTD simulation is comprised of 3 “layers”:
Event generation – MARLEY (Model of Argon Reaction Low Energy Yields)
  Creates the neutrino events for both Charged Current (CC) and Elastic Scattering (ES) processes
Particle propagation and interaction through the LArTPC – Geant4
  Produces the hits the detector is expected to detect
Pixel triggering simulation (RTD) – Custom made code
  Takes the Geant4 hits and converts into charge deposit into the pixels which then reset when their ∆Q threshold is reached.
Q-Pix RTD Simulations

## Slide 19
Neutrino Initial Energy - CC
Neutrino Initial Energy - ES
B8 Reaction Event Simulations

## Slide 20
Deposited Energy - CC
Deposited Energy - ES
B8 Reaction Event Simulations

## Slide 21
Deposited Energy Ratio - CC
Deposited Energy Ratio - ES
B8 Reaction Event Simulations
Charged current “mostly” preserves the incoming neutrino energy spectrum

## Slide 22
Electron Scatter Angle- CC
Electron Scatter Angle- ES
B8 Reaction Event Simulations
Elastic scattering preserves the incoming neutrino direction

## Slide 23
Q-Pix RTD simulations
How well can the detector identify signal events from RTDs?
We begin by defining 2 parameters:
  Completeness: Out of all signal events, how many are we able to detect?
  Cleanliness: Out of all the events detected, how many are signal?
Then we use a simple DBSCAN algorithm to cluster the pixel resets and compute the Completeness and Cleanliness for varied combinations of input parameters
  Density-based spatial clustering of applications with noise (DBSCAN) is one of the most common data clustering algorithm in the scientific literature.
  Input parameters: Minimum number of samples (resets) and maximum distance (ε) between them to consider part of the same cluster

## Slide 24
Completeness & Cleanliness - CC
Weighted histogram of completeness and cleanliness logical association*
Arbitrarily normalized for better visualization.
Energy spectrum after data cuts - CC
B8 Reaction Completeness & Cleanliness
All
Valid
Optimum
* Completeness multiplied by cleanliness term by term
Valid cut excludes DBSCAN clustering failures
Optimum values:
Min samples = 14
ε = 3.2
Repeating pattern due to anode geometry with
Equal sized repeating pixels
Energy spectrum mostly preserved after cuts

## Slide 25
Completeness & Cleanliness - ES
Weighted histogram of completeness and cleanliness logical association*
Arbitrarily normalized for better visualization.
Energy spectrum after data cuts - ES
B8 Reaction Completeness & Cleanliness
All
Valid
Optimum
* Completeness multiplied by cleanliness term by term
Valid cut excludes DBSCAN clustering failures
Optimum values:
Min samples = 14
ε = 3.2
Optimum parameters seem to depend on the geometry of the detector but not on the scattering process
Events below 6 MeV are lost as the produce few resets

## Slide 26
Motivation
Conclusion
Detector Readout
Detector Geometry
Presentation outline

## Slide 27
The detector geometry is still being studied and optimized based on the electric field simulations and production practicality
We have found potential configurations which maximize charge collection on pixels and protects the SiPMs from strong fields
Geometry
Readout
Next steps
Continue our studies of the detector geometry for the first prototype
Proceed into calibrating the Q-Pix detector dE/dX using the RTD simulations
Conclusions
Based on preliminary simulations, we are able to determine the energy spectrum of the incoming neutrinos from CC events and their incoming direction from ES events.
Using a simple DBSCAN algorithm we managed to cluster resets on signal events above 6 MeV with good completeness and cleanliness values.