## Slide 1: Cooling systems by AM
Samuel Unterhofer, Olha Sereda CSEM
March 30th, 2022

## Slide 2: AIDAINNOVA
  Select materials
  Parts production
  Post processing
  Characterization
Define the optimal geometrical features attainable for 3D printed ultra-thin cold plates in metal alloys

## Slide 3: AIDAINNOVA
  Select materials
  Parts production
  Post processing
  Characterization
AlSi12 | INVAR/COVAR
AM experience | No AM experience
Better thermal conductivity | Worse thermal conductivity
Worse CTE | Better CTE
  First project part
  Second project part

## Slide 4: AIDAINNOVA
    Geometrical features
    Powder removal
  Select materials
  Parts production
  Post processing
  Characterization
0.8mm x 1.8mm channels
0.25 mm wall thickness
No. channels 48
Condenser section 24mm
    First printing is planned for 02-04.05.2022
Notes: Straight & 180° bent, minimum wall thickness, single pipe & multi-microchannel

## Slide 5: AIDAINNOVA
    Heat treatments
    HIP
    Chemical etching (to assure particle removal)
  Select materials
  Parts production
  Post processing
  Characterization

## Slide 6: AIDAINNOVA
    Dimensional measurements
    Pressure leakage
    Roughness & flatness
    Thermal tests
  Select materials
  Parts production
  Post processing
  Characterization
Notes: Diameter to length ratio
Minimum wall thickness