## Slide 1: Design activities towards stitched sensor
Geunhee Hong
Yonsei University

## Slide 2: Outline
Introduction
  ITS3 detector concept
  ITS3 timeline
MLR1
  Chip production
  TTS Measurement
ER1
  MOSS Monolithic Stitched Sensor
  Digital pixel implementation
Next generation sensor design for LS3

## Slide 3: Introduction
ITS3 detector concept
  The inner barrel in ITS2 is ultra-light but rather packed and irregular
  circuit board (power&data) / mechanical support / water cooling
   Integrating on chip / Rolling Si Wafer / power consumption below 20mW/cm2
https://indico.cern.ch/event/932973/contributions/4073514/attachments/2141373/3608219/2020-11-12_FCC_ALICE_MAPS.pdf
“Technical Design Report for the Upgrade of the ALICE Inner Tracking”. ALICE Collaboration, B. Abelev et al. System. J. Phys. G 41, 087002 (2014).
https://indico.ph.liv.ac.uk/event/2/contributions/144/attachments/94/125/MBuckland_ALICE_HEPXmasMeeting.pdf
Inner Barrel

## Slide 4: ITS3 detector concept
Chip size is traditionally limited by CMOS manufacturing (“reticle size”)
  typical sizes of few cm2
  modules are tiled with chips connected to a flexible printed circuit board
New option: stitching, i.e. aligned exposures of a reticle to produce larger circuits
  actively used in industry
  a 300 mm wafer can house a chip to equip a full half-layer
https://indico.cern.ch/event/813597/contributions/3727803/attachments/1989307/3315951/2020-02-18_Trento2020_ITS3.pdf
https://indico.cern.ch/event/813597/contributions/3727803/attachments/1989307/3315951/2020-02-18_Trento2020_ITS3.pdf

## Slide 5: ITS3 detector concept
Key ingredients:
  300 mm wafer-scale chips, fabricated using stitching
  thinned down to 20-40 μm (0.02-0.04% X0), making them flexible
  bent to the target radii
  mechanically hold in place by carbon foam ribs
Key benefits:
  extremely low material budget: 0.02-0.04% X0 (beampipe: 500 μm Be: 0.14% X0)
  homogeneous material distribution: essentially zero systematic error from material distribution
“Technical Design Report for the Upgrade of the ALICE Inner Tracking”. ALICE Collaboration, B. Abelev et al. System. J. Phys. G 41, 087002 (2014).
https://indico.ph.liv.ac.uk/event/2/contributions/144/attachments/94/125/MBuckland_ALICE_HEPXmasMeeting.pdf
https://indico.cern.ch/event/974424/contributions/4158313/attachments/2185864/3693273/2021-02-08_DAQFEET-ITS3sensor.pdf
Inner Barrel

## Slide 7: MLR1 production
GDS submission in Dec 2020
Chip delivery in July 2021

## Slide 8
https://indico.cern.ch/event/1071914/

## Slide 9: Stitched sensor development
MLR1
ER1
ER2
~12mm
~16mm
~260mm
~14mm
~280mm
~100mm
 70 chips inside
25.5mm
x10
Full-scale Prototype
1-D stitching

## Slide 10: MOSS Monolithic Stitched Sensor Prototype
https://indico.cern.ch/event/1091910/

## Slide 11: Concept for Pixels Readout in a Region
Global Strobe
In-Pixel Latch
Row OR output line
Selection of row (token)
  Skip rows with no hits
Column out line
  Pixels of the selected row drive the column line

## Slide 12: Digital pixel logic

## Slide 13: Signal Regeneration

## Slide 14
Post-layout extraction simulation results
PWELL=0 V
Typical corner (1.2V, typical process, 27degrees)
Output delay
(FE output over Vth 0.6V  ROW_PIXEL_OUT) : 24 ns
(ROW_PIXEL_OUT  ROW_OR) : 1.022ns
(ROW_OR  ROW_OR) : 0.612ns
STROBE group-to-group delay 0.719ns
STROBE regeneration dynamic energy 84.1 fJ
SELECT_ROW group-to-group delay 1.21ns
Pixel digital
Dynamic energy 2.32pJ
Static energy 16.2fJ for 5us
Static leakage current 2.71nA
Group digital
Static energy 3.65pJ for 5us
Static leakage current 608nA
delay
Group extraction
Group extraction
Group extraction
risetime
delay
Power, leakage

## Slide 15: Pre-mock submission – Dec 2021
https://indico.cern.ch/event/1104620/

## Slide 16: Next generation sensor design for LS3
Good timing (10’s of 𝑝𝑠?)
  Avalanche photodiode
  Digital operation without the analog front end
High spatial resolution
  Pixel detector
Low power consumption
  Low digital activity (~ low occupancy)
  Digital periphery with the sparcified readout
Simple operation
  Built-in tolerance in the APD operation

## Slide 17: Digital pixel coupled with low gain APD
Thick epitaxial layer of about 25 m for charge collection
Low gain APD ()
Collection electrode with small capacitance
1.2(V) LVCMOS digital pixel operation
Snoeys, W. "CMOS monolithic active pixel sensors for high energy physics." Nuclear Instruments and Methods in Physics Research Section A 2014

## Slide 18: Publications of interest
Mori, Mitsuyoshi, et al. "6.6 A 1280× 720 single-photon-detecting image sensor with 100dB dynamic range using a sensitivity-boosting technique." 2016 IEEE ISSCC
Patent EP 3448018A1 - PANASONIC 2019
3.8um pixel
Normal mode / High-sensitivity mode
Abrupt p-n junction between a p- region and n region
Vertical field strength is controlled by the potential of a surface p+ layer (either Vp+ or VAPD)

## Slide 19
APD into the pixel
Noise current through
shared bulk
Defects caused by the wafer sawing
Junction Termination Edge
Younghoon Han
Kiwon seo