## Slide 1: Experimental tests of a scanner prototype for imaging with protons developed at IEM-CSIC
A.N. Nerio
Instituto de Estructura de la Materia (CSIC)
J.A. Briza,b, M.J.G. Borgea, E. Nácherc, O. Tengblada, A. Pereaa, V.G. Távoraa
aInstituto de Estructura de la Materia, CSIC, Madrid, Spain
bFacultad de CCias Físicas, Universidad Complutense de Madrid, Madrid, Spain
cInstituto de Física Corpuscular, CSIC-Universidad de Valencia, Valencia, Spain

## Slide 2: Protontherapy
Proton beams with energy between 70-250 MeV
Better tumor control
  Less toxicity
  Minimal exit dose
  Less dose to healthy cells
1 Robert P. Johnson et al. Rep. Prog. Phys. 81 (2018) 016701
Images from: https://www.newswise.com/articles/media-article/741601
H. Suit et al., Radiother. Oncol. (2010) 95, 3–22
Treatment plans use X-ray CT (in HU) to generate the RSP maps
The conversion process induces large uncertainties on the proton range (up to 11%!!)1

## Slide 3: Experimental setup
DSSSD1
DSSSD2
CEPA4
Phantom
PROTON BEAM
DSSSDs:
Area: 50x50 mm2
16x16 pixels
CEPA4:
4 phoswich detectors
  LaBr3: 4 cm
  LaCl3: 6 cm
Area: 54x54 mm2

## Slide 4: Experimental setup
Ti foil
Scattered beam
Non-scattered beam
0o
Experimental chamber

## Slide 5: Study of uniform thickness phantoms

## Slide 6: Imaged phantoms
Cross phantom
Derenzo-type phantom
Uniform phantom
PMMA: Poly(Methyl MethAcrylate)
Aluminum

## Slide 7: pRads: Cross-shaped phantom
The shape of the phantoms were reproduced.
Process to get the energy per hit on the scanner detectors (E=ED1+ED2+ECEPA4)
Sum of the energy deposited
Number of hits
Energy deposited per proton
39.70(5) mm
39.85(5) mm

## Slide 8: pRads: Cross-shaped phantom
Three well-differentiated zones are observed: PMMA, air, and aluminum.
As expected, higher statistics increased the uniformity of the images.
Average energy deposited per hit on each material was consistent.
PMMA
Air
Aluminum
1-hour measurement (~1.6x106counts)
30-min measurement (~8x105counts)

## Slide 9: pRads: Derenzo phantom
Experimental image
Simulated image
The different structures of the phantom are observed.
Simulated results displayed more intense red and blue zones.
Circles of d=2mm are less defined in the experimental image but they are still distinguished.
f=s=5 mm
f=s=3 mm
f=s=2 mm
f=s=1 mm
5 mm
3 mm
2 mm

## Slide 10: Derenzo measurements
1 Briz, J. A., et al., IEEE Transactions on Nuclear Science 69.4 (2022): 696-702.

## Slide 11: Conclusions
An experimental system that has been used to take radiograph images was designed.
Data has been taken with different beam energies.
Different phantoms were studied
Experimental results were compared with the simulated results, obtaining a good agreement.

## Slide 12: Study of cylindrical phantoms

## Slide 13
Measurements
Tomography:
3D Derenzo pattern
Ethanol-Water inserts
ethanol
water
Beam energy: 110 MeV
Ethanol-Water:
- 0-180º in 18º steps
3D Derenzo pattern:
- 0-360º in 18º steps
- 0-180º in 9º steps
- 0-180º in 1.8º steps
(Scan recording images
at multiple positions)

## Slide 14: Ethanol and water phantom
Region | RSP [2] | RSP exp
Water | 1.000 | 1.00(4)
Ethanol | 0.815 | 0.81(3)
PMMA | 1.153 | 1.15(1)
[2] NIM B 436 (2018) 99-106
Ethanol
Water
PMMA

## Slide 15: Derenzo 3/5/7

## Slide 16: Comparison: lowest statistics reconstructions
Sinograms obtained taking 80, 320, 1280 and 5120 protons/mm2 per projection.
All structures are observed, even with the lowest statistics achieved.
The structures are better observed and defined at least 320 protons/mm2 per pRad.

## Slide 17: Comparison: varying the angular step
Conclusion:
It was possible to reproduce well the structures of the phantom using at least 20 projections (one each 9 degrees) with 3600 protons/mm2 each.
Image quality improves as we take more projections with smaller angular steps.

## Slide 18: Conclusions
Our experimental system has been used for pCT imaging.
Different phantoms were studied
Outlook
Data analysis of the experiment performed in June 2022.
Third experiment expected for December 2022.

## Slide 19: Thanks for your attention