## Slide 1
FCC-hh circumference for RF synchronization
H. Damerau, I. Karpov, L. Zhang
FCC-ee Parameters Meeting #08
14/12/2021
Many thanks to Philippe Baudrenghien, Tor Raubenheimer, and Elena Shaposhnikova

## Slide 2
Introduction
Conventional cogwheel rephasing
Common fiducial frequency between two accelerators of revolution frequency ratio
Other schemes may be conceivable, but doors for the conventional transfer from SPS and LHC to FCC-hh should not be closed
Follow-up of presentation at 148th FCC-ee Optics Design Meeting & 19th FCCIS WP2.2 Meeting (I. Karpov, HD)
Allow numerators and denominators, n1, n2 > 100

## Slide 3
Introduction
Constraints
FCC and injector parameters (design values)
Additional constraints
 | Value | Remark
2pR, FCC | 91172.7 m | Intended circumference
2pR, LHC | 26658.7 m | 2p ∙ 11 ∙ 100 m ∙ 27/7, hLHC = 35640
2pR, SPS | 6911.5 m | 2p ∙ 11 ∙ 100 m, hSPS = 2 ∙ 4620
 | Value | Remark
Bunch spacing | ~25 ns | Every 10th bucket occupied at fRF ≈ 400 MHz
Maximum wait time | ~30 ms | Transfer possible at least every 100 turns
fRF,SPS and fRF,LHC | 400.79 MHz | Slightly change RF frequency?
2pR, PS | 628.3 m | 2p ∙ 100 m, still in use as FCC-hh pre-injector?

## Slide 4
Most restrictive constraints
Everything respected, solution with less than 100 turns periodicity in FCC
hLHC = 35640, hSPS = 2 ∙ 4620
Three interesting candidates, hFCC = 121440, 121880, 122760
hFCC | 2pRFCC [m] | D2pRFCC [m] | hFCC/hLHC | hFCC/hSPS | Largest prime factor
121880 | 91166.0 | -6.66 | 277/81 | 277/21 | 277
121770 | 91083.7 | -88.9 | 41/12 | 369/28 | 41
122040 | 91285.7 | 113.2 | 113/33 | 1017/77 | 113
121680 | 91016.4 | -156.3 | 338/99 | 1014/77 | 13
122100 | 91330.6 | 157.9 | 185/54 | 185/14 | 37
122320 | 91495.1 | 322.5 | 278/81 | 278/21 | 139
121440 | 90836.9 | -335.8 | 92/27 | 92/7 | 23
122400 | 91555.0 | 382.3 | 340/99 | 1020/77 | 17
121320 | 90747.1 | -452.5 | 337/99 | 1011/77 | 337
122760 | 91824.3 | 651.6 | 31/9 | 93/7 | 31
Ascending FCC circumference change

## Slide 5
Less constrained case: hFCC
Keep harmonics in LHC and SPS: hLHC = 35640, hSPS = 2 ∙ 4620
Allow non-continuous bunch clock in FCC: hFCC not dividable by 10
hFCC | 2pRFCC [m] | D2pRFCC [m] | hFCC/hLHC | hFCC/hSPS | Largest prime factor
121880 | 91166.0 | -6.66 | 277/81 | 277/21 | 277
121905 | 91184.7 | 12.0 | 301/88 | 1161/88 | 43
121968 | 91231.9 | 59.2 | 154/45 | 66/5 | 11
121770 | 91083.7 | -88.9 | 41/12 | 369/28 | 41
122040 | 91285.7 | 113.2 | 113/33 | 1017/77 | 113
121680 | 91016.4 | -156.3 | 338/99 | 1014/77 | 13
122100 | 91330.6 | 157.9 | 185/54 | 185/14 | 37
121572 | 90935.6 | -237.0 | 307/90 | 921/70 | 307
122265 | 91454.0 | 281.3 | 247/72 | 741/56 | 19
122320 | 91495.1 | 322.5 | 278/81 | 278/21 | 139
…seven further combinations more… |  |  |  |  | 
122760 | 91824.3 | 651.6 | 31/9 | 93/7 | 31
Ascending FCC circumference change

## Slide 6
Less constrained case: fRF
Continuous bunch clock, fRF/10
Allow RF frequency to vary around
hLHC = 35640 + 27 ∙ 10 ∙ 11 ∙ n, n = …-2, -1, 0, 1, 2, … (33.4 MHz)
No better ratios found, even for fRF = 367.4 MHz or 434.2 MHz
hFCC | 2pRFCC [m] | D2pRFCC [m] | hLHC | hFCC/hLHC | hFCC/hSPS | Largest prime factor
111870 | 91285.7 | 113.0 | 32670 | 113/33 | 1017/77 | 113
132210 | 91285.7 | 113.0 | 38610 | 113/33 | 1017/77 | 113
111540 | 91016.4 | -156.3 | 32670 | 338/99 | 1014/77 | 13
131820 | 91016.4 | -156.3 | 38610 | 338/99 | 1014/77 | 13
131670 | 90912.9 | -259.8 | 38610 | 133/39 | 171/13 | 19
112200 | 91555.0 | 382.3 | 32670 | 340/99 | 1020/77 | 17
132600 | 91555.0 | 382.3 | 38610 | 340/99 | 1020/77 | 17
… |  |  |  |  |  | 
Ascending FCC circumference change

## Slide 7
Less constrained case: new pre-injector
Continuous bunch clock fRF/10, but different RF frequency?
No PS as pre-injector: prime factor 11 not needed in h
hLHC = 35640 + 27 ∙ 10 ∙ n, n = …-2, -1, 0, 1, 2… (3.04 MHz)
Only few additional options
hFCC | 2pRFCC [m] | D2pRFCC [m] | hLHC | hFCC/hLHC | hFCC/hSPS | Largest prime factor
several | 91166.0 | -6.66 | several | 277/81 | 277/21 | 277
119070 | 91135.4 | -37.3 | 34830 | 147/43 | 567/43 | 43
several | 91231.9 | 59.2 | several | 154/45 | 66/5 | 11
several | 91083.7 | -88.9 | several | 41/12 | 369/28 | 41
several | 91285.7 | 113.0 | several | 113/33 | 1017/77 | 113
113400 | 91029.5 | -143.1 | 33210 | 140/41 | 540/41 | 41
130410 | 91320.1 | 147.4 | 38070 | 161/47 | 621 | 47
… |  |  |  |  |  | 
Ascending FCC circumference change

## Slide 8
Summary
Best match for RF: hFCC = 122760 = 23 ∙ 32 ∙ 5 ∙ 11 ∙ 31, but for 651.6 m longer FCC circumference
Alternative hFCC = 121880 = 23 ∙ 5 ∙ 11 ∙ 277 seems to be an interesting choice, but 277 is large prime factor
  Shorten FCC by 6.66 m with respect to 91172.7 m
Next interesting case hFCC = 121770 = 2 ∙ 33 ∙ 5 ∙ 11 ∙ 41 requires already 88.9 m shorter ring
Non-continuous bunch clock option? hFCC = 121968 = 24 ∙ 32 ∙ 7 ∙ 112 for 59.2 m longer ring
No further extremely favorable options when allowing RF frequency to change in range 337.4…449.8 MHz
Different pre-injector length: hFCC = 119070 = 2 ∙ 35 ∙ 5 ∙ 72 for 37.3 m shorter FCC circumference

## Slide 9
Questions and further study
How flexible is 2pRFCC = 91.17 km?
  Selected range of rations and frequencies
Acceptable to wait for transfer?
  Longest presently for SPS-AWAKE transfer (1/9.97 Hz  ~100 ms)
Continuity of bunch clocks? Need of hFCC dividable by 10?
  Impact on accelerator and experiments
Pre-injector replacing PS and change RF frequency?
  Retire factor 11 in all harmonics
Solutions for other RF frequencies: 600, 650, 800 MHz?
  To be checked